## Slide 1
Through the implementation of GIS, major challenges faced by Utilities as mentioned below are addressed
Need for GIS – Challenges faced prior to GIS implementation and Current Use Cases
To address the issue, GOI intervened and took initiative under R-APDRP for establishment of IT system with extensive use of GIS
However, over the years, DISCOMs have accumulated losses due to high T&D and Commercial losses. This has been mainly attributed to Non-adoption of IT in network management, operations and energy accounting
Power Distribution Company deals with HT & LT electrical networks and related consumers spread over wide geographical area to ensure supply availability
Challenges faced by Utilities before GIS
In past, Discoms have been using conventional Physical Area Maps for proper O&M and management of the system
With respect to above, GIS implementation in power utilities finds following use cases:
  Mapping of all assets (66kV/33KV/11KV, LT) including HT & LT network entities upto poles & major landmarks
  Collection of consumers attributes through door-to-door survey and indexing with network assets.
  Overlaying of digitized electrical network & consumers on the base map with area features and attributes using SW for GIS application.
  Integration of GIS system with other IT applications

## Slide 2
GIS implementation typically is laced with some challenges as outlined below
Major challenges in GIS implementation by Utilities in Power Sector
Shortage of technical manpower
Available manpower not technically adept to replicate the network topology and connection logic
Dependence on third party vendors
Over dependence on vendor and non-availability of internal monitoring capability by utility, many a time led to vendor service quality issues are unrecognized.
Non-maintenance of data records
Utilities don’t maintain records, and as a result, entire work has to be carried out through field survey. This in turn brings dependencies on linemen, who may not be too keen to engage or cooperate for lack of personal interest
Delayed decisions at Utility side
Due to absence of clear understanding of the use of GIS use cases, decisions are delayed at utility side.
Costly software
Most of the SIs implemented ArcFM solution or GESmall world with additional custom development during RAPRDP; which are costly in terms of maintenance
Lack of continual data updation
As utility network constantly evolves, in the absence of continual update, legacy data become unreliable or unusable. So, for starting fresh the old data also need complete refresh.
Non-availability of vendor support
Due to non-availability of vendor support most utilities are not able to download data created or migrate to low cost solutions
Complexity of Enterprise GIS Technologies
The deployment of Enterprise GIS within the power sector involves the integration of complex technologies, such as spatial databases, web mapping services, and real-time monitoring systems.

## Slide 3
Detailed implementation outlay of GIS for Tata Power Delhi Distribution Ltd (TPDDL) is provided below
GIS Implementation Case Studies – Tata Power Delhi Distribution Limited (1/2)
Use Cases of GIS at TPDDL
End User
System/Process Integration
Search Assets
View Asset Location
View Asset Connectivity
Get Network Reports
Outage Management System (OMS)
Energy Audit
Connection Management
Asset Management
GIS Outlay as adopted by TPDDL
Geographic Information System (GIS) implemented by TPDDL
SAP-ISU
CYMDIST
Energy Auditing
Network Planning
Feeder to DT and DT to Consumer hierarchy from GIS
SAP-ISU
Connection Management
Subscriber Indexing
Digitization
SAP-PM
Design manager
Job Order Management
Field Automation
Operations Management
SCADA
DMS
OMS
Fault Management
Planned Interruptions Management
Network Planning
Notes: CYMDIST - Distribution system analysis package

## Slide 4
GIS-based models of TPDDL wherein Asset, Operation, Connection and Network Management is carried out
GIS Implementation Case Studies – Tata Power Delhi Distribution Limited (2/2)
GIS Processing
Design/Notification for -
  Network changes (ST/HT)
  New Installation /Augmentation
  Movement
  Retirement
  Scheme clearance requests
Geo-referenced mapping of Assets
Single Line Diagram Update
Tagging of Scheme
Integration with SAP
Asset Equalization with GIS-SAP-FAR
Integration with OMS
Planned Outage
Complaint Management
Integration with DMS
Geo-tagged SLD
OUTPUT
GIS Processing
Network details through notification
Consumer linkage with Pole No.
LT network intimation
OMS notification
INPUT
Geo-referenced mapping of Assets and network
Mapping of consumers.
Data Merging and Creation of Circuit id
Delivery of updated GIS for operation.
OUTPUT
GIS Processing
Network changes due to
Load Balancing
Network Extension
Network Augmentation
New Electrification
Network Shifting
INPUT
Geo-referenced digitization of -
Revised network route
Revised network connectivity
Integration with Network Planning tool (CYMDIST)
GIS based Network Planning
OUTPUT
GIS Processing
Pole No. from Meter Management Group
INPUT
Consumer Mapping in GIS
Connectivity of consumer with -
LT Feeder
Transformer
HT Feeder
ST Feeder
Integration with SAP
Energy auditing
Revenue Protection
Integration with OMS
List of affected consumers
Location of affected consumers
Crew management
OUTPUT
GIS Input Output for Asset Management
GIS Input Output for Operation Management
GIS Input Output for Connection Management
GIS Input Output for Network Management
INPUT
Notes: CYMDIST - Distribution system analysis package

## Slide 5
Key Takeaways
Growth trend in both Indian Power Sector as well as global GIS market (with countries like India and China leading in the Asia Pacific region as per market research reports)
Increasing trend of Indian Power Utilities adopting GIS
Opportunity for Deloitte to tap into growing GIS market especially with respect to the Power sector
Significant on-ground personnel with relevant experience would likely be required
Relook at Deloitte’s current capabilities to carry out such projects and addressing gaps if any finds some merit