## Slide 1
Bid Tariff Analysis for Competitive Bidding
810 MW RVUNL Solar Park Tender
Jan 2023

## Slide 2: Salient Points of RVUNL 810 MW Tender
Mode of selection
The selection will be carried out through e-bidding followed by e-Reverse Auction process
Capacity offered
Entire 810 MW capacity to be awarded to L1 bidder
No part capacity to be awarded (through bucket filling process)
Responsibility of Solar Project Developer (SPD)
Design, installation and operation of Solar PV Power Project including the electrical network up to the Pooling Substation
Securing connectivity up to Pooling substation
Connectivity
Solar plant to be connected to pooling substation at 33 kV level
Power would be finally evacuated from RVPN 400 kV substation
Key Timelines
Last date of Bid Submission: 22nd Feb 2023
Date of Bid Opening: 24th Feb 2023
PPA signing: Within 90 days of LOI (date may be modified to align with commissioning timeline of transmission evacuation infrastructure)
Land Handover to developer: 3 months from PPA
Financial Closure: 9 months from PPA
Scheduled Commissioning Date: 15 months from PPA
Key competitors attending pre-bid meeting
Avaada Energy, Renew Power, NTPC, Tata Power, ACME Solar, Sprng Energy, Blupine Energy

## Slide 3: Approach for Estimation of Bid Tariff
Assessment of Key Input Parameters based on market intelligence
Preparation of Financial Model based on the Major Input Parameters with estimation of Tariff and Equity IRR
Simulation of the Major Input Parameters based on Permissible Range to arrive at a range of tariffs and corresponding Equity IRRs
Assessment of a competitive range of bid tariff based on market trend and permissible equity IRR
Key Parameters Considered:
Module Price
Balance of System (BOS) Cost
Interest Rate

## Slide 4: Key driving factors for Equity IRR for solar generation project
BOS Price
For every Rs. 0.1 Cr/MWp fall in BOS, Equity IRR increases by around 0.8%
Balance of System (BOS) comprises 30-35% of capital cost – its optimization at can also lead to cost saving
Module Price
For every Rs 0.1 Cr/MWp fall in Module Price, Equity IRR increases by around 0.8% - 0.9%
Module cost comprises around 65-70% of capital cost (based on past bids obtained from EPC players for CIL’s projects as well as market trends) – it is important to explore avenues to optimize module cost
Rate of Interest
For every 0.5% fall in interest rate, Equity IRR increases by around 0.75% – 0.8%
Refinancing option through External Commercial Borrowings (ECB) post COD may be considered in line with the practice followed by leading CPSUs in solar power generation business

## Slide 5: Module Procurement Modalities
Modalities of Module Procurement
A. Direct import of Modules
C. Use of indigenous modules using domestically manufactured cells
B. Use of domestically manufactured modules using imported cells
As per MNRE Order dated 02.02.2019, only the models and manufacturers including in the list of ALMM (Approved List of Models and Manufacturers) as updated from time to time by MNRE can be utilized in Govt. Related solar projects including Tariff Based Competitive Bidding. Thus this modality can not be adopted
Module manufacturing capacity in India is currently more than 6 times that of cell manufacturing capacity; thus there is significant demand supply mismatch
Even if demand supply position improves in future, owing to lack of economies of scale, the cost of domestic cells even without the imposition of BCD would be significantly higher than the Chinese counterparts (including BCD)
This is the model used by majority of the domestic module manufacturers wherein they procure cells from outide (majorly China), and domestically manufacture the modules using the imported cells
Cell manufacturing capacity in China was 361 GW in 2021 end and is estimated to have grown to 600 GW by Dec 2022*

## Slide 6: Basis of Module Price Forecast
Present Module Price based on inputs from Module Suppliers:
Costs (Rs./Wp) (excl. GST) | Current Price | 2024 (Predicted) | Remarks, if any
Cell Price | 12.80 | 7.59 | Based on market trend and inputs from key module suppliers
Aluminium Price | 1.71 | 1.70 | Based on Deloitte Research; Aluminium cost forecasts provided as Annexure 1
Copper Price | 0.70 | 0.62 | Based on Deloitte Research; Copper cost forecasts provided as Annexure 2
Glass Price | 2.92 | 3.15 | Based on Deloitte Research; Glass price forecast provided as Annexure 3
Other Materials* | 7.73 | 7.73 | Insignificant change envisaged
Module Price (Rs/Wp)(excl GST) | 25.85 | 20.79 | 
Total Cost (Rs./Wp) including Transportation Cost ( ~30p/Wp) | ~26.15 | ~21.09 | 
*EVA, Back sheet, Tolling and Minor Raw Materials |  |  | 
Forecasted module cost Rs 21/Wp (excl. GST) is in line with price forecast as discussed with key module suppliers
Thus, range of module prices considered for scenario analysis to determine corresponding Equity IRR:
Rs 21/Wp – Rs 26/Wp (excl GST)
Further, if CIL can negotiate cell prices on behalf of Module Manufacturer and if certain discount is resultantly achieved, then it will have further beneficial impact on the overall Module cost vis a vis the Equity IRR of the project. Same is shown in Annexure A

## Slide 7: Basis of BOS Cost Forecast
Based on recent awarded tenders, average BOS cost considered: Rs 1.32 Cr/MWp
BOS Costs (incl. GST) | 2022 | 2024 (Predicted) | Remarks
 | Rs Cr/MWp | Rs Cr/MWp | 
MMS | 0.33 | 0.28 | Based on impact of decrease in predicted steel prices
BOS | 0.78 | 0.76 | Based on impact of decrease in predicted steel prices
Works | 0.21 | 0.22 | Escalation rate of 5% considered
Total Cost (Rs. Cr/MWp) (incl GST) | 1.32 | 1.27 | 
Thus, BOS cost considered for scenario analysis to determine corresponding Equity IRR:
Rs 1.27 Cr/MWp – Rs 1.32 Cr/MWp (incl GST)
Forecasted BOS costs based on price forecasts of key materials like Aluminium, Steel and Copper are presented below as follows:

## Slide 8: Basis of Interest Rate Considered (1/2)
It is proposed that CIL may secure loan (from Commercial Banks/FI) initially for achievement of Financial Closure
After Commissioning and achievement of COD (Commercial Date of Operationalization), it can avail the route of refinancing through External Commercial Borrowings (ECB) as is also adopted by several PSUs
Rationale for Pre-COD interest rate considered:
For previous GUVNL 100 MW tender, CIL had secured loan for then repo rate + 1.97% spread
Current repo rate as on December 2022 is 6.25%*
Thus, current repo rate + ~2.25% spread i.e. 8.5% rate has been considered as interest rate pre COD
*Historical trend of Repo rate and SBI PLR are provided in Annexure 4

## Slide 9: Basis of Interest Rate Considered (2/2)
Rationale for Post-COD (ECB) interest rate considered:
Leading PSUs like NTPC, NHPC and NLC avail the option of ECB (External Commercial Borrowings). Snapshot of status of details of outstanding loan for the PSUs are provided as below:
NTPC
As on 31st March 2022, NTPC has an outstanding balance of Rs 18,002 Cr w.r.t unsecured Foreign Currency Loans from Banks and Other FIs
SJVN
As on 31st March 2022, SJVN has an outstanding balance of Rs 3,764 Cr w.r.t unsecured Foreign Currency Loans from World Bank (guaranteed by GoI) and PNB, Dubai
NHPC
As on 31st March 2022, NTPC has an outstanding balance of Rs 1,476 Cr w.r.t unsecured Foreign Currency Loans from JICA, MUFG Bank (Singapore)
NLC
As on 31st March 2022, NLC has an outstanding balance of Rs 392 Cr w.r.t unsecured Foreign Currency Loans from KfW, Germany
ECB Interest Rates:
6M USD LIBOR / 6M EURIBOR / 3M TONA / 6M TONA + varying spreads; Fixed rates (1.8%-4.13%) also considered
ECB Interest Rates:
6M USD LIBOR + varying spreads
ECB Interest Rates:
TONA; Fixed rates (1.3%-2.3%) also considered
ECB Interest Rates:
Interest Rate of 0.75% p.a
NTPC
As on 31st March 2022, NTPC has an outstanding balance of Rs 18,002 Cr w.r.t unsecured Foreign Currency Loans from Banks and Other FIs
SJVN
As on 31st March 2022, SJVN has an outstanding balance of Rs 3,764 Cr w.r.t unsecured Foreign Currency Loans from World Bank (guaranteed by GoI) and PNB, Dubai
NHPC
As on 31st March 2022, NHPC has an outstanding balance of Rs 1,476 Cr w.r.t unsecured Foreign Currency Loans from JICA, MUFG Bank (Singapore)
Details of Outstanding Balances against ECBs for above PSUs provided in Annexure 5
Historical Trend of ECB Benchmark Rates provided in Annexure 6
For CIL, current 6M LIBOR rate + spread of 0.3%-1.3% p.a has been considered; and thus, three ECB interest rates post COD have been considered viz. 5.5%, 6% and 6.5%

## Slide 10: Basis of Tariff Considered (1/3)
Key Considerations for determination of Tariff Range
A. Recently Discovered Tariffs through Reverse Auctions
B. Average ECR of RVUNL TPPS
Based on recently discovered solar tariffs; a range is determined w.r.t probable tariffs that may be discovered
Cost of solar power (tariff) has to be less than the Energy Charge Rate of existing TPPs of RVUNL with which solar power is proposed to be bundled. Thus, probable tariff range can be envisaged through prevalent ECR rates of current existing TPPS of RVUN:

## Slide 11: Basis of Tariff Considered (2/3) - Recently Discovered Tariffs through Reverse Auctions
Source: Deloitte Research
All figures are in Rs/kWh
Chart: 
| Calpine Subsico Solar | NTPC Renewable | Sprng Natural Power Source | METKA EGN Singapore | ReNew Solar | ACME Solar | Project Eight (Ayana) | SolarOne Energy (Fortum) | Project Eight (Ayana) | SolarOne Energy (Fortum) | SJVN | SolarXL Alpha Energy | Amsa Solar Energy | Hinduja Renewables | Aditya Birla | Hinduja Renewable | SJVN | SJVN Green Energy | Juniper Green Energy | Tata Power Renewable Energy | Sukhbir Agro Energy | Avaada Energy | NTPC Renewable Energy | Avaada Energy | Solarcraft (Blupine Energy) | Solairedirect (Engie) | Tata Power Renewable Energy | Utkrrisht Solar (UPC Renewables) | SolarArise | SJVN Green Energy | Tata Power Renewable Energy | SECI RAJASTHAN 1785 MW (Dec '21) | SECI KOPPAL 600 MW (Feb '22) | SECI GADAG 600 MW (Feb '22) | GUVNL 500 MW Ph-XIII (Mar '22) | GUVNL 500 MW Ph-XIV (Jun '22) | MSEDCL 500 MW Ph-VII (Aug '22) | MSEDCL 500 MW Ph-VIII (Sep '22) | GUVNL 750 MW Ph-XVI (Sep '22) | MSEDCL Solar Ph-IX (Intra State)
Final Bid Tariff (Rs/kWh) | 2.17 | 2.17 | 2.17 | 2.17 | 2.18 | 2.18 | 2.36 | 2.37 | 2.35 | 2.36 | 2.29 | 2.29 | 2.29 | 2.29 | 2.3 | 2.3 | 2.31 | 2.9 | 2.9 | 2.91 | 2.91 | 2.91 | 2.82 | 2.83 | 2.49 | 2.5 | 2.65 | 2.66 | 2.9 | 2.95 | 2.97

## Slide 12: Basis of Tariff Considered (3/3) - ECR and PLF of RVUNL Coal TPPs
Chart: 
| Suratgarh Thermal Power Station (SSTPS) | Kota Super Thermal Power Station (KSTPS) | Suratgarh Super Critical Thermal Power Station (SSCTPP) | Kalisindh Thermal Power Plant (KaSTPP) | Chhabra Thermal Power Plant (CTPP) | Chhabra Super Critical Thermal Power Projec (CSCTPP)
Avg ECR for Mar '22 - Oct '22 (Rs/kWh) | 4.32 | 3.39 | 3.3 | 2.99 | 2.84 | 2.39
PLF for Apr '22 - Aug '22 (%) | 0.5368 | 0.7114 | 0.3085 | 0.5762 | 0.5769 | 0.7078
ECR Figures in Rs/kWh
Source: RVUNL website, National Power Portal
Range of Tariff Considered: Rs 2.50/kWh – Rs 2.90/kWh; based on tariffs discovered and ECR rates of RVUNL TPPs

## Slide 13: Ranges considered for Financial Scenario Analysis
Range of Module Cost
Rs 21/Wp – Rs 26/Wp (excl GST) (including Transportation cost)
Range of BOS Cost
Rs 1.27 Cr/MWp – Rs 1.32 Cr/MWp (incl GST)
Scenarios for ECB Interest Rate (Post COD)
5.5%, 6%, 6.5% (Pre COD Interest Rate for Commercial Loan considered at 8.5%)
Range of Tariff Rates Considered*
Rs 2.50/kWh – Rs 2.90/kWh
*ECR of RVUNL TPPs and latest tariffs discovered have been provided in Annexure 4 and Annexure 5 respectively

## Slide 14: Scenarios of Equity IRR for varying Project Cost and Tariff (1/3)
Module Price (Rs/Wp) (excl. GST) | BOS Price (Rs Cr/MWp) (incl GST) | Capex - hard cost excl. land, solar park charges (Rs Cr/MW) | Upfront Charges for Land and Solar Park (Rs Cr/MW) | Tariff (Rs/kWh) |  |  |  | 
 |  |  |  | 2.50 | 2.60 | 2.70 | 2.80 | 2.90
21 | 1.27 | 5.08 | 0.52 | 5.48% | 6.91 | 8.43% | 10.05% | 11.76%
22 | 1.28 | 5.25 | 0.52 | 4.64% | 5.97% | 7.38% | 8.88% | 10.47%
23 | 1.29 | 5.42 | 0.52 | 3.89% | 5.12% | 6.44% | 7.83% | 9.30%
24 | 1.30 | 5.59 | 0.52 | 3.21% | 4.36% | 5.59% | 6.88% | 8.26%
25 | 1.31 | 5.76 | 0.52 | 2.59% | 3.67% | 4.82% | 6.03% | 7.31%
26 | 1.32 | 5.94 | 0.52 | 2.03% | 3.05% | 4.12% | 5.25% | 6.45%
Scenario-1: Interest Rate on loan pre-COD – 8.5%; Refinanced ECB rate post COD: 6.5%
Note: The above scenario analysis is based on preliminary study basis market inputs and is subject to change

## Slide 15: Scenarios of Equity IRR for varying Project Cost and Tariff (2/3)
Scenario-2: Interest Rate on loan pre-COD – 8.5%; Refinanced ECB rate post COD: 6.0%
Note: The above scenario analysis is based on preliminary study basis market inputs and is subject to change
Module Price (Rs/Wp) (excl. GST) | BOS Price (Rs Cr/MWp) (incl GST) | Capex - hard cost excl. land, solar park charges (Rs Cr/MW) | Upfront Charges for Land and Solar Park (Rs Cr/MW) | Tariff (Rs/kWh) |  |  |  | 
 |  |  |  | 2.50 | 2.60 | 2.70 | 2.80 | 2.90
21 | 1.27 | 5.08 | 0.52 | 6.25% | 7.77% | 9.39% | 11.10% | 12.92%
22 | 1.28 | 5.25 | 0.52 | 5.36% | 6.77% | 8.26% | 9.86% | 11.54%
23 | 1.29 | 5.42 | 0.52 | 4.55% | 5.87% | 7.26% | 8.74% | 10.30%
24 | 1.30 | 5.59 | 0.52 | 3.83% | 5.05% | 6.35% | 7.73% | 9.19%
25 | 1.31 | 5.76 | 0.52 | 3.17% | 4.32% | 5.53% | 6.82% | 8.18%
26 | 1.32 | 5.94 | 0.52 | 2.57% | 3.65% | 4.79% | 6.00% | 7.27%

## Slide 16: Scenarios of Equity IRR for varying Project Cost and Tariff (3/3)
Scenario-3: Interest Rate on loan pre-COD – 8.5%; Refinanced ECB rate post COD: 5.5%
Note: The above scenario analysis is based on preliminary study basis market inputs and is subject to change
Module Price (Rs/Wp) (excl. GST) | BOS Price (Rs Cr/MWp) (incl GST) | Capex - hard cost excl. land, solar park charges (Rs Cr/MW) | Upfront Charges for Land and Solar Park (Rs Cr/MW) | Tariff (Rs/kWh) |  |  |  | 
 |  |  |  | 2.50 | 2.60 | 2.70 | 2.80 | 2.90
21 | 1.27 | 5.08 | 0.52 | 7.09% | 8.71% | 10.42% | 12.24% | 14.16%
22 | 1.28 | 5.25 | 0.52 | 6.14% | 7.64% | 9.23% | 10.92% | 12.70%
23 | 1.29 | 5.42 | 0.52 | 5.28% | 6.68% | 8.16% | 9.73% | 11.39%
24 | 1.30 | 5.59 | 0.52 | 4.50% | 5.81% | 7.19% | 8.66% | 10.21%
25 | 1.31 | 5.76 | 0.52 | 3.80% | 5.02% | 6.32% | 7.69% | 9.13
26 | 1.32 | 5.94 | 0.52 | 3.16% | 4.31% | 5.52% | 6.81% | 8.16%

## Slide 17: ANNEXURES

## Slide 18: Annexure A: Illustrative benefit on further Discount on Cell Prices
BACK TO MAIN SLIDE
Costs (Rs./Wp) (excl. GST) | 2024 (Predicted) | 2024 (Predicted) (with further discount of 5% on Cell price)
Cell Price | 7.59 | 7.20
Aluminium Price | 1.70 | 1.70
Copper Price | 0.62 | 0.62
Glass Price | 3.15 | 3.15
Other Materials + assembly* | 7.73 | 7.73
Module Price (Rs/Wp)(excl GST) | 20.79 | 20.38
Total Cost (Rs./Wp) including Transportation Cost (~30p/Wp) | ~21.09 | ~20.68
Thus, with 5% further discount in cell price, there is opportunity for reduction in module price by almost Rs. 0.04 Cr/MWp which would resultantly improve the Equity IRR by further 0.35%
Thus, CIL may explore this opportunity to possibly further optimize the Capex and improve the Equity IRR

## Slide 19: Annexure 1: Aluminium Price Forecast (1/2)
Aluminium (US$/lb) |  |  | 
Date | Firm | 2023 | 2024
28-Nov-22 | CIBC | $1.28 | $1.24
25-Nov-22 | Deutsche Bank | $1.01 | $1.22
24-Nov-22 | Macquarie | $1.04 | $1.02
23-Nov-22 | JP Morgan | - | -
23-Nov-22 | UBS | $1.12 | $1.25
21-Nov-22 | Morgan Stanley | - | -
21-Nov-22 | RBC | $1.20 | $1.15
21-Nov-22 | Credit Suisse | $1.10 | $1.30
21-Nov-22 | BMO | $1.05 | $1.09
21-Nov-22 | BofA | $1.24 | $1.59
19-Nov-22 | Jefferies | $0.98 | $1.16
16-Nov-22 | Barclays | $1.13 | $1.32
13-Nov-22 | HSBC | $1.00 | $1.02
09-Nov-22 | BNP Paribas | $1.00 | $1.04
18-Oct-22 | Berenberg | $0.85 | $0.94
Average |  | $1.08 | $1.18
Pound to Kg: 2.205
 | USD/Pound | USD/ton
Average of 2023 and 2024 (Forecast) | $1.13 | $2,488.27
Source: Deloitte Research
BACK TO MAIN SLIDE

## Slide 20: Annexure 1: Aluminium Price Forecast (2/2)
BACK TO MAIN SLIDE
 | Jan-23 | Average 2023-2024
Aluminium Cost (USD/ton) | 2511 | 2488.3
Unit Required per Wp (kg) | 0.008 | 0.008
USD INR Exchange Rate | 81.71 | 85
For Module (INR/Wp) | 1.71 | 1.70

## Slide 21: Annexure 2: Copper Price Forecast (1/2)
Copper (US$/lb) |  |  | 
Date | Firm | 2023 | 2024
28-Nov-22 | CIBC | $3.95 | $3.75
25-Nov-22 | Deutsche Bank | $3.31 | $3.99
23-Nov-22 | JP Morgan | - | -
23-Nov-22 | UBS | $3.00 | $3.50
22-Nov-22 | Canaccord | $3.94 | $4.25
22-Nov-22 | Stifel | $4.00 | $4.50
21-Nov-22 | Morgan Stanley | - | -
21-Nov-22 | Raymond James | $3.75 | -
21-Nov-22 | RBC | $3.75 | $3.75
21-Nov-22 | Credit Suisse | $3.00 | $3.00
21-Nov-22 | Eight Capital | $4.00 | $4.25
21-Nov-22 | BMO | $3.28 | $3.40
21-Nov-22 | Desjardins | $3.50 | $3.80
21-Nov-22 | BofA | $3.91 | $4.48
20-Nov-22 | National Bank | $3.40 | $3.50
19-Nov-22 | Jefferies | $3.29 | $4.31
16-Nov-22 | Barclays | $3.03 | $3.00
15-Nov-22 | Macquarie | $3.28 | $3.45
14-Nov-22 | Paradigm | $4.00 | $4.00
14-Nov-22 | Cormark | $3.85 | $3.75
13-Nov-22 | HSBC | $3.45 | $3.40
09-Nov-22 | TD | $3.50 | $4.00
09-Nov-22 | BNP Paribas | $3.29 | $3.40
01-Nov-22 | Scotia | $3.50 | $4.00
27-Oct-22 | Berenberg | $3.40 | $3.60
25-Oct-22 | Haywood | $3.75 | $4.00
Average |  | $3.55 | $3.79
Source: Deloitte Research
Pound to Kg: 2.205
 | USD/Pound | USD/ton
Average of 2023 and 2024 (Forecast) | $3.66 | $8,079.75
BACK TO MAIN SLIDE

## Slide 22: Annexure 2: Copper Price Forecast (2/2)
BACK TO MAIN SLIDE
 | Jan-23 | Average 2023-2024
Copper Cost (USD/ton) | 9107 | 8080
Unit Required per Wp (kg) | 0.0009 | 0.0009
USD INR Exchange Rate | 81.71 | 85
For Module (INR/Wp) | 0.70 | 0.62

## Slide 23: Annexure 3: Glass Price Forecast
CAGR | Glass Price (USD/sq. mm) |  | 
CAGR | 2021 (Historical) | 2023 (Current) | 2024 (Predicted)
4.0% | 3.7 | 4.0 | 4.2
 | 2023 (Current) | 2024 (Predicted)
Glass (USD/sq mm) | 4.00 | 4.16
Unit required per Wp is 0.0089 sq. mm |  | 
Glass (Rs/Wp) | 2.92 | 3.15
BACK TO MAIN SLIDE
Source: Deloitte Research

## Slide 24: Annexure 4: Historical Trend of Repo Rate and SBI PLR
BACK TO MAIN SLIDE
Source: Deloitte Research
Chart: 
6.25%

## Slide 25: Annexure 5: Details of Outstanding Balances against ECBs for Leading PSUs
Particulars | (Rs. Cr)* | Details for FY 2021-22
NTPC: |  | 
Unsecured Foreign Currency Loans from Banks | 13194 | Floating rate of interest linked to 6M USD LIBOR / 6M EURIBOR / 3M TONA / 6M TONA
 | 84 | Fixed rate of interest of 1.88%
Unsecured Foreign Currency Loans from other Fis | 1863 | Fixed rate of interest ranging from 1.88% p.a. to 4.13% p.a
 | 1540 | Floating rate of interest linked to 3M TONA/6M TONA
Unsecured Foreign Currency Loans from other FIs and guaranteed by GOI | 1321 | Fixed rate of interest ranging from 1.80% p.a. to 2.30% p.a.
SJVN: |  | 
Unsecured Foreign Currency Loan - World Bank (IBRD) (Guaranteed by Govt of India) Repayable in 30 half yearly instalments from May 2013 | 1534 | Interest@ 6M LIBOR+variable spread of 0.33% p.a.
Unsecured Foreign Currency Loan - Punjab National Bank, Dubai Repayable after 5 years from the date of drawal starting w.e.f. september 2026 | 2230 | Interest @ 6M LIBOR+spread 1.30% p.a
NHPC: |  | 
Unsecured Foreign Currency Loan - Japan International Cooperation Agency Tranche-I (guaranteed by Government of India) (Repayable in 8 equal half yearly instalments of Rs. 7.60 Crore each upto 20.01.2026) | 61 | Fixed interest rate of 2.3% as on 31.03.2022
Unsecured Foreign Currency Loan - Japan International Cooperation Agency Tranche-II (guaranteed by Government of India) (Repayable in 12 equal half yearly instalments of Rs. 24.93 Crore each upto 20.12.2027) | 299 | Fixed interest rate of 2.3% as on 31.03.2022
Unsecured Foreign Currency Loan - Japan International Cooperation Agency Tranche-III (guaranteed by Government of India) (Repayable in 24 equal half yearly instalments of Rs. 18.42 Crore each upto 20.03.2034) | 442 | Fixed interest rate of 1.3% as on 31.03.2022
Unsecured Foreign Currency Loan - MUFG Bank Limited, Singapore (Repayable in one installment bullet on 25.07.2024) | 674 | 6 monthly compounded reference rate (CAS+ Tona + 0.75% ). The loan is hedged at coupon only swap fixed rate of 0.931 % (INR) p.a. & call spread coupan at fixed rate of 6.25% (INR) p.a. with JPY strike price of Rs. 0.90.)
NLC: |  | 
Unsecured Foreign Currency Loan from KfW-Germany - 6.36 Million Euro (6.80 Million Euro) - I Bi- annual equal repayment (€ 0.219 Million each) commenced from 30-12-2001, ending on 30-06-2036. This loan is unsecured but guaranteed by GoI @ guarantee fee of 1.20%. | 50 | Interest rate @ 0.75% p.a
Unsecured Foreign Currency Loan from KfW-Germany - 43.44 Million Euro (46.24 Million Euro) - II (Guaranteed by the Government of India) Bi-annual equal repayment (€ 1.401 Million each) commenced from 30-06-2002, ending on 30-06-2037. This loan is unsecured but guaranteed by GoI @ guarantee fee of 1.20%. | 342 | Interest rate @ 0.75% p.a
*As on 31st Mar 2022
BACK TO MAIN SLIDE

## Slide 26: Annexure 6: Historical Trend of ECB Benchmark Rates
BACK TO MAIN SLIDE
Chart: 
| 43101 | 43132 | 43160 | 43191 | 43221 | 43252 | 43282 | 43313 | 43344 | 43374 | 43405 | 43435 | 43466 | 43497 | 43525 | 43556 | 43586 | 43617 | 43647 | 43678 | 43709 | 43739 | 43770 | 43800 | 43831 | 43862 | 43891 | 43922 | 43952 | 43983 | 44013 | 44044 | 44075 | 44105 | 44136 | 44166 | 44197 | 44228 | 44256 | 44287 | 44317 | 44348 | 44378 | 44409 | 44440 | 44470 | 44501 | 44531 | 44562 | 44593 | 44621 | 44652 | 44682 | 44713 | 44743 | 44774 | 44805 | 44835 | 44866 | 44896
USD 6-M LIBOR | 0.01907 | 0.02089 | 0.02345 | 0.02494 | 0.025 | 0.02496 | 0.0252 | 0.0252 | 0.02569 | 0.02687 | 0.02864 | 0.02889 | 0.02848 | 0.02735 | 0.02675 | 0.02633 | 0.02568 | 0.02301 | 0.02206 | 0.02057 | 0.02049 | 0.01957 | 0.01914 | 0.01901 | 0.01839 | 0.01679 | 0.00964 | 0.01068 | 0.00627 | 0.00426 | 0.00339 | 0.00313 | 0.00279 | 0.00247 | 0.0025 | 0.00256 | 0.00241 | 0.00206 | 0.00201 | 0.00212 | 0.00186 | 0.0016 | 0.00156 | 0.00155 | 0.00152 | 0.00167 | 0.0023 | 0.00306 | 0.00426 | 0.00714 | 0.0121 | 0.01647 | 0.02021 | 0.02633 | 0.03194 | 0.03506 | 0.03989 | 0.04639 | 0.05116 | 0.05162
6-M EURIBOR | -0.00271 | -0.00278 | -0.00271 | -0.0027 | -0.00269 | -0.00269 | -0.00269 | -0.00269 | -0.00268 | -0.00268 | -0.00258 | -0.00248 | -0.00238 | -0.00235 | -0.0023 | -0.00228 | -0.00232 | -0.00254 | -0.00313 | -0.00363 | -0.00439 | -0.00387 | -0.00348 | -0.00345 | -0.00323 | -0.00338 | -0.004 | -0.00276 | -0.00157 | -0.00163 | -0.00295 | -0.00417 | -0.00441 | -0.00481 | -0.00513 | -0.00508 | -0.00532 | -0.00528 | -0.00508 | -0.00512 | -0.00518 | -0.00517 | -0.00513 | -0.00523 | -0.00521 | -0.00526 | -0.00529 | -0.00541 | -0.00539 | -0.00503 | -0.00496 | -0.00362 | -0.00204 | -0.00034 | 0.00238 | 0.00654 | 0.0124 | 0.01775 | 0.02168 | 0.02405
TONA | -0.0004 | -0.00042 | -0.00062 | -0.00063 | -0.00061 | -0.00071 | -0.0007 | -0.00059 | -0.00059 | -0.0006 | -0.0007 | -0.00068 | -0.00064 | -0.00055 | -0.00044 | -0.00068 | -0.0005 | -0.00063 | -0.00071 | -0.00046 | -0.00059 | -0.00022 | -0.00043 | -0.00038 | -0.00032 | -0.00016 | -0.00047 | -0.00036 | -0.00047 | -0.00048 | -0.00028 | -0.00035 | -0.00054 | -0.0002 | -0.00032 | -0.00026 | -0.00017 | -0.00016 | -0.00017 | -0.00012 | -0.00017 | -0.00029 | -0.00036 | -0.00034 | -0.00022 | -0.00027 | -0.0004 | -0.00026 | -0.0002 | -0.00018 | -8e-05 | -0.00012 | -0.00018 | -0.00038 | -0.00012 | -0.00018 | -0.00049 | -0.0005 | -0.00067 | -0.00066

## Slide 27: Annexure 7: Demand-Supply scenario for domestic modules in India - current landscape and projected scenario (1/3)
Source: Deloitte Research
Current Demand Supply Scenario of Module in India
Total Capacity of Modules in India as per latest ALMM list (August 2022)* | ~18 GW
Supply:
Demand:
Total demand based on solar capacity awarded in from April 2021 onwards** | ~16.5 GW
Thus, as can be seen from above, supply of modules in India is barely aligned with the demand, and hence, price has not decreased substantially in recent times
*Latest ALMM list (August 2022) is provided as Annexure 6A
**List of awarded capacities in various tenders since April 2021 is provided as Annexure 6B

## Slide 28: Annexure 7: Demand-Supply scenario for domestic modules in India - current landscape and projected scenario (2/3)
Forecasted Demand Supply Scenario of Module in India
Supply based on expansion plans of Leading Module Suppliers in India:
S. No. | Name of the Manufacturer | Expansion Plans | Capacity expected to be added by 2023 (GW)* | Reference
1 | Waaree | 12 GW by March 2023 | 3 | As per discussion with Module Supplier
2 | Vikram Solar | 6.3 GW by 2024 | 2 | https://www.thehindu.com/business/vikram-solar-mulls-expansion-of-solar-module-production-capacity-to-63-gw/article65411527.ece
3 | Adani (Mundra) | 10 GW of polysilicon-to-solar module capacity by 2025 | 3 | https://www.pv-magazine-india.com/2022/09/29/adani-plans-to-have-10-gw-of-polysilicon-to-solar-module-capacity-by-2025/#:~:text=India's%20Adani%20Solar%20will%20expand,up%20to%20the%20polysilicon%20stage.
4 | RenewSys | 4 GW by end of 2023 (540 Wp and above) | 2 | As per discussion with Module Supplier
5 | Premier Energies | 2.25 GW by Dec 2022 | 1.05 | http://investors.azurepower.com/press-releases/2022/06-13-2022-130204532
6 | Tata Power Solar | Addition of 4 GW module capacity by end of 2023 (16 months from July 2022) | 4 | https://www.tatapower.com/media/PressReleaseDetails/1957/tata-power-to-set-up-mega-solar-manufacturing-plant-in-tamil-nadu
7 | Jakson | 1 GW by March 2023; 2 GW by end of 2024 | 1 | https://www.pv-magazine-india.com/2022/09/28/jakson-reveals-plans-to-manufacture-solar-cells-electrolyzers/
8 | Saatvik Green Energy Pvt. Ltd. | 3 GW by end of 2023 | 2.5 | https://saatvikgroup.com/saatvik-secures-solar-modules-supply-order-for-solar-project-in-mauritius/#:~:text=About%20Saatvik&text=Saatvik%20is%20expanding%20its%20capacity,Modules%20utilising%20M10%20Cell%20technology.
9 | Emmvee Photovoltaic | 3 GW by July 2023 | 1.75 | As per discussion with Module Supplier
10 | Goldi Solar Pvt. Ltd. | 4 GW by end of 2023 | 1.5 | As per discussion with Module Supplier
11 | Pixon Green Energy Pvt. Ltd. |  |  | As per discussion with Module Supplier
12 | Websol Energy System Ltd. | Additional 1.8 GW upcoming | 0.6* | https://www.pv-magazine.com/2022/07/04/indias-websol-to-build-1-8-gw-solar-cell-module-factory/
13 | Sova Solar Ltd. |  | 0.25 | As per discussion with Module Supplier
TOTAL CAPACITY ADDITION EXPECTED BY END OF 2023 | M/s. Novus Green Energy Systems Ltd |  | 23.65 | 

## Slide 29: Annexure 7: Demand-Supply scenario for domestic modules in India - current landscape and projected scenario (3/3)
Forecasted Demand Supply Scenario of Module in India
Supply based on expansion plans of Leading Module Suppliers in India (contd.):
 | Module capacity in current FY (as on August 2022) | Estimated Module Capacity Addition by 2024 | Estimated Total Module Manufacturing Capacity in India by 2024
FUTURE SUPPLY | ~18 GW | ~24 GW | ~42 GW
Demand of Solar Modules based on rate of Capacity awarded in two years from April 2021 onwards:
 | Capacity awarded from April 2021 onwards till date | Estimated capacity further to be awarded by 2024 | Estimated Total Module Manufacturing Capacity in India by 2024
FUTURE DEMAND | ~16.5 GW | ~10 GW | ~26.5 GW
Thus, as can be seen from above, supply of modules in India will be ~59% higher than the expected demand by 2024; hence module prices are expected to decrease significantly with respect to current high rates

## Slide 30: Annexure 7A: List of Module Manufacturers with Capacity as per latest ALMM list (Aug 2022) (1/3)
S. No. | Name of the Manufacturer | Enlisted Capacity (MWs / Year)
1 | Mundra Solar PV Ltd. | 1,100
2 | Vikram Solar Ltd. | 1,050
3 | Bharat Electronics Ltd. | 10
4 | Emmvee Photovoltaic Power Pvt. Ltd. | 500
5 | ORB Energy Pvt. Ltd. | 68
6 | Tata Power Solar Systems Ltd. | 710
7 | Swelect Energy Systems Ltd. | 140
8 | RenewSys India Pvt. Ltd. | 750
9 | Premier Energies Ltd. | 482
10 | Visaka Industries Ltd. | 30
11 | Websol Energy System Ltd. | 250
12 | Sova Solar Ltd. | 240
13 | Goldi Solar Pvt. Ltd. | 500
14 | Australian Premium Solar (India) Pvt. Ltd. | 50
15 | Solex Energy Ltd | 45
16 | Topsun Energy Ltd. | 100
17 | Waaree Energies Ltd. | 1,100
18 | Waaree Energies Ltd. | 500
19 | Waaree Renewables Pvt. Ltd. | 500
20 | Icon Solar-En Power Technologies Pvt. Ltd. | 125
21 | PV Power Technologies Pvt. Ltd. | 200
22 | Saatvik Green Energy Pvt. Ltd. | 510
23 | Navitas Green Solutions Pvt. Ltd. | 100
24 | Central Electronics Ltd. | 35
25 | Patanjali Renewable Energy Pvt. Ltd. | 70
26 | Jakson Engineers Ltd. | 583
Sub-total (MW) |  | 9,748
BACK TO MAIN SLIDE

## Slide 31: Annexure 7A: List of Module Manufacturers with Capacity as per latest ALMM list (Aug 2022) (2/3)
S. No. | Name of the Manufacturer | Enlisted Capacity (MWs / Year)
27 | Himalayan Solar Pvt. Ltd. | 41
28 | Sun N Sand Exim (India) Pvt. Ltd. | 40
29 | Insolation Energy Pvt. Ltd. | 98
30 | Pennar Industries Ltd. | 75
31 | GreenBrilliance Renewable Energy LLP. | 50
32 | Sanelite Solar Pvt. Ltd. | 20
33 | Gautam Solar Pvt. Ltd. | 110
34 | Solarium Green Energy LLP. | 70
35 | Novasys Greenergy Pvt. Ltd | 100
36 | Pahal Solar | 100
37 | Pixon Green Energy Pvt. Ltd. | 355
38 | Alpex Solar Pvt. Ltd. | 240
39 | Vikram Solar Ltd. (Chennai, Kanchipuram, Tamil Nadu Plant) | 972
40 | Contendre Greenergy Pvt. Ltd. | 47
41 | Ritika Systems Pvt. Ltd. | 40
42 | M/s. ECE (India) Energies Pvt. Ltd. | 45
43 | M/s. Rayzon Green Energies. | 200
44 | M/s. Lubi Electronics. | 125
45 | M/s. Kosol Energie Pvt. Ltd. | 171
46 | M/s. Citizen Solar Pvt. Ltd. | 50
47 | M/s. The Wolt Techniques | 20
48 | M/s. Redren Energy Pvt. Ltd | 71
49 | M/s. Nyalkaran Energy LLP | 50
50 | M/s. JJ PV Solar Pvt. Ltd | 17
51 | M/s. Premier Energies Photovoltaic Pvt. Ltd | 711
52 | M/s. Sri Savitr Solar Pvt. Ltd | 68
Subtotal (MW) |  | 3,886
BACK TO MAIN SLIDE

## Slide 32: Annexure 7A: List of Module Manufacturers with Capacity as per latest ALMM list (Aug 2022) (3/3)
S. No. | Name of the Manufacturer | Enlisted Capacity (MWs / Year)
53 | M/s. Novus Green Energy Systems Ltd | 215
54 | M/s. Sirius Solar Energy Systems Pvt. Ltd | 50
55 | M/s. Tata Power Solar Systems Ltd | 100
56 | M/s. Integrated Batteries India Pvt. Ltd | 35
57 | M/s. Bluebird Solar Pvt. Ltd | 20
58 | M/s. Shanti Solar | 20
59 | M/s. Rajasthan Electronics and Instruments Limited (REIL) | 23
60 | M/s. Neety Euro Asia Solar Energy | 28
61 | M/s. Shivam Photovoltaics Private Limited | 30
62 | M/s. Sahaj Solar Private Ltd | 100
63 | M/s. Raajratna Ventures Limited | 96
64 | M/s. Mundra Solar Energy Ltd | 562
65 | M/s. Renewsys India Pvt. Ltd | 487
66 | M/s. Waaree Energies Limited | 2,650
Sub-total (MW) |  | 4,416
Total Module Manufacturing Capacity (MW) |  | 18,050
BACK TO MAIN SLIDE

## Slide 33: Annexure 7B: List of Solar Capacity Awarded since April 2021 (1/3)
Tender | Bidder | Capacity | Tariff | Month of RA
MAHAGENCO 250 MW Solar | TP Saurya (Tata Power) | 250 | 2.51 | May-21
GUVNL R/T-X (100 MW) | SJVN | 100 | 2.64 | May-21
MSEDCL 500 MW Hybrid | Tata Power | 300 | 2.62 | Jul-21
 | Azure Power | 200 | 2.62 | 
MSEDCL (500 MW) | ACME | 300 | 2.42 | Jul-21
 | ReNew | 200 | 2.43 | 
RUMSL Agar (550 MW) | O2 Power | 350 | 2.444 | 
 | Avaada | 200 | 2.459 | 
RUMSL Shahjapur (450 MW) | NTPC | 105 | 2.35 | 
 | NTPC | 220 | 2.33 | 
 | Solar Arise | 125 | 2.339 | 
RUMSL Neemuch (500 MW) | Tata Power | 170 | 2.14 | Aug-21
 | Tata Power | 160 | 2.149 | 
 | Aljomaih | 170 | 2.15 | 
BREDA 200 MW Solar | SJVN | 200 | 3.11 | Aug-21
SECI 1.2 GW (T-IV) Hybrid | NTPC | 225 | 2.34 | Aug-21
 | Ayana | 225 | 2.34 | 
 | NLC India | 75 | 2.34 | 
 | Azure Power | 75 | 2.35 | 
IREDA 5 GW TRANCHE III | SJVN Limited | 1,000 | 2.45 | Sep-21
 | NLC India Limited | 510 | 2.45 | 
 | NHPC Limited | 1,000 | 2.45 | 
 | IRCON International Limited | 500 | 2.45 | 
 | NTPC Limited | 1,990 | 2.45 | 
SECI RJ T-IV (1785 MW) | NTPC | 500 | 2.17 | Dec-21
 | Sprng Energy | 200 | 2.17 | 
 | UPC Renewables | 90 | 2.17 | 
 | Metka EGN Singapore | 20 | 2.17 | 
 | ReNew | 600 | 2.18 | 
 | ACME | 375 | 2.18 | 
BACK TO MAIN SLIDE

## Slide 34: Annexure 7B: List of Solar Capacity Awarded since April 2021 (2/3)
Tender | Bidder | Capacity | Tariff | Month of RA
SECI ISTS-X KTK Koppal | Ayana | 300 | 2.36 | Feb-22
 | Fortum | 300 | 2.37 | 
SECI ISTS-X KTK Gadag | Ayana | 300 | 2.35 | 
 | Fortum | 300 | 2.36 | 
PSPCL 250 MW | Renew | 100 | 2.33 | Mar-22
 | Adani | 150 | 2.34 | 
GUVNL T-XIII (500 MW) | SJVN | 100 | 2.29 | Mar-22
 | Fortum | 200 | 2.29 | 
 | UPC Renewables | 80 | 2.29 | 
 | Hinduja Renewables | 120 | 2.29 | 
SECI 1.2 GW (T-V) Hybrid | TP Saurya (Tata Power) | 300 | 2.53 | May-22
 | NTPC Renewable | 225 | 2.53 | 
 | Amp Energy | 60 | 2.53 | 
 | SJVN | 15 | 2.54 | 
RUMSL Omkareshwar Floating (300 MW) | NHDC Ltd | 100 | 3.22 | May-22
 | AMP Energy | 100 | 3.21 | 
 | SJVN | 100 | 3.26 | 
GUVNL T-XIV (500 MW) | Aditya Birla | 300 | 2.3 | Jun-22
 | Hinduja Renewables | 120 | 2.3 | 
 | SJVN | 80 | 2.31 | 
MSEDCL 500 MW Ph-VII (Aug '22) | SJVN Green Energy | 200 | 2.90 | Aug-22
 | Juniper Green Energy | 75 | 2.90 | 
 | Tata Power Renewable Energy | 150 | 2.91 | 
 | Sukhbir Agro Energy | 50 | 2.91 | 
 | Avaada Energy | 25 | 2.91 | 
MSEDCL 500 MW Ph-VIII (Sep '22) | NTPC Renewable Energy | 200 | 2.82 | Sep-22
 | Avaada Energy | 300 | 2.83 | 
BACK TO MAIN SLIDE

## Slide 35: Annexure 7B: List of Solar Capacity Awarded since April 2021 (3/3)
Tender | Bidder | Capacity (MW) | Tariff | Month of RA
GUVNL 750 MW Ph-XVI (Sep '22) with Greenshoe | Solarcraft (Blupine Energy) | 120 | 2.49 | 
 | Solairedirect (Engie) | 200 | 2.50 | 
 | Tata Power Renewable Energy | 300 | 2.65 | 
 | Utkrrisht Solar (UPC Renewables) | 130 | 2.66 | 
RUMSL 750 MW Hybrid Project | Sprng Ojas | 80 | 3.03 | Sep-22
 | Tata Power Renewable Energy | 100 | 3.03 | 
 | Renew | 150 | 3.03 | 
 | O2 Power | 45 | 3.04 | 
RUMSL Ph II 300 MW Floating Solar | NTPC Renewable Energy | 90 | 3.69 | Nov-22
 | SJVN Green Energy | 83 | 3.70 | 
 | Hinduja Renewables | 80 | 3.70 | 
TPDDL 255 MW Hybrid | Tata Power Renewable Energy | 127.5 | 3 (for entire hybrid capacity of 225 MW) | Dec-22
MSEDCL Solar Ph-IX (Intra State) (Dec '22) | SolarArise | 100 | 2.90 | Dec-22
 | SJVN Green Energy | 200 | 2.95 | 
 | Tata Power Renewable Energy | 200 | 2.97 | 
 |  | 16.5 GW |  | 
Note: For Hybrid Tenders, total hybrid capacity awarded to each developer is double of figures mentioned above (It has been assumed that 50% of hybrid capacity will be solar), and corresponding tariffs are for entire hybrid capacity
BACK TO MAIN SLIDE

## Slide 36
Deloitte refers to one or more of Deloitte Touche Tohmatsu Limited, a UK private company limited by guarantee (“DTTL”), its network of member firms, and their related entities. DTTL and each of its member firms are legally separate and independent entities. DTTL (also referred to as “Deloitte Global”) does not provide services to clients. Please see www.deloitte.com/about for a more detailed description of DTTL and its member firms.
This material has been prepared by Deloitte Touche Tohmatsu India LLP (“DTTI LLP”), a member of Deloitte Touche Tohmatsu Limited, on a specific request from you and contains proprietary and confidential information. This material may contain information sourced from publicly available information or other third party sources. DTTI LLP does not independently verify any such sources and is not responsible for any loss whatsoever caused due to reliance placed on information sourced from such sources. The information contained in this material is intended solely for you. Any disclosure, copying or further distribution of this material or its contents is strictly prohibited.
Nothing in this material creates any contractual relationship between DTT ILLP and you. Any mutually binding legal obligations or rights may only be created between you and DTTI LLP upon execution of a legally binding contract. By using this material and any information contained in it, the user accepts this entire notice and terms of use.
©2022 Deloitte Touche Tohmatsu India LLP. Member of Deloitte Touche Tohmatsu Limited
Deloitte Touche Tohmatsu India Private Limited (U74140MH199 5PTC093339), a private company limited by shares, was converted into Deloitte Touche Tohmatsu India LLP, a limited liability partnership (LLP Identification No. AAE-8458),with effect from October 1, 2015.