## Slide 1
October 2024
Open Access for different countries

## Slide 2: Concept of “open access”
Bulk Consumer
Distribution
Utility
Transmission Utility
Power plant owned by distribution utility
Power plant having PPA with distribution utility
Captive / merchant power plant
Transactions facilitated by open access
Non-discriminatory access to electricity networks
Electricity network function is typically a monopoly business. In usual course of business, they do not have any incentive to allow sharing of their network or supporting competition; especially when the network owner is also the sole supplier of electricity
Open access in the context of an electricity network refers to non-discriminatory access provided to various users, for the use of an electricity network to transmit power, instead of restricting the access to only the network owners and/or their associates
Open access is a key enabling requirement for wholesale power markets. It allows bulk users to buy power from generators or traders, using the existing electricity network
Facilitation of direct power purchase, through open access

## Slide 3: Advantages of open access to electricity networks
Open access facilitates competition and is also a key driver of direct purchases of renewable energy by corporates
Allows the operation of competitive markets
Open access facilitates
wholesale electricity markets
Allows the bulk consumers to buy from alternative sources of power, which may be cheaper and/or greener; without having to create parallel network
Facilitates optimum development of transmission network
Without open access, if bulk consumers want to buy power from sources other than utility, new electricity network will have to be laid out
Decreases the monopoly power of utilities
Consumers will have a choice other than the existing electricity supplier

## Slide 4: Various types of open access transactions
There is a variety of options, which can be adopted and customized for each country’s needs
Based on duration
Based on consumer’s relationship with utility
Based on consumer’s ownership* on the generator
Short-term
Partial open access – Consumer retains contract demand with utility
Captive – Power plant is fully or partially owned by the consumer
Medium-term
Long-term
Full open access - Consumer does not have / does not retain a demand contract with the utility. A standby power support arrangement may be in place with the utility
Third-party – Consumer does not have any ownership in the power plant
*Duration thresholds, ownership threshold etc. to be defined in policy/regulatory framework

## Slide 5: Key concepts relating to open access
A few key connects relevant for open access are defined below
Transmission Open Access
Open access to transmission lines
Distribution Open Access
Open access to distribution lines
Non-discriminatory open access
Equal rights for applicants, to obtain open access, irrespective of ownership (However, priorities for scheduling and curtailment may be made in terms of open access duration, time of application etc.)
Wheeling
The process of using electricity network / grid as a medium for conveying electricity, as part of the open access transaction
Wheeling charges vs transmission charges
Typically, charges for use of distribution network is covered under wheeling charge, and charges for use of transmission network is covered under transmission charges
Surcharge
An amount that is recovered from the open access consumers, to compensate the utility for loss of cross subsidy and for compensation towards recovery of stranded generation costs of utility

## Slide 6: Country-wise Assessment – Afghanistan (1/3)
Legal and Policy Framework
In Afghanistan, the electricity legal, policy and regulatory framework had been developed by Ministry of Energy and Water, Afghanistan. A draft law on electricity services was issued in 2009 which was finalized in 2016.
As per the Power Services Regulations Act 2016 (introduced in 2015), the provisions recognized international power trade and specified the responsibilities of the MEW for coordinating the same. Under articles 10 and 11 of the law, five kinds of licenses for energy services are proposed:
  Electricity generation license for a maximum of 25 years.
  Electricity transmission license for a maximum of 25 years.
  Electricity distribution license for a maximum of 20 years.
  Electrical energy import license for a maximum of 15 years.
  Electrical energy export license for a maximum of 21 years.
Under Chapter 6 of the Electricity Law: License holders must ensure nondiscriminatory interconnection of electricity networks. Dominant permit holders are required to facilitate interconnections with other permit holders in feasible technical areas.
Afghanistan’s Power Sector: The sector needs further development in infrastructure and institutions to implement the OA framework. Cross-border energy trade is partially enabled through existing connections with neighboring countries.
Notes: Source: https://policy.asiapacificenergy.org/sites/default/files/Power%20Services%20Regulation%20Act%202016.pdf

## Slide 7: Country-wise Assessment – Afghanistan (2/3)
Regulatory Framework
Power Services Regulations Act 2016 establishes the Afghanistan Electricity Regulatory Authority (AERA), defining its powers and duties.
Covers licensing, technical standards, network interconnection, access, etc.
Mandates AERA to regulate cross-border electricity exchanges, aligning with international agreements.
Requires transmission licensees to provide fair, nondiscriminatory access and tariffs to all users.
No current regulations for Open Access (OA) on transmission and distribution networks.
OA mechanism elements (e.g., metering code, energy accounting, transmission pricing, grid code) remain unspecified.

## Slide 8: Country-wise Assessment – Afghanistan (3/3)
Operational Framework
Afghanistan's domestic power sector is vertically integrated, lacking an Open Access (OA) framework.
The CASA 1000 Master Agreement allows power trade with Central Asia and Pakistan, setting procedures for transmission access among member countries.
Provides OA during non-supply periods, enabling allocation of all available transmission capacity per OA rules.
Member countries can assess market demand and set prices for OA use.

## Slide 9: Country-wise Assessment – Bangladesh (1/3)
Legal and Policy Framework
Bangladesh Electricity Act 1910 (Amended 2012): Enables power market development with an open market for power (Part 2, Clause 6).
Electricity Commission: Authorized to study the feasibility of open market operations and frame regulations with stakeholders.
Transmission Utility Functions (Part 2, Clause 7, 2(d)): Must offer non-discriminatory Open Access (OA) to licensees/generators at regulated charges.
BPDB/Single Buyer: May import/export electricity with government approval, at rates set by the government.
Electricity Grid Code 2012 (Clause 1.2): Ensures non-discriminatory access, covering technical standards for transmission use.
National Electricity Policy: To be periodically updated by the Government in consultation with Bangladesh Energy Regulatory Commission (BERC).
Private Sector Participation (2008 Policy): Aims to introduce competition and enhance public-private partnerships, ensuring non-discriminatory access to PGCB transmission/distribution lines for power wheeling.

## Slide 10: Country-wise Assessment – Bangladesh (2/3)
Regulatory Framework
Bangladesh Energy Regulatory Commission (BERC)
Established under the Bangladesh Energy Regulatory Commission Act 2003 (BERC Act 2003), oversees energy pricing, licensing, and consumer rights.
Licensing Authority
(Clause 28)
Licenses for power generation, transmission, distribution, and energy marketing.
Power Market Operationalization
BERC, in consultation with the Government, is tasked with enabling the power market under Clause 6, Part II of the Electricity (Amendment) Act 2012.
Grid Code and Open Access (OA) Framework
BERC has implemented the Grid Code and related regulations, though non-discriminatory OA for transmission and distribution is pending.
Non-Discriminatory Distribution OA
Required for Cross-Border Electricity Trade (CBET) to allow eligible consumers access to alternative power sources.
Power Grid Company of Bangladesh (PGCB) Transmission Charges
Calculated on a cost-plus basis, considering total investments and energy wheeled.

## Slide 11: Country-wise Assessment – Bangladesh (3/3)
Operational Framework
Private Sector Investment Guidelines (2007) and Policy on Sale of Excess Power from Captive Power Plants (2006):
Include some provisions related to Open Access (OA) operations.
No Specific OA Provisions:
Currently, no specific OA provisions allow private generators or consumers to transfer power across the transmission network.
Bangladesh Energy Regulatory Commission (BERC):
Yet to establish a comprehensive OA framework, which would set eligibility criteria, OA grants, and other requirements to enable an OA market in Bangladesh.

## Slide 12: Country-wise Assessment – Bhutan (1/2)
Legal and Policy Framework
Electricity Act 2001 (Article 39): Establishes a system operator license for coordinating power supply and balancing generation with consumption.
System Coordinator (BPC): Bhutan Power Corporation (BPC) manages the National Load Dispatch Centre (NLDC), established in 2011, to ensure system reliability and coordinate power exports to India.
Hydro Development Policy 2008 (Clause 10.1): Requires project developers to have a power evacuation agreement with BPC, responsible for domestic transmission and connectivity to the international border for exports. Transmission and wheeling charges apply as set by the Bhutan Electricity Authority (BEA).
Sustainable Hydro Power Development Policy 2008: Project developers may export electricity after licensing and fulfilling royalty power requirements. The Royal Government of Bhutan has first purchase rights at the generating station bus bar rate (Clause 9.1 and 9.2).

## Slide 13: Country-wise Assessment – Bhutan (2/2)
Regulatory Framework
Electricity Act 2001 (Clause 11.2 & Clause 38.1)
Mandates non-discriminatory Open Access (OA) to transmission and distribution, with access provided to all users on payment of fees.
Licensing Requirement
No entity may operate in electricity generation, transmission, distribution, or trade without a BEA-issued license (Clause 18.1).
BEA Grid Code Regulation 2008
Ensures non-discriminatory access to transmission/distribution (Clause 3.3.2) and prohibits discrimination by the system operator (Clause 3.4.2).
System Operator Responsibilities
Coordinates planning, receives data from licensees for load forecasting and system expansion (Clauses 4.5.1 & 4.7.1).
Tariff Determination Regulation 2007
(updated 2013)
Tariff setting for all domestic transactions, excluding imports, exports, and PPAs governed by license terms.
Operational Framework
Bhutan does not have any well-established guidelines, processes and procedures for availing the OA by the generators or the consumers.
However, export projects are allowed access to the grid on payment of wheeling charges.

## Slide 14: Country-wise Assessment – Pakistan (1/2)
Legal and Policy Framework
Electric Power Act 1997 (Clause 18.1): Provides for Open Access (OA), requiring the national grid company to ensure non-discriminatory transmission and interconnection services, including for bulk-power consumers.
National Power Policy 2013: Although it doesn’t directly mention OA, it outlines objectives to:
  Introduce wheeling charges and wholesale markets, promoting multiple buyers and sellers.
  Develop a business model centered on wholesale transactions, exchanges, and wheeling charges.
Regulatory Framework
Grid Code 2005
(Clause CC3: Principles)
Emphasizes Open Access (OA) by requiring the National Transmission and Despatch Company (NTDC) to allow new connections and apply uniform terms and conditions for all applicants.
Tariff Determination
Governed by NEPRA (Tariff Standards and Procedure) Rules 1998, with guidelines in Part 3 advocating for tariffs based on marginal cost principles and favoring competition.
Wheeling Charges (NEPRA Act, Section 22)
Power producers selling to bulk consumers must pay “Wheeling Charges” or “Use of System Charges” as determined by NEPRA for using transmission and distribution networks to deliver power.

## Slide 15: Country-wise Assessment – Pakistan (2/2)
Operational Framework
Operational Parameters:
Wheeling and use-of-system charges are defined, but no agency oversees granting Open Access (OA), setting eligibility, or conducting technical grid capacity studies for new OA applicants.
Lack of Pure OA Cases:
Pakistan has no dedicated OA cases within its domestic power sector.
Cross-Border Electricity Trade (CBET):
Through participation in the CASA-1000 project, Pakistan shares transmission infrastructure and an operational OA framework with three other countries.

## Slide 16: Country-wise Assessment – Sri Lanka
Legal and Policy Framework
No Direct OA Reference: Sri Lanka’s legal framework, including the Electricity Act 2009, lacks a direct provision for Open Access (OA).
PUCSL’s Role: The Public Utilities Commission of Sri Lanka (PUCSL) is expected to issue regulations or orders to promote competition and ensure non-discriminatory transmission access.
Commission's Objective: The Act mandates the PUCSL to promote competition within the power sector as a key objective
Regulatory Framework
There is no direct reference to OA in the Sri Lanka regulatory framework. According to the Regulatory Manual, PUCSL 2014, the Commission will exercise, perform, and discharge the powers, functions, and duties conferred on it to promote competition.

## Slide 17: Country-wise Assessment – India
About Open Access
Section 2(47) of the EA, 2003 defines Open Access to mean “non-discriminatory provision for the use of transmission lines or distribution system or associated facilities with such lines or system by any licensee or consumer or a person engaged in generation in accordance with the regulations specified by the Appropriate Commission”
No license required for developing a Generating station;
could sell power to any person through Open Access;
Easy change in purchaser in the event of default in honoring contract by purchaser.
Buy power from anywhere – could explore cheaper sources; especially useful for high demand Industrial/ Commercial consumers.
Industrial houses could consolidate power supply to plants at various locations & build captive power plant to achieve economy
Open Access Provides Opportunities to
Generating Station
Consumers
According to sub-section 2, of section 42 of the Electricity Act 2003, electricity consumers now have the right to procure power from the supplier of their choice other than the distribution company that they were buying from.
They can use the existing transmission and distribution infrastructure after paying appropriate charges determined by their respective State Electricity Regulatory Commissions (SERCs).
Different Technical and Financial Requirement to avail Open Access
Minimum Load should be 1 MW or load allowed in respective State regulation to avail open access
Availability of Distribution and Transmission Corridor
Installation of special Energy Meters (SEM) and Remote Terminal Units (RTU) having provision to communicate with SLDC in real time
Payment security mechanism Clearance of outstanding dues
No Objection Certificate from Nodal Agency. It may be SLDCs/ STU/Discoms

## Slide 18: Country-wise Assessment – India
CERC (Open Access Regulations) 2008
Specifies roles of different agencies system operators, CTU & Transmission licensees and others
Specifies Timelines; Provide for congestion management- Setting relative priorities
Separate procedures for ‘Day-Ahead Market (collective transactions) and OTC transactions on inherent margins
CERC (Grant of connectivity, Long Term Access and Medium-Term Open Access) in inter state transmission Regulation, 2009
Nodal agency for grant of Long and Medium access: CTU
Defines criteria for grant of access and application procedure for medium- and long-term access
Procedure for Scheduling STOA in
Interstate Transmission (Collective Transaction)
Collective Transaction: Application procedure, treatment of losses, congestion management at PXs
Bilateral Transaction: Procedure for Advance Scheduling/FCFS/Day-Ahead Bilateral/Contingency Transaction
National Tariff Policy, 2016
Define formula for computation of Cross Subsidy Surcharge (CSS) and additional Surcharge for OA Consumer (Surcharge shall not exceed 20% of tariff applicable to category of consumer)
CERC (Connectivity and General Network Access to the inter-State Transmission System) Regulations, 2022
Facilitates non-discriminatory access to the ISTS for licensees, generating companies, and consumers.
They provide generators with open access rights without requiring them to specify the injection point and drawal point.
Detailed Procedure for Connectivity and General Network Access (GNA) to the ISTS
Applicable to the processing of applications made by the applicants for Grant of Connectivity and/or General Network Access (GNA) to the Inter-State Transmission System (ISTS), received by the Central Transmission Utility (CTU) or any other actions in accordance with GNA Regulations.
CERC/MOP Regulations related to Open Access

## Slide 19: Typical process for open access in states in India (1/2)
In India, depending on the duration of open access, applications are processed either by the system operator or the transmission utility
Generator applies for connectivity to transmission line
Transmission utility to inform regarding the connectivity point
Generator builds dedicated Tx line from plant to the connectivity point
Generator applies for open access to the network
Load flow studies by open access nodal agency (Tx Utility or System Operator)
Grant of open
access
Scheduling of open
access transactions
Payment of Tx and wheeling charges; Payment of surcharges, if applicable
Energy accounting carried out by Tx Utility and the DISCOM
19

## Slide 20: Typical process for open access in states in India (2/2)
Wholesale Market
Generating Companies
Captive Power Generation
Generation Network
Transmission Network (Immediate for Open Access)
Distribution Licensee
Distribution Companies (DISCOMs)
Licensee Area
Bulk Consumer
(Industries)
Domestic and Commercial Consumer
Other Categories of Consumer
Distribution Network
Trading Platforms
PTC
IEX
PXIL
Working Process of Open Access
Structure of Open Access
Open Access
Intra-state
Inter State
Short Term
Medium Term
Long Term
Traders, Power Exchange
Traders, Power Exchange
Power Purchase Agreement
This result in Competitive l Flexible Structure l Enabling Choice to Consumer

## Slide 21: Different Charges applicable to OA Consumers in India
Different Charges | West Bengal | Chhattisgarh | Assam | Punjab | Jharkhand | Tamil Nadu | Andhra Pradesh | Gujarat | Haryana | Maharashtra
Transmission Charge |  |  |  |  |  |  |  |  |  | 
Wheeling Charge |  |  |  |  |  |  |  |  |  | 
SLDC Charges |  |  |  |  |  |  |  |  |  | 
UI/Imbalance Charges |  |  |  |  |  |  |  |  |  | 
Cross Subsidy Surcharge |  |  |  |  |  |  |  |  |  | 
Additional Surcharge |  |  |  |  |  |  |  |  |  | 
Standby Charges |  |  |  |  |  |  |  |  |  | 
Reactive Energy Charges |  |  |  |  |  |  |  |  |  | 
Energy Losses |  |  |  |  |  |  |  |  |  | 
Voltage Surcharge |  |  |  |  |  |  |  |  |  | 
Parallel Operation Charges |  |  |  |  |  |  |  |  |  | 
Restoration Charge |  |  |  |  |  |  |  |  |  | 
Source : Forum of Regulator (FOR) - Review of Status of Open Access in Distribution and Different States Open Access Regulations

## Slide 22: Cross Subsidy Computational Methodology
Average Consumer Category Wise Tariff (T)
Per Unit Cost associated with Regulatory Assets
CSS (S) = T – [ C/(1 – L/100)+ D+R)
T – Tariff payable to relevant category of Consumer including RPO
L – Aggregated Transmission and commercial loss at relevant voltage level
D – Aggregate of transmission, distribution and wheeling charge applicable to relevant voltage
R – per unit cost of carrying regulatory assets
Method 1 : Based on Tariff Rate Vs Cost of Supply for relevant Category
T – C
Average Cost of Supply (C)
Chhattisgarh
Assam
Punjab
Gujarat
Method 2 : Based on National Tariff Policy, 2016
West Bengal
(Additional Component )
Jharkhand
Tamil Nadu
Andhra Pradesh
Gujarat
Maharashtra
Source : Forum of Regulator (FOR) - Review of Status of Open Access in Distribution

## Slide 23: Examples of Open Access - India
20% free power to Govt. of Himachal Pradesh
Remaining power sold to industrial consumers through power exchanges and power traders, utilizing transmission network of state transmission utility and the national grid
Generator pays transmission charges for the use of transmission network
There are over 15 small hydro power plants (< 25 MW) with a total capacity of more than 150 MW, which utilizes open access to sell electricity to commercial and industrial consumers
Power plants use the transmission network of the state transmission utility and the distribution network of the distribution utilities to supply power to the consumers
The power plant is set up and owned by Winsome Textile Industries Limited
Electricity from the power plant is supplied to Winsome’s factory utilizing the existing transmission and distribution network. Nearly 1/3rd of factory’s electricity requirement is met from the power plant.
86 MW HPP of Malana Power Company (Statkraft), Himachal Pradesh
Mini Hydro Power Plants in Karnataka
3.5 MW Manuni HPP, Himachal Pradesh
While examples of hydropower are highlighted below, there is a larger market of open access based solar and wind power suppliers

## Slide 24: Evolution of Regional Energy Cooperation, Cross Border Electricity Trade
Political, Policy & Regulatory Initiative

## Slide 25: Other Examples of Open Access - USA
In USA, while open access in earlier years drove wholesale market development, more recently, it has also supported large corporate RE procurement
In USA, the core framework for open access was provided in two orders of Federal Energy Regulatory
Commission (FERC) issued in 1996
Order 888 laid the foundation of transmission OA for generators in the USA. Order 888 required utilities to unbundle their transmission function and provide OA to their transmission facility. Order 889 established Open Access Same-Time Information System (OASIS) and set standards on how customers and utilities would share information regarding transmission system availability
Some of the large open access PPAs in US include:
  Microsoft: 110 MW PPA with Keechi Wind Project,Texas
  Amazon: 100 MW PPA with Southampton Solar,Virginia
  Apple: 201 MW PPA with Montague Wind Facility, Oregon
  Facebook: 227 MW PPA with Colbert County Solar Facility, Alabama

## Slide 26: Other Examples of Open Access - Vietnam
Vietnam uses financial and market-based arrangements to facilitate competitive markets rather than implementing physical PPAs
An innovative model is being piloted in Vietnam (with the support of USAID funded Vietnam Low Emission Energy Program), for direct purchase of energy by consumers
In the proposed ‘Direct Power Purchase Agreement (DPPA)’ pilot, the generators sell to a wholesale energy market. Interested consumers also buy power from the wholesale energy market
A ‘Contract for Difference’ (CfD) agreement between consumers and generators ensures protection of interests of both consumers and generators
  Generators with more than 30 MW capacity can sell
  Consumers at 22 KV and above can buy
  The parties sign a long term CfD agreement to settle the difference between the price in the spot electricity market and the price committed in the contract
Source: USAID’s VLEEP
26

## Slide 27: Thank You