## Slide 1: Karnataka

## Slide 2: Power market structure
Government of Karnataka owns and operates a significant portion of the power sector value chain with separate entities for generation, transmission and distribution
Policy
State Government
Regulations
KERC
RE development
KREDL
Generation
KPCL, UPCL, NTPC, IPPs
System operation
KSLDC
Transmission
KPTCL
Distribution
BESCOM, MESCOM, HESCOM, GESCOM, CESC
Energy Department is responsible for the issue of electricity sector policies in the state. Government of Karnataka owns 100% stake in KPCL and KPTCL. KPTCL has been unbundled into five discoms – BESCOM, MESCOM, HESCOM, GESCOM and CESC
It promotes competition, efficiency and economy in Karnataka’s power sector; regulates electricity tariffs and protects interests of consumers and other stakeholders.
Promotes renewable energy in the State and initiates all necessary actions for Energy Conservation in the State
Apex body for integrated operation of electricity grid in the state. The SLDC and SCADA Centre operate out of Bangalore
KPCL is the major power generating company in the state of Karnataka. It has installed capacity of 8738.30 MW, as on 09.06.2020 and is one of the largest state government owned generation companies in India. The state also has generation capacity from NTPC and private IPPs (thermal, hydro and RE).
KPTCL is the sole transmission company in the state and operates 37652.58 Circuit KM of transmission lines and 1222 substations.
Karnataka has five distribution licensee namely - BESCOM (Bangalore Electricity Supply Company Limited), MESCOM (Mangalore Electricity Supply Company Limited), HESCOM (Hubli Electricity Supply Company Limited), GESCOM (Gulbarga Electricity Supply Company Limited) and CESC (Chamundeshwari Electricity Supply Corporation) to cater to electricity supply in different districts of the state based on their jurisdiction.

## Slide 3: Industrial Growth in the state
Karnataka has vibrant automobile, agro, aerospace, textile and garment, biotech, and heavy engineering industries and SEZs for key industries such as IT, biotechnology, and engineering
Karnataka is surrounded by the Arabian Sea on the west, Goa on the northwest, Maharashtra on the north, Andhra Pradesh on the east, Tamil Nadu on the southeast, and Kerala on the southwest.
The state’s per capita GSDP was Rs. 253,444 (US$ 3,595) in 2019-20. Per capita GSDP (in Rs.) increased at a CAGR of 11.70% between 2011-12 and 2019-20.
Merchandise export from Karnataka reached US$ 17.36 billion in 2018-19 and US$ 16.64 billion in 2019-20.
Karnataka has vibrant automobile, agro, aerospace, textile and garment, biotech, and heavy engineering industries. The state has sector specific special economic zone (SEZs) for key industries such as IT, biotechnology, and engineering, food processing and aerospace.
Karnataka is the IT hub of India and home to the fourth largest technology cluster in the world. It has 23 operational IT/ ITeS SEZs, five software technology parks and dedicated IT investment regions.
The state attracted Foreign Direct Investment (FDI) equity inflow worth US$ 7,948.53 million between October 2019 and September 2020 according to the data released by Department for Promotion of Industry and Internal Trade (DPIIT).
Karnataka offers a wide range of fiscal and policy incentives for businesses under the Karnataka Industrial Policy, 2014 19. Through the ESDM Policy 2013, the Government of Karnataka planned to facilitate, promote and develop the ESDM sector in Karnataka and make the state a preferred destination for investment in this sector.
In September 2017, the Government of Karnataka passed the ‘Karnataka Electric Vehicle and Energy Storage Policy 2017’. Electric Vehicles manufacturing in Karnataka is expected to attract investment worth US$ 4.82 billion and create 55,000 jobs.

## Slide 4: Industrial Growth in Karnataka – industrial policy initiatives and investment
Karnataka fosters a great hassle-free climate for investment in industries and has always focused on policy support and incentives to boost industrial growth
Special Economic Zones Government of Karnataka has formulated a State policy for SEZs as per the Central SEZ Act 2005 & Rules 2006. The Policy aims to provide a hassle-free environment for the manufacturing & service sectors and to attract FDI. The Board of approval of SEZ constituted under SEZ Act 2005 has granted formal approvals for 75 SEZs in the State. SEZs numbering 36 are operational in the State with an investment of Rs.99055.56 crores and generating employment for 372927 persons. Currently there are 495 SEZ units. The value of exports from these SEZs during the year 2020-21 (April to September) accounted to Rs.62547.44 crores.
Key Highlights of Karnataka’s industrial growth in FY 2019-20 1.2 % of overall organized industrial growth in FY 2019-20 40% increase in number of MSME units registered 25% increase in MSME investment Major policy initiatives and incentives New Industrial Policy 2020-25: To make Karnataka a global manufacturing hub; focus on manufacturing and innovation Production Linked Incentive: Upto 2.25% of annual turnover for 6-10 years to boost exports Industrial Facilitation Act Amendment: Brought in affidavit based clearance system for quick start to approved projects
Key Initiatives Information Technology Investment Region (ITIR) Project: Keonics involved in establishing IT Parks in Tier-II Cities: Hubbali, Kalburgi, Shivamogga, Mysuru and Mangaluru Centre for Open Data Research: Established in Planning Department in collaboration with IIIT-B and PAC for data analytics and evidence based policy making Karnataka Optical Network: Setup under Bharat Net to connect all government offices upto Gram Panchayat level Karnataka Open Data Initiative: Utilize Open Data Architecture enabling efficient and transparent governance
Karnataka Udyog Mitra (KUM) Karnataka Udyog Mitra (KUM) is a single contact point for all investors who are looking at setting up enterprises/business in Karnataka. As a nodal agency, its role is to facilitate investments & execute initiatives to enable a smooth transition, from receiving an investment proposal to them eventual implementation of the project. During 2019-20, total 203 projects with an investment of Rs.12,694.27 crores were approved for SLSWCC* which created employment to 89270 people. For SHLCC* with a total of 16 projects were approved with an investment of Rs.22,413.73 crores which created employment to 10374 people.
Source: MIDC, Economic Survey of Maharashtra 2020-21
*State Level Single Window Clearance Committee (SLSWCC); State High Level Clearance Committee (SHLCC)
New Industrial Corridors The Industrial Policy proposes the establishment of new industrial corridors within the state to boost growth namely – 1) Bangalore-Mandya-Mysore-Chamrajnagar 2) Chitradurga-Bellary-Gulbarga-Bidar 3) Dharwad-Koppal-Raichur 4) Bangalore-Hassan-Mysore 5) Tumkur-Shimoga-Honnavar 6) Raichur-Bagalkot-Belgaum

## Slide 5: Electricity sector overview
State is successful meeting its electricity demand with a staggering increase in installed capacity at a 6-year CAGR of ~ 12.31%
Electricity | FY 2020 Demand (MUs) | FY 2020 Supply (MUs) | Generation capacity as on 31st Dec-2020 (MW)
Karnataka | 72,799 | 72,796 | 30,209
India | 12,91,010 | 12,84,444 | 3,82,151
Karnataka as % of India | 5.63% | 5.67% | 7.90%
Source: CEA Reports
Karnataka is the one of the largest states in India in terms of electricity demand, electricity supply and power generation capacity. It contributes to nearly 8% of all India generation capacity.
The state has around 10.26 million households, all of which are electrified.
The energy deficit of Karnataka has significantly come down in the last eight years to almost 0%. This is due to moderate growth rate in energy demand at 7-year CAGR (FY13 to FY20) of around 1.35% and a staggering increase in installed generation capacity at 6-year CAGR of around 12.31%. The state has sufficient capacity to meet the future demand.
19th EPS projects the state demand to grow at a CAGR of around 4.9% for FY22 to FY27.
Source: CEA Reports
Chart: 
| Thermal | Hydro | Wind | CGS | Solar | Co-gen | Bio mass | Captive | IPP
Column1 | 5020 | 4701 | 4898 | 4158 | 7370 | 1731 | 139 | 992 | 1200
Karnataka generation capacity break-up 2020
30,209
MW
Chart: Energy Demand - Supply Scenario in Karnataka (MUs)
| FY13 | FY14 | FY15 | FY16 | FY17 | FY18 | FY19 | FY20
Energy requirement | 66274 | 64150 | 62643 | 64302 | 66900 | 67869 | 71764 | 72799
Energy available | 57044 | 58052 | 59926 | 60971 | 66538 | 67702 | 71695 | 72796
Energy deficit | 0.13927 | 0.095058 | 0.043373 | 0.051802 | 0.0054111 | 0.0024606 | 0.00096148 | 4.1209e-05

## Slide 6: Sales mix
Agricultural & Domestic consumers dominate the sales mix, contributing ~61% of the total sales mix while ~40% of the revenue is contributed by C&I segments apart from 30% of revenue as subsidy from the State Government
Total sales of the Karnataka Discoms has grown at a CAGR of 4.5% between (FY15 to FY19).
Sales growth from the agriculture sector has been at a 5-year CAGR of 5.9% and sales growth from the domestic sector has been at a 5-year CAGR of 5.55% which are more than the total sales growth rate.
The state is dependent on the industrial and commercial category consumers to recover its costs.
Industrial and commercial sector contributes the highest to the revenue mix with 40% of total revenue.
Industrial & commercial consumers cross subsidize agriculture consumers; the subsidy provided by the Karnataka Government covers ~30% of the revenue from sale of power
The Agriculture sector with the lowest ABR is contributing to 39% of the sales mix of Karnataka discoms in FY 2019.
Source: Karnataka Discoms Tariff Orders and PFC Report
Sales mix (MUs) | FY 2014 | FY 2015 | FY 2016 | FY 2017 | FY 2018 | FY 2019 | CAGR for 5 years | ABR for FY 2019 (True Up Order)
Domestic | 9,813.00 | 10,821.00 | 11,174.00 | 11,778.99 | 12,371.69 | 12,855.17 | 5.55% | Rs. 5.77/kWh
Commercial | 5,905.00 | 6,323.00 | 6,628.00 | 6,870.84 | 7,083.33 | 7,070.52 | 3.67% | Rs. 10.24/kWh
Agriculture | 16,970.00 | 17,935.00 | 19,284.00 | 21,617.23 | 19,994.19 | 22,609.36 | 5.91% | Rs. 0.08/kWh
Industrial | 10,309.00 | 10,068.00 | 9,781.00 | 9,328.04 | 9,652.58 | 10,324.59 | 0.03% | Rs. 8.26/kWh
Others | 3,859.00 | 4,016.00 | 3,927.00 | 4,241.38 | 4,756.29 | 5,477.36 | 7.26% | Rs. 7.03/kWh
Total | 46,856.00 | 49,163.00 | 50,794.00 | 53,836.47 | 53,858.07 | 58,337.00 | 4.48% | Rs. 6.72/kWh
Chart: FY 2019 Revenue Mix
| Domestic | Commercial | Agriculture | Industrial | Others | Subsidy
True Up Order Revenue Mix | 0.18947 | 0.18477 | 0.0048111 | 0.21774 | 0.098321 | 0.3049
Chart: FY 2019 Energy Sales Mix
| Domestic | Commercial | Agriculture | Industrial | Others
Sales | 0.22036 | 0.1212 | 0.38756 | 0.17698 | 0.093892
Sales in FY2019: 58,337 MUs
Revenue in FY2019: INR 391,820 Mn

## Slide 7: Industrial & Commercial Tariff Trend in Karnataka
HT Industrial and Commercial consumers can be a lucrative market for RE sale since their tariffs have grown at rate ~4% or more in the past 5 years
HT-2(a): Applicable to Industries, Factories, Workshops, Research & Development Centres, Industrial Estates
HT-2(b): Applicable to Commercial Complexes, Cinemas, Hotels, Boarding & Lodging, Amusement Parks, Railway Stations, AirPort, KSRTC bus stations, All offices, Banks, Commercial Multi-storied buildings
HT-2(c): Applicable to hospitals and educational institutions
Source: Tariff Orders of Karnataka discoms
Chart: HT-2(a)
| FY16 | FY17 | FY18 | FY19 | FY20 | FY21
BESCOM | 5.9 | 6.25 | 6.65 | 6.9 | 7.1 | 7.35
Rest four discoms | 5.85 | 6.2 | 6.6 | 6.75 | 6.95 | 7.2
Chart: HT-2(b)
| FY16 | FY17 | FY18 | FY19 | FY20 | FY21
BESCOM | 7.55 | 8.05 | 8.45 | 8.7 | 8.9 | 9.15
Rest four discoms | 7.35 | 7.85 | 8.25 | 8.45 | 8.65 | 8.9
Chart: HT-2(c)
| FY16 | FY17 | FY18 | FY19 | FY20 | FY21
BESCOM | 6.1 | 6.5 | 6.9 | 7.15 | 7.35 | 7.6
Rest four discoms | 6.1 | 6.5 | 6.9 | 7.1 | 7.3 | 7.55
In Karnataka, demand charges for HT industrial consumers for BESCOM has grown at a 5-year CAGR of 4.49% and that for other four discoms at a 5-year CAGR of 4.24% during FY16 to FY21.
Demand charges for HT commercial consumers for BESCOM has grown at a 5-year CAGR of 3.92% and that for other four discoms at a 5-year CAGR of 3.90% during FY16 to FY21.
Karnataka has been carrying out kVAh based billing of HT Industrial and Commercial consumers.

## Slide 8
KERC RPO-REC Regulations,2011 [Sixth Amendment 2018] (effective 15th Nov’ 2018)
State’s RPO-REC regulations applicable to all captive users/ generators, OA consumers & Discoms
OBLIGATED ENTITIES
Captive
Captive User / Generator consuming electricity generated from grid connected captive plants using other than renewable sources and having a total capacity > 5 MW;
Open Access
Consumer with Contract Demand > 5 MW with the distribution licensee and procuring electricity >1MW through Open Access from sources other than renewable sources of energy
Discom
Distribution Licensees in the State of Karnataka
Renewable Energy Certificates:
Certificates issued under CERC’s REC Regulations to be valid for Obligated Entities to discharge its RPO;
Solar purchase obligation may be fulfilled only by purchase of Solar Certificates;
Non-Solar purchase obligation may be fulfilled only by purchase of non-Solar Certificates.
RPO Target:
RPO Target for the next years:
  FY21 – Solar 8.50% & Non-Solar 10.25%;
  FY22 - Solar 10.50% & Non-Solar 10.25%;
Penalty for not meeting RPO Target:
Failure to purchase RECs to the extent of 110% of the shortfall in meeting RPO for a particular year can lead to action under Section 142 of Electricity Act, 2003.
Adjustment of surplus energy:
Obligated Entity can use surplus Solar energy upto 15% of total RPO target to meet short fall in non-Solar RPO target and vice-versa.
To adjust more than 15% surplus energy from one category against shortfall in other RPO category, prior approval of KERC with detailed justification may be sought.
Eligible RE sources
Small, Mini, Micro
Hydro Power
Non-fossil fuel
(incl. bagasse)
based Co-generation
Waste to Energy
(MNRE approved technologies)
Biomass Power
(Rankine Cycle)
Wind energy
Hybrid RE
(MNRE / MERC approved technologies)
Power generated from co-firing of biomass in thermal power plants
Any other source recognized / approved by MNRE or MERC
Solar power
Source: KERC

## Slide 9
Karnataka: RPO Target and Compliance
RPO Targets set by KERC in its RPO Regulations, 2018 (Sixth Amendment) |  |  |  | 
Discom | Non-solar RPO |  |  | 
 | 2019-20 | 2020-21 | 2021-22 | FY 2022-23 onwards
BESCOM | 12.00% | 12.00% | 12.00% | To be determined
MESCOM | 13.00% | 13.00% | 13.00% | 
CESC | 12.00% | 12.00% | 12.00% | 
HESCOM | 11.00% | 11.00% | 11.00% | 
GESCOM | 8.00% | 8.00% | 8.00% | 
With 12667 MW of solar & wind installed capacity Karnataka is one of the states with the highest % of installed capacity of RES.
In the past 5 years, the state has achieved its RPO targets each time.
Considering the ambitious RPO targets set by the State regulatory commission for FY21, FY 22 and beyond, the Obligated Entities (Captive User/ Generator, Open Access Consumer, Discoms) in Karnataka would have to considerably increase their RE procurement in order to catch up with the steeply rising RPO targets.
RPO Compliance Trajectory for Karnataka (up to FY 2018-19) |  |  |  |  | 
Particular | FY15 | FY16 | FY17 | FY18 | FY19
Input energy (Excluding hydro sources) | 60,262.52 | 61,601.34 | 65,331.24 | 57,951.93 | 59,022.07
Solar RPO Target (MUs) | 150.66 | 154.00 | 489.98 | 1,602.40 | 3,541.32
Solar RPO Target achieved (MUs) | 230.30 | 297.31 | 625.04 | 2,487.66 | 6,993.34
Non-solar RPO target (MUs) | 5,435.20 | 5,366.24 | 6,303.47 | 6,098.46 | 6,490.16
Non-solar RPO target achieved (MUs) | 6,072.24 | 6,905.56 | 6,280.44 | 7,728.26 | 11,074.36
Total shortfall (MUs) | - | - | - | - | -
Total shortfall (%) | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
RPO Targets set by KERC in its RPO Regulations, 2018 (Sixth Amendment) |  |  |  | 
Discom | Solar RPO |  |  | 
 | 2019-20 | 2020-21 | 2021-22 | FY 2022-23 onwards
BESCOM | 7.25% | 8.50% | 10.50% | To be determined
MESCOM | 7.25% | 8.50% | 10.50% | 
CESC | 7.25% | 8.50% | 10.50% | 
HESCOM | 7.25% | 8.50% | 10.50% | 
GESCOM | 7.25% | 8.50% | 10.50% | 
Obligated entities in Karnataka would have to increase their RE procurement in order to meet the growing RPO targets

## Slide 10: Industry category wise captive installed capacity, RE share & energy consumption (FY19)
S. No. | Industry Type | No. of Industries | Installed Capacity (MW) | RE (Solar, Wind & Hydro) capacity as % of Total Capacity (respective industry) | Total Energy Consumption (MUs) | % of Consumption from Captive
1 | Iron & Steel | 39 | 1289.95 | 0.0% | 7018.70 | 95.95%
2 | Miscellaneous | 351 | 1445.87 | 5.78% | 3205.08 | 8.75%
3 | Cement | 22 | 729.19 | 0.84% | 2703.53 | 90.62%
4 | Sugar | 93 | 1359.64 | 0.0% | 1457.53 | 87.27%
5 | Mineral Oil & Petroleum | 8 | 263.37 | 0.0% | 1355.19 | 97.19%
6 | Chemical | 28 | 223.3 | 0.28% | 1297.10 | 38.79%
7 | Light Engineering | 56 | 225.82 | 9.49% | 618.62 | 29.34%
8 | Textile | 28 | 66.72 | 13.49% | 145.38 | 5.78%
9 | Paper | 8 | 137.64 | 0.0% | 462.67 | 84.15%
10 | Jute | 3 | 8 | 7.50% | 34.75 | 76.40%
11 | Rubber | 9 | 36.41 | 0.0% | 144.10 | 0.65%
12 | Colleries | 1 | 0.25 | 0.0% | 0.07 | 100.00%
13 | Automobile | 9 | 41.62 | 20.18% | 142.43 | 6.99%
14 | Electrical Engineering | 9 | 40.63 | 37.37% | 57.05 | 47.50%
15 | Mining & Quarrying | 7 | 46.48 | 0.0% | 328.93 | 19.00%
16 | Aluminium | 2 | 7.69 | 0.0% | 9.37 | 0.32%
17 | Non Ferrous | 4 | 51.86 | 31.96% | 215.93 | 92.57%
18 | Heavy Engineering | 14 | 88.73 | 45.19% | 254.77 | 22.31%
19 | Food Products | 15 | 57.23 | 0.24% | 134.51 | 11.38%
Total Karnataka |  | 706 | 6120.4 | 3.30% | 19585.71 | 65.85%
Highly energy intensive industries i.e., Iron & Steel, Cement and Miscellaneous consume ~66% of the total energy consumption by all captive industries in Karnataka.
Energy intensive industries like Chemical and Light Engineering are meeting most of their energy requirements from Discom’s supply.
Industries like Iron and Steel, Cement, Mineral Oil & Petroleum, Sugar and non-ferrous which are energy intensive, majorly meet their energy requirement from their captive generation.
RE penetration in energy intensive industries (except Textile & Chemical) is quite low, with only 0.5% to 1.5% of their total captive capacity being RE based.
Energy intensive industries
(consumption 500-2000 MUs)
Highly energy intensive industries
(consumption >2000 MUs)
With meagre RE captive capacity, most of the energy intensive industries seem to be a good market for RE sale
Source: CEA Reports

## Slide 11: Karnataka | Industry category wise solar power based captive plants (FY2018-19)
Most of the energy intensive industries in Karnataka are consuming 100% of the energy generated from their captive solar plant.
There is huge potential for sale of RE to the energy intensive industries in Karnataka considering their present solar captive installation, energy consumption from solar captive units and their RPO targets.
Solar based captive capacity constitutes only ~2% of the total captive capacity in Karnataka.
Energy generation from solar based captive plants is just ~0.5% of the total energy generated from all captive power plants in Karnataka.
~15% of the total energy generated from solar based captive power plants in Karnataka is sold to Utility.
S. No. | Industry Type | No. of Industries | Installed Solar Capacity (MW) | Solar as % of Total Captive Capacity of respective industry | % consumed of total captive solar generation | % Solar captive consumption of total captive consumption
1 | Iron & Steel | 0 | 0 | - | - | -
2 | Miscellaneous | 23 | 53.85 | 3.72% | 57.67% | 0.51%
3 | Cement | 1 | 0.1 | 0.01% | 100.0% | 0.00%
4 | Sugar | 1 | 0.02 | 0.00% | 100.0% | 0.00%
5 | Mineral Oil & Petroleum | 0 | 0 | - | - | -
6 | Chemical | 1 | 0.62 | 0.28% | 100.0% | 0.02%
7 | Light Engineering | 3 | 15.7 | 6.95% | 100.0% | 5.32%
8 | Automobile | 2 | 8.4 | 20.18% | 100.0% | 5.78%
9 | Textile | 0 | 0 | - | - | -
10 | Paper | 0 | 0 | - | - | -
11 | Jute | 0 | 0 | - | - | -
12 | Rubber | 0 | 0 | - | - | -
13 | Colleries | 0 | 0 | - | - | -
14 | Electrical Engineering | 1 | 1.28 | 3.16% | 100.0% | 2.73%
15 | Mining & Quarrying | 1 | 0 | - | 100.0% | 0.12%
16 | Aluminium | 0 | 0 | - | - | -
17 | Non Ferrous | 0 | 0 | - | - | -
18 | Heavy Engineering | 2 | 35.1 | 39.56% | 100.0% | 0.05%
19 | Food Products | 0 | 0 | - | - | -
Total Karnataka |  | 35 | 115.08 | 1.88% | 85.06% | 0.35%
With only ~0.35% of total energy consumption being from solar captive, industries in Karnataka offer good opportunities for Solar Group Captive sale
Source: CEA Reports
Energy intensive industries
(consumption 500-2000 MUs)
Highly energy intensive industries
(consumption >2000 MUs)

## Slide 12: Karnataka | Industry category wise wind power based captive plants (FY2018-19)
Most of the energy intensive industries in Karnataka are consuming 100% of the energy generated from their captive wind plant.
There is huge potential for sale of RE to the energy intensive industries in Karnataka considering their present wind captive installation, energy consumption from wind captive units and their non-solar RPO targets.
Wind based captive capacity constitutes only ~1% of the total captive capacity in Karnataka.
Energy generation from wind based captive plants is just ~0.9% of the total energy generated from all captive power plants in Karnataka.
~8.4% of the total energy generated from wind based captive power plants in Karnataka is sold to Utility.
S. No. | Industry Type | No. of Industries | Installed Wind Capacity (MW) | Wind as % of Total Captive Capacity of respective industry | % consumed of total captive wind generation | % Wind captive consumption of total captive consumption
1 | Iron & Steel | 0 | 0 | - | - | -
2 | Miscellaneous | 2 | 29.75 | 2.06% | 99.59% | 2.29%
3 | Cement | 1 | 6 | 0.82% | 100.0% | 0.32%
4 | Sugar | 0 | 0 | - | - | -
5 | Mineral Oil & Petroleum | 0 | 0 | - | - | -
6 | Chemical | 0 | 0 | - | - | -
7 | Light Engineering | 4 | 5.72 | 2.54% | 68.77% | 1.51%
8 | Automobile | 0 | 0 | - | - | -
9 | Textile | 0 | 0 | - | - | -
10 | Paper | 0 | 0 | - | - | -
11 | Jute | 0 | 0 | - | - | -
12 | Rubber | 0 | 0 | - | - | -
13 | Colleries | 0 | 0 | - | - | -
14 | Electrical Engineering | 1 | 13.9 | 34.21% | 100.0% | 43.34%
15 | Mining & Quarrying | 0 | 0 | - | - | -
16 | Aluminium | 0 | 0 | - | - | -
17 | Non Ferrous | 0 | 0 | - | - | -
18 | Heavy Engineering | 1 | 5 | 5.64% | 2.01% | 0.06%
19 | Food Products | 1 | 0.13 | 0.24% | 100.0% | 0.59%
Total Karnataka |  | 10 | 60.51 | 0.99% | 91.59% | 0.68%
With only ~0.68% of total energy consumption being from wind captive, industries in Karnataka offer good opportunities for Wind Group Captive sale
Source: CEA Reports
Energy intensive industries
(consumption 500-2000 MUs)
Highly energy intensive industries
(consumption >2000 MUs)

## Slide 13: Karnataka | Top 25 (Installed Capacity wise) captive power plants (FY2018-19)
S. No. | Name of Industry | Fuel Type | Installed Capacity (MW) | Type of Industry
1 | JSW Steel Ltd | Steam | 600.00 | Iron & Steel
2 | Mangalore Refinery& Petrochemicals Ltd, | Gas | 239.50 | Mineral Oil & Petroleum
3 | BMM ISPAT Ltd, | Steam | 140.00 | Iron & Steel
4 | JSW Steel Ltd | Gas | 130.00 | Iron & Steel
5 | Acc Limited Wadi Cement Works, Gulbarga | Steam | 125.00 | Cement
6 | The Associated Cement Companies Ltd., |  | 125.00 | Cement
7 | Ultra Tech Cements Ltd. (Unit;Rajashree Cements),Gulbarga |  | 108.50 | Cement
8 | JSW Steel Ltd | Gas | 100.00 | Iron & Steel
9 | BMM ISPAT Ltd, | Steam | 95.00 | Iron & Steel
10 | Indain Cane Power Ltd. |  | 83.00 | Misc.
11 | Vasavadatta Cements ( Kesoram Industries Ltd.'s Cement Divn.) |  | 79.20 | Cement
12 | The West Coast Paper Mills Ltd, |  | 74.80 | Paper
13 | Shree Renuka Sugars Ltd.- Unit-4 |  | 68.00 | Sugar
14 | Nirani Sugars Ltd, Mudhol | Diesel | 62.00 | Sugar
15 | RMZ Ecoworld | Diesel | 61.33 | Misc.
16 | Jaypee Cement Corpn. Ltd(Formerly M/s Zawar cement Works | Steam | 60.00 | Cement
17 | Godavari Biorefineries Ltd, |  | 54.06 | Sugar
18 | Shree Hirnyakeshi sahakari sakkare karkhane niyamit |  | 52.00 | Sugar
19 | Shri Hiranyakeshi SSK Niyamit, |  | 52.00 | Sugar
20 | M/s Sathavahana Ispat Pvt. Ltd, |  | 50.00 | Iron & Steel
21 | J.K.CEMENT WORKS MUDDAPUR | Diesel | 50.00 | Cement
22 | Mangalore Chemicals & Fertilizers Ltd, | Steam | 48.00 | Chemical
23 | Coramandel Sugars,Makavally,K R Pet Taluk, Mandya District. | Diesel | 46.12 | Sugar
24 | Orient Cements ltd | Steam | 45.00 | Cement
25 | Mysore Paper Mills Ltd., | Steam | 41.00 | Paper
Total Karnataka (all captive plants) |  |  | 6120.44 | 
Complete list of Captive Power Plants in Karnataka is annexed

## Slide 14: Solar power based Captive Power Plants in Karnataka for FY 2018-19 (1/2)
S. No. | Name of Industry | Industry Type | Installed Solar Capacity (MW)
1 | TVS Motor Co.Ltd., PB No.01, Byathahalli, Kadakola post, Mysore | Heavy Engg. | 35.00
2 | Integrated Food park Pvt Lt | Misc. | 30.00
3 | BHARATH ELECTRICALS LTD | Light Engineering | 14.88
4 | Bangalore International Airport Ltd | Misc. | 9.39
5 | M/S TOYOTA KIRLOSKAR AUTO PARTS LTD.,Ramnagara Dist. | Automobiles | 8.20
6 | M/S intel Technology india Pvt ltd Varthur Hobli | Misc. | 2.50
7 | Halo Energie Chitradurga |  | 2.00
8 | Halo Energie Challaki |  | 2.00
9 | Halo Energie Chitranayaki |  | 2.00
10 | M/s Bharat Electronics Ltd, | Elect. Engg. | 1.28
11 | New Mangalore Port Trust, | Misc. | 1.19
12 | Janatha Fish Meal & Oil Products, Udupi |  | 1.00
13 | EIT Services India P. Ltd., Bangalore |  | 0.85
14 | BHARAT FRITZ WERNER LTD, | Light Engineering | 0.82
15 | TEMIC Industies Systems India | Misc. | 0.75
16 | SIGMA ALDRICH CHEMICALS P LTD | Chemical | 0.62
17 | M/S CENTRE FOR DEVELOPMENT OF TELEMATICS(CDOT) | Misc. | 0.56
18 | ITC Limited Maruthiseva Nagar Bangalore |  | 0.38
19 | Nxtgen Datacentre and Cloud Technologies, Bidadi, I/A, Ramanagara, Karnataka |  | 0.27
20 | M/S Hewlett Packard India Software Corpn. Pvt.Ltd, |  | 0.22
Total Solar Captive Power Plants in Karnataka |  |  | 115.08 MW

## Slide 15: Solar power based Captive Power Plants in Karnataka for FY 2018-19 (2/2)
S. No. | Name of Industry | Industry Type | Installed Solar Capacity (MW)
21 | T.A.PAI MANAGEMENT INSTITUTE | Misc. | 0.21
22 | sonsera sengineering ltd | Automobiles | 0.20
23 | KARLE INFRA PVT. LTD | Misc. | 0.13
24 | Ultra Tech Cements Ltd. (Unit;Rajashree Cements),Gulbarga | Cement | 0.10
25 | Bharatiya Reserve Bank Note Mudran Ltd. | Misc. | 0.10
26 | Dept. of Space,Master Control Facility | Misc. | 0.10
27 | Bharat Earth Movers Ltd, Engine. Divn. | Heavy Engg. | 0.10
28 | University of Agricultural Sciences | Misc. | 0.10
29 | Trelleborg India Private Ltd., Bengaluru | Misc. | 0.06
30 | Wonderla Holidays Ltd., 28th Km, Mysore Road, Hejjala P.O., Ramanagaram Talulk, Bangalore | Misc. | 0.05
31 | GEM SUGARS LTD | Sugar | 0.02
32 | Mangalore Refinery& Petrochemicals Ltd, | Mineral Oil & Petroleum | -
33 | Arvind Ltd, | Textile | -
34 | M/S INFOSYS TECHNOLOGY LTD Bangalore | Misc. | -
35 | HIKAL LTD, | Light Engineering | -
36 | Scald Energy Pvt. Ltd. | Misc. | -
37 | KIOCL Ltd., Blast Furnace Unit | Mining & Quarrying | -
Total Solar Captive Power Plants in Karnataka |  |  | 115.08 MW