## Slide 1: PJ_ST_CDD Final Report
AUGUST 2025

## Slide 2: Disclaimer
TO BE ADDED BY DELOITTE JAPAN

## Slide 3: TABLE OF CONTENT
1 | COMMERCIAL RISK ASSESSMENT OF PJ_ST Project
1.1 | Project Details
1.2 | Commercial Risk Assessment
2 | CURRENT STATE ASSESSMENT OF NEPAL POWER MARKET
2.1 | As-is Assessment of Electricity Sector In Nepal
2.2 | Cross Border Electricity Trade (CBET) Landscape in Nepal
3 | SECTORAL OUTLOOK IN NEPAL
3.1 | Demand Supply Outlook
3.2 | Policy & Regulatory Outlook
4 | INDIA POWER MARKET ASSESSMENT
4.1 | Electricity Trading Market and the Underlying Regulatory And Policy Landscape
4.2 | Framework For Discovery of The Market Clearing Price in The Power Exchanges
4.3 | Profile of Key Buyers/Off-takers in The Power Exchanges
4.4 | Trends of Volumes and Average Market Clearing Prices In Power Exchange For The Past 3-5 Years
4.5 | Payment Security Mechanism and Key Associated Risks
4.6 | Outlook For Short-term Market in India
4.7 | View on The Future Market Clearing Prices In Light Of Increase In Renewables
 | ANNEXURE

## Slide 4: Abbreviations
ACRONYM | DESCRIPTION
CAGR | Compound Annual Growth Rate
CBET | Cross Border Electricity Trade
CEA | Central Electricity Authority (India)
CERC | Central Electricity Regulatory Commission
COD | Commercial Operation Date
DAM | Day Ahead Market
G-G | Government to Government
GoI | Government of India
GoN | Government of Nepal
IEX | Indian Energy Exchange
IPP | Independent Power Producers
DoED | Department of Electricity Development
ERC | Electricity Regulatory Commission, Nepal
KV | Kilo Volt
KWh | Kilo Watt Hour
MW | Mega Watt
NDC | Nationally Determined Contribution
NEA | Nepal Electricity Authority
NPR | Nepalese Rupee
NVVN | NTPC Vidyut Vyapar Nigam Limited
PEC | Power Exchange Committee
PPA | Power Purchase Agreement
RCOD | Required Commercial Operation Date
RTM | Real Time Market
RPGCL | Rastriya Prasaran Grid Company Limited

## Slide 5: Assumptions & Declarations
No. | Name | Nepali | Days | Corresponding Gregorian months
1 | Baishakh | बैशाख | 30 / 31(30.950 exactly) | mid-April to mid-May
2 | Jestha | जेष्ठ or जेठ | 31 / 32(31.429 exactly) | mid-May to mid-June
3 | Ashadh | आषाढ़ or असार | 31 / 32(31.638 exactly) | mid-June to mid-July
4 | Shrawan | श्रावण or साउन / सावन | 31 / 32(31.463 exactly) | mid-July to mid-August
5 | Bhadra | भाद्र or भदौ/भादो | 31 / 32(31.012 exactly) | mid-August to mid-September
6 | Ashwin | आश्विन or असोज or कुआर/क्वार | 30 / 31(30.428 exactly) | mid-September to mid-October
7 | Kartik | कार्तिक | 29 / 30(29.879 exactly) | mid-October to mid-November
8 | Mangsir | मार्ग or मंसिर/अगहन | 29 / 30(29.475 exactly) | mid-November to mid-December
9 | Poush | पौष or पुष/पूस | 29 / 30(29.310 exactly) | mid-December to mid-January
10 | Magh | माघ | 29 / 30(29.457 exactly) | mid-January to mid-February
11 | Falgun | फाल्गुन or फागुन | 29 / 30(29.841 exactly) | mid-February to mid-March
12 | Chaitra | चैत्र or चैत | 30 / 31(30.377 exactly) | mid-March to mid-April

## Slide 6
 | Responses to the Comments received on the Interim Report

## Slide 7: Response to the Comments on Interim Report
Sl. No | Queries | Response
RCOD Extension |  | 
1 | With regard to the RCOD extension, is the delay due to governmental agencies other than NEA (i.e. the forest authority) be recognized as a reason for extension under the PPA? | As per the provisions of the PPA, extensions to the RCOD are permissible only under two scenarios: Force Majeure, as outlined in the PPA; or NEA’s non-fulfilment of obligations, such as delays in the completion of transmission infrastructure. Delays arising from the actions or inactions of other governmental agencies, such as the forest authority, are not explicitly recognized in the PPA as grounds for RCOD extension. However, based on market soundings with IPPAN and other stakeholders, this has emerged as a matter of ongoing debate. IPPs have raised concerns regarding procedural delays in securing government permits and clearances, and there have been industry-wide discussions to consider such delays as valid grounds for extension. Market feedback indicates that NEA has, in certain instances, granted RCOD extensions for projects that experienced procedural delays in securing statutory approvals. These extensions have not been automatic but granted at NEA’s discretion, contingent on the developer’s ability to substantiate that the delay was solely attributable to government processes. Such decisions appear to be case-specific and merit-based, lacking a consistent framework within the PPA. In conclusion, while the current PPA framework does not explicitly permit RCOD extensions due to delays by government bodies other than NEA, there is limited precedent for such relief being granted in practice, albeit on a discretionary basis.
2 | If the force majeure was activated, did Breeze issue a notice at the time of the flood? | During the Field Visit, Breeze mentioned that they conducted a technical study on impact of the flood based on which they are seeking extension on RCOD. A confirmation on the issuance of notice at the time of flood can be gathered from either Breeze or the technical consultant. PPA Clause 15.2 on issuance of notice during force majeure - The Party claiming the occurrence of a Force Majeure Event as specified in Clause 15.1, shall notify to the other party within 7 (seven) business days of occurrence of such event with the details of the event. Failure to notify with details within specified time shall not be considered an occurrence of Force Majeure Event. Likewise, the Party claiming a Force Majeure Event shall, after the end of such event, notify the same to the other party without any unreasonable delay. In case where the Force Majeure Event already ended at the time of notice of occurrence of Force Majeure Event, the notice shall be given together by disclosing the period of the occurrence of the Force Majeure Event

## Slide 8: Response to the Comments on Interim Report
Sl. No | Queries | Response
RCOD Extension |  | 
3 | Will the flood with be recognized as a force majeure (once in a 100-year event)? | Clause 15.1 of the PPA provides that a flood event exceeding the one-hundred-year Design Flood Discharge, as specified in Schedule 1 of the PPA, qualifies as a Force Majeure event. In the context of the flood, recognition under Force Majeure will depend on whether the actual flood discharge exceeded the threshold defined in the PPA. A post-flood Technical Study has reportedly been undertaken by Breeze. It is essential that the Technical DD team reviews the findings of this study to determine whether the flood meets the specified criteria for a Force Majeure declaration..
4 | Are there cases of force majeure being activated for other IPPs? | Force Majeure clauses are a standard feature in Power Purchase Agreements (PPAs) for hydropower projects in Nepal, given the sector's exposure to natural hazards such as floods, landslides, and earthquakes. There are precedents where IPPs have successfully invoked Force Majeure provisions to secure extensions of their Commercial Operation Date (COD) in response to such events. Notable examples include: Likhu 2 Hydropower Project (L2HP): Granted a 3-month RCOD extension due to flood-related disruptions. Middle Bhotekoshi Hydropower Project: Received COD extension following flood damage. These cases demonstrate that NEA has, in practice, acknowledged natural disasters as valid Force Majeure events when supported by appropriate technical evidence. However, such extensions are typically granted on a case-by-case basis and require substantiation of the event’s severity and its direct impact on project timelines.

## Slide 9: Response to the Comments on Interim Report
Sl. No | Queries | Response
RCOD Extension |  | 
5 | The actual downtime due to the flooding was about a week, but how does Breeze perceive that? Even if flooding is recognized as a force majeure, how much period will the extension be granted? | Technical DD team to review the technical report and its applicability as force majeure event and confirm its impact
6 | If the extension of RCOD is granted, will the PPA contract period also be extended? | As per Clause 2.1 of the PPA, the contract period is defined as the earlier of 30 years from the Commercial Operation Date (COD), or The validity period of the Generation License. Accordingly, if an extension to the RCOD is granted, the term of the PPA will also shift forward and commence from the revised COD. However, this extension is bounded by the overall validity of the Generation License. In other words, while the PPA term is linked to COD, it cannot exceed the duration specified in the Generation License. This interpretation has also been reaffirmed in discussions with NEA.

## Slide 10: Response to the Comments on Interim Report
Sl. No | Queries | Response
Sales of electricity to IEX/ alternative off-takers |  | 
1 | Regarding the planned revision of Nepal's electricity law, how long is it expected to take for IPPs to actually be able to do business with off-takers other than NEAs (domestic/IEX)? | Estimating the timeline for legislative reforms in Nepal, particularly the enactment of a new Electricity Act, is difficult given Nepal’s track record of political instability and frequent changes in administrative leadership. Although the proposed Electricity Act has been in development for several years and has reached Parliament on multiple occasions, it has not yet been enacted. However, recent developments offer optimism. The Draft Electricity Bill 2080 and the Draft Open Access Directives by the Electricity Regulatory Commission (ERC) signal serious intent to reform the market. These initiatives are aimed at enabling IPPs to transact with off-takers beyond the NEA. As per discussions with ERC officials, the Draft Open Access Directives will remain open for stakeholder and public feedback for a period of two months. Following this consultation, the directives will be revised and then submitted for final approval. Based on the current trajectory, the notification of these directives is expected to take at least six to nine months from the draft stage. Further, sub-regulations to implement open access like amendments to grid code, deviation settlement mechanism, connectivity regulation, grievance redressal etc. are still under preparation. The Energy Development Roadmap 2081, released earlier this year, reinforces this direction by calling for the passage of the revised Electricity Act within six months. IPPAN has also been actively advocating for these reforms and is engaging closely with relevant government and regulatory bodies. In summary, while it remains difficult to provide a precise timeline, the recent policy signals and regulatory steps suggest some optimism that IPPs may gain access to non-NEA off-takers.

## Slide 11: Response to the Comments on Interim Report
Sl. No | Queries | Responses | Reference in the report
Sales of electricity to IEX/ alternative off-takers |  |  | 
2 | Please share with us specific, quantitative data, such as supply and demand trends in electricity sales to India, risks in cross-border sales, and transmission congestion trends. | Cross Border Power Export from Nepal to India has become more than 15 times in the last 5 years from FY 2019-20 (107 GWh) to FY 2023-24 (1943 GWh). There is also dependency of import of power from India during dry seasons and net value of power import for FY 2023-24 reached 1834 GWh. Risks in cross-border sales – Dependency on NEA - As per the prevailing regulatory regime, NEA will decide on the cross-border power sale of excess power from the plant and payment will be made in PPA Rates to the IPPs Approval requirement - Export approval from the Government of India (GoI) is project-specific and subject to Cross Border Trade of Electricity (CBTE) guidelines Transmission Congestion - Real-time access to Indian power exchanges can be restricted due to grid congestion Transmission Congestion Trends – 400 kV Dhalkebar-Muzzafarpur cross-border transmission line mainly involved in the cross-border transactions between India and Nepal. As per the analysis of the latest available data (June 2024 to November 2024), considering 1000 MW as the Available Transmission Capacity of the transmission line, there is 75%-85% (approx.) utilization on the 400 kV Dhalkebar – Muzaffarpur transmission line during the dry months. Based on the analysis of data of Monthly Grid Disturbance/Incidence reports from March 2023 to May 2025, we have not found any instance in which there were any interruptions reported in 400 kV Dhalkebar – Muzaffarpur transmission line. | Page 46 of includes the details of Cross Border Power Export from Nepal to India during past 5 years Page 102 - Analysis of the supply and demand trends in electricity sales to India in past years Page 103 - Analysis of the transmission utilization of 400 kV Dhalkebar-Muzzafarpur lines

## Slide 12: Response to the Comments on Interim Report
Sl. No | Queries | Responses | Reference in the report
Sales of electricity to IEX/ alternative off-takers |  |  | 
3 | At present, it is understood that electricity can only be sold to India through the NEA, but is there room for PJ ST to enter the Indian IEX market in the future? | Under Nepal’s current regulatory framework, cross-border electricity sales to India are permitted through the Nepal Electricity Authority (NEA). NEA functions as the bulk purchaser of electricity under all Power Purchase Agreements (PPAs), and payments for cross-border transactions are made at the agreed PPA rates. The Government of Nepal is currently undertaking initiatives to promote cross-border electricity trade. In June 2025, the Draft Open Access Directives were published, aiming to facilitate such transactions. Additionally, the Draft Electricity Bill, 2080, currently under parliamentary review includes provisions designed to support cross-border electricity trade. If these bill and directives are enacted without any deviating amendments, PJ ST may have the opportunity to participate in the Indian power market in the future subject to applicable GoI rules. | 
4 | Is there a trade of electricity between NEA and purely private IPP operators, rather than NEA and state-owned (i.e. NPVN)? Which companies in Nepal will be competitors if Stream enter the IEX market? | At present, NEA is a bulk purchaser of power from all IPPs in Nepal and payments for cross-border transactions are made at the agreed PPA rates. All the IPPs companies in Nepal (existing and upcoming) who have inclination towards participation in CBET/IEX markets and have contracted capacities under Take and Pay obligations will be the probable competitors to Stream in IEX market. | Page 27 - A few projects having take and pay obligations have been detailed.

## Slide 13: Response to the Comments on Interim Report
Sl. No | Queries | Responses | Reference in the report
Sales of electricity to IEX/ alternative off-takers |  |  | 
5 | On slide pg.87, there is a time when the price of electricity in the IEX falls below Rs 3. In that case, it is expected that the NEA will refuse to purchase power under the terms of the Take and Pay, because IEX selling price is lower than PPA Take and Pay price. Therefore, the client would like to know how frequent the price of electricity in the IEX falls below Rs 3 and what kind of transactions were made at that time (whether the NEA chose to not sell electricity to India). In addition, the client would like to receive any forecast data on the reserve rate and future prospects, and to predict the amount of additional energy purchased by the NEA for PJ ST. | As per the information shared, NEA can potentially sell the electricity from the target's hydro power plant in wet season (monsoon). The Market Clearing Price (MCP) in the electricity exchange (IEX) is likely to below INR 3/kWh from 11 AM to about 3 PM in a typical day. There is no differentiation in the source of power sold in power exchange. While there are time blocks when the MCP falls below INR 3/kWh, there are also certain time slots when the MCP is higher than INR 5/kWh. We understand that NEA, historically, sells power on the Indian power exchange through NVVN. NEA contracts a certain capacity (MW) for sale in the exchange. It may be appropriate to consider the average MCP in the power exchange vis-a-vis the PPA price to consider whether it will be viable for NEA to sell electricity in the Indian Power exchange or not. Workings for the same indicate that the NEA may end up having a positive cost arbitrage in the transaction pertaining to sell electricity in the power exchanges in India. | Page 130 - Historical sale of electricity by NEA in IEX
6 | Based on above question, how much stress should be applied to the purchase amount of additional energy by NEA in the valuation (considering cases such as IEX selling price might fall below NEA’s Take and Pay PPA price)? |  | Pages 131 to 133 – Estimated impact of sale of electricity from the project in IEX

## Slide 14: Response to the Comments on Interim Report
Sl. No | Queries | Responses
1 | What positions did the interviewees hold? | Mr. Lunar Shrestha - Manager - Power Trade Department and Ms. Mandira Adhikary Deputy Manager, Power Trade Department
2 | Are the interviewees affiliated with departments responsible for the practical operations related to RCOD extension? | Yes, the interviewees are affiliated with NEA's Power Trade Department which handles all PPAs of NEA.

## Slide 15: Response to the Comments on Interim Report
Sl. No | Queries | Responses
1 | Is it possible to investigate whether ST could also qualify as an export-eligible project for India, similar to Likhu-1 mentioned on pg.14? | There are two types of export-oriented power plants in Nepal: Dedicated Export Plant - These are 100% export-oriented power plants with entire planned generation to be exported. They have no PPA with NEA for domestic offtake. Example include the under construction 900 MW Arun 3 Hydropower Project (developed by SJVN Ltd for export of power to India via dedicated 400 kV Arun-Dhalkebar line connecting to Indian Grid) Export Eligible Plants - These plants are allowed to participate in the Indian Power Market through NEA. The decision for determining which plants should be submitted for approval of selling power to India depends on NEA. The approval is accorded by Govt. of India based on the "Procedure for Approval and Facilitating Import/Export (Cross Border) of Electricity by the Designated Authority " and its extant amendments. (Source: Designated Authority Procedure 2021). The Key eligibility criteria (as per Section 6.3 of the procedures) are: (i) Indian Entity nominated by Government of India to import electricity from generating projects of neighbouring country and sign PPAs with DISCOMs for the power being imported. OR Indian entities may import electricity from the generation projects located in neighbouring country(ies) directly or through Government or a Government Company or a licensed trader of that country after taking approval of the Designated Authority, provided that the generating company is not owned, directly or indirectly by any natural/ legal personality(ies) whose effective control or source of funds or residence of beneficial owner, is situated in/ citizen of a third country with whom India shares land border and that third country does not have a bilateral agreement on power sector cooperation with India. For any relaxation in this provision, the Designated Authority will consult Ministry of Power and Ministry of External Affairs. (ii) The generation project(s) of the neighbouring country should submit the permission to export power to India from the respective Government of the neighbouring country. (iii) The Applicant shall submit a copy of Power Purchase Agreement (PPA)/ or of Letter of Intent (LOI) from generator of neighbouring country, for import of such power. (iv) The Applicant shall submit the application to the Nodal Officer in the format enclosed at Annex-I. (v) The person making the application shall submit an affidavit stating that he/she is the authorized person to make an application on behalf of the entity and approval from his board need to be submitted. (vi) The Applicant shall submit an undertaking on affidavit that any change in the equity pattern (after the date of approval by the Designated Authority) of the generating company/trading licensee of the neighbouring country from where electricity to be imported, shall be intimated to the Designated Authority, within thirty (30) days of such change. Failure to notify this change may be considered by the Designated Authority as a ground for revocation of the approval. The Applicant should obtain similar undertaking from the generating company/ trading licensee of the neighboring country in its contract.

## Slide 16: Response to the Comments on Interim Report
Sl. No | Queries | Responses
2 | Would it be possible to investigate NEA’s sales performance by time zone as described in Pg.86, Section III? | This information is not published by NEA or by IEX for public consumption

## Slide 17
CHAPTER 1 | COMMERCIAL RISK ASSESSMENT OF PJ_ST Project

## Slide 18: PJ_ST Project I Current Project Structure
Sale of additional 30 MW is subject to domestic market demand, regulatory and policy framework and NEA’s participation in CBET markets
PJ_ST Project
RCOD as per PPA
28th February 2026
Installed Capacity
100 MW
Power Purchaser
NEA
PPA Duration
30 Years
Contracted PPA Capacity : 70 MW
Project Additional Capacity :
30 MW Offtake by NEA
Contractual Obligation for NEA – Take or Pay
Purchase Season – Dry and Wet Months Electricity Purchase Price – As per PPA (dry season - NPR 8.4/kwh and wet season – NPR 4.8/kwh)
Price Escalation – 3% till 8 times
Contractual Obligation for NEA – Take and Pay
Purchase Season – Wet Months
Electricity Purchase Price – As per PPA
Price Escalation – 3% till 8 times
NEA sells excess electricity in domestic market at PPA rates
NEA sells excess electricity in cross border markets at PPA rates
1
2
The project’s current transaction structure makes sale of additional 30 MW subject to NEA’s discretion which further depends on futuristic seasonal domestic market demand, regulatory and policy framework and NEA’s participation in CBET markets. It is therefore important to assess the market and the commercial aspects of the domestic market in Nepal and export markets in India.
Nepal Electricity Authority

## Slide 19: PJ_ST Project I Monthly Generation Profile
The hydro plant is envisaged to generate additional power during the wet season
Chart: 
 | 28578.158 | 49496.959 | 51093.636 | 49496.96 | 49496.96 | 49496.96 | 40399.477 | 22278.666 | 16844.134 | 13523.835 | 13983.608 | 16399.433
 | 11807.918 | 21897.084 | 21212.8 | 21212.8 | 21212.8
 | 40.416 | 86.699 | 100 | 100 | 100 | 100 | 59.039 | 33.68 | 24.616 | 20.445 | 20.435 | 23.996
40
16Apr-15May
16May-15June
16June-15Jul
16Aug-15Sep
16Sep-15Oct
59
16Oct-15Nov
34
16Nov-15Dec
16Dec-15Jan
16Jan-15Feb
16Feb-15Mar
16Mar-15Apr
61,305
72,991
70,710
70,710
70,710
16Jul-15Aug
Project Monthly Power Generation Profile (MWh)
Source: PPA Schedule 2.1 Table II
Contract Energy for 70 MW
Additional Wet Energy
Power (MW)
WET MONTHS
The monthly generation profile under the PPA indicates additional wet season energy generation exceeding the contracted capacity of 70 MW, reaching up to 87–100 MW. As per the PPA terms, NEA has a take-and-pay obligation to purchase this excess energy at the PPA tariff of NPR 4.80/kWh, for sale in the domestic or cross-border power markets.
For simplification, Nepali Months have been converted as per English Calendar. For example, Baishakh month corresponds to Mid April to Mid May

## Slide 20: PJ_ST Project I Commercial Risk Assessment Framework
It is imperative for STHPP to evaluate the potential commercial risks and devise necessary mitigation strategies
1
3
2
4
添加标题
Contract energy sale – Reserve margin, transmission infrastructure, excess generation
Un-contracted or unobligated energy sale – Domestic market, Export market
Off-take approvals
Operational Performance
Executive Risk
Regulatory and Compliance
Monthly Delivery Compliance– >80% of contract energy or availability declaration
Dry season obligation – >30% dry season energy
Hydrology variation – Risk of hydrology with developer
Delay in RCOD (Commercial Operation Date): Increases Interest During Construction (IDC), Impacts tariff escalation schedule and returns
Transaction Approvals: DOED and ERC approval
Policy and Regulatory landscape: Could pose risk if planned interventions don’t happen
Market and Off-take Risk

## Slide 21: PJ_ST Project I Market and Off-take assessment
Reserve margin limits affect revenue, but expanding market access and evolving pricing may offer new offtake opportunities
Sl. No | Category | Sub-category | Description/Reference Clause | Impact | Reference in the report
1 | Contracted Energy Sale Risk | Reserve Margin | As per the first Amendment of PPA, during the wet season, NEA is obligated to buy only 90% of the availability and the remaining will be reserve margin. NEA will not pay for the reserve margin in case not purchased. However, this is applicable till end of 2027-28. | Limits monetization of full generation potential in wet season; unutilized reserve margin leads to foregone revenue, affecting project returns particularly during high generation periods. | -
2 | Contracted Energy Sale Risk | Transmission Infrastructure – Project | Readiness of the transmission infrastructure for evacuating power from the current project. Though the receiving substation has been commissioned, the evacuation from project to the substation has to be completed in line within the COD or else will have impact on RCOD. As per the discussion with NEA and Breeze, the transmission infrastructure development for this project is on track. | Delay in completing project-side evacuation infrastructure could defer RCOD, triggering financial penalties, and loss of early generation revenue. Incase of delay, contingency arrangements could also be discussed with NEA. There are precedent cases where contingency arrangement has been made on Take and Pay basis. Few projects were this contingency plan has been implemented include: 1) Ghalemdi Khola Hydroelectric Project - 5MW; 2) Upper Khorunga small hydropower project - 7.5MW; 3) Dovan Khola Hydropower Project - 24.5 MW. the contingency arrangement above has been made on a case-to-case basis by consulting with NEA when the delay arises. Thus, PJ ST will need need to consult with NEA (Grid Operation Department and Power Trade Department) periodically to monitor and discuss if there is a risk of delay in construction of interconnection facility (either from Breeze or NEA-side). The power evacuation related aspects are handled by the Grid Operation Department at NEA. | 

## Slide 22: PJ_ST Project I Market and Off-take assessment
Reserve margin limits affect revenue, but expanding market access and evolving pricing may offer new offtake opportunities
Sl. No | Category | Sub-category | Description/Reference Clause | Impact | Reference in the report
3 | Contracted Energy Sale Risk | Transmission Infrastructure – Cross Border | As per the provisions of the clause 10.1 (a), NEA will not pay any compensation due to the following reasons: If there is any problem in one of the double circuits of Dhalkebar-Muzaffarpur 400 K.V. Transmission Line during 2022/23 A.D. to 2024/25 A.D. If there is overload in Dhalkebar-Muzaffarpur 400 K.V Transmission Line during 2022/23 A.D. to 2024/25 A.D. If the second cross border double circuit New Butwal-Gorakhpur 400 K.V.Transmission Line does not come into operation after getting constructed till 2025/26 A.D. then from 2025/26 A.D. to such Line comes into operation. | Non-compensable outages or delays in cross-border infrastructure directly reduce energy evacuation and revenue; will expose project to curtailment risk in export markets during critical revenue-earning periods. The restriction for outage or interruption or overloading, during wet-off-peak period for the Dhalkebar-Muzzaffarpur 400 kV line was limited till FY 2024-25 (15-July-2025). Since, we are past this deadline this restriction is no longer applicable. The second restriction that will be applicable in case the New Butwal–Gorakhpur 400 kV D/C transmission line is not operational and loading of any circuit of Dhalkebar–Muzaffarpur line is beyond 120% during the Wet Period. This restriction will also be applicable during the Wet Off Peak Period (irrespective of the loading of any circuit). We have also carried the review of the line utilization on a month-on-month basis for June-Nov 2024. | Chapter 2.2, 3.1 and Annexure
4 | Contracted Energy Sale Risk | Excess Generation | As per the provisions of the Clause 12.2 in the PPA, NEA may purchase the Excess Energy by issuing Dispatch Instruction at 50% of the PPA rate | Excess energy earns only 50% of the base tariff, which reduces project returns during high-flow months when generation is highest. | -

## Slide 23: PJ_ST Project I Market and Off-take assessment
Reserve margin limits affect revenue, but expanding market access and evolving pricing may offer new offtake opportunities
Sl. No | Category | Sub-category | Description/Reference Clause | Impact | Reference in the report
5 | Uncontracted Energy Sale Risk | Domestic market in Nepal | As per the current PPA, 70 MW has been contracted capacity with NEA and there is additional 30 MW which is under ‘Take and Pay’ arrangement. Ability of Nepal to absorb the additional energy for the domestic consumption is under the discretion of NEA based on the requirement of energy. | Revenue realization for uncontracted energy is uncertain; reliance on NEA’s discretionary purchase introduces cash flow volatility and curtailment risk in periods of excess supply. However, there are other projects as well in Nepal with Take and Pay clause and NEA is purchasing ‘Additional Energy’ from them (in 2023-24). | Chapter 1, 2 and 3
6 | Uncontracted Energy Sale Risk | Export Market | As per the current PPA, 70 MW has been contracted capacity with NEA and there is additional 30 MW which is under ‘Take and Pay’ arrangement. Probability of Sale of excess power via cross border mechanism during wet season is subject to availability and decision by NEA and then approval by Government of India. Further, the developer will be paid only the PPA Rates which results in no price benefits for the project developer even if there is power export in the CBET mode, but it assures revenue recovery in PPA Tariff. | Export provides a fallback for surplus energy, but pricing is capped at PPA rates, offering no upside from market-based prices; further, reliance on annual GoI approvals introduces regulatory and continuity risk for cross-border sales. However, proposed market reforms (Electricity Bill and ERC initiatives) may open the export market for IPPs in Nepal. | Chapter 3, 4

## Slide 24: PJ_ST Project I Execution risk
Timely project delivery remains a challenge, but strong planning / execution and NEA buy-in crucial to avoid impact of delays
Sl. No | Category | Sub-category | Description/Reference Clause | Impact | Reference in the report
1 | Execution risk | Delay in RCOD | As per the second amendment of PPA, the RCOD of the project is 28th February 2026. Considering the current project status, there may be requirement of extension of RCOD. Based on discussion with IPPAN, the RCOD extension has been provided to generating companies (IPPs) once due to COVID. Any RCOD extension will be done by NEA, only due to two reasons: Force Majeure - As specified under PPA NEA's non-fulfilment of its obligations like delay in transmission infrastructure. Applications are usually submitted to NEA 2-3 months before the RCOD. In this project, initial extension of RCOD was allowed due to COVID-19. RCOD extension is common in Nepal. Based on the discussions with Breeze, they mentioned that the project was impacted by flood and the study of impact has been conducted by them. RCOD extension on account of flood will have to meet the following criteria – “in excess of the one-hundred-year Design Flood Discharge mentioned in Schedule 1“ as mentioned in the force majeure conditions. | Impact on overall project cashflow - If there is delay in the RCOD, based on the delay, there will be impact on the number of escalations in the tariff (3% escalation each year up to 8 times) this will have impact on the cashflow of the project. (For instance - Where COD is late by more than six months and less than 18 months when compared to RCOD, then there will be only 7 price escalations). There are several projects that face delay in Nepal and NEA extends the RCOD depending on the merit of the case. | Illustration provided in Annexure

## Slide 25: PJ_ST Project I Operational performance risk
Hydrological and performance-linked risks exist, though prudent design, forecasting, and contractual compliance can ensure operational stability
Sl. No | Category | Sub-category | Description/Reference Clause | Impact | Reference in the report
1 | Operational performance | Monthly delivery compliance | Failure to Deliver Contract Energy If monthly delivery is less than 80% of the lesser of Contract Energy or Availability Declaration (excluding Force Majeure, Scheduled Outage, or Emergency Maintenance), the Company pays compensation. Compensation = [0.8 × Declared Energy – Delivered Energy] × Purchase Rate | Creates monthly cash flow volatility and exposes the project to financial penalties during low-generation periods, increasing operational risk and requiring conservative generation forecasts. | -
2 | Operational performance | Dry Season Obligation | Dry Season Minimum Delivery If energy delivered during Dry Months is less than 30% of annual Contract Energy, compensation is calculated and adjusted in future bills. Compensation = [Total Annual Energy – (Dry Season Energy / 0.30)] × Wet Season Rate | Under delivery in dry months results in revenue clawback, impacting project liquidity and financial planning; managing seasonal flows becomes critical to maintaining PPA compliance and profitability. | -
3 | Operational performance | Hydrological risk | Nepal’s run-of-river hydropower plants are highly dependent on river flow, which varies significantly across seasons—typically peaking during the monsoon and dropping sharply in the dry months. As a result, hydrological risk is effectively transferred to the developer, with no compensation for shortfalls in energy generation (below contract energy) due to low water availability or plant outages. In practice, projects in Nepal have underperformed relative to their initial energy projections | High seasonal variability in river flow can lead to underperformance against PPA targets, posing long-term revenue risk and challenging debt servicing capacity without adequate hydrology buffers in the DPR or financial model. | -

## Slide 26: PJ_ST Project I Regulatory and Compliance
The regulatory landscape is evolving, and with active engagement and compliance, approval and licensing risks are largely navigable
Sl. No | Category | Sub-category | Description/Reference Clause | Impact | Reference in the report
1 | Regulatory and compliance | Transaction approvals | DoED Approval Requirement As per the Generation License, any alteration or change in the ownership structure of the organization requires prior approval from the Department of Electricity Development (DoED). ERC Approval Requirement As per the provisions of Electricity Regulatory Commission Rules, 2018, there is requirement to obtain prior Approval of the Commission to make Change in Share Structure (more than 5% change) | DOED - Based on the discussions with DoED, since the Generation License includes the provision that mandates the prior approval from the Department of Electricity Development (DoED), the same should be attained. It requires submission of Net Worth certificate, attested by a CA. Approval process usually takes 1 week, if all documents are in order. There is no specified format. ERC - Prior approval from ERC is required for share transfer beyond 5%. The process usually takes 15 days. | -
2 | Regulatory and compliance | Approval for sale by NEA | As per Clause 5.2 of PPA, the electric energy to be generated from the Project cannot be sold to any other entity or such rights cannot be transferred without prior approval of the Authority. As per Clause 10.1(c) of PPA, NEA allows third-party sales only if technically feasible and with NEA’s approval. NEA may permit use of its transmission system by charging a Wheeling Charge. | Commercial flexibility is constrained; inability to secure timely NEA approval can constrain market-based energy sales or export opportunities (in future). | -
3 | Policy and regulatory | Anticipated reforms | Effect on delay in the Planned Reforms – Open access directives, Electricity Bills | Slower policy evolution on Electricity Bill may limit future upside for merchant sales (in Nepal or India), wheeling, and open access, reducing long-term monetization potential of uncontracted power beyond the current PPA framework. | Chapter 3.2

## Slide 27: Similar Projects in Nepal I Mix of ‘Take or Pay’ and ‘Take and Pay’ PPAs
Existing hydro projects with partial take-and-pay capacity are also operating in Nepal; NEA is off-taking the ‘Additional Energy’ and exporting too
Details | Likhu 1 (Pan Himachal Energy Limited ) | Likhu 2 (Global Hydropower Associate Limited) | Likhu Khola A (Numbur Himalaya Hydropower Limited)
Installed Capacity | 77 MW | 55 MW | 29.04 MW
Capital Cost | NPR 15,604 Mn | NPR 9,313 Mn | NPR 7,791 Mn
COD | March 2024 | July 2023 | February 2022
PPA Contract |  |  | 
Additional Energy Offtake by NEA (2023-24) |  |  | 
PPA Rate | Dry Season – 8.4 NPR/kWh; Wet Season 4.8 NPR/kWh |  | 
If Exporting? | Yes (NEA is exporting full capacity) | No | No
Chart: 
 | 51.4
 | 25.6
77
Take or Pay (MW)
Take and Pay (MW)
Chart: 
 | 33.4
 | 19.2
53
Take or Pay (MW)
Take and Pay (MW)
Chart: 
 | 24.2
 | 4.8
29
Take or Pay (MW)
Take and Pay (MW)
Some operational IPP-led hydropower projects in Nepal—including Likhu-1, Likhu-2, and Likhu Khola A—have commissioned capacities under ‘Take-and-pay’ contracts and are selling “Additional Energy” and “Excess Energy” to NEA. For Likhu 1, NEA is exporting the entire generation (approval till October 2027) to India at INR 5.4-5.5/kWh through NVVN (Settlement Nodal Agency in India). While exports are currently routed through NEA, proposed power market reforms may enable direct export access for IPPs in the future.
Source: Likhu1, Likhu2, LikhukholaA
Note: The projects highlighted are illustrative and there may be several other projects as well on similar PPA model involving both ‘Take or Pay’ and ‘Take and Pay’ arrangement.

## Slide 28: Summarizing Additional Power Sale Scenarios (1/2)
Possible scenarios to assess additional 30 MW power transaction during the wet season in the current context
1
SCENARIO 1 - EXISTING POLICY & REGULATORY LANDSCAPE
Nepal Electricity Authority
Sell excess electricity in domestic market at PPA rates (NPR 4.8/kWh with
escalation over years))
Sell excess electricity in CBET market at PPA rates (NPR 4.8/kWh with
escalation over years))
Dependency on domestic seasonal demand – supply scenario
Dependency on NEA’s agreement to off-take
Offtake not guaranteed
Dependency on wet season demand in India
Dependency on GOI approvals
Offtake not guaranteed
I
II
POTENTIAL
CONSIDERATIONS
To enable a favorable transaction for the project, it is imperative to assess seasonal domestic power demand and CBET market outlook

## Slide 29: Summarizing Additional Power Sale Scenarios (2/2)
Possible scenarios to assess additional 30 MW power transaction during the wet season in case anticipated reforms happen
2
SCENARIO 2 - OUTLOOK – ANTICIPATED REGULATORY &
POLICY FRAMEWORK DEVELOPMENTS
Competitive pricing from other plants
No fixed timelines for the initiative adoption
Draft Open Access directives are published for public comments to be further followed by amendments in Electricity Bill/Act and trading license
Competitive pricing from other plants
No fixed timelines for the initiative adoption
Approval from GOI
POTENTIAL
CONSIDERATIONS
Sell additional power to domestic open access consumers
Export power through
Directly in exchange
Bilateral/Trilateral arrangements
I
II
Probable developments across enablement of Open Access, Trading Licenses, Favorable provisions in Electricity Act, Direct participation in cross border power markets initiatives
PROJECT ST
In the subsequent sections, the report focuses on current state and outlook of Nepal’s power sector landscape (demand-supply dynamics, regulatory and policy framework) for cross-border power trade

## Slide 30: Deep-dive areas
Analytical Flow for the Deep-dive: Assessing Nepal’s Power Sector Context and Cross-Border Market Linkages
Institutional, Policy and Regulatory Assessment of Nepal
As-Is Assessment of the power sector including CBET
Outlook of the Nepal Power Sector
As-is Assessment and Outlook of the power market in India
Power sector institutional set-up including key stakeholders
Policy and Regulatory landscape
Key regulations and development in cross border electricity trade (CBET)
Assessment of the electricity demand and supply
Assessment of the transmission infrastructure both for domestic and cross-border
Status of current CBET transactions
Demand supply outlook for the next 10-15 years
Policy and regulatory outlook – focus on Electricity Bill and ERC Roadmap
Assessment of the electricity demand and supply in India
Trends in the power market in India
Price analysis
Outlook of the pricing
1
2
3
4

## Slide 31
CHAPTER 2 | CURRENT STATE ASSESSMENT

## Slide 32
2.1 | AS-IS ASSESSMENT OF ELECTRICITY SECTOR IN NEPAL
Notes: .

## Slide 33: Institutional Structure of Nepal Electricity Sector
Generation
(3157 MW)
Nepal Electricity Authority
(661.57 MW)
Independent Power Producers
(2495.61MW)
Single Buyer
Purchase
Nepal Electricity Authority
Transmission
Distribution
Sales
Government / Regulator
Ministry of Energy, Water Resources and Irrigation
Overall Sector Planning & Development
Electricity Regulatory Commission
Regulation of power markets, tariff setting, consumer protection
Office of Investment Board of Nepal (OIBN)
Investment Appraisal and Approval for Large Projects
Alternative Energy Promotion Centre
Development of RE below 10 MW
NEA remains the dominant actor in G-T-D segments, and power procurement, functioning as the country’s single buyer of electricity
Nepal Electricity Authority
RPGCL
Nepal Electricity Authority

## Slide 34: Evolving Policy and Regulatory Framework
Key Inferences | 
In the earlier decades, the Government’s focus was on enhancing capacity and promote power trade to meet the rising demand in the country. With rising installed capacity, there has been a shift in focus from early 2010s to drive domestic electricity demand, reducing carbon emissions and position Nepal as a sustainable economy. | 
Recent reforms led by ERC aim to promote transparency, boost domestic demand, and enable regional electricity trade
1992
Electricity Act, 2049
Governs generation, transmission and distribution of electricity; includes provisions of Import/Export of power, basis for royalty
Electricity Regulations 2050
Mandated licensing regime; emphasis on the applicability of the export duty for exporting electricity
1993
2001
Hydro Power Development Policy, 2058 Emphasis on development of hydropower projects as export-oriented projects; royalty computation mechanism
2017
Electricity Regulatory Commission Act, 2074 Empowers ERC to regulate tariffs, issue licenses, resolve disputes; approves tariffs for export and trade agreements.
Policy/Plan/ Name, Publish Year | Key Targets
National Energy Strategy of Nepal, 2013 | Replace 50% of Traditional Cookstoves with Improved Cookstoves (ICS) by 2030
Nepal's Energy Sector Vision 2050 A.D., 2013 | Target to reach a share of 10% LPG, 50% fuelwood, and 40% electricity in rural cooking by 2030 100% electrification in urban cooking by 2030 Enhancing the efficiency of Improved Cookstoves to 15% by 2030 and remain constant till 2050
Sustainable Development Goals Status and Roadmap 2016-2030, 2017 | 99% of population with access to electricity by 2030 Households using fossil fuels to be reduced to 30% by 2030 Share of people using LPG for cooking and heating to reach 39% by 2030 Efficiency of residential appliances to increase till 60% by 2030
Second Nationally Determined Contribution, 2020 | By 2025 : Install 5 lakhs ICS, 2 lakhs additional household biogas plants, 500 large scale biogas plants By 2030 – Ensure 25% of households use electric stoves as their primary mode of cooking by 2030
Nepal's Long -term Strategy for Net-zero emissions, 2021 | 1.7 mMTCO2e reduction in emissions by 2030 4.45 mMTCO2e reduction in emissions by 2050
Sixteenth Plan, 2024 | By 2029 - 100% of households to have access to electricity, 5 lakhs households biogas plants, 10 lakhs Electric stoves connection, 6.45 lakhs improved cookstoves connection

## Slide 35: Electricity Demand Rises Rapidly Amid Economic and Policy-Driven Growth
Driven by rapid electrification, Nepal’s electricity consumption has surged, recording the highest growth rate in South Asia.
Chart: 
 | 1291 | 1444 | 1408 | 1482 | 1748 | 2212
2015
2017
2020
2021
2022
2024
National Peak Demand (MW)
National Peak Demand (MW) and Energy Consumption (GWh)
Key Inferences | 
Driven by policy interventions, rising consumption, rapid industrialization and expanding infrastructures, the national peak demand grew at 6% CAGR However, the consumption mix grew with 14% CAGR over the years, export sales witnessed more than 18x exponential growth from 2020 onwards | 
Source - NEA Annual Report; JICA Integrated Power System Development Plan 2024
Key Demand Drivers
Driven by NDC targets and national goals, policy Interventions to promote increased electricity consumption across –
ELECTRIC VEHICLES
ELECTRIC COOKING
SMART STREET LIGHTING
ELECTRIC RAILWAYS
INDUSTRIAL AND SPECIAL ECONOMIC ZONES
ENERGY EFFICIENCY MEASURES
Chart: 
 | 3741 | 4774 | 6418 | 7275 | 8842 | 10219
 | 3 | 3 | 107 | 38 | 494 | 1946
3
2015
3
2017
107
2020
38
2021
494
2022
2024
3,744
4,777
6,525
7,313
9,336
12,165
+14%
Internal Sales
Export Sales

## Slide 36: Industrial and Domestic Sectors Power Internal Electricity Demand Growth
Expanding industrial activity and a broadening residential consumer base have significantly scaled up domestic electricity sales since 2015
Consumers Growth (thousands)
Chart: 
 | 2671.039 | 3061.709 | 3933.574 | 4208.208 | 4418.593 | 4997.612
 | 41.825 | 46.345 | 55.888 | 60.782 | 64.626 | 68.831
 | 120.923 | 150.474 | 229.08 | 260.299 | 282.802 | 392.832
42
121
2015
46
150
2017
56
229
2020
61
2021
65
2022
69
2024
2,834
3,259
4,219
4,529
4,766
5,459
260
283
+8%
Source - NEA Annual Report;
Internal Electricity Sales Categorization (GWh)
Domestic
Industrial
Others
Chart: 
 | 1679 | 2164 | 2852 | 3138 | 3730 | 4309
 | 1352 | 1719 | 2301 | 2816 | 3448 | 3694
 | 710 | 891 | 1265 | 1321 | 1664 | 2216
2015
2017
2020
2021
2022
2024
3,741
4,774
6,418
7,275
8,842
10,219
+12%
Domestic
Industrial
Others
Key Inferences | 
Industrial and Domestic sectors emerge as biggest power consumers fueling overall surge in internal electricity sales over years (~2.5-2.8x from 2015 levels) While the industrial consumers grew to ~1.65X times, their consumption increased 2.7X+ indicating aggressive industrial expansion in the country Domestic consumers continue to be the largest electricity consumer with sustained growth in consumer base over the years | 
13% CAGR
12% CAGR
11% CAGR
Other categories cover commercial, non-commercial, water supply and irrigation, streetlight, temporary supply, transport, temple, non-domestic, entertainment and community sales

## Slide 37: Hydropower Dominates Nepal’s Growing Installed Capacity Mix
Capacity growth driven by NEA subsidiaries and IPPs has reduced reliance on Indian power imports and expanded solar capacity alongside hydro
Chart: 
 | 477.93 | 507.93 | 581.93 | 1076.06
 | 255.647 | 512.6954 | 814.645 | 1914.772
 | 53.41 | 53.41 | 53.41 | 53.41
 | 0.1 | 0.1 | 1.35 | 106.94
 | 6
7%
2015
53
2018
53
1
2021
2%
3%
2024
787
1,074
1,451
3,157
32%
61%
34%
61%
Total Bagasse (IPP)
Total Solar (NEA)
Total Thermal (NEA)
Total Hydro (IPP)
Total Hydro (NEA + Subsidiaries)
Installed Capacity (MW)
Source - NEA Annual Report
Total Available Electricity (MU)
Chart: 
 | 2368 | 2308 | 2804 | 2911
 | 147 | 149 | 148 | 2597
 | 1122 | 2019 | 3093 | 6564
 | 1370 | 2582 | 2806 | 1895
3%
2015
149
2018
148
2021
2024
5,007
7,058
8,851
13,967
47%
19%
21%
14%
27%
47%
22%
Power Purchase - India
Power Purchase - IPP
Power Purchase - NEA Sub
NEA Own Generation
Key Inferences | 
Hydro dominant IC mix has increased with ~17% CAGR between 2015-24. Rapid surge from 2021 onwards (30%+ CAGR). 493 MW projects from NEA subsidiaries Over the years, IC mix witnessed constant 53.1MW thermal projects indicating inclination towards hydro and clean solutions Additional to hydro projects, solar based projects witnessed a surge from 1 MW in 2021 to ~100 MW in 2024 With increased purchase from IPPs, power purchase from India has declined from 2021 onwards | 
NEA subsidiary companies
Project Developer / Company | Project | IC (MW) | NEA Stake
Chilime Hydropower Company Limited | Chilime | 22.1 | 51%
Upper Tamakoshi Hydropower Ltd. | Upper Tamakoshi | 456 | 41%
Sanjen Hydropower Co.Limited | Upper Sanjen | 14.8 | 10.4%
Madhya Bhotekoshi Jalavidyut Co. Ltd. |  |  | 10%
Rasuwagadhi Hydropower Co. Ltd |  |  | 18%
Total |  | 492.90 | 

## Slide 38: Nepal Became a Net Power Exporter for the First Time in FY 2023/24
Hydropower capacity additions and strategic trade with India enabled Nepal to reverse its historic import reliance and emerge as a net exporter
Source - NEA Annual Report;
Chart: 
 | 176.49 | 183.86 | 164.29 | 87.05 | 187.9 | 326.58 | 311.75 | 323.97 | 275.55 | 260.82 | 270.38 | 244.44
 | 514.98 | 495.07 | 523.1 | 446.09 | 341.94 | 273.01 | 227.5 | 234.67 | 292.46 | 421.16 | 480.81 | 520.06
 | -2.0059 | -3.541 | -5.5642 | -7.4702 | -0.29328 | -0.21456 | -0.18432 | -0.04032 | -2.989 | -2.0021 | -2.5483 | -15.6448
Jul-Aug (Shrawan)
Aug-Sep
Sep-Oct
Oct-Nov
0
Nov-Dec
0
Dec-Jan
0
Jan-Feb
0
Feb-Mar
-3
Mar-Apr
-2
Apr-May
-2
May-Jun
-16
Jun-Jul
689
675
682
526
530
599
539
559
565
680
749
749
-4
-7
-3
Monthly Energy Balance Curve (GWh)
Chart: 
 | 10 | 1 | 1 | 1186 | 27 | 163 | 324 | 395 | 349 | 357 | 188 | 19
 | 1467 | 1452 | 1456 | 0 | 949 | 727 | 657 | 592 | 642 | 836 | 1212 | 1612
 | -256 | -305 | -418 | -380 | -114 | 0 | 0 | 0 | 0 | 0 | -68 | -401
0
Oct-Nov
1
-114
Nov-Dec
163
0
Dec-Jan
0
Jan-Feb
0
Feb-Mar
0
Jul-Aug (Shrawan)
Mar-Apr
0
1
Apr-May
188
Aug-Sep
May-Jun
10
Jun-Jul
Sep-Oct
1,148
1,039
806
862
890
1,221
987
991
1,193
1,332
1,230
981
2023/24
2018/19
Monthly System Energy Demand (IPP+NEA+NEA Sub+Storage+Thermal+Interruption)
Import
Export
The sector has leveraged hydro capacity additions over the years to export surplus power to India. Nepal’s hydroelectric generating capacity has complemented India’s growing variable renewables. In 2023/24, by exporting 1,943 GWh power vis-à-vis 1,834 GWh imports, Nepal has become net exporter of power
Chart: 
 | 2813.08
 | 4770.85
 | -42.498
-42
Total Annual
7,541
Chart: 
 | 1834
 | 12788
 | -1942
Total Annual
12,680
-1,942

## Slide 39: Transmission Network Growth in Nepal
Transmission capacity at 220 kV and 400 kV levels is being scaled up to match generation growth and facilitate domestic and cross-border flow
Source – NEA Transmission Reports
Nepal currently operates transmission lines and substations in the voltage level of 66 kV, 132 kV. 220kV and 400 kV
Historically, transmission projects in Nepal are owned and implemented by NEA. RPGCL has been established to develop 220 kV and above transmission projects in the country
Over the years significant the transmission system in the country has witnessed significant growth in transmission lines and transformation capacity.
Initially transmission network comprised of network elements operating at 66kV and 132 kV level only
However, the focus of transmission network planners has shifted towards development of transmission network (ckM) and capacity addition (MVA) at 220 kV and 400 kV level.
Chart: Sub-Station Capacity Increment
| 2014-15 | 2015-16 | 2016-17 | 2017-18 | 2018-19 | 2019-20 | 2020-21 | 2021-22 | 2022-23 | 2023-24
Sub_Station Capacity (MVA) | 2132 | 2223 | 2618 | 3198 | 3935 | 4300 | 6434 | 7149 | 8867 | 13050
Chart: Transmission Line Length (Circuit kM)
| 2014-15 | 2015-16 | 2016-17 | 2017-18 | 2018-19 | 2019-20 | 2020-21 | 2021-22 | 2022-23 | 2023-24
66 kV | 0.18826 | 0.1697 | 0.15233 | 0.15189 | 0.12882 | 0.1204 | 0.10546 | 0.096435 | 0.089516 | 0.078992
132 kV | 0.81174 | 0.8303 | 0.80049 | 0.8029 | 0.78772 | 0.75896 | 0.72651 | 0.71614 | 0.69296 | 0.63562
220 kV | 0 | 0 | 0.023127 | 0.022163 | 0.06391 | 0.10237 | 0.15203 | 0.16829 | 0.19175 | 0.18641
400 kV | 0 | 0 | 0.024052 | 0.02305 | 0.019549 | 0.018271 | 0.016003 | 0.019137 | 0.025775 | 0.09897
Total | 2624 | 2911 | 3243 | 3384 | 3990 | 4269 | 4874 | 5330 | 5742 | 5971

## Slide 40: Decadal Shift: From Capacity Expansion to Green Growth and Market Efficiency
Nepal’s energy strategy is evolving from infrastructure-led development to a focus on domestic demand stimulation, and export readiness.
2000 - 2015
Infrastructure Development & Expansion Era
2015 – Present
Stabilization & Green Growth Era
KEY MARKET CHARACTERISTICS
KEY FOCUS AREAS
LOW ENERGY ACCESS
SUPPLY DEFICIT
POOR RELIABILITY OF SERVICES
IMPORT DEPENDENCE (FUEL & ELECTRICITY)
PRIORITY-BASED PROJECT DEVELOPMENT
IMPROVED ENERGY ACCESS
SURPLUS OF SEASONAL POWER
IMPROVED RELIABILITY OF SERVICES
DOMESTIC DEMAND STIMULATION
TARGETING AGREEMENTS WITH INDIA/BANGLADESH
ENERGY ACCESS AND GRID EXPANSION
CAPACITY ADDITION IN MW (HYDROPOWER)
WEAK POLICY LANDSCAPE
GRID EXPANSION & MODERNIZATION
FOCUS ON OTHER RENEWABLES
POLICY AND REGULATORY REFORMS
This decadal shift in energy landscape over the decades has resulted a positive surge in demand-supply dynamics in the country. The consumer mix witnessed increased industrial consumers. Similarly, inclusion of several hydro projects have enabled Nepal to meet its domestic demand and export surplus power in the wet season

## Slide 41
2.2 | CROSS-BORDER ELECTRICITY TRADE FROM NEPAL
Notes: .

## Slide 42: Evolution of Cross Border Electricity Trade (CBET) Landscape of Nepal with India (1/2)
Key Inferences | 
Till the late 2000s, cross border power trading for Nepal was mainly governed through bilateral treaties which led to support of India in development of specific river basin projects in Nepal. In 2014, India and Nepal signed a Power Trading Agreement ushering reforms such as non-discriminatory access to their transmission systems for power trading, encourage investment in power generation and transmission infrastructure, enable private sector participation along with G2G-level coordination and establish long-term cooperation for regional energy security. | 
CBET landscape has evolved significantly, driven by vast hydropower potential, regional energy demands, and strategic geopolitical positioning
1954
Koshi Treaty
bilateral agreement between India and Nepal for construction, operation, and maintenance of the Koshi Barrage
1958
The Gandak Irrigation and Power Project
joint India-Nepal initiative under the 1959 agreement for shared use of the Gandak River’s
Nepal - India Power Exchange Committee (PEC) constituted for consultation of power trade. This mechanism has been used mainly for imports
Mahakali Treaty
bilateral agreement between India and Nepal for the integrated development of the Mahakali River
Trisuli Hydro-electric Project
landmark India-Nepal collaboration initiated in 1958 for developing Nepal’s hydroelectric capacity with Indian technical and financial support.
Koshi Treaty
Originally signed in 1954, the Koshi Treaty was amended in 1966 to strengthen Nepal’s sovereignty, clarify water and irrigation rights, and address concerns over Indian control.
Power Tx via 132 KV
The 132 kV Kataiya–Kusaha and Ramnagar–Gandak lines are key cross-border transmission links enabling electricity trade between India and Nepal
Power Tx via 132 KV
The 132 kV Tanakpur–Mahendranagar line is a key cross-border transmission corridor facilitating electricity exchange between India and Nepal under the Mahakali Treaty.
1959
1966
1992
1995
1996
1999
2014
G to G Trade
power trading between Nepal and India for a period of 25 years. After 25 years, the contract will be automatically renewed every 10 year
Notes: Source :
1 https://moewri.gov.np/storage/listies/May2020/revised-agreement-on-nepal-and-india-koshi-river-1966.pdf 2 https://www.commonlii.org/in/other/treaties/INTSer/1958/14.html
3 https://moewri.gov.np/storage/listies/May2020/aggrement-on-nepal-and-india-gandak-river-1959.pdf
4 https://www.nvvn.co.in/assets/Directors_Report_NVVN_2023-24.pdf
5 https://moewri.gov.np/storage/listies/May2020/treaty-between-nepal-and-india-on-mahakali-rive-1996.pdf
6 https://www.nvvn.co.in/assets/Directors_Report_NVVN_2023-24.pdf
* https://www.idsa.in/publisher/comments/revisiting-the-kosi-agreement-lessons-for-indo-nepal-water-diplomacy
** Project On Integrated Power System Development Plan In Nepal Final Report

## Slide 43: Evolution of Cross Border Electricity Trade (CBET) Landscape of Nepal with India (2/2)
Key Inferences | 
The CBET mechanism has significantly evolved over the last decade with Nepal participating in Indian Power Exchange, selling power bilaterally to Indian discoms, exporting to Bangladesh via India The transmission capacity has also expanded to meet the rising CBET transactions | 
CBET landscape has evolved significantly, driven by vast hydropower potential, regional energy demands, and strategic geopolitical positioning
2016
Power Tx via 132KV NVVN – DM Line
The 132 kV Dhalkebar–Muzaffarpur line, operated by NVVN, was the first high-capacity cross-border transmission link enabling grid-to-grid power trade between India and Nepal.
2018
Power Tx via 400 KV NVVN – DM Line
Dhalkebar–Muzaffarpur line, upgraded to 400 kV, is the main India–Nepal transmission corridor enabling large-scale, grid-to-grid electricity trade through NVVN
2021
Power Exchange via IEX
Power exports through IEX has started in October 2021. The list of power plants for this trade will be renewed annually. RTM trading was opened from October 2023.
2023
Power trade Haryana
Discom
Mid-term RTC cross-border power export June to Oct months for 5 years from FY23-24 to FY 27-28 for onward supply to HPPC, Haryana.
2024
G to G trade between Nepal and India was which is a 25-year energy trade deal under which Nepal will export 10,000MW of electricity to India over the next 10 years.
2024
G to G Trade
Bangladesh via India
For five years starting in 2024, 40 MW will be exported to Bangladesh via India from 15th June to 15th November.
Notes: Source :
1 https://moewri.gov.np/storage/listies/May2020/revised-agreement-on-nepal-and-india-koshi-river-1966.pdf 2 https://www.commonlii.org/in/other/treaties/INTSer/1958/14.html
3 https://moewri.gov.np/storage/listies/May2020/aggrement-on-nepal-and-india-gandak-river-1959.pdf
4 https://www.nvvn.co.in/assets/Directors_Report_NVVN_2023-24.pdf
5 https://moewri.gov.np/storage/listies/May2020/treaty-between-nepal-and-india-on-mahakali-rive-1996.pdf
6 https://www.nvvn.co.in/assets/Directors_Report_NVVN_2023-24.pdf
* https://www.idsa.in/publisher/comments/revisiting-the-kosi-agreement-lessons-for-indo-nepal-water-diplomacy
** Project On Integrated Power System Development Plan In Nepal Final Report

## Slide 44: Involved Stakeholders for Cross Border Electricity Trade (CBET) in Nepal
Key stakeholders involved and their roles in the CBET
Licensing Requirements
Feasibility Study Environmental Clearance (EIA/IEE), Land acquisition, Grid connection plans and Financial Closure
Department of Electricity Development (DoED)
Grid Connection Application
Submit power flow studies, evacuation plan
NEA
(Grid Operation Department)
Approval of PPA
Submit final PPA for approval
Nepal Electricity Regulatory Commission (NERC)
Cabinet-Level Approval
NEA approaches GoN for final export approval.
Government of Nepal
PPA including export provision
PPA execution NEA acts as the off-taker and trading intermediary
NEA
Source - Electricity Act 2049 (1992), DoED – License related documents, Nepal Electricity Grid Code 2080, Hydropower Development Policy, 2058 (2001)
Oversees hydropower procurement, grants licenses, and ensures compliance.
Primary utility; manages procurement of power, generation, transmission, distribution, and export-import operations.
Primary utility; manages procurement of power, generation, transmission, distribution, and export-import operations.
Regulate the generation, transmission, distribution or the business of electricity.
Provides approval for the power export
Issues Survey and Generation License
NEA conducts System Impact Study and grants technical clearance for interconnection.
Approval of PPA
Final approval for power export
Final negotiation of PPA
Entity
Role
IPP requirements
Entity Action

## Slide 45: Cross Border Electricity Trade (CBET) Landscape of Nepal and India
Current practice of CBET between India and Nepal
Nodal Authority
Nepal Electricity Authority
Government Of Nepal
(MoEWRI)
Bilateral Framework through Power Exchange Committee (PEC) Mechanism
Tripartite Framework
NVVN (NTPC Vidyut Vyapar Nigam Ltd)
Export
Import
Import & Export
Import & Export
33 KV - 132 kV Transmission lines With Distribution Company {in Bihar, Uttar Pradesh, Uttarakhand state of India, Bihar State Power Transmission Company Ltd (BSPTCL), Uttar Pradesh Power Corporation Limited (UPPCL) & Uttarakhand Power Corporation Limited (UPCL)
G to G Trade Bangladesh via India- Export of 40 megawatts (MW) of electricity to Bangladesh via India. This arrangement is set to continue for a period of five years from 2024.
Import & Export
As a Settlement Nodal Agency
IEX
(Indian Exchange Market) – Day Ahead Market and Real Time Market
Exchange Market
Key Inferences | 
Nepal Electricity Authority (NEA) serves as the primary trader, sourcing electricity from its own plants and IPPs to export surplus power to India from selected approved projects India-Nepal CBET is moving from a bilateral model to a market-based model with strong momentum towards trilateral trade (Nepal–India–Bangladesh) | 
Source – JICA report

## Slide 46: Nepal became a net exporter of electricity in 2023-24
Nepal's electricity exports have witnessed a remarkable surge over the past five years; became net exporter last year
Source : NEA Annual Report 2023/24, NEA Annual Report 2021/22, NEA Annual Report 2019/20
Chart: Electricity Import v/s Export between Nepal and India (GWh)
| 2019/20 | 2020/21 | 2021/22 | 2022/23 | 2023/24
Energy Import from India (GWh) | 1729 | 2806 | 1543 | 1833 | 1895
Energy Export to India (GWh) | 107 | 44 | 493 | 1346 | 1946
Key Inferences | 
Cross Border Power Export from Nepal to India has become more than 10 times in the last 5 years from FY 2019-20 to FY 2023-24. Some of the key factors which driven the increase in power export includes: Surplus Generation - Increase in generation capacity in Nepal with peak generation exceeding domestic demand during monsoon months. Power Markets Access - Since November 2021, NEA and select Nepalese IPPs (through NEA) have gained access to the Indian Day-Ahead Market (DAM) and Real-Time Market (RTM) on IEX. Transmission Links - Nepal and India currently have over 11 cross-border transmission links (33 kV, 132 kV, and 400 kV), enabling both grid support and commercial trade. In FY 2023-24, Nepal has become Net Exporter of Power | 

## Slide 47: Monthly Electricity Export and Import between Nepal and India (GWh)
During the last 3 years wet season exports have surged, whereas the dry season imports have remained at similar levels
Source: Annual Report 23/24
Key Inferences | 
Power export has been increased from 494 GWh in FY 2021-22 to 1943 GWh in FY 2023-24 at a CAGR of 58% whereas there has been a very steady increase rate in the Power import from 1543 GWh in FY 2021-22 to 1834 GWh in FY 2023-24 to the tune of CAGR of 5.9% during FY 2021-22 to FY 2023-24 Exports to India in recent years has increased from the months of Mid-July to and mid-December and reaching peak around mid-September. Then after the dry season (mid – December to mid April) in which minimal export (NIL); the power export gradually increase and reaches to peak levels. | 
Chart: Monthly Electricity Export to India (in GWh) – Nepal (FY 2021/22 to FY 2023/24)
| July/Aug | Aug/Sep | Sep/Oct | Oct/Nov | Nov/Dec | Dec/Jan | Jan/Feb | Feb/Mar | Mar/Apr | Apr/May | May/June | June/July
2021/22 | 3 | 38 | 81 | 33 | 28 | 0 | 0 | 0 | 0 | 0 | 70 | 240
2022/23 | 252 | 256 | 281 | 202 | 88 | 0 | 0 | 0 | 0 | 0 | 24 | 230
2023/24 | 256 | 305 | 418 | 380 | 114 | 0 | 0 | 0 | 0 | 0 | 68 | 401
Chart: Monthly Electricity Import from India (in GWh) – Nepal (FY 2021/22 to FY 2023/24)
| July/Aug | Aug/Sep | Sep/Oct | Oct/Nov | Nov/Dec | Dec/Jan | Jan/Feb | Feb/Mar | Mar/Apr | Apr/May | May/June | June/July
2021/22 | 92 | 14 | 5 | 0 | 21 | 183 | 281 | 327 | 251 | 230 | 87 | 51
2022/23 | 25 | 21 | 6 | 1 | 19 | 203 | 311 | 318 | 336 | 396 | 184 | 35
2023/24 | 10 | 1 | 1 | 0 | 26 | 163 | 324 | 395 | 349 | 357 | 188 | 19

## Slide 48: Trading for hydropower projects from Nepal to India
Significant quantum of IPP power is traded with India; it is managed by NEA
Source: NVVN Directors Report 2023-24, CEA Report
Chart: Mode of Trading
| Power exchange | Bilateral Mode
 | 711.4 | 184.61
 | No. of projects | Quantum (MW)
NEA | 5 | 194.27
IPPs | 15 | 701.74
Total | 20 | 896.01
Chart: Bilateral with Haryana (MW)
| Applied for 2023-27 | Applied for 2024-27
Proposed (MW) | 89.87 | 200
Approved (MW) | 75 | 109.61
Above table shows the number of projects and Total Quantum involved in the CBET between Nepal and India based on the approval of India
As compared to number of projects from NEA, there are more number of IPPs involved in power export from Nepal to India. All the transactions are handled by NEA.
Majority of the power export (79%) has been done through the DAM and RTM Market of the power exchange.
Bilateral transactions to Haryana has been done via NTPC Vidyut Vyapar Nigam Limited (NVVN) as the trader and settlement and nodal agency.
Significant increase in export capacity proposals, but approval rates remain moderate relative to proposals
Projects which are considered are having approval validity till 31st October 2027
Ownership Restrictions
Government Approval
Detailed project documentation
Documentation & clearances
Intimation of change in equity
Key Enablers/ Restrictions for participating in the cross-border transactions with India

## Slide 49: Transmission Lines involved in CBET
Overview of the key transmission lines involved CBET between Nepal and India
Sl. No. | Project Name | Voltage (kV) | Quantum (MW)
1 | Dhalkebar - Muzaffarpur | 400 | 1000
2 | Kusaha –Kataiya (I & II) | 132 | 280
3 | Parwanipur – Raxaul (I & II) | 132 | 160
4 | Mainahiya - Sampatiya (Nautanwa) (I & II) | 132 | 160
5 | Tanakpur - Mahendranagar | 132 | 75
6 | Gandak – Ramnagar and Muzaffarpur | 132 | 60
7 | Jaleshwar – Sursand | 33 | 12
8 | Birgunj – Raxaul | 33 | 12
9 | Nepalgunj – Nanpara | 33 | 12
10 | Rajbiraj – Kataiya | 33 | 8
11 | Siraha – Jaynagar | 33 | 7
Existing Cross Border Transmission Lines
Updates related to Existing Cross Border Transmission Lines
Source: South Asia Regional Energy Partnership (SAREP), South Asia Subregional Economic Cooperation (SASEC), Press Information Bureau (PIB), Kathmandu Post, Engineering Sarokar, The Annapurna Express, NLDC Data
Key Inferences | 
The Dhalkebar–Muzaffarpur transmission line has played a transformational role in enabling and expanding cross-border electricity trade (CBET) between Nepal and India. It enabled Nepal Electricity Authority (NEA) to begin commercial exports to India via the Indian Energy Exchange (IEX) starting in June 2021. The project is strategically located between the two main demand centres in Nepal – Kathmandu and Pokhara | 
As per the latest data (June 2024 to November 2024), there is 75%-85% utilization on the 400 kV Dhalkebar – Muzaffarpur transmission line and 85% - 95% utilization on 132 kV Tanakpur – Mahendranagar transmission line
PJ_ST Project

## Slide 50
CHAPTER 3 | OUTLOOK

## Slide 51
3.1 | DEMAND-SUPPLY OUTLOOK

## Slide 52: Nepal Power Sector Future Outlook | Demand Projections
High electricity demand growth anticipated, driven by low base, clean energy transition, and rapid economic development
Chart: 
 | 12999 | 20074 | 29745 | 43017
 | 14864 | 24957 | 40710 | 66097
 | 16546 | 29865 | 52983 | 94851
 | 22432 | 35335 | 51772 | 81959
 | 24265 | 41265 | 65657 | 115294
 | 12191 | 17682
 | 13632 | 22189
 | 16690 | 30879 | 47294 | 133185
12,191
2025
2030
2035
43,017
133,185
2040
12,999
16,690
20,074
30,879
29,745
WECS ED (2015-40) BAU (4.5% GDP)
WECS ED (2015-40) Ref (7.2% GDP)
WECS ED (2015-40) High (9.2% GDP)
WECS ED (2015-40) Ref + Policy
WECS ED (2015-40) High + Policy
NEA Load Forecast (Base)
NEA Load Forecast (Optimistic)
JICA Master Plan (Optimum)
Source - NEA Annual Report; IBN Energy Demand – MAED; Electricity Demand Forecast (2015-40) WECS; NEA Load Forecast
Key Inferences | 
Several factors are driving the rising electricity demand in Nepal, as reflected in the projections above. One of the key drivers is the low base effect—Nepal’s current per capita electricity consumption stands at approximately 320 kWh/year, while the government aims to increase this to 1,500 kWh by 2035. In addition, various government initiatives are stimulating domestic demand, further contributing to growth. The ongoing energy transition, including the broader adoption of electric stoves, electric vehicles, and other clean technologies, is also expected to significantly boost electricity consumption in the coming years | 
Demand Projections from various sources (GWh)
 | Electric Power Consumption (kWh per capita) | Annual Growth of RE Capacity - 2013 – 2023 (%)
Bangladesh | 603 | 9.4%
Bhutan | 3,160 | 4.6%
India | 1,075 | 10.7%
Maldives | 1,490 | 33.5%
Myanmar | 319 | 1.4%
Nepal | 321 | 14.2%
Sri Lanka | 636 | 6.1%
South Asia | 984.31 | 10.3%

## Slide 53: Drivers of Demand Growth I Domestic and Export Aspirations
Sectoral electrification and export ambitions to India and Bangladesh anchor Nepal’s long-term demand surge
Source - NEA Annual Report; IBN Energy Demand – MAED; Electricity Demand Forecast (2015-40) WECS; NEA Load Forecast
Key Aspirations across various sectors - domestic
Residential
E-cooking in 25% Households by 2030
LPG use capping to 40% by promoting e-cooking
Industrial
95% emission reduction by 2050
Use of green fuels in Thermal Processes
Transport
Electrification of 90% Private vehicles by 2030
Development of 200-kilometer electric rail network by 2030
Agri & Waste
Electrification in farm machinery and promotion of solar PV pumping
Maintaining 45% forest cover across Nepal by 2030
Key Aspirations across various sectors - exports
10 GW MW
5 GW MW
15 GW
Exports to India
Exports to Bangladesh
Total Exports by 2035

## Slide 54: Installed Capacity Outlook | Scaling to Meet Demand and Enable Exports
Planned capacity additions are aligned with national demand growth and regional power trade commitments
Chart: 
 | 5787 | 8937 | 13242 | 19151
 | 6617 | 11111 | 18124 | 29247
 | 7366 | 13296 | 23588 | 42228
 | 9987 | 15731 | 23049 | 36489
 | 10803 | 18371 | 29231 | 51330
 | 6289 | 14546 | 28215 | 36327
5,787
10,803
2025
2030
2035
19,151
51,330
2040
WECS ED (2015-40) BAU (4.5% GDP)
WECS ED (2015-40) Ref (7.2% GDP)
WECS ED (2015-40) High (9.2% GDP)
WECS ED (2015-40) Ref + Policy
WECS ED (2015-40) High + Policy
JICA Master Plan (Optimum)
Source - NEA Annual Report; IBN Energy Demand – MAED; Electricity Demand Forecast (2015-40) WECS; NEA Load Forecast
Key Inferences | 
The future outlook indicates a continued upward trend in electricity supply, reflecting Nepal’s growing capacity and commitment to meeting both domestic and regional energy demands. As outlined in the Energy Development Roadmap, Nepal aims to reach an installed capacity of 13,000 MW by 2030, with plans to export 10,000 MW to India and 5,000 MW to Bangladesh. This reflects a strong commitment to regional energy cooperation through power exports. The projected capacity additions are expected to not only meet domestic demand but also position Nepal as a leading player in the cross-border electricity trade market. | 
Installed Capacity targets of various projections (MW)
Energy Development Roadmap targets 28,500 MW IC by 2035 – Feb 2025

## Slide 55: Installed Capacity Pipeline I Insights from JICA's Optimum Generation Scenario
Visibility of ~10 GW capacity under various stages of development; will position Nepal as a surplus generator
Chart: 
 | 21 | 21 | 21 | 21
 | 827.2 | 6 | 6 | 6
 | 14 | 2182.7 | 3082.7 | 4107.7
 | 1760 | 781.4 | 5691.8 | 9429.9
 | 3667.2 | 3711.6 | 8302.8 | 10930
 | 7843.7 | 11110.8 | 11832.4
 | 0 | 1 | 2 | 3
2025
6
2030
6
2035
6
21
2040
6,289
14,546
28,215
36,327
3,712
781
21
21
Peak Demand
ROR
PROR
STO
Solar
Wind
Biomass
Installed Capacity (MW) Projections till 2040
Source - JICA Integrated Power System Development Plan 2024; STO – Storage; NEA Annual Report; Deloitte Insights
Key Inferences | 
As of FY 2024, NEA had tied-up generation capacity totaling 10,961 MW. This figure is expected to have increased in FY 2025, with updated data to be released in NEA’s forthcoming annual report. Based on market insights and stakeholder discussions, NEA is anticipated to sign additional PPAs amounting to approximately 5,000 MW over the next 2–3 years. Cumulatively, this positions Nepal as an emerging surplus power nation, with a growing strategic emphasis on export-led monetization. | 
Projects under Pipeline
3,905 MW
3,157 MW
3,899 MW
10,961 MW
FY 24 Installed Capacity
Under Construction
PPA Signed – Awaiting Financial Closure
Total PPA tied capacity

## Slide 56: Forecasted Seasonal Demand-Supply Dynamics I Monthly Generation and Load Profile
Nepal is expected to maintain seasonal and annual electricity surpluses, as early as 2030 due to improved dry season supply
Key Inferences from JICA Study | 
Monthly variations across different years indicate a rise in the installed capacity of hydropower plants, leading to an overall increase in electricity supply. Monthly load curve clearly illustrates a reduction in power import requirements during the dry season, reflecting improved supply capacity from FY 2025 to FY 2040. From 2030 onwards, operations during February—when power generation is at its lowest, shall be optimized to manage peak demand periods more efficiently. | 

## Slide 57: Scaling Transmission Infrastructure to Match Supply and Demand Growth
Nepal is reinforcing its grid through 220 kV and 400 kV systems to integrate generation additions and support both domestic and regional flows.
Source – Grid Operations Department, Deloitte Analysis
A total of 46 sub-stations with total transformation capacity of 7501 MVA are under various stages of construction. These will be supported by 2281 Ckm (including 132 kV, 220 kV and 400 kV) of Transmission lines which are also under various stages of construction
A total of 38 sub-stations with total transformation capacity of 15750 MVA have been planned.
To meet the energy demand of Kathmandu, a Kathmandu Valley Transmission System Expansion project has been planned with construction of 31 sub-stations (4129 MVA) and ~ 160 Km of Transmission line
Kathmandu Valley Reinforcement
Major Planned Projects
Arun-InaruwaTingla-Mirchaiya 400 kV
Dudhkoshi-Dhalkebar 400 kV Project
New Butwal-Lamhi 400 kV Project
Marsyangdi Corridor 220 kV Project
Parameter | Voltage | Planned
Line (Ckt KM) | 66kV | -
 | 132kV | 936
 | 220 kV | 1780
 | 400 kV | 3634
Sub-station (MVA) | 33kV | 176.5
 | 132kV | 2935
 | 220 kV | 1840
 | 400 kV | 6670
 | Aggregate* | 4129
Chart: 
 | 54.7128 | 25.559 | 19.7282
1,248 (55%)
583 (26%)
450 (20%)
Under Construction Transmission Network (Ckm)
Chart: 
 | 4.979 | 45.5109 | 32.6468 | 16.8633
374 (5%)
3,414 (46%)
2,449 (33%)
1,265 (17%)
Under Construction Transformer Capacity (MVA)
33kV
132kV
220 kV
400 kV

## Slide 58: Transmission Readiness for PJ ST – Evacuation via New-Marsyangdi Substation
New-Marsyangdi substation, energized in Jan-2025, is the designated evacuation point for PJ_ST Project, with transmission work on track
Particulars | Details
Capacity (Unit Configuration) | 100 MW
Location | 100km west of Kathmandu on Prithvi highway Gorkha-Zone, Chitwan District
Transmission Evacuation details | About 18.8 km long 220kV double circuit transmission line to New Markichauk substation
Photo Credit – Blue Energy
Photo Credit – ESRI
The project is located in between the Demand Centres of Kathmandu (100 km) and Pokhara (109 km).
This river basin is one of the most developed basins in Nepal.
The project's strategic location helps reduce the congestion in the transmission network, facilitates its optimal year-round utilization, and contributes to more efficient load management, thereby enhancing overall grid stability and reliability.
Strategic Location of the project
As per the DPR, 220/132 kV New-Marsyangdi (Marki Chowk) substation has been most optimised transmission network for evacuation of 100 MW power from PJ_ST Project .
220/132 kV New-Marsyangdi (Marki Chowk) substation, located in Tanahun, Nepal, was officially energized on January 2, 2025.
Based on the discussion with NEA and Breeze, the transmission infrastructure development for this project is on track.
Current Status of the transmission evacuation
infrastructure of the project

## Slide 59: Upcoming Cross Border Transmission Lines I Enabling export targets
Ongoing and planned transmission corridors with India is in line with the export targets of Nepal
Upcoming Cross Border Transmission Lines & their present status
Sl. No. | Project Name | Voltage (kV) | Quantum (MW) | Proposed COD | Current Status of the project
1 | Inaruwa – New Purnea | 400 | 2500 (Planned) | 2027-28 | MoU signed between GON and GOI for the development of transmission line on April,2025
2 | Dododhara – Bareilly | 400 | 2500 (Planned) | 2028-29 | MoU signed between GON and GOI for the development of transmission line on April,2025
3 | New Butwal – Gorakhpur (MCC Nepal) | 400 | 2500 (Planned) | 2026-27 | Though there has been some delay in the development in Nepal side, the work is expected to resume soon
4 | Dhalkebar – Sitamarhi (Arun 3) | 400 | 2500 (Planned) |  | Transmission project is under construction and project is dedicated to evacuating power generated by the Arun-3 hydropower project
5 | Nijgadh (Bara)-Motihari (Bihar) | 400 | NA | 2028-29 | Study of cross-border transmission line has been completed
6 | Kohalpur-Lucknow | 400 | NA | 2028-29 | Study of cross-border transmission line has been completed
7 | Chameliya-Jaulajiwi | 220 | NA | NA | Feasibility Study under progress
8 | Nepalgunj – Nanpara | 132 | 200 | 2025-26 | Project is under-construction with primary focus of importing power from India to Nepalganj
Source: South Asia Regional Energy Partnership (SAREP), South Asia Subregional Economic Cooperation (SASEC), Press Information Bureau (PIB), Kathmandu Post, Engineering Sarokar, The Annapurna Express

## Slide 60
3.2 | POLICY & REGULATORY OUTLOOK

## Slide 61: Policy & Regulatory Outlook
The Draft Electricity Bill 2080 ERC Roadmap (2024–2029) signal Nepal’s intent to strengthen regulatory frameworks and foster greater competition in the electricity market.
Source: Draft Five-year Roadmap for ERC (2024-2029), Association of Power Producers Comments Draft Electricity Amendment Bill, 2080
Nepal’s policy and regulatory regime is evolving to support a more efficient and investment-ready power market. Several ongoing reforms and initiatives are aimed at improving market efficiency, strengthening regulatory oversight, and creating a more conducive environment for private sector participation across the electricity value chain.
Draft Electricity Amendment Bill, 2080
Structural Reforms
Provision of Payment Security Mechanism
Electricity Trading
Open Access
Extensions for Export-Oriented Projects
Draft ERC Roadmap (2024-2029)
Directives of Open Access to Transmission Network
Directives to determine Transmission and Distribution Wheeling Charges
Directives of Cross-Border Electricity Trade
Studies on Wholesale and Retail Market Studies
Measuring Key Performance Indicators (KPI) of generation licensees.

## Slide 62: Policy Outlook I Draft Electricity Amendment Bill, 2080 and Its Implications for PJ_ST Project
The draft bill introduces key reforms that enhance IPP viability and create enabling conditions for merchant capacity projects like PJ_ST Project
Source: Association of Power Producers Comments Draft Electricity Amendment Bill, 2080
Provision of Payment Security Mechanism
Inclusion of the provision of Payment Security Mechanism in the PPA
This may be applicable for future projects
Initiatives
Description on the Initiative
Possible impact on this Project
Electricity Trading
Bill proposes electricity trading licenses for private entities, enabling domestic and international electricity trade
Opens up opportunities for IPPs to sell surplus electricity, especially during the monsoon season when Nepal often has excess generation capacity.
Structural Reforms
Breaking the monopoly of the Nepal Electricity Authority (NEA) by separating electricity generation, transmission, and distribution into distinct entities
Structural reforms point towards wider benefits for private sector
Open Access
Provisions for open access, allowing licensed entities to use transmission and distribution infrastructure without discrimination
Option of selling power directly to large consumers or other licensees
Extensions for Export-Oriented Projects
Export-oriented hydropower projects may be granted longer permit durations (up to 40 years),
Improving investment security for IPPs targeting export markets.

## Slide 63: Strengthening Market Structures I Key Provisions from the Draft ERC Roadmap (2024–2029)
Focus areas include open access, pricing, cross-border trade, market design, and performance benchmarking to advance sectoral reform
Source: Draft Five-year Roadmap for ERC (2024-2029), Deloitte Research
Directives of Open Access to Transmission Network
Open Access Directives to allow multiple buyers and sellers to use the transmission network.
Option of selling power directly to large consumers or other licensees, bypassing NEA (Nepal Electricity Authority).
Initiatives
Description on the Initiative
Relevance for the project
Directives of Cross-Border Electricity Trade
Will facilitate direct international sales by licensees.
Aims to unlock export potential and reduce dependency on domestic off-takers.
Direct access to regional markets, improving revenue certainty and project bankability.
Directives to determine Transmission and Distribution Wheeling Charges
To determine wheeling charges for using the grid.
This is essential for enabling open access and fair competition.
More clarity on costs for using the grid, aiding financial planning and tariff setting
Studies on Wholesale and Retail Market Studies
Conducting studies on Wholesale competitive markets (e.g., power exchanges, OTC platforms)
Retail competition, allowing consumers to choose suppliers
In the long term, option of participating in power exchanges or sell directly to consumers, increasing flexibility and market access
Measuring Key Performance Indicators (KPI) of generation licensees
KPIs for measuring the performance of generation licensees and for implementing mechanisms that ties the achievement of these targets to certain discounts and prioritizations.
Improving the Operational Performance parameters, performance & incentives and improved financial planning
Current Status
Draft Directives issued for stakeholder comments
Under preparation
Under preparation
Planning phase
Planning phase

## Slide 64
CHAPTER 4 | INDIA POWER MARKET ASSESSMENT

## Slide 65
4.1 | ELECTRICITY TRADING MARKET AND THE UNDERLYING REGULATORY AND POLICY LANDSCAPE

## Slide 66: Electricity sector in India | Overview of capacity additions and generation mix trends
89 GW of non-fossil power generation capacity was added in the last five years vis-a-vis 16 GW of coal-based capacity
Sources: Central Electricity Authority (India), Ministry of Power (India), Deloitte Analysis
Electricity generation installed capacity (India)
FY20-25, GW
Chart: 
| FY20 | FY21 | FY22 | FY23 | FY24 | FY25
Coal/lignite | 205 | 209 | 211 | 212 | 218 | 222
Natural gas | 25 | 25 | 25 | 25 | 25 | 25
Nuclear | 7 | 7 | 7 | 7 | 8 | 8
Hydro | 46 | 46 | 47 | 47 | 47 | 48
RES | 87 | 94 | 110 | 125 | 144 | 172
Column1 | 370 | 381 | 400 | 416 | 442 | 475
Source | FY20 | FY25 | Net change
Coal/ lignite | 994 | 1,332 | 338
Natural gas | 49 | 32 | (17)
Nuclear | 46 | 57 | 11
Hydro | 156 | 149 | (7)
Renewables | 138 | 255 | 117
Import | 6 | 5 | (1)
Total | 1,391 | 1,830 | 441
Chart: 
| Coal/lignite | Natural gas | Nuclear | Hydro | RES
FY20 | 0.5517 | 0.2175 | 0.7803 | 0.383 | 0.17846
FY25 | 0.6855 | 0.145 | 0.7907 | 0.3552 | 0.16663
Source-wise electricity supply change
FY20-25, BU
India has a lower share of natural gas (5%) and nuclear (2%) based power capacity hence, majority of the electricity requirement is met through coal. Coal-based plants supplied ~77% i.e., ~338 BU of incremental electricity requirement from FY20 to FY25
Gas-based plants are used sparingly due to the high cost of generation on account of high-cost imported Liquified Natural Gas and the low availability of cheaper domestic gas leading to a decline in utilization of gas-based power plants in the last 5 years.
Share of renewables (excluding large hydro) in total electricity generation installed capacity increased from 24% in FY20 to 36% at the end of FY24 mainly driven by 70 GW of solar and 12 GW of wind utility scale capacities added over the same period
In addition to above, ~7-10 GW of solar and wind capacities are estimated to have been installed by large Commercial & Industrial (C&I) consumers for captive or self-use
Government of India has target to have a capacity of 430 GW of solar and wind generation by 2030; this will require ~55 GW of installation each year for next 5 years
Key observations
Capacity utilization of plants
FY20-25, %
Utilization of coal plants increased to 69% in FY25 from 55% in FY20, with improvements in domestic coal supply
RES: Renewable Energy Sources (includes small hydro power plants of capacity less than 25 kW

## Slide 67: Electricity sector in India | Electricity supply position and seasonal variations
Firm electricity supply varies across seasons, with the deficit peaking in summers and winters
Anticipated seasonal electricity supply position in Indian regions (Mn kWh | FY26 )
The variation in supply is based on weather conditions, variability of RE generation, and varied regional demands in agriculture, industry, and residential categories
Sources: Central Electricity Authority (India), Ministry of Power (India), Deloitte Analysis
Chart: 
| April | May | June | July | August | September | October | November | December | January | February | March
Northern Region | 3521 | -2882 | -3183 | -3520 | 1008 | -709 | 1022 | 953 | 624 | -1657 | 676 | 396
Western Region | -922 | -1110 | -1124 | 911 | 2334 | 1859 | -972 | -113 | -1866 | -1910 | -3394 | -1909
Southern Region | -3238 | 2063 | 3473 | 4556 | 840 | 1342 | -128 | 511 | 96 | -942 | -2664 | -4256
Eastern Region | -1158 | -324 | -586 | -96 | 1299 | 1383 | 2522 | 4277 | 4530 | 4746 | 3924 | 3389
North-Eastern | 13 | 26 | 347 | 438 | 404 | 298 | 332 | 180 | 112 | -49 | -13 | 114
Summer
Monsoon
Autumn
Winter
Summer
Demand-supply situation:
Agricultural demand continues to remain high
Improvement in coal plant generation vis-à-vis previous season
Demand-supply situation:
Increase in cooling / air-conditioning demand
Increase in agricultural (irrigation) demand in pre-monsoon period
Low wind and hydro-generation
Demand-supply situation:
Increase in agricultural demand
Low solar generation, high hydro generation period
Decrease in coal plant generation due to supply chain issues
Demand supply situation
Increase in tourism related demand
Decrease in hydro and wind generation
Deficit is gap between electricity demand (MU) and electricity supply (MU) (ex-bus)
Legend:
April | May | June | July | August | September | October | November | December | January | February | March
Over the last five years, in the planning India was anticipated to have demand deficit in the norther region
This deficit varies significantly across seasons, with the deficit in summers (Apr - Jul) reaching 3-4 BU and ~2-4 BU in winters (Dec - Mar)
Seasonality of RE further intensifies supply-demand imbalance; solar power peaks in April-June while wind has peak output in August-September
Sources: CEA, MoP, Deloitte Analysis

## Slide 68: Electricity sector in India | Electricity supply position and seasonal variations
 | Apr-23 | May-23 | Jun-23 | Jul-23 | Aug-23 | Sep-23 | Oct-23 | Nov-23 | Dec-23 | Jan-24 | Feb-24 | Mar-24 | FY24
Northern region |  |  |  |  |  |  |  |  |  |  |  |  | 
Antic. surplus/(deficit) | 1,536 | (352) | (2,498) | (2,060) | (3,130) | (2,970) | 720 | (109) | (71) | (1,081) | 1,779 | (400) | (8,637)
In % of anticipated req. | 4% | 1% | 5% | 4% | 6% | 7% | 2% | 0% | 0% | 3% | 6% | 1% | 2%
Actual surplus/(deficit) | (135) | (135) | (65) | (87) | (440) | (243) | (146) | (61) | (24) | (400) | (130) | (186) | (2,049)
in % of actual req. | 0.40% | 0.34% | 0.15% | 0.19% | 0.85% | 0.52% | 0.37% | 0.19% | 0.07% | 1.01% | 0.39% | 0.48% | 0.43%
Western region |  |  |  |  |  |  |  |  |  |  |  |  | 
Antic. surplus/(deficit) | 1,248 | 1,351 | 2,976 | 4,296 | 3,725 | 3,492 | 7,731 | 3,894 | (1,442) | (58) | 1,790 | 5,110 | 34,113
In % of anticipated req. | 3% | 3% | 7% | 12% | 10% | 9% | 21% | 10% | 3% | 0% | 4% | 12% | 7%
Actual surplus/(deficit) | (31) | (14) | (25) | (10) | (128) | (92) | (15) | - | (1) | (48) | (48) | (42) | (453)
in % of actual req. | 0.07% | 0.03% | 0.06% | 0.02% | 0.30% | 0.22% | 0.03% | - | 0.00% | 0.11% | 0.11% | 0.10% | 0.09%
Southern region |  |  |  |  |  |  |  |  |  |  |  |  | 
Antic. surplus/(deficit) | (1,414) | 3,901 | 1,027 | 3,300 | 4,386 | 5,391 | 5,607 | 2,682 | 3,518 | 1,515 | 189 | (3,116) | 26,986
In % of anticipated req. | 4% | 12% | 3% | 11% | 14% | 18% | 19% | 9% | 11% | 4% | 1% | 7% | 7%
Actual surplus/(deficit) | (9) | (17) | - | - | (113) | (7) | (80) | (1) | (6) | (3) | - | (24) | (259)
in % of actual req. | 0.02% | 0.05% | - | - | 0.31% | 0.02% | 0.22% | 0.00% | 0.02% | 0.01% | - | 0.06% | 0.06%
Eastern region |  |  |  |  |  |  |  |  |  |  |  |  | 
Antic. surplus/(deficit) | 296 | 222 | 8 | (1,008) | (1,209) | (1,015) | 374 | 838 | 1,472 | 1,570 | 1,672 | 401 | 3,620
In % of anticipated req. | 2% | 1% | 0% | 6% | 7% | 6% | 2% | 6% | 11% | 11% | 13% | 2% | 2%
Actual surplus/(deficit) | (115) | (136) | (118) | (79) | (124) | (144) | (142) | (51) | (97) | (158) | (52) | (121) | (1,338)
in % of actual req. | 0.71% | 0.79% | 0.66% | 0.42% | 0.68% | 0.80% | 0.86% | 0.38% | 0.74% | 1.13% | 0.40% | 0.75% | 0.70%
Northeastern region |  |  |  |  |  |  |  |  |  |  |  |  | 
Antic. surplus/(deficit) | 170 | 90 | 279 | 38 | (7) | (24) | 158 | 92 | 19 | (152) | 53 | (1) | 715
In % of anticipated req. | 12% | 5% | 16% | 2% | 0% | 1% | 9% | 6% | 1% | 9% | 4% | 0% | 3%
Actual surplus/(deficit) | (42) | (42) | (37) | (24) | (47) | (42) | (9) | (1) | (4) | (26) | (17) | (29) | (318)
in % of actual req. | 2.77% | 2.52% | 2.13% | 1.22% | 2.35% | 2.09% | 0.51% | 0.07% | 0.27% | 1.71% | 1.19% | 1.83% | 1.58%
India |  |  |  |  |  |  |  |  |  |  |  |  | 
Antic. surplus/(deficit) | 1,835 | 5,211 | 1,793 | 4,565 | 3,765 | 4,873 | 14,590 | 7,395 | 3,494 | 1,794 | 5,484 | 1,996 | 56,797
In % of anticipated req. | 1% | 4% | 1% | 3% | 3% | 4% | 12% | 6% | 3% | 1% | 4% | 1% | 4%
Actual surplus/(deficit) | (332) | (344) | (245) | (200) | (852) | (528) | (392) | (114) | (132) | (635) | (247) | (402) | (4,417)
in % of actual req. | 0.25% | 0.25% | 0.17% | 0.14% | 0.56% | 0.37% | 0.28% | 0.10% | 0.11% | 0.47% | 0.19% | 0.28% | 0.27%
CEA anticipated average deficit of 5-6% in high-demand months of June-Sep and Mar-Apr in FY24
Sources: Central Electricity Authority (India), Ministry of Power (India), Deloitte Analysis
Anticipated vs actual seasonal electricity supply surplus/ (deficit) as % of energy requirement in Indian regions
FY24, MU
Key observations
As per CEA, the average deficit was anticipated to be between 5-6% of the requirement specifically in the high-demand months in Northern, Southern and Eastern regions. To meet the demand, the Government of India laid some directives such as:
Planned maintenance to be conducted before high demand period
Maximization of coal production for domestic coal-based plants
Imported coal-based plants to keep ready stock
Additional arrangements for gas required by gas-based plants
These steps resulted in an average deficit of less than 0.5% in the high-demand months.
Relative to FY23, the energy requirement grew by 7.5% in FY24 and the energy availability grew by 7.8%, resulting in a reduction in total energy shortfall from 0.5% in FY23 to 0.2% in FY24.
Government of India took necessary steps resulting in an average deficit of less than 0.5% in the high-demand months

## Slide 69: Electricity sector in India | Electricity supply position and seasonal variations
CEA anticipated average deficit of 2-3% in high-demand months of June-Sep and Mar-Apr in FY25
Sources: Central Electricity Authority (India), Ministry of Power (India), Deloitte Analysis
Anticipated vs actual seasonal electricity supply surplus/ (deficit) as % of energy requirement in Indian regions
FY25, MU
Key observations
There was an anticipation of shift in the high-demand months and regions. Which is observed in the western region in the second half of the FY and the eastern region in the first half of the FY
Government of India laid some directives such as:
Gas-based plants to be operationalized
Planned maintenance to be shifted to monsoon season
Plant outages to be brought down
Minimum technical load (55%) for coal-based plants (to be used at discretion)
Shifting of hydro generation to peak hours
Surplus power with captive generators to be harnessed
Imported coal-based plants to keep full capacity available for generation
These steps have resulted in an average deficit of less than 0.1% in FY25
Shifting demand scenario was neutralized by Government efforts such as operationalization of gas-based plants, shifting of plant maintenance, imported-coal based plants on standby etc. bringing the monthly and overall average deficit near to 0.1%
 | Apr-24 | May-24 | Jun-24 | Jul-24 | Aug-24 | Sep-24 | Oct-24 | Nov-24 | Dec-24 | Jan-25 | Feb-25 | Mar-25 | FY25
Northern region |  |  |  |  |  |  |  |  |  |  |  |  | 
Antic. surplus/(deficit) | 7,416 | 3,487 | 1,031 | 1,271 | 3,318 | 2,011 | 2,371 | 5,054 | 4,529 | 2,268 | 3,209 | 3,840 | 39,805
In % of anticipated req. | 19% | 8% | 2% | 3% | 6% | 4% | 6% | 15% | 12% | 6% | 9% | 10% | 8%
Actual surplus/(deficit) | (25) | (117) | (213) | (268) | (82) | (38) | (19) | (10) | (160) | (9) | (4) | (9) | (954)
in % of actual req. | 0.07% | 0.23% | 0.39% | 0.49% | 0.17% | 0.08% | 0.04% | 0.03% | 0.44% | 0.02% | 0.01% | 0.02% | 0.18%
Western region |  |  |  |  |  |  |  |  |  |  |  |  | 
Antic. surplus/(deficit) | (2,952) | (1,122) | 2,330 | 780 | (326) | 1,111 | 130 | (465) | (2,235) | (3,651) | (2,889) | (789) | (10,079)
In % of anticipated req. | 6% | 2% | 5% | 2% | 1% | 3% | 0% | 1% | 5% | 8% | 6% | 2% | 2%
Actual surplus/(deficit) | (23) | (4) | (3) | (30) | (44) | (47) | (2) | (2) | (13) | (19) | (22) | (13) | (222)
in % of actual req. | 0.05% | 0.01% | 0.01% | 0.07% | 0.11% | 0.12% | 0.00% | 0.00% | 0.03% | 0.04% | 0.05% | 0.03% | 0.04%
Southern region |  |  |  |  |  |  |  |  |  |  |  |  | 
Antic. surplus/(deficit) | (901) | 1,839 | 1,008 | 1,852 | (1,049) | 899 | 262 | 445 | 3,734 | 1,454 | 569 | 326 | 10,436
In % of anticipated req. | 2% | 5% | 3% | 5% | 2% | 3% | 1% | 1% | 11% | 4% | 1% | 1% | 2%
Actual surplus/(deficit) | (2) | - | - | (7) | (2) | (3) | (2) | (7) | (3) | - | (1) | - | (27)
in % of actual req. | 0.00% | - | - | 0.02% | 0.01% | 0.01% | 0.01% | 0.02% | 0.01% | - | 0.00% | - | 0.01%
Eastern region |  |  |  |  |  |  |  |  |  |  |  |  | 
Antic. surplus/(deficit) | (1,148) | (789) | (1,971) | (3,875) | (3,050) | (1,406) | 1,730 | 2,826 | 3,648 | 2,402 | 1,729 | 1,135 | 1,232
In % of anticipated req. | 6% | 4% | 10% | 19% | 15% | 7% | 10% | 19% | 26% | 16% | 13% | 7% | 1%
Actual surplus/(deficit) | (72) | (64) | (61) | (74) | (26) | (26) | (6) | (5) | (10) | (21) | (6) | (4) | (375)
in % of actual req. | 0.39% | 0.34% | 0.31% | 0.39% | 0.14% | 0.15% | 0.03% | 0.04% | 0.07% | 0.15% | 0.04% | 0.02% | 0.19%
Northeastern region |  |  |  |  |  |  |  |  |  |  |  |  | 
Antic. surplus/(deficit) | 161 | 9 | 50 | (56) | 59 | 127 | 212 | 80 | 80 | (8) | 107 | (56) | 765
In % of anticipated req. | 10% | 0% | 3% | 2% | 2% | 6% | 11% | 5% | 5% | 0% | 7% | 3% | 3%
Actual surplus/(deficit) | - | (4) | - | - | - | - | - | - | - | - | (4) | (6) | (14)
in % of actual req. | - | 0.23% | - | - | - | - | - | - | - | - | 0.29% | 0.39% | 0.07%
India |  |  |  |  |  |  |  |  |  |  |  |  | 
Antic. surplus/(deficit) | 2,576 | 3,424 | 2,448 | (28) | (1,048) | 2,742 | 4,705 | 7,940 | 9,756 | 2,465 | 2,725 | 4,456 | 42,159
In % of anticipated req. | 2% | 2% | 2% | 0% | 1% | 2% | 3% | 6% | 7% | 2% | 2% | 3% | 2%
Actual surplus/(deficit) | (122) | (189) | (277) | (379) | (154) | (114) | (29) | (24) | (186) | (49) | (37) | (32) | (1,592)
in % of actual req. | 0.08% | 0.12% | 0.18% | 0.25% | 0.11% | 0.08% | 0.02% | 0.02% | 0.14% | 0.04% | 0.03% | 0.02% | 0.09%

## Slide 70: Electricity sector in India | Short term electricity market contract types
Chart: 
| FY10 | FY15 | FY20 | FY21 | FY22 | FY23 | FY24 | FY25
Short-term transactions (BU) | 65.9 | 98.99 | 137.16 | 146.01 | 186.75 | 194.35 | 217 | 258.554
% of total electricity generation | 0.081863 | 0.08918 | 0.098676 | 0.10573 | 0.12525 | 0.11967 | 0.12587 | 0.14173
Majority of demand is fulfilled through long/medium-term contracts, however short-term transactions have grown at CAGR of 15% since FY21
Long/medium term contracts: up to 25 years
Bilateral: less than 1 year
Exchanges:
Real time (1 hour) to 90 days
Deviation Settlement Mechanism (DSM)
Total power generation in India (FY25): ~1,824 billion kWh
Long/medium term supply: ~86%
Short-term supply: ~14%
Long term contracts i.e. long-term Power Purchase Agreements (PPAs) are 25 years contracts (thermal - 25 years, hydro - 35 years)
Medium-term contract duration usually ranges from 1 to 5 years
There are 3 power exchanges in India offering following trades:
Day Ahead Market (DAM)
Real Time Market (RTM)
Intraday, Contingency, Term Ahead up to 90 days
Green Term Ahead, Green DAM
High-Price DAM
Direct bilateral transactions
Bilateral trading through intermediaries
Banking transactions between electricity distribution utilities
Such transactions take place via traders/bilaterally/via DEEP^ portal
DSM mechanism maintains grid stability by penalizing electricity generators and consumers for deviations from scheduled power generation or consumption, thereby incentivizing adherence to schedules and grid frequency norms
^DEEP refers to Discovery of Efficient Electricity Price portal which is an e-bidding portal for procurement of short-term power by electricity distribution utilities.
4%
8%
2%
Volume of short-term electricity transactions as a % of total generation
CAGR: 15%
CAGR: 8%
Electricity sold in exchange in FY25:
~144 Bn units
Sources: Central Electricity Authority (India), Central Electricity Regulatory Commission (India), Ministry of Power (India), Deloitte Analysis

## Slide 71: Electricity trading in India | Overview of segments in power exchanges
Entities with membership in power exchanges can transact on real time, day ahead and term ahead (up to 90 days) basis
Intraday Market & Contingency Market Segment
Intraday Market: hourly and or 15-minute contracts on same day on rolling basis
Day-Ahead Contingency: 24-hourly and/or 15-minute contracts on day-ahead basis for 00:00 hours to 24:00 hours of next day
Continuous trading (Buyers & sellers are matched on continuous basis with price-time priority)
Term Ahead Market (TAM) and Green TAM
Green Attributes as Certificates
Sellers: RE generators not covered under feed in tariffs
Buyers: Obligated entities; 1 MWh is equivalent to 1 REC
Renewable Energy Certificates
Half-hourly market (48 times per day)
Delivery for 30 mins in two-time blocks of 15 min each
Double sided closed auction with uniform price
Ancillary services# (RTM-AS)
Real Time Market (RTM)
1 ESCert = 1 Mtoe (Metric tonne Oil Equivalent)
Energy Saving Certificates (ESCerts)
DAM
Delivery for next day; 15-min contracts; daily trade
Price discovery through closed double-sided auction
Integrated Day Ahead Market (IDAM)
Green DAM (GDAM)
In addition to DAM characteristics:
Priority for GDAM in price & volume
Option to carry forward uncleared bids in GDAM to conventional DAM
High price DAM (HPDAM)
Segment within I-DAM on day ahead basis; Double-Sided Closed Auction
Bidding during DAM, GDAM hours
Separate price discovery with price cap of INR 20/unit and floor price of zero
Term-Ahead Contracts1
Any day(s) single side Reverse Auction
Daily (up to 14 days), Weekly (up to 12 weeks), Monthly (up to 3 months)
Green Term-Ahead Contracts
15-minute quotation of quantity (MW) and price (INR/MWh)
Price discovery and matching on ‘Continuous Trade’ basis
Revision in schedule not allowed
High Price Term-Ahead Contracts
Contracts include HP-Intraday, HP-DAC, HP Daily, HP Monthly, HP Any Day Single Side
Key milestones
[1] Power exchanges have filed a petition with CERC for extension of TAM and GTAM contracts for up to 11 months. Final order awaited; pending additional submissions by parties, [2]Ancillary Services (AS) are deployed to control the grid frequency. AS are of 3 types: Primary Reserve, Secondary Reserve and Tertiary Reserve Ancillary Services (TRAS); based on their response times.
Ancillary services2 (DAM-AS)
Procurement of capacity for TRAS by NLDC
Membership fee details: IEX PXIL
Trading durations on IEX for different segments
Sources: Central Electricity Authority (India), Central Electricity Regulatory Commission (India), Ministry of Power (India), Deloitte Analysis
IEX membership requirements

## Slide 72: Electricity trading in India | Overview of transactions in the power exchanges
Short term transactions on exchanges has increased significantly from ~40% in FY20 to ~56% in FY25 vs the regulated short-term market
Exchange based transactions accounted for ~56% of short-term market in India in FY25
Chart: 
| DAM | RTM | TAM | GDAM | DAC & ID | Others
IEX | 0.99907 | 0.99732 | 0.38284 | 0.99991 | 0.26641 | 0.21063
PXIL | 0.00091858 | 0.0014226 | 0.38332 | 8.8927e-05 | 0.48691 | 0.34502
HPX | 9.4632e-06 | 0.0012562 | 0.23385 | 0 | 0.24668 | 0.44435
Share of electricity transacted on exchanges segment-wise in FY25
Chart: 
 | 120642.75 | 14262.97 | 8771.28
IEX accounted for ~84% of total electricity traded on exchanges in FY25
Chart: 
| DAM | RTM | TAM | GDAM | DAC & ID | Others
FY25 | 0.42658 | 0.27149 | 0.17693 | 0.057917 | 0.053014 | 0.014069
Spot trades (DAM + RTM) accounted for ~70% of the exch. volume in FY25
Chart: 
| FY10 | FY15 | FY20 | FY21 | FY22 | FY23 | FY24 | FY25
Bilateral through traders | 27 | 35 | 30 | 27 | 39 | 34 | 40 | 49.7158
On power exchanges | 7 | 29 | 56 | 80 | 101 | 103 | 120 | 143.677
Directly between discoms | 6 | 16 | 28 | 17 | 21 | 31 | 30 | 31.199
DSM | 26 | 19 | 23 | 23 | 25 | 26 | 27 | 33.9625
TOTAL | 66 | 99 | 137 | 147 | 186 | 194 | 217 | 258.5543
Spot market (day ahead and intra-day (also called as real-time market in India) accounted for ~70% of the total traded volumes in India. Day ahead market is further broken down into different segments like GDAM (exclusively for trading green power – solar and non-solar), HPDAM or high price DAM (for the benefit of plants having high variable cost of generation), DAM where all types of (fossil, non-fossil) power can be traded on day ahead basis
Term Ahead Market (TAM) on exchanges is for daily, weekly or monthly term ahead contracts traded bilaterally
Electricity distribution utilities are the main participants in Real Time Market (RTM) to address the real time variations in demand
Key observations
259
Sources: Central Electricity Authority (India), Central Electricity Regulatory Commission (India), Ministry of Power (India), Deloitte Analysis
Details of power exchanges

## Slide 73: Electricity trading in India | Prices on power exchanges
Due to significant shortages in peak hours, price in the exchanges shot up to INR 20/ kWh in FY22; CERC has now capped it at INR 10/ kWh
Sources: Central Electricity Authority (India), Central Electricity Regulatory Commission (India), Ministry of Power (India), Deloitte Analysis
Chart: 
| 44986 | 45017 | 45047 | 45078 | 45108 | 45139 | 45170 | 45200 | 45231 | 45261 | 45292 | 45323 | 45352 | 45383 | 45413 | 45444 | 45474 | 45505 | 45536 | 45566 | 45597 | 45627 | 45658 | 45689 | 45717
Maximum | 12 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10
Minimum | 2.2 | 1.9 | 1.9 | 1.5 | 1 | 2 | 1.2 | 1.5 | 2 | 2.1 | 2 | 2.2 | 1 | 1.71 | 1.2 | 1 | 0.5 | 0.3 | 0.4 | 0.5 | 0.57 | 1.61 | 1.62 | 2.03 | 1
Average | 5.4 | 5.4 | 4.7 | 5.4 | 4.5 | 6.8 | 6.2 | 6.5 | 4 | 4.5 | 5.8 | 4.9 | 3.9 | 4.65 | 4.76 | 4.84 | 4.64 | 4.15 | 4.28 | 4.03 | 3.52 | 3.84 | 4.4 | 4.32 | 4.19
A
Chart: 
| 44621 | 44652 | 44682
Maximum | 20 | 20 | 12
Minimum | 2.4 | 2.8 | 1
Average | 8.2 | 10 | 6.8
Average electricity price traded on exchange (DAM, bilateral contracts)
FY10-25, INR/kWh
Monthly price of electricity traded on exchanges (DAM)
FY23-25, INR/kWh
In early 2022 (Q4 FY22), prices on exchanges (DAM) reached INR 20/kWh due to an increase in the economic activities following the easing of COVID-19 restrictions, pushing average exchange prices (all segments) higher than prices of bilateral contracts executed through traders
The Ministry of Power directed CERC to put a price cap of INR 12/kWh on the exchanges
This move stabilized prices for buyers, however, due to high international gas prices, gas-generated electricity became costly, exceeding INR 12/kWh
Consequently, capacity from natural gas and imported coal-based plants, as well as RE plants with battery storage systems could not participate in exchange transactions due to their high generation costs
Anticipating growing electricity demand in the coming years, the Ministry of Power, introduced HP-DAM (High Price-DAM), a separate segment within the DAM segment, exclusively for generating capacities with high production costs
DAM was subjected to a price cap of INR 10 per kWh, making average exchange price competitive with prices of bilateral contracts executed through traders
Chart: 
| FY15 | FY20 | FY21 | FY22 | FY23 | FY24 | FY25
Bilateral | 4.28 | 4.51 | 3.47 | 3.72 | 5.85 | 7.33 | 6.85
Power exchange (IEX) | 3.49 | 3.16 | 2.99 | 4.78 | 6.03 | 5.16 | 4.25
Legend: Maximum, Minimum, Weighted Average
B
C
A
B
C

## Slide 74: Bilateral transactions for sale of electricity
Sale of electricity to Discoms or Commercial & Industrial consumers directly or through traders is another avenue for sale of power in India
Sources: Central Electricity Authority (India), Central Electricity Regulatory Commission (India), Ministry of Power (India), Deloitte Analysis
Electricity supply through grid
Tariff + trading margin (INR/kWh)
Tariff - trading margin (INR/kWh)
Trader can charge margin to both buyer and seller. However, total margin should not exceed INR 0.07//kWh
Bilateral transactions
Customer/ Discom
Generator
Trading licensee
Trader typically enters in bilateral contract with generator at one side and discom or bulk consumer on other side
These are short-term contracts (<1 year) for supply of power at fixed rate to consumer/ Discom looking to meet short term requirements
Total traded volume under bilateral contracts through traders grew from 34 BU in FY23 to 70 Bn kWh in FY25
Market presence and coverage in the key industrial clusters and access to generators are key success factors in this segment
The top 3 (PTC, NVVN, Tata Power Trading Company Ltd.) account for 50% of total bilateral volumes
Other major players include Adani Enterprises, Manikaran Power, GMR Energy Trading and Kreate
As per discussions with industry experts, 80-90% i.e. ~50 Bn kWh of the transactions on the DEEP portal are also facilitated by electricity traders
Traders also offer other value-added services such as energy management, power procurement cost optimization, and decarbonization solutions to acquire consumers

## Slide 75
4.2 | FRAMEWORK FOR DISCOVERY OF THE MARKET CLEARING PRICE IN THE POWER EXCHANGES

## Slide 76: Market clearing price discovery | Double sided closed bid uniform price auction
Day ahead market and real time market use double sided closed bid uniform price auction method for market price discovery
Sources: Central Electricity Authority (India), Ministry of Power (India), Deloitte Analysis
Double-sided closed bid uniform price auction methodology
In case of non intersecting aggregate buy and sell curves, curves are shifted suitably so that curves can intersect i.e., In case of over supply, sell offers are reduced whereas in case of over demand, purchase bids are reduced to intersect at the minimum and maximum price respectively
Multiple buy and sell bids received for specific time block and bid area
Each buy bid needs to have non increasing quantity while each sell bid needs to have nondecreasing quantity
Every bid is assumed to vary linearly between consecutive prices
Buy/ sell bids placed
All buy and sell bids for a specific time block and bid area are aggregated together
In a bid where quantity at a specific price is not quoted, it is calculated through straight line equation
Bids aggregated
The aggregated buy and sell bids are traced to create aggregate buy and sell curves
The intersection of buy/sell curves give the market clearing price and volume
Straight line method is thereafter used to allocate bid volume to respective buyers and sellers
Bid volume allocation
Sample buy and sell bids |  |  |  | 
Bids | Price/ Quantity | P/ Q 1 | P/ Q 2 | P/ Q 3
Buy bid 1 | Price | - | 3,000 | 8,000
 | Quantity | 200 | 200 | 100
Buy bid 2 | Price | - | 2,000 | 6,000
 | Quantity | 200 | 120 | 80
Sell bid 1 | Price | - | 2,000 | 4,000
 | Quantity | - | (50) | (100)
Sell bid 2 | Price | - | 3,000 | 6,000
 | Quantity | - | (90) | (150)
Bids | Price/ Quantity | P/ Q 1 | P/ Q 2 | P/ Q 3 | P/ Q 4 | P/ Q 5
Buy bid | Price | - | 2,000 | 3,000 | 6,000 | 8,000
 | Quantity | 400 | 320 | 310 | 220 | 170
Sell bid | Price | - | 2,000 | 3,000 | 4,000 | 6,000
 | Quantity | - | (110) | (165) | (210) | (255)
Example
Quantities for each price point across buy and sell bids respectively is calculated before aggregation
Price: 6,000 | Buy bid 1 | Buy bid 2 | Total
Quantity | 200-(100/5,000)*3,000 = 140 | 80 | 220
Aggregated buy and sell curves cut each other to give area clearing price and volume
A
A
Chart: 
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400
 | 20000 | 15500 | 10000 | 7000 | 5000 | 3000 | 1500 | 0
 | 0 | 1000 | 2000 | 3000 | 4000 | 6000 | 13000 | 20000
Example

## Slide 77: Market clearing price discovery | Continuous matching algorithm
Intraday & contingency market use the continuous matching algorithm for price discovery where best buy/ sell bids are calculated and matched continuously
Sources: Central Electricity Authority (India), Ministry of Power (India), Deloitte Analysis
Continuous matching algorithm
Best buy bid > = best sell bid
Else
No action, orders in pending
New
buy/ sell bid
Order matching rules
Order matching is done continuously, i.e., Any new buy/ sell order changes the best buy and sell bid
Orders are matched based on price and time priority. In case of multiple orders at same price, orders are prioritized based on bid time
Best buy bid is the highest priced buy bid while the best sell bid is the lowest priced sell bid
Orders can be matched partially
Type of orders
Timing constraints
Rest of day (Day): Order is valid till end of trading hours of the trading day
Immediate or cancel (IOC): Order will not go in pending state and will be cancelled immediately if not matched
End of Session (EOS): Order will get cancelled post the specific trading session is closed
Execution constraints
Fill or kill (FoK): Partial order matching is not allowed
Buy/ Sell bids placed
Best buy & sell bid
Trade execution
Buy and sell bids are arranged based on best buy and sell bids
Best buy bid is the highest priced buy bid
Best sell bid is the lowest priced sell bid
Whenever a new buy or sell bid is placed, best buy and sell bids are recalculated
Top 5 buy and sell bids are displayed to all the participants
Buy bids |  | 
Buyer | Buy price | Buy qty.
Buyer 3 | 3,300 | 300
Buyer 2 | 3,200 | 400
Buyer 1 | 3,000 | 500
Sell bids |  | 
Seller | Sell price | Sell qty.
Seller 1 | 3,200 | 200
Seller 2 | 4,000 | 300
Seller 3 | 4,200 | 500
Order of 200 units shall be executed at price of 3,300 between Buyer 3 and Seller 1
Example
Example

## Slide 78: Market clearing price discovery | Double sided open bid uniform price step auction
Term Ahead Market uses step auction to arrive at price, executing multiple step principles to get maximum tradable volume & minimum unbalance
Sources: Central Electricity Authority (India), Ministry of Power (India), Deloitte Analysis
Term ahead market (TAM) follow the double-sided open bid uniform price step auction for price discovery
Buy/ Sell bids placed
Multiple surplus unbalances: Buy side market pressure, hence highest price
Multiple deficit unbalances: Sell side market pressure, hence lowest price
Unbalance is calculated for the respective prices
Unbalance = Cuml. Buy quantity – Cuml. Sell quantity
Regardless of surplus/ deficit, price of lowest unbalance is selected
Maximum tradable volume
Minimum unbalance
Market pressure tests
Equilibrium price
Else
Cumulative buy and sell quantities are calculated for each buy and sell price to find tradable volume at a price
Tradable volume = Minimum of cuml. buy and sell quantity
Price at which there is highest tradable volume, is the auction price
In case of multiple prices
In case of multiple prices
Else
Multiple buy and sell bids received are sorted based on best buy and sell bids post session
1
2
3
Formula In case of multiple equal surplus and deficit or multiple 0 unbalances is explained in annexure
All matching orders are traded at the determined auction price, where order matching is governed by “price-time” priority, i.e., in case of equal price, earliest bid gets executed
Example

## Slide 79
4.3 | PROFILE OF KEY BUYERS/OFF-TAKERS IN THE POWER EXCHANGES

## Slide 80: Buyers/offtakers in the power exchange | Day ahead market
Top 5 buyers/off-takers have ~60% market share in DAM. Almost all power in the exchange is procured by state DISCOMs.
Sources: Central Electricity Authority (India), Ministry of Power (India), Deloitte Analysis
Chart: 
| 45406 | 45436 | 45467 | 45497 | 45528 | 45559 | 45589 | 45620 | 45650 | 45681 | 45712 | 45740
Telangana | 512.5 | 216.66 | 846.52 | 1954.62 | 1967.1 | 798.06 | 350.33 | 698.5 | 2325.82 | 2192.41 | 1750.99 | 1571.87
Gujarat | 797.25 | 600.69 | 704.42 | 528.01 | 514 | 894.55 | 695.76 | 1213.87 | 885.93 | 965.62 | 681.72 | 669.69
Maharashtra | 283.56 | 153.3 | 150.87 | 76.49 | 287.46 | 244.38 | 617.08 | 903.04 | 578.4 | 484.17 | 756.92 | 822.69
Uttar Pradesh | 227.03 | 450.25 | 463.93 | 260.49 | 236.99 | 231.44 | 362.33 | 269.69 | 274.6 | 338.75 | 234.7 | 205.58
Rajasthan | 119.36 | 715.91 | 592.22 | 312.55 | 50.77 | 483.72 | 205.6 | 374.05 | 219.19 | 30.4 | 125.56 | 78.69
Chart: 
| Telangana | Gujarat | Maharashtra | Uttar Pradesh | Rajasthan | Others
Sales | 15185.38 | 9151.51 | 5358.36 | 3555.78 | 3308.02 | 24736.01
Key buyers/offtakers
%, FY25
61,295 MU
MoM trend – Top 5 buyers/ offtakers
MU, FY25
Top 10 buyers/ offtakers catered to ~79% of the total day ahead market
Key observations
Telangana purchased 15,185 MU of electricity in FY25 purchasing ~52% of the total power from Dec’24 to Mar’25 with surge in demand driven by increase in agricultural requirements
Gujarat purchased 9,152 MU of electricity in FY25 with offtake spread evenly across the months
Maharashtra purchase ~78% of total 5,358 MU of FY25 in Oct’24 to Mar’25 with a peak of 903 MU in Nov’24

## Slide 81: Buyers/offtakers in the power exchange | Real time market
Top 5 buyers/off-takers have ~55% market share in RTM. Almost all power in the exchange is procured by state DISCOMs.
Sources: Central Electricity Authority (India), Ministry of Power (India), Deloitte Analysis
Chart: 
| 45383 | 45413 | 45444 | 45474 | 45505 | 45536 | 45566 | 45597 | 45627 | 45658 | 45689 | 45717
Punjab | 129 | 347 | 506 | 593 | 625 | 804 | 575 | 318 | 396 | 769 | 778 | 901
Telangana | 339 | 284 | 302 | 359 | 666 | 521 | 376 | 396 | 407 | 425 | 369 | 504
Rajasthan | 240 | 775 | 511 | 484 | 77 | 335 | 229 | 264 | 234 | 121 | 165 | 70
Maharashtra | 245 | 173 | 191 | 128 | 192 | 182 | 373 | 407 | 318 | 362 | 422 | 429
Uttar Pradesh | 168 | 341 | 305 | 230 | 318 | 219 | 220 | 174 | 228 | 217 | 114 | 251
Chart: 
| Punjab | Telangana | Rajasthan | Maharashtra | Uttar Pradesh | Others
Sales | 6741 | 4947 | 3504 | 3424 | 2786 | 17410
Key buyers/offtakers
%, FY25
38,812 MU
MoM trend – Top 5 buyers/ offtakers
MU, FY25
Top 10 buyers/ offtakers catered to ~79% of the total day ahead market
Key observations
Punjab purchased 6,741 MU of electricity from RTM in FY25 with demand surges in Jun-Oct’24 due to paddy season and hot summer while in Jan-Mar’25 due to harsh winter, increasing morning and evening peak demand
Telangana purchased 4,947 MU of electricity in FY25 with a peak of 666 units in Aug’24
Rajasthan purchased 3,504 MU of electricity in FY25 with ~51% power purchased in peak summer during May’24 to jul’24

## Slide 82: Buyers/off-takers in the power exchange | Integrated ratings of distribution utilities across states
State DISCOMs witnessed improvement in their operational performance, reflected in the improved integrated ratings (by the Ministry of Power)
Sources: Central Electricity Authority (India), Ministry of Power (India), Deloitte Analysis
 | Telangana (2 Discoms) |  | Gujarat (4 Discoms) |  |  |  | Mahara-shtra | Uttar Pradesh(5 Discoms) |  |  |  |  | Rajasthan (3 Discoms) |  |  | Andhra Pradesh (3 Discoms) |  |  | Punjab | West Bengal | Tamil Nadu | Uttarak-hand | Kerala
Discom #  | 1 | 2 | 1 | 2 | 3 | 4 | 1 | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 1 | 1 | 1 | 1
FY22 | C- | C- | A+ | A+ | A+ | A+ | B- | C- | C- | C- | B- | C- | B | C | B- | C | B | C | A | B | C- | A | B
FY23 | C | C | A+ | A+ | A+ | A+ | C | C- | B- | C- | B | C- | B | B- | B | B- | A | B- | B | B- | C- | B- | B-
FY24 | C- | C- | A+ | A+ | A+ | A+ | C- | C- | B- | C- | B | C- | B- | B- | B- | C | B | C | A | B | C- | B | B
ACS - ARR gap
Average Cost of supply (ACS) considers total expenditure and Average Revenue Realized (ARR) considers the total revenue (net of subsidy/grants).
ACS-ARR shows the recovery on per unit of energy sold. Positive value means the DISCOM is making money per unit sold and vice-versa.
Payable days
Liability for power purchase costs is divided by the total generation costs including transmission and SLDC charges.
Higher payable days means that the DISCOM is not able to tender its dues on time and there are liquidity issues.
Tariff order timeliness
Timeliness of tariff orders means that the DISCOM is able to charge appropriate tariff timely and there is no mismatch in cost recovery.
This also indicates that the DISCOM has filed the tariff petition in time.
Fuel Adjustment Charge (FAC)
Fuel Adjustment Charge is towards recovery of unprecedented power purchase costs incurred during the tariff period.
Automatic pass-through of FAC indicates that the DISCOM recovers the costs instantly during the billing cycle rather than waiting for approval after filing of tariff petition.
Billing efficiency
Total energy units billed divided by total energy input. It is and indicator of the billings done in relation to energy supplied.
High billing efficiency means that there are less cases of defective meters, energy theft etc.
Collection efficiency
Revenue collected divided by amount billed. It is and indicator of the collections in relation to bills raised..
High collection efficiency means that there are less cases of non-payment of dues by consumers.
Some of the key aspects considered for the integrated ratings include:
ACS: Average Cost of Supply; ARR: Aggregate Revenue Requirement

## Slide 83
4.4 | TRENDS OF VOLUMES AND AVERAGE MARKET CLEARING PRICES IN POWER EXCHANGE FOR THE PAST 3-5 YEARS

## Slide 84: India short-term market | Trends in spot prices and solar hour discounts
Rising solar penetration has driven FY25 solar-hour prices ~25% below average, reinforcing its role in moderating intraday market volatility.
Sources: IEX DAM prices data, Deloitte Analysis
Average annual day ahead short-term power prices on exchanges across different time blocks during day
FY23 – FY25, INR/ kWh
Chart: 
 | 6.03 | 5.16 | 4.28
 | 5.13 | 4.36 | 3.2
 | 5.73 | 5.1 | 4.36
 | 6.33 | 5.36 | 4.52
 | 8.2 | 6.85 | 6.56
FY23
FY24
FY25
-25%
-15%
-16%
-16%
-4%
Annual average MCP
Solar hours (10 AM to 6 PM)
Night hours (10 PM to 6 AM)
Morning peak (6 AM to 10 AM)
Evening peak (6 PM to 10 PM)
Over the past three fiscal years, the average spot electricity prices in India have ranged between INR 4.00 and INR 6.00 per kilowatt-hour (kWh), reflecting prevailing supply-demand dynamics.
In FY25, the market-clearing prices observed during solar generation hours have been ~25% lower than the overall average spot prices, indicating the impact of increased solar penetration on intraday price volatility.

## Slide 85: India short-term market | FY 23 hourly DAM prices on IEX
Electricity prices stayed low during solar hours, with a notable spike in Apr’22 driven by post-COVID economic recovery and reduced RE output
Sources: IEX DAM prices data, Deloitte Analysis
Average monthly day ahead short-term power prices on exchanges across 24 hours
FY23, INR/kWh
Hour | Apr-22 | May-22 | Jun-22 | Jul-22 | Aug-22 | Sep-22 | Oct-22 | Nov-22 | Dec-22 | Jan-23 | Feb-23 | Mar-23
1 | 11.84 | 9.00 | 10.68 | 7.33 | 5.57 | 6.88 | 3.44 | 3.57 | 2.88 | 2.97 | 5.29 | 5.90
2 | 11.42 | 7.93 | 9.06 | 5.83 | 4.62 | 5.69 | 3.22 | 3.36 | 2.70 | 2.77 | 4.54 | 5.09
3 | 11.05 | 7.12 | 7.88 | 4.76 | 4.02 | 5.00 | 3.02 | 3.22 | 2.57 | 2.66 | 4.19 | 4.48
4 | 10.70 | 6.57 | 6.94 | 4.27 | 3.77 | 4.54 | 2.87 | 3.14 | 2.55 | 2.63 | 3.99 | 4.30
5 | 10.43 | 6.59 | 7.41 | 4.11 | 4.00 | 4.63 | 3.01 | 3.31 | 2.79 | 2.78 | 4.66 | 4.90
6 | 10.92 | 6.72 | 6.80 | 4.94 | 5.80 | 5.76 | 3.53 | 4.05 | 3.64 | 3.72 | 6.65 | 5.88
7 | 11.07 | 6.46 | 6.05 | 5.69 | 6.44 | 7.04 | 4.14 | 4.83 | 5.62 | 6.38 | 9.33 | 6.85
8 | 9.62 | 5.41 | 4.32 | 5.40 | 5.51 | 5.42 | 4.02 | 5.61 | 8.63 | 9.19 | 10.02 | 6.94
9 | 7.99 | 4.58 | 3.27 | 3.89 | 4.11 | 3.97 | 3.39 | 5.21 | 8.13 | 9.60 | 9.39 | 5.41
10 | 7.73 | 4.69 | 2.98 | 3.42 | 3.69 | 3.51 | 3.10 | 5.00 | 7.67 | 10.01 | 8.97 | 5.48
11 | 7.98 | 4.98 | 3.35 | 3.22 | 3.43 | 3.38 | 2.97 | 4.67 | 6.99 | 9.21 | 7.82 | 4.84
12 | 7.60 | 5.31 | 3.67 | 3.07 | 3.41 | 3.44 | 2.82 | 4.45 | 5.82 | 7.38 | 6.46 | 4.32
13 | 6.52 | 5.06 | 3.94 | 2.99 | 3.18 | 3.47 | 2.67 | 4.04 | 4.86 | 6.16 | 5.24 | 3.65
14 | 5.89 | 5.30 | 4.16 | 2.84 | 2.90 | 3.20 | 2.56 | 3.83 | 4.05 | 4.64 | 4.08 | 3.22
15 | 7.33 | 6.28 | 5.35 | 3.12 | 3.36 | 3.88 | 2.77 | 4.06 | 4.35 | 4.60 | 4.12 | 3.54
16 | 8.78 | 7.10 | 6.48 | 3.82 | 4.04 | 4.70 | 3.06 | 4.40 | 5.01 | 5.70 | 4.99 | 4.23
17 | 9.60 | 6.79 | 5.64 | 4.06 | 4.57 | 5.11 | 3.46 | 4.82 | 6.78 | 7.16 | 6.99 | 5.22
18 | 9.94 | 6.63 | 4.90 | 4.25 | 4.62 | 5.99 | 4.60 | 6.60 | 7.90 | 8.12 | 7.79 | 5.04
19 | 10.67 | 6.86 | 5.42 | 6.96 | 7.05 | 9.09 | 8.73 | 8.72 | 9.24 | 10.21 | 10.25 | 6.82
20 | 11.11 | 8.10 | 9.43 | 9.81 | 9.76 | 11.18 | 8.49 | 6.12 | 7.99 | 10.29 | 10.70 | 8.80
21 | 10.61 | 7.95 | 9.53 | 10.07 | 9.57 | 9.47 | 5.00 | 4.86 | 5.15 | 7.57 | 7.26 | 7.11
22 | 11.02 | 8.93 | 10.66 | 10.07 | 9.32 | 8.75 | 4.20 | 4.49 | 4.33 | 5.83 | 6.05 | 6.34
23 | 11.06 | 9.37 | 10.87 | 9.95 | 8.67 | 8.44 | 3.87 | 4.48 | 3.60 | 4.16 | 5.64 | 6.30
24 | 11.82 | 9.26 | 10.72 | 9.20 | 7.38 | 8.17 | 3.51 | 3.83 | 3.14 | 3.33 | 5.28 | 6.20
Wet season (May – December)
Dry season
Dry season (January – April)

## Slide 86: India short-term market | FY 24 hourly DAM prices on IEX
Spot prices stayed consistently low during solar hours, driven by record renewable additions boosting supply and lowering market prices
Sources: IEX DAM prices data, Deloitte Analysis
Average monthly day ahead short-term power prices on exchanges across 24 hours
FY24, INR/kWh
Wet season (May – December)
Dry season
Dry season (January – April)
Hour | Apr-23 | May-23 | Jun-23 | Jul-23 | Aug-23 | Sep-23 | Oct-23 | Nov-23 | Dec-23 | Jan-24 | Feb-24 | Mar-24
1 | 7.48 | 7.85 | 8.97 | 6.73 | 8.40 | 7.17 | 7.04 | 3.39 | 2.94 | 3.04 | 3.25 | 4.33
2 | 7.13 | 6.62 | 8.14 | 5.07 | 7.84 | 6.45 | 6.79 | 3.19 | 2.81 | 2.80 | 3.09 | 3.71
3 | 6.73 | 5.23 | 6.77 | 4.04 | 7.32 | 5.64 | 6.54 | 3.05 | 2.71 | 2.62 | 2.96 | 3.47
4 | 6.39 | 4.47 | 5.32 | 3.64 | 6.57 | 5.18 | 6.13 | 2.95 | 2.65 | 2.57 | 2.88 | 3.35
5 | 6.75 | 4.22 | 4.88 | 3.47 | 6.75 | 5.05 | 6.08 | 3.15 | 2.79 | 2.72 | 3.05 | 3.43
6 | 7.40 | 4.49 | 4.90 | 3.58 | 7.50 | 5.72 | 6.93 | 3.83 | 3.18 | 3.38 | 3.48 | 3.78
7 | 6.08 | 3.95 | 3.95 | 4.20 | 8.13 | 6.64 | 7.02 | 3.96 | 4.37 | 6.09 | 6.04 | 4.36
8 | 4.18 | 3.28 | 3.16 | 3.30 | 7.10 | 5.93 | 6.23 | 4.14 | 6.96 | 9.23 | 8.70 | 5.20
9 | 3.74 | 2.96 | 2.71 | 2.83 | 5.18 | 4.63 | 5.32 | 4.01 | 7.41 | 9.96 | 8.53 | 4.54
10 | 3.56 | 2.96 | 2.81 | 2.90 | 4.88 | 4.58 | 5.07 | 3.96 | 6.63 | 9.88 | 7.18 | 4.02
11 | 3.26 | 2.97 | 2.92 | 2.80 | 4.45 | 4.28 | 4.76 | 3.59 | 5.43 | 9.69 | 5.85 | 3.52
12 | 3.11 | 3.06 | 3.11 | 2.81 | 4.18 | 4.15 | 4.66 | 3.40 | 4.31 | 7.30 | 4.23 | 3.30
13 | 2.98 | 3.04 | 3.21 | 2.78 | 4.15 | 4.02 | 4.62 | 3.19 | 3.48 | 4.75 | 3.75 | 3.04
14 | 2.80 | 2.94 | 3.22 | 2.75 | 4.02 | 4.06 | 4.44 | 3.05 | 3.17 | 3.57 | 3.37 | 2.74
15 | 3.15 | 3.37 | 3.87 | 2.94 | 4.98 | 4.68 | 5.19 | 3.30 | 3.32 | 3.75 | 3.43 | 3.05
16 | 3.46 | 3.86 | 4.43 | 3.13 | 5.59 | 5.35 | 5.96 | 3.69 | 3.58 | 4.40 | 3.71 | 3.30
17 | 3.85 | 3.96 | 4.39 | 3.15 | 6.06 | 5.54 | 7.04 | 4.87 | 5.57 | 7.33 | 4.74 | 3.71
18 | 4.19 | 3.97 | 4.07 | 3.20 | 6.26 | 5.81 | 8.28 | 8.15 | 8.70 | 9.63 | 6.35 | 3.77
19 | 6.34 | 4.55 | 4.59 | 4.13 | 7.42 | 7.58 | 8.83 | 8.30 | 8.71 | 9.78 | 7.64 | 4.72
20 | 7.58 | 7.21 | 7.73 | 7.56 | 8.82 | 9.20 | 8.11 | 5.24 | 6.26 | 9.38 | 8.27 | 5.76
21 | 7.24 | 6.93 | 8.32 | 8.38 | 8.94 | 8.76 | 7.27 | 4.23 | 4.37 | 7.04 | 6.23 | 4.52
22 | 7.35 | 7.59 | 9.07 | 8.93 | 9.40 | 8.66 | 7.29 | 3.81 | 3.51 | 4.46 | 4.59 | 4.46
23 | 7.73 | 7.98 | 9.50 | 9.10 | 9.31 | 8.40 | 7.12 | 3.58 | 3.10 | 3.47 | 3.75 | 4.30
24 | 7.43 | 8.00 | 9.32 | 8.76 | 8.91 | 8.21 | 7.28 | 3.36 | 3.02 | 3.26 | 3.50 | 4.26

## Slide 87: India short-term market | FY 25 hourly DAM prices on IEX
The trend persisted in the subsequent year as rising renewables and moderate demand kept prices broadly lower
Sources: IEX DAM prices data, Deloitte Analysis
Average monthly day ahead short-term power prices on exchanges across 24 hours
FY25, INR/kWh
Wet season (May – December)
Dry season
Dry season (January – April)
Hour | Apr-24 | May-24 | Jun-24 | Jul-24 | Aug-24 | Sep-24 | Oct-24 | Nov-24 | Dec-24 | Jan-25 | Feb-25 | Mar-25
1 | 8.27 | 9.62 | 9.69 | 8.20 | 5.78 | 5.17 | 5.06 | 2.80 | 2.37 | 2.53 | 3.11 | 4.49
2 | 6.75 | 8.11 | 8.13 | 6.53 | 4.55 | 4.10 | 3.91 | 2.65 | 2.28 | 2.38 | 3.09 | 4.29
3 | 5.68 | 5.43 | 6.46 | 4.94 | 3.73 | 3.67 | 3.56 | 2.62 | 2.20 | 2.29 | 3.01 | 3.88
4 | 5.12 | 4.38 | 5.29 | 4.69 | 3.69 | 3.46 | 3.32 | 2.59 | 2.20 | 2.27 | 2.97 | 3.71
5 | 4.77 | 4.37 | 5.33 | 4.56 | 3.80 | 3.46 | 3.20 | 2.62 | 2.28 | 2.38 | 3.05 | 3.90
6 | 4.92 | 4.37 | 4.99 | 3.83 | 3.55 | 3.49 | 3.38 | 2.86 | 2.82 | 2.92 | 3.49 | 4.54
7 | 5.30 | 4.24 | 5.08 | 4.67 | 4.27 | 3.98 | 3.53 | 3.39 | 3.75 | 4.12 | 5.95 | 6.17
8 | 4.34 | 3.45 | 3.70 | 3.67 | 3.74 | 3.42 | 3.42 | 3.93 | 6.20 | 8.40 | 9.25 | 6.01
9 | 3.54 | 2.97 | 2.87 | 3.04 | 2.93 | 2.75 | 2.98 | 3.60 | 7.03 | 9.15 | 7.35 | 3.63
10 | 3.36 | 2.87 | 2.64 | 2.71 | 2.61 | 2.50 | 2.62 | 3.22 | 6.05 | 7.78 | 5.79 | 3.39
11 | 3.04 | 2.81 | 2.62 | 2.41 | 2.37 | 2.28 | 2.25 | 2.55 | 4.01 | 4.44 | 3.66 | 2.91
12 | 2.85 | 2.70 | 2.51 | 2.30 | 2.13 | 2.22 | 2.12 | 2.22 | 3.19 | 3.42 | 3.35 | 2.74
13 | 2.65 | 2.78 | 2.59 | 2.12 | 1.95 | 2.01 | 2.05 | 1.96 | 2.78 | 3.07 | 3.12 | 2.56
14 | 2.55 | 2.76 | 2.62 | 2.04 | 1.86 | 1.99 | 2.05 | 1.85 | 2.51 | 2.69 | 2.78 | 2.38
15 | 2.95 | 3.55 | 3.49 | 2.61 | 2.27 | 2.56 | 2.60 | 2.38 | 2.84 | 2.98 | 2.85 | 2.58
16 | 3.40 | 3.92 | 3.81 | 3.08 | 2.76 | 3.08 | 3.04 | 2.92 | 3.22 | 3.22 | 3.15 | 2.94
17 | 3.91 | 4.31 | 3.91 | 3.25 | 3.19 | 3.48 | 3.49 | 3.68 | 4.20 | 4.04 | 3.65 | 3.49
18 | 4.19 | 4.09 | 3.90 | 3.32 | 3.27 | 4.16 | 4.89 | 7.40 | 8.28 | 6.80 | 4.76 | 3.73
19 | 4.97 | 4.72 | 4.23 | 4.10 | 4.19 | 5.87 | 8.03 | 8.30 | 8.96 | 9.57 | 8.40 | 6.59
20 | 6.73 | 7.85 | 7.16 | 8.00 | 8.09 | 9.02 | 6.80 | 4.25 | 4.92 | 7.91 | 7.72 | 8.63
21 | 6.16 | 9.00 | 8.95 | 9.23 | 8.58 | 8.34 | 5.55 | 3.58 | 3.51 | 4.45 | 4.18 | 7.52
22 | 7.45 | 9.66 | 9.78 | 9.75 | 8.76 | 8.19 | 5.50 | 3.31 | 3.14 | 3.51 | 3.77 | 5.56
23 | 8.10 | 9.83 | 9.96 | 9.85 | 8.39 | 7.27 | 5.34 | 3.03 | 2.72 | 3.00 | 3.36 | 5.68
24 | 8.84 | 9.83 | 10.00 | 9.79 | 7.67 | 6.88 | 5.28 | 2.86 | 2.61 | 2.78 | 3.04 | 5.13

## Slide 88
4.5 | PAYMENT SECURITY MECHANISM AND KEY ASSOCIATED RISKS

## Slide 89: Payment risk management in power exchanges
Key reason for rising short-term transactions is a well-established payment security mechanism, requiring off-takers to maintain a minimum margin
Sources: CERC, Deloitte analysis
Contract type | Trading licensee members | 
 | Initial margin | Basis/additional margin
I-DAM | Avg of last 7 days’ transaction value | N/A
TAM Intraday | 105% of order value | N/A
TAM/GTAM Day-ahead contingency | 105% of order value | N/A
TAM/GTAM Daily | 5% of order value | 50% of trade value
TAM/GTAM weekly | 5% of order value | 50% of trade value
TAM/GTAM monthly | 1% of order value | 20% of trade value
Anyday single sided | Buyer: INR 100,000 Seller: INR 30,000/MW/Month | 50% / 25% / 20% for contracts up to 7/ 15/ >15 days
REC | 100% of order value | N/A
ESCerts | 100% of order value | N/A
Power exchange rules require participants to maintain a minimum balance for transactions, with funds credited to the exchange's account, not the sellers
The sellers receive the payment one day after the delivery of contracted electricity (D+1).
In case of default by the seller on the contracted volume, the exchange will refund the prorated amount to the buyer and take appropriate punitive actions against the seller based on the reasons for default.
In case of participants have their own settlement account, no margins shall be collected.
However, to manage risk of default such participants shall be allowed to bid only to the extent of funds available in their settlement bank account.
All the mentioned margins can be deposited in form Cash, Bank-Guarantee (BG), Fixed-deposit (FD) and Letter of Credit (LC)

## Slide 90: Government of India measures and initiatives to improve viability of electricity sector
Electricity distribution, traditionally the weakest link due to state ownership, has seen improvements from measures introduced in last 10 years
Sources: CERC, Deloitte analysis
28 states and 8 Union territories having 70 DISCOMs sold 1,692 Bn kWh of energy in FY25 against 1,622 Bn kWh in FY24 at a 4% growth rate
Electricity sale to agricultural and certain domestic customers are highly subsidized (more than 60-70%); C&I customers pay higher tariff than Average Cost of Supply (ACS) to cross-subsidize
Historically, distribution sector has been the weakest link in the power supply value chain primarily due to:
  Inadequate tariff requisition by DISCOMs
  Delay in tariff filing/orders
  Delay in release of state subsidy and
  Inadequate tariff approved by the state regulatory commissions
Net-worth of DISCOMs continues to be negative, however, several initiatives are/were undertaken by the Government of India to improve the financials such as:
R-APDRP: Re-structured Accelerated Power Development and Reforms Programme ; IPDS: Integrated Power Development Scheme ; UDAY : Ujwal DISCOM Assurance Yojana ; RDSS: Revamped Distribution Sector Scheme
IPDS
UDAY
RDSS
Late Payment Surcharge (LPS), Rules
Fuel Adjustment Charge (FAC)
Scheme for strengthening of infrastructure, metering, IT enablement
Debt-restructuring programme for Discoms enabled by intervention of both the central and the state governments
A result-linked financial support for prepaid smart metering and up-gradation of the distribution infrastructure
One-time liquidation scheme allowing payment of power purchase overdue payments for power purchase in equated monthly installments
Automatic pass-through of FAC in the tariff i.e. the recovery of change in power purchase costs due to instances such as increase in fuel costs
R-APDRP
Scheme for IT applications, consumer data mapping and renovation and modernization of infrastructure
Above measures have resulted in improvement of the operational performance of the state-owned utilities, especially in the last 2-3 years

## Slide 91: Introduction of the Late Payment Surcharge (LPS), Rules
Government, via policy interventions streamlined the payment by DISCOMs resulting in a 79% reduction of outstanding dues in ~2 years
Sources: CERC, Deloitte analysis
Notification of the Rules
Notification of the Rules
The Ministry of Power issued the Electricity (Late Payment Surcharge and Related Matters) Rules (LPS Rules) in June 2022
Mechanism
Distribution companies (Discoms) allowed to pay their outstanding dues in (up to) 48 monthly installments through a one-time liquidation scheme
Chart: 
| June'22 | Aug'24 | Jan'25
Series 1 | 17 | 3.6 | 3.56
Impact
~ USD 13 Billion of overdue payments have been settled between the Discoms, generating companies & transmission companies from Jun’22-Aug’24
As per the Government of India, all current dues are being paid since August 2022 within a timeframe of maximum 75 days
Chart: 
| Telangana | Gujarat | Maharashtra | Uttar pradesh | Rajasthan | Andhra Pradesh | Punjab | West Bengal | Tamil Nadu | Uttarakhand | Kerela
FY22 | 380 | 0 | 177 | 212 | 203 | 166 | 45 | 147 | 223 | 24 | 78
FY24 | 310 | 3 | 109 | 153 | 63 | 105 | 40 | 162 | 184 | 39 | 95
FY22 National average | 169 | 169 | 169 | 169 | 169 | 169 | 169 | 169 | 169 | 169 | 169
FY24 National average | 132 | 132 | 132 | 132 | 132 | 132 | 132 | 132 | 132 | 132 | 132
Payable days (days) have decreased substantially across states after the introduction of LPS Rules
Outstanding dues payable by Discoms for power purchase
Jun’22-Jan’25, USD Bn

## Slide 92
4.6 | OUTLOOK FOR SHORT-TERM MARKET IN INDIA

## Slide 93: Indian electricity market | Outlook on short-term power market
Short-term market volumes are expected to grow at a CAGR of 12-14% CAGR over 6 years
Sources: CERC, MoP, Power Exchanges, Deloitte Analysis
The growth is driven by procurement by Discoms, deepening of the exchange market, excess RE generation, increase in FDRE projects and C&I procurement
Key growth drivers
Chart: 
| FY19 | FY20 | FY21 | FY22 | FY23 | FY24 | FY30 E
billion units | 1375.86 | 1390.93 | 1380.06 | 1491.85 | 1624.47 | 1738 | 2536
Chart: 
| FY19 | FY20 | FY21 | FY22 | FY23 | FY24 | FY30 E (Scenario 1) | FY30 E (Scenario 2)
Short term market volume (bn kWh) | 145.2 | 137.16 | 146.01 | 186.75 | 194.35 | 217 | 380 | 507
% share in total demand | 0.10553 | 0.09861 | 0.1058 | 0.12518 | 0.11964 | 0.12 | 0.13 | 0.15 | 0.2
India’s power demand is expected to register 6-7% CAGR growth over FY24 to FY30
Share of short-term transactions in overall demand is likely to rise to 15%-20% by FY30
1
2
3
4
Increase in short-term procurement by Discoms
Rise in exchange-based transactions with deepening of the spot markets
Excess RE generation with increase in tendering of RTC, hybrid, FDRE tenders
Increase in C&I consumption driven by sustainability targets and innovative products like VPPAs

## Slide 94: Indian electricity market | Rise in exchange-based transactions
New exchange segments (RTM, GDAM, GTAM etc.), new exchange (HPX), and electricity derivatives will boost short-term market volumes
Sources: CERC, MoP, Power Exchanges, Deloitte Analysis
Exchange based transactions have clocked ~14% CAGR over FY18 to FY24 driven by launch of new products
Chart: 
| FY18 | FY19 | FY20 | FY21 | FY22 | FY23 | FY24
billion units | 48 | 54 | 56 | 80 | 101 | 103 | 120
Along with traditional day ahead market (DAM) and term ahead market (TAM) products, exchanges have launched new products
  Real time market (RTM): half-hourly auctions helping discoms and large consumers to manage requirement in real-time, generators to sell excess power in real-time
  Green day ahead (GDAM) and Green term ahead (GDAM): Exclusively for solar and non-solar renewable power enabling discoms and RE generators to sell excess RE power and industries and utilities to buy clean energy to meet RPO
  Ancillary services (DAM-AS and RTM-AS): capacity procurement by National load dispatch center (NLDC)
  High price DAM and TAM: Separate market for costly power with cap of INR 20/kWh and floor price of zero
Chart: 
| FY18 | FY19 | FY20 | FY21 | FY22 | FY23 | FY24 E
Nos | 4248 | 4362 | 4555 | 4768 | 4967 | 5159 | 5200
Rising number of open access consumers registered on exchanges to drive short term volumes
Started in 2008, largest exchange in India, ~85% market share (in FY24)
Started in 2009, ~3-4% market share
Newly launched exchange to drive competitions

## Slide 95
4.7 | VIEW ON THE FUTURE MARKET CLEARING PRICES IN LIGHT OF INCREASE IN RENEWABLES

## Slide 96: Electricity demand in India (1/2)
India’s fast-growing economy drove strong electricity demand growth FY20–FY25, with renewable energy playing a major role in meeting the demand
Sources: CEA, MoP, MNRE, Deloitte Analysis
Electricity demand
FY20-25, TWh
With a growing economy, the demand for electricity has also increased at a robust rate of growth
While thermal power generation has remained the main stay of electricity generation in India, that from renewable energy sources has nearly doubled in the last 5 years
Chart: 
| Thermal | Hydro | Nuclear | Renewables
FY20 | 1042838 | 155769 | 46472 | 138337
Total:
1,383 TWh
RE:
138 TWh
Chart: 
| Thermal | Hydro | Nuclear | Renewables
FY25 | 1363000 | 149000 | 57000 | 252000
Total:
1,821 TWh
RE:
252 TWh
Gross electricity generation in India (TWh)
Chart: 
| FY20 | FY21 | FY22 | FY23 | FY24 | FY25(e)
Series 1 | 1291 | 1276 | 1380 | 1512 | 1629 | 1690
Chart: 
| FY20 | FY21 | FY22 | FY23 | FY24 | FY25
Series 1 | 184 | 190 | 203 | 216 | 243 | 250
Chart: 
| FY20 | FY21 | FY22 | FY23 | FY24 | FY25
Series 1 | 1208 | 1161 | 1255 | 1331 | 1395 | 1538
5.5% CAGR
6.3% CAGR
4.9% CAGR
Electricity generation capacity addition in India (GW)
Chart: 
| Thermal | Hydro | Nuclear | Renewables
FY20 | 230 | 46 | 7 | 87
Chart: FY25 (as of Jun’26)
| Thermal | Hydro | Nuclear | Renewables
FY25 | 240 | 48 | 8.8 | 178.9
Total:
370 GW
RE:
87 GW
Total:
475 GW
RE:
179 GW
CAGR
5.7%
CAGR
5+%
Electricity peak demand
FY20-25, GW
Per capita electricity consumption
FY20-25, kWh
Chart: 
| Thermal | Large hydro | Nuclear | Renewables
FY24 | 1326549 | 134054 | 47937 | 225835

## Slide 97: Electricity demand in India (2/2)
Electricity demand is expected to grow at a CAGR of 5.5%from FY24–FY30, requiring additional ~621 TWh supply to meet FY30 demand
Sources: Central Electricity Authority (CEA), Ministry of Power (MoP), Ministry of New and Renewable Energy, (MNRE), Deloitte Analysis
India’s GDP grew at a CAGR of ~5.5% between FY16 and FY24, even with the slowdown during the COVID-19 period. This indicates a resilient and steadily growing economy over the eight-year span, despite the significant economic challenges posed by the pandemic
Historically, the demand for electricity grew at a rate of ~0.9 times the GDP growth rate
At the same time, India steadily reduced the demand-supply deficit from ~2.1% in FY16 to 0.4% in FY24 by increasing the power generation capacity.
Chart: 
 | 1114.408 | 1274.595 | 1379.812 | 1511.847 | 1629 | 2246.1349 | 2799.0928
 | 1090.85 | 1267.526 | 1374.024 | 1504.264 | 1625
FY16
FY19
FY22
FY23
FY24
FY30P
FY35P
4.9% CAGR
+4.5%
2.1%
0.6%
0.4%
0.6%
0.4%
Outlook on electricity base demand growth in India by FY30
FY16-30, TWh
Note: FY: Financial year (April to March), GDP: Gross domestic product, TWh: trillion-watt-hour, CAGR: Compound annual growth rate, P: Projections
Supply deficit
621
Incremental electricity supply (TWh) needed to meet demand in FY30
Demand
Supply
5.5% CAGR

## Slide 98: Peak power demand outlook in India
Peak electricity demand is expected to vary widely due to higher share of intermittent renewables, climate change, and limited thermal flexibility
Sources: Central Electricity Authority (CEA), Ministry of Power (MoP), Ministry of New and Renewable Energy, (MNRE), Deloitte Analysis
Outlook on electricity peak demand growth in India
FY16-30, GW
Note: FY: Financial year (April to March), GW: giga-watt, CAGR: Compound annual growth rate, P: Projections
Seasonal variations lead to demand variations across different months of the year
Electricity demand also varies across different months on account of other factors such as increase in agricultural demand in the August to November period
Peak electricity demand increased by ~14% in FY24 vis-a-vis FY23, which is one of highest on-year increases in peak demand over past decade
Going forward, peak demand is expected to reach ~334 GW by FY30 largely led by increased industrial and household consumption
Chart: 
 | 153 | 177 | 203 | 213 | 243 | 334 | 416.2248
 | 149 | 176 | 201 | 211 | 240
Peak demand
Peak met
3.2%
0.8%
1.0%
0.9%
1.2%
Peak deficit
94
Incremental firm supply (GW) needed to meet peak demand in FY30
6% CAGR
+4.5%
5.4% CAGR
FY16
FY19
FY22
FY23
FY24
FY30P
FY35P

## Slide 99: Capacity additions projection till FY40
Solar and wind are expected to make up 57% of capacity by FY35 and 64% by FY40, increasing the need for long-duration energy storage.
Sources: Central Electricity Authority (CEA), Ministry of Power (MoP), Ministry of New and Renewable Energy, (MNRE), Deloitte Analysis
Long-term capacity additions projections
FY24-40P, GW
Note: FY: Financial year (April to March), GW: giga-watt, P: Projections
Chart: 
 | 210.9695 | 230.0495 | 250 | 270
 | 6.62 | 6.62 | 5 | 5
 | 25.0382 | 25.0382 | 21 | 18
 | 0.5892 | 0.5892 | 0 | 0
 | 8.18 | 10.18 | 13 | 18
 | 46.9282 | 48.9282 | 54 | 63
 | 81.8136 | 225.8136 | 376 | 570
 | 45.8865 | 77.3865 | 100 | 140
 | 15.9443 | 16.2944 | 17 | 22
22
18
0
10
FY30P
FY35P
FY40P
442
FY24
641
1
8
16
1
47
46
16
836
1,106
17
13
0
49
18
+45.0%
+30.4%
+32.3%
Solar
Coal
Nuclear
Lignite
Gas
Diesel
Hydro
Wind
Other RE
29%
(in-firm RE share)
47%
(in-firm RE share)
57%
(in-firm RE share)
64%
(in-firm RE share)

## Slide 100: Spot price dynamics: Dry vs wet season pricing
During the wet season in Nepal, spot electricity prices on IEX range from INR 2.1 / kWh in solar hours to INR 7.8/ kWh during the evening peak
Sources: Central Electricity Authority (CEA), Ministry of Power (MoP), Ministry of New and Renewable Energy, (MNRE), Deloitte Analysis
The wet season for Nepal overlaps with Indian wet season (May-Dec), which has lower prices driven by higher renewable generation and reduced agricultural and HVAC demand
Note: FY: Financial year (April to March), GW: Giga-Watt, CAGR: Compound Annual Growth Rate, P: Projections
Average day ahead market clearing price during wet season when excess electricity is available (Jun to Sep/ Oct) or 16th Jeshta to Ashwin– 5 months
Jun-Oct’22 – Jun-Oct’24, INR/kWh
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | 6.7785 | 5.6855 | 4.9346 | 4.4761 | 4.6321 | 5.3665 | 5.8731 | 4.9364 | 3.7268 | 3.3415 | 3.2718 | 3.2849 | 3.25 | 3.1314 | 3.6962 | 4.4196 | 4.5682 | 4.8734 | 7.4501 | 9.7335 | 8.7279 | 8.6006 | 8.3611 | 7.7949
 | 7.6614 | 6.8588 | 6.0643 | 5.3693 | 5.2457 | 5.7258 | 5.9872 | 5.1434 | 4.1359 | 4.0516 | 3.843 | 3.7813 | 3.7556 | 3.6984 | 4.3324 | 4.8911 | 5.2377 | 5.5206 | 6.508 | 8.2824 | 8.3321 | 8.6695 | 8.6863 | 8.4976
 | 6.7798 | 5.4424 | 4.4723 | 4.0895 | 4.0694 | 3.8498 | 4.3076 | 3.5917 | 2.9135 | 2.6159 | 2.3851 | 2.2538 | 2.1449 | 2.1125 | 2.7035 | 3.1549 | 3.4637 | 3.9101 | 5.2851 | 7.8143 | 8.1301 | 8.3962 | 8.163 | 7.9245
4.48
4.94
3.13
9.73
7.81
8.36
Jun’22 to Oct’22
Jun’23 to Oct’23
Jun’24 to Oct’24
Solar hours consistently show lower prices due to higher solar generation during morning 10 AM to evening 4 PM coinciding with moderate demand.
Wet season prices (May-Dec) are even lower during solar hours due to:
  Increased hydropower during monsoon.
  High wind generation (June–Sept).
  Reduced agricultural and HVAC loads due to cooler weather and rain-fed irrigation.
With rising share of renewables, especially solar energy, in India’s electricity generation mix, market clearing prices of electricity in power exchanges, particularly in the solar hours (10 AM to 5 PM) are likely to decrease over the long term to reach about average of INR 1.5 per kWh (nominal tariff) while tariff in evening and night hours are likely to be in the range of INR 5 to 7 per kWh (nominal tariff) by 2040
MORNING PEAK
SOLAR HOURS
NIGHT HOURS
EVENING PEAK
NIGHT

## Slide 101
ANNEXURE
Deloitte refers to one or more of Deloitte Touche Tohmatsu Limited, a UK private company limited by guarantee (“DTTL”), its network of member firms, and their related entities. DTTL and each of its member firms are legally separate and independent entities. DTTL (also referred to as “Deloitte Global”) does not provide services to clients. Please see www.deloitte.com/about for a more detailed description of DTTL and its member firms.
This material has been prepared by Deloitte Touche Tohmatsu India LLP (“DTTI LLP”), a member of Deloitte Touche Tohmatsu Limited, on a specific request from you and contains proprietary and confidential information. This material may contain information sourced from publicly available information or other third -party sources. DTTI LLP does not independently verify any such sources and is not responsible for any loss whatsoever caused due to reliance placed on information sourced from such sources. The information contained in this material is intended solely for you. Any disclosure, copying or further distribution of this material or its contents is strictly prohibited.
Nothing in this material creates any contractual relationship between DTT ILLP and you. Any mutually binding legal obligations or rights may only be created between you and DTTI LLP upon execution of a legally binding contract. By using this material and any information contained in it, the user accepts this entire notice and terms of use.
©2025 Deloitte Touche Tohmatsu India LLP. Member of Deloitte Touche Tohmatsu Limited
Deloitte Touche Tohmatsu India Private Limited (U74140MH199 5PTC093339), a private company limited by shares, was converted into Deloitte Touche Tohmatsu India LLP, a limited liability partnership (LLP Identification No. AAE-8458),with effect from October 1, 2015.

## Slide 102: Annexure-1
Analysis of the supply and demand trends in electricity sales to India in past years
Key Inferences | 
Power export has been increased from 494 GWh in FY 2021-22 to 1943 GWh in FY 2023-24 at a CAGR of 58%. Exports to India in recent years has increased from the months of Mid-June to and mid-December and reaching peak around mid-September. Then after the dry season (mid December to mid May) in which there is minimal export; the power export gradually increase and reaches to peak levels In FY 2023-34, Nepal has become Net exporter of power to India. | 

## Slide 103: Annexure-2
Analysis of the transmission utilization of 400kV Dhalkebar-Muzzafarpur lines
Key Inferences | 
400kV Dhalkebar-Muzzafarpur line is the first 400kV transmission link between India and Nepal and has been playing a pivotal role in India-Nepal cross-border electricity trade. Initially designed for capacity of 600 MW, the lines capacity was upgraded to 800 MW and then to1000 MW. Considering 1000 MW as the Annual Transmission Capacity (ATC) and Total Transmission Capacity (TTC) for the 400kV Dhalkebar-Muzzafarpur line, the utilization during the dry months (June 2024 to November 2024) are in the range of 75%-85%. | 
Chart: Utilization trends of 400kV Dhalkebar-Muzzafarpur lines (in MW)
| June | July | August | September | October | November
Max | 676 | 794 | 856 | 868 | 462 | 556
Min | 0 | 18 | 229 | 30 | 0 | 1
Avg | 267.2667 | 594.7097 | 626.9032 | 608.6667 | 257.2903 | 278.1154

## Slide 104: Key drivers to promote increased CBET between Nepal and India
Some of the key drivers for CBET are includes increase in electricity demand in India and Hydro Purchase Obligations
Source: CEA National Electricity Plan, Renewable Purchase Obligation (RPO) and Energy Storage Obligation Trajectory till 2029-30 - Ministry of Power
Rising Electricity Demand in India
As per 20th EPS report and National Electricity Plan by CEA, India’s projected electricity demand growth is 6.67% for FY22-27 and 5.33 % for FY27-32
Peak demand in India projected to increase to 366 GW by 2031-32 and energy requirement is expected to reach 2,538 BU by 2031-32
India’s target of 500 GW non-fossil fuel capacity by 2030 creates demand for firm green energy.
Cross-border participation allowed in DAM, TAM, RTM, GDAM via CERC framework
Hydro Purchase Obligations (HPO)
DISCOMs, captive and open access consumers are obligated to procure power from hydro power projects, to reach 1.33% by 2029-30
Only hydro energy from projects commissioned after 31st March 2024 qualifies towards the hydro renewable energy obligation.
Cross-Border Sourcing:
Hydro energy from projects outside India can be counted if approved by the Central Government/CEA.
Nepal’s hydro aligns with India’s clean energy compliance needs, creating strong demand for hydro imports from Nepal.
“ Projected growth in Nepal’s hydroelectric generating capacity can complement India’s growing variable renewables “
Chart: 
 | 1381646 | 1907835 | 2473776
 | 203115 | 277201 | 366393
203,115
2021-22
277,201
2026-27
366,393
2031-32
+6%
Energy Requirement (MU)
Peak Demand (MW)
India’s Demand & Energy Requirement as per National Electricity Plan

## Slide 105: How can Nepal Emerge as a CBET Champion?
To be added..
Policy & Regulatory Readiness
Enhance Grid Code Compatibility
Open Access Licensing
CBET-specific licensing structure to allow market-based trade, beyond bilateral PPAs
Infrastructure Strengthening
High-Capacity Interconnections
Exploration of more regional power corridors
Regional Grid Synchronization
Institutional Strengthening
Empower NEA & encourage IPPs to trade more on Indian markets
Dedicated G2G-cum-market power trading entity, modeled on Bhutan Power Corporation or PTC India

## Slide 106: PJ_ST Project | Salient Features
Salient Features of the STHPP
Particulars | Details
Capacity (Unit Configuration) | 100 MW
Location | 100km west of Kathmandu on Prithvi highway Gorkha-Zone, Chitwan District
Latitude & Longitude | 27’51’38.45 N and 84’38’38.31” E
Project Type | Run of River type project with Dam Toe Powerhouse arrangement.
Current Status | Under Construction
Expected COD | 2027
Current Ownership | Licensed to Blue Energy Ltd. on BOOT basis for 35 years
Technical Details | Gross head - 21m, Design discharge - 725m3/sec Annual energy - 498 million units
Transmission Evacuation details | About 18.8 km long 220kV double circuit transmission line to New Markichauk substation
Estimated Project Cost | 24 billion Yen
Photo Credit – Blue Energy
Photo Credit – Blue Energy

## Slide 107: PJ_ST Project | Transmission Evacuation of the project
Salient Features of the STHPP
Particulars | Details
Capacity (Unit Configuration) | 100 MW
Location | 100km west of Kathmandu on Prithvi highway Gorkha-Zone, Chitwan District
Transmission Evacuation details | About 18.8 km long 220kV double circuit transmission line to New Markichauk substation
Photo Credit – Blue Energy
Photo Credit – ESRI
The project is located in between the Demand Centres of Kathmandu (100 km) and Pokhara (109 km).
This river basin is one of the most developed basins in Nepal.
The project's strategic location helps reduce the congestion in the transmission network, facilitates its optimal year-round utilization, and contributes to more efficient load management, thereby enhancing overall grid stability and reliability.
Strategic Location of the project
As per the DPR, 220/132 kV New-Marsyangdi (Marki Chowk) substation has been most optimised transmission network for evacuation of 100 MW power from PJ_ST Project .
220/132 kV New-Marsyangdi (Marki Chowk) substation, located in Tanahun, Nepal, was officially energized on January 2, 2025.
Based on the discussion with NEA and Breeze, the transmission infrastructure development for this project is on track.
Current Status of the transmission evacuation
infrastructure of the project

## Slide 108: PJ_ST Project | Financial Features
Financial Features of the STHPP
Particulars | Details
Debt: Equity Ratio | 75 : 25
Term Loan Period | 15 Years
Annual O&M Cost (for electromechanical equipments) | 2% of project cost
Annual O&M Cost (for civil works) | 1% of project cost
Office Running Costs | 0.1% of project cost (expenses in water bills, telephone, furniture, office equipments, etc.)
Insurance | 0.25% of project cost
Annual Depreciation | 3.7% for all the civil structures, electromechanical equipment and transmission line components
Source: Detailed Project Report – Executive Summary

## Slide 109: Summary of Stakeholder Consultations…1/3
Deloitte team had conducted visit to Nepal and had consultations with key stakeholders
Discussions with NEA
Queries | Response | Remarks / Implications
We understand the 70 MW has been contracted by NEA as per PPA. Has there been any discussion with them for assistance in sale of remaining 30 MW through IEX? In the event that CBET (Cross Border Electricity Trade) clearance faces delays or challenges, would NEA be willing to consider scheduling the 30 MW uncontracted capacity domestically as an interim measure? Is there sufficient transmission capacity to offtake 100 MW from the planned tranmsission lines? | Currently 70 MW is structured as Take or Pay and 30 MW is structured as Take and Pay. For the 30 MW portfolio, if NEA buys it will be pay as per the PPA rates. In the existing policy scenario, following are the possible options Domestic Sale - 30 MW is only possible during the wet season. But, if there is domestic requirement, NEA will buy as per PPA rates. However, if NEA is having domestic wet season surplus , then there will be an option of power exports. Power Exports - Currently NEA is the only agency who undertakes import/export. In case, NEA sells power from the project (if approved by the GOI), NEA will compensate the project as per PPA rates and not on the actual off-take rate in the export market. As per the PPA first Amendment, during the wet season, NEA is obligated to buy only 90% of the availability and the remaining will be reserve margin. NEA will not pay for the reserve margin in case not purchased. | Probability of Sale of excess power via cross border mechanism during wet season is subject to availability of domestic wet season surplus for NEA. In case, NEA is opting for the CBET, the developer will be paid only the PPA Rates which results in no benefits for the project developer even if there is power export in the CBET mode, but it assures revenue recovery in PPA Tariff.
Queries | Response | Remarks / Implications
As per the Generation License, any alteration or change in the ownership structure of the organization requires prior approval from the Department of Electricity Development (DoED). In this regard, please clarify the process for obtaining this approval, including any documentation requirements, timelines, and potential limitations that developers should be aware of? | Since the Generation License includes the provision that mandates the prior approval from the Department of Electricity Development (DoED), the same should be attained. It requires submission of Net Worth certificate, attested by a CA. Approval process usually takes 1 week, if all documents are in order. There is no specified format. | Needs to initiate the process
Discussions with DoED

## Slide 110: Summary of Stakeholder Consultations…2/3
Deloitte team had conducted visit to Nepal and had consultations with key stakeholders
Discussions with ERC
Queries | Response | Remarks / Implications
Please outline the Share Agreement approval process for hydropower projects, including key steps, involved authorities, and tentative timelines | Prior approval from ERC is required for share transfer beyond 5%. The process usually takes 15 days. | Needs to initiate the process
Please provide status on the introduction of electricity trading licenses in Nepal | ERC has currently floated the draft Open Access directives for comments. It is kept open for 2 months. It may take another 4-6 months for approval. Trading licenses may be taken subsequently take it is very closely linked with Electricity Bill. Since trading is not a recognized licensing activity currently in Nepal, government may wait for the Electricity bill to recognize it and then take steps to operationalize the trading licenses. | 
We understand that the Draft Open Access Regulations have been published for Stakeholder comments. By when does the ERC expect for operationalizing of the same? | 4-6 months | 
Discussions with WECS
Queries | Response | Remarks / Implications
Please share insights on the current Project Priority Matrix for hydropower development in Nepal? | Very confidential document and not be released by the government. | 

## Slide 111: Summary of Stakeholder Consultations…3/3
Deloitte team had conducted visit to Nepal and had consultations with key stakeholders
Discussions with IPPAN
Queries | Response | Remarks / Implications
Please provide your views on NEA’s payment consistency to IPPs | NEA is very consistent with payment and is usually done with 45 days. As per IPPAN, there hasn’t been any event of default by NEA | There is no risk envisaged
Are there any issues in extension of RCOD by NEA? If yes, then what are the remedies that IPPAN is pursuing with authorities? Are there any specific issues which NEA is not accepting for RCOD extension? | RCOD extension has been provided to generating companies (IPPs) once due to COVID. Any RCOD extension will be done by NEA, only due to two reasons: Force Majeure - As specified under PPA NEA's non-fulfilment of its obligations like delay in transmission infrastructure. Applications are usually submitted to NEA 2-3 months before the RCOD. As per discussion with Breeze, they mentioned that the project was impacted by flood and the study of impact has been conducted by them. RCOD extension on account of flood will have to meet the following criteria – “in excess of the one-hundred-year Design Flood Discharge mentioned in Schedule 1" | This needs action from Breeze to submit the application to NEA for RCOD extension.
Can IPPAN shed light on the issue of handover of projects to NEA which have completed their lifespan? What does original condition clause entail when the process of handover is initiated? Are there any discussions in NEA/DOED/Ministry on this issue and possible solutions? | Handover is usually considered under "good working condition". | Currently, there is no risk envisaged

## Slide 112: List of IPPs involved in Cross Border Electricity Trade (CBET)…1/2
List of projects approved by Central Electricity Authority, India for CBET
Source: CEA
Sl. No. | Project Name | Quantum (MW) | Project Type | Transaction | PX Segment/ Buyer
1 | Devighat Hydropower Project | 14.55 | NEA | Power Exchange | DAM and RTM
2 | Trishuli Hydropower Project | 23.28 |  | Power Exchange | DAM and RTM
3 | Marsyangdi Hydropower Project | 67 |  | Power Exchange | DAM and RTM
4 | Middle Marsyangdi Hydropower Project | 68 |  | Power Exchange | DAM and RTM
5 | Kaligandaki ‘A’ Hydropower Project | 140 |  | Power Exchange | DAM and RTM
6 | Upper Dordi | 24.25 | IPP | Power Exchange | DAM and RTM
7 | Lower Modi | 19.4 |  | Power Exchange | DAM and RTM
8 | Dordi Khola | 26.19 |  | Power Exchange | DAM and RTM
9 | Solu Khola | 83.42 |  | Power Exchange | DAM and RTM
10 | Upper Balephi ‘A’ | 34.92 |  | Power Exchange | DAM and RTM
11 | Solu Hydropower Project | 22.8 |  | Power Exchange | DAM and RTM

## Slide 113: List of IPPs involved in Cross Border Electricity Trade (CBET)…2/2
List of projects approved by Central Electricity Authority, India for CBET
Source: CEA
Sl. No. | Project Name | Quantum (MW) | Project Type | Transaction | PX Segment/ Buyer
12 | Chilime Hydropower Project | 21.44 | IPP (Subsidiary of NEA) | Power Exchange | DAM and RTM
13 | Likhu IV Hydropower Project | 51 | IPP | Power Exchange | DAM and RTM
14 | Kabeli B-1 Hydro Power Project | 24.25 |  | Power Exchange | DAM and RTM
15 | Lower Modi Hydro Power Project | 19.4 |  | Power Exchange | DAM and RTM
16 | Upper Kalangagad Hydro Power Project | 32.7 |  | Power Exchange | DAM and RTM
17 | Upper Chameliya | 38.8 |  | Power Exchange | DAM and RTM
18 | Likhu-1 HPP | 75 | IPP | Bilateral | Haryana
19 | Solu Khola (Dudhkoshi) Hydro Power Project | 83.42 |  | Bilateral | Haryana
20 | Dordi Khola Hydro Power Project | 26.19 |  | Bilateral | Haryana

## Slide 114: Nepal’s Seasonal Generation Variations and Energy Balance
Nepal tends to import heavily power during the dry seasons (between December- June)
Source - NEA Annual Report;
Chart: 
 | 10 | 1 | 1 | 1186 | 27 | 163 | 324 | 395 | 349 | 357 | 188 | 19
 | 1467 | 1452 | 1456 | 0 | 949 | 727 | 657 | 592 | 642 | 836 | 1212 | 1612
 | -256 | -305 | -418 | -380 | -114 | 0 | 0 | 0 | 0 | 0 | -68 | -401
Jul-Aug (Shrawan)
1
Aug-Sep
1
Sep-Oct
0
Oct-Nov
Nov-Dec
0
Dec-Jan
0
Jan-Feb
0
Feb-Mar
0
Mar-Apr
10
Apr-May
-68
May-Jun
19
Jun-Jul
1,221
1,148
1,039
806
862
890
981
987
991
1,193
1,332
1,230
0
Monthly System Energy Demand (IPP+NEA+NEA Sub+Storage+Thermal+Interruption)
Import
Export
Monthly Energy Balance Curve 2024 (GWh)
Key Inferences | 
Nepal’s power import-export variations are directly linked with the climatic seasonal variations – tends to export hydro based surplus power during the rainy season and import deficit during the dry months This variation indicates heavy reliance of capacity mix on the ROR projects necessitating more push for storage based and other renewable solutions | 

## Slide 115: Power exchanges in India
Source: Deloitte analysis
2008
2008
2022
Public
Public
Public
Yes; NSE and BSE*
No
No
Chart: 
| Promoters | Government | Bodies corporate
Column1 | 0.6341 | 0.2333 | 0.1325
Chart: 
| Promoters | Government | Bodies corporate
Column1 | 0.5439 | 0.2333 | 0.1325
Chart: 
| Individuals | Bodies corporate | Mutual funds | Financial investors | FII | Others
Column1 | 0.3426 | 0.1784 | 0.1361 | 0.0509 | 0.001 | 0.291
Launch year
Ownership
Public listing
Shareholding pattern
Key investors
*NSE=National Stock Exchange; BSE=Bombay Stock Exchange

## Slide 116: IEX membership
Membership of power exchange requirements
Source: Deloitte analysis
Trader member
Entity holding a valid inter-state trade license from CERC
Entity can trade & clear for its own account and on behalf of its clients
1
2
3
Proprietary member
Entity should be a grid connected entity
Entity can trade for its own account, and clear those contracts
Facilitator member
Entity who is neither a trade licensee or a grid connected entity
Cannot trade for itself but can act on behalf of clients and cannot clear contracts
Category
Eligible transaction
Electricity trader
REC trader
ESCerts trader
Electricity + REC + ESCerts
REC + ESCerts
ESCerts
Net worth required (INR Mn)
150
50
50
Category
Eligible transaction
Electricity trader
REC trader
ESCerts trader
Electricity + REC + ESCerts
REC + ESCerts
ESCerts
Net worth required (INR Mn)
150
-
-
Category
Eligible transaction
Electricity trader
REC trader
ESCerts trader
Electricity + REC + ESCerts
REC + ESCerts
ESCerts
Net worth required (INR Mn)
150
50
50

## Slide 117: Trading durations for different market segments on IEX
Source: IEX, Deloitte analysis
Segment | Type of contract | Description | Trading hours | Price discovery
DAM & G-DAM | - | Block-wise, next day | Auction timing: 10:00 to 12:00 hours | Closed, double-sided auction
TAM & G-TAM | Day Ahead Contingency | Hourly and/or block-wise, next day | 15:00 to 23:00 hours | 
 | Intra-day |  | TAM: 00:30 to 20:30 hours G-TAM: 00:00 to 24:00 hours | 
 | Daily | Full day, T+2 onwards (beyond T+11) | 12:00 to 17:00 hours | 
 | Weekly | Weekly, T+5 to T+11/weekly, weekdays and weekend |  | 
 | Fortnightly | 15 days (First half or second half of month) | 12:00 to 17:00 hours on trading days | 
 | Monthly | Monthly, quarterly, half-yearly, yearly, etc. |  | 
 | Any-day | Any-day and any block: user defined |  | 
 | Any-day single sided |  | On trading day | Reverse and forward auction bidding
RTM | - | Block-wise | 22:45 to 23:00 then 23:15 to 23:30 hours and so on. | Closed, double-sided auction

## Slide 118: Power exchange - IEX
Fees and deposit structure
Source: IEX, Deloitte analysis
Segment – Type of Membership | Electricity (Trader/Facilitator/Proprietary) | REC (Trader/Facilitator/ Proprietary) | ESCerts (Trader/Facilitator/ Proprietary)
Eligible for Trading | Electricity + REC + ESCerts | REC + ESCerts | ESCerts
Admission Fee | 3.5 | 1 | 0.5
Security Deposit | 2.5 | 0.5 | 2.5
Processing Fee | 0.01 | 0.51 | 0.01
Annual Subscription Fee | 0.5 | 0.2 | 0.1 (Per Pat cycle)
IEX Transaction Fee (Rs/MWh or REC or ESCerts) | 2 | 2 | 2
Annual Client /Portfolio Subscription Fee | 0.1 | 0.02 | 0.020(Per Pat Cycle)
Minimum Net Worth | 15 (Only for Facilitator and Proprietary member) | 5 (Only for Facilitator member) | 5 (Only for Facilitator member)

## Slide 119: Power exchange - PXIL
Fees and deposit structure
Source: PXIL, Deloitte analysis
 | ALL SEGMENT (PHYSICAL, REC & ESCERTS) (In INR) |  |  |  | )
Sr. | Fees Structure | TM | PM | FM | Client
1 | Processing Fees | 5,000 | 5,000 | 5,000 | -
2 | One Time Fees | 10,00,000 | 10,00,000 | 2,50,000 | -
3 | Annual Fees | 2,50,000 | 2,50,000 | 1,00,000 | 1,00,000
4 | ISD | 40,00,000 | 25,00,000 | - | -
5 | Total Amount (1+2+3+4) | 52,55,000 | 37,55,000 | 3,55,000 | 1,00,000
6 | Goods and Service tax* @ 18 % on Fees amount (1+2+3) | 2,25,900 | 2,25,900 | 63,900 | 18,000
7 | Total Fees (5+6) | 54,80,900 | 39,80,900 | 4,18,900 | 1,18,000
 | GREEN SEGMENT (REC , GREEN PHYSICAL / G-TAM & ESCERTS ) (in INR) |  |  |  | 
Sr. | Fees Structure | TM | PM | FM | Client (Applicable to: REC Only Seller ESCERTS Buyer & Seller)
1 | Processing Fees | 5,000 | 5,000 | 5,000 | -
2 | One Time Fees | 6,50,000 | 6,50,000 | 2,50,000 | -
3 | Annual Fees | 1,00,000 | 1,00,000 | 50,000 | 20,000
4 | ISD | 2,00,000 | 2,00,000 | - | -
5 | Total Amount (1+2+3+4) | 9,55,000 | 9,55,000 | 3,05,000 | 20,000
6 | Goods and Service tax* @ 18 % on Fees amount (1+2+3) | 1,35,900 | 1,35,900 | 54,900 | 3,600
7 | Total Fees (5+6) | 10,90,900 | 10,90,900 | 3,59,900 | 23,600
 | ESCERTS SEGMENT Only (in INR) |  |  |  | 
Sr. | Fees Structure | TM | PM | FM | Client
1 | Processing Fees | 5,000 | 5,000 | 5,000 | -
2 | One Time Fees | 5,00,000 | 5,00,000 | 2,00,000 | -
3 | Annual Fees | 80,000 | 80,000 | 45,000 | 20,000
4 | ISD | 2,00,000 | 2,00,000 | - | -
5 | Total Amount (1+2+3+4) | 7,85,000 | 7,85,000 | 2,50,000 | 20,000
6 | Goods and Service tax* @ 18 % on Fees amount (1+2+3) | 1,05,300 | 1,05,300 | 45,000 | 3,600
7 | Total Fees (5+6) | 8,90,300 | 8,90,300 | 2,95,000 | 23,600
PXIL offers a volume-based incentive on the transaction fee on all trades
The volume slabs of the incentive rate are given below:
Monthly cleared volumes (MU) | Rate of Incentive as% of Transaction fees
<=30 | 15
>30 to <=180 | 20
>180 | 25

## Slide 120: Double sided closed bid uniform price auction
Source: Deloitte analysis
Sample bids (buy/ sell)
INR/ MWh, MW
Bids | Price/ Quantity | P/ Q 1 | P/ Q 2 | P/ Q 3 | P/ Q 4
Buy bid 1 | Price | - | 3,000 | 8,000 | 20,000
 | Quantity | 200 | 200 | 100 | 50
Buy bid 2 | Price | - | 2,000 | 6,000 | 20,000
 | Quantity | 200 | 120 | 80 | 10
Sell bid 1 | Price | - | 2,000 | 4,000 | 20,000
 | Quantity | - | (50) | (100) | (140)
Sell bid 2 | Price | - | 3,000 | 6,000 | 20,000
 | Quantity | - | (90) | (150) | (200)
Bids | Price/ Quantity | P/ Q 1 | P/ Q 2 | P/ Q 3 | P/ Q 4 | P/ Q 5 | P/ Q 6
Buy bid 1 | Price | - | 2,000 | 3,000 | 6,000 | 8,000 | 20,000
 | Quantity | 200 | 200 | 200 | 140 | 100 | 50
Buy bid 2 | Price | - | 2,000 | 3,000 | 6,000 | 8,000 | 20,000
 | Quantity | 200 | 120 | 110 | 80 | 70 | 10
Sell bid 1 | Price | - | 2,000 | 3,000 | 4,000 | 6,000 | 20,000
 | Quantity | - | (50) | (75) | (100) | (105) | (140)
Sell bid 2 | Price | - | 2,000 | 3,000 | 4,000 | 6,000 | 20,000
 | Quantity | - | (60) | (90) | (110) | (150) | (200)
Bids | Price/ Quantity | P/ Q 1 | P/ Q 2 | P/ Q 3 | P/ Q 4 | P/ Q 5 | P/ Q 6
Buy bid | Price | - | 2,000 | 3,000 | 6,000 | 8,000 | 20,000
 | Quantity | 400 | 320 | 310 | 220 | 170 | 60
Sell bid | Price | - | 2,000 | 3,000 | 4,000 | 6,000 | 20,000
 | Quantity | - | (110) | (165) | (210) | (255) | (340)
Chart: 
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400
 | 20000 | 15500 | 10000 | 7000 | 5000 | 3000 | 1500 | 0
 | 0 | 1000 | 2000 | 3000 | 4000 | 6000 | 13000 | 20000
Aggregate buy
Aggregate sell
Bids | Quantity
Buy bid 1 | 153.33
Buy bid 2 | 86.67
Sell bid 1 | (103.33)
Sell bid 2 | (136.67)
Aggregated buy and sell curves cut each other to give area clearing price and volume (i.e., INR 5,333/ MWh and 240 MW
Bid volume allocations
MW
Aggregate line curves (buy/ sell)
INR/ MWh, MW
Aggregate bids (buy/ sell)
INR/ MWh, MW
Processed sample bids (buy/ sell)
INR/ MWh, MW
For aggregation of buy/ sell bids, quantity at certain price points in bids has been calculated using the straight-line equation

## Slide 121: Continuous matching algorithm
Source: Deloitte analysis
Sample bids (buy/ sell)
INR/ MWh, MW
Buy bids |  | 
Buyer | Buy price | Buy qty.
Buyer 1 | 3,000 | 500
Buyer 2 | 3,200 | 400
Buyer 3 | 3,300 | 300
Buyer 4 | 2,800 | 200
Buyer 5 | 2,500 | 300
Sell bids |  | 
Seller | Sell price | Sell qty.
Seller 1 | 3,500 | 200
Seller 2 | 4,000 | 300
Seller 3 | 4,200 | 500
Seller 4 | 4,400 | 400
Seller 5 | 3,200 | 500
Best buy bid |  | 
Buyer 3 | 3,300 | 300
Best sell bid |  | 
Seller 1 | 3,500 | 200
As the best buy bid < sell bid, the order can not be matched and hence shall remain pending in the system
New sell bid
Best buy bid |  | 
Buyer 3 | 3,300 | 300
Best sell bid |  | 
Seller 5 | 3,200 | 500
Order of 300 units by Buyer 3 shall get executed at INR 3,300/ MWh
Best buy bid |  | 
Buyer 2 | 3,200 | 400
Best sell bid |  | 
Seller 5 | 3,200 | 200
Order of 200/400 units by Buyer 3 shall get executed at INR 3,200/ MWh
Buy bids |  | 
Buyer | Buy price | Buy qty.
Buyer 2 | 3,200 | 200
Buyer 1 | 3,000 | 500
Buyer 4 | 2,800 | 200
Buyer 5 | 2,500 | 300
Sell bids |  | 
Seller | Sell price | Sell qty.
Seller 1 | 3,500 | 200
Seller 2 | 4,000 | 300
Seller 3 | 4,200 | 500
Seller 4 | 4,400 | 400
Pending bids (buy/ sell)
INR/ MWh, MW
Trades executed
INR/ MWh, MW
Transaction | Price | Quantity
Buyer 3 – Seller 5 | 3,300 | 300
Buyer 2 – Seller 5 | 3,200 | 200
Orders shall remain pending as the best buy bid of Buyer 2 at INR 3,200/ MWh , best sell bid of Seller 1 at INR 3,500/ MWh

## Slide 122: Continuous matching algorithm
Source: Deloitte analysis
Cumulative buy quantity | Buy quantity | Price | Sell quantity | Cumulative sell quantity | Total tradable volume | Minimum surplus
32,700 | 28,200 | 824 | 0 | 21,100 | 21,100 | +11,600
34,600 | 1900 | 822 | 0 | 21,100 | 21,100 | +13,500
84,300 | 49,700 | 820 | 17,500 | 21,100 | 21,100 | +63,200
Sample bids received during trading hours (buy/ sell)
INR/ MWh, MW
Buy bids |  | 
Buyer | Buy price | Buy qty.
Buyer 5 | 4,500 | 825
Buyer 3 | 28,200 | 824
Buyer 1 | 1,900 | 822
Buyer 4 | 49,700 | 820
Buyer 2 | 8,000 | 819
Sell bids |  | 
Seller | Sell price | Sell qty.
Seller 4 | 831 | 290
Seller 2 | 826 | 21,650
Seller 1 | 825 | 8,500
Seller 5 | 820 | 17,500
Seller 3 | 819 | 3,600
Order book is sorted on best buy and best sell bid prices after auction session
Maximum tradable volume is the maximum amount of electricity that can be traded at respective price
Cumulative buy quantity | Buy quantity | Price | Sell quantity | Cumulative sell quantity | Total tradable volume
- | - | 831 | 290 | 51,540 | -
- | - | 826 | 21,650 | 51,250 | -
4,500 | 4,500 | 825 | 8,500 | 29,600 | 4,500
32,700 | 28,200 | 824 | 0 | 21,100 | 21,100
34,600 | 1900 | 822 | 0 | 21,100 | 21,100
84,300 | 49,700 | 820 | 17,500 | 21,100 | 21,100
92,300 | 8,000 | 819 | 3,600 | 3,600 | 3,600
Eligible prices for auction
Minimum surplus is the residual electricity quantity post trade at respective price
As there is lowest unbalance of 11,600 MW at price of INR 824, hence it is the auction uniform price
However, there are a few other cases where further processing needs to be done to calculate the uniform auction price
Condition | Uniform market price
Multiple equal positive minimum surplus (+) | Uniform market price = MAX ( Prices )
Multiple equal positive minimum surplus (-) | Uniform market price = MIN (Prices)
Multiple equal positive and negative minimum surplus (+, -) | Uniform market price = AVERAGE (2 prices where the sign changes)
Multiple zero minimum surplus ( 0 ) | Uniform market price = AVERAGE (highest and lowest price)
Minimum surplus is the diff. of cumulative buy and sell quantity
Total tradable volume is minimum of cumulative buy or sell quantity at a price

## Slide 123: Analysis of impact of delay in RCOD
Period | Dry Months | Wet Months
 | (NPR. per unit) | (NPR. per unit)
From 1st month to 12th month | 8.4 | 4.8
From 13th month to 24th month | 8.65 | 4.94
From 25th month to 36th month | 8.9 | 5.09
From 37th month to 48th month | 9.16 | 5.23
From 49th month to 60th month | 9.41 | 5.38
From 61st month to 72nd month | 9.66 | 5.52
From 73rd month to 84th month | 9.91 | 5.66
From 85th month to 96th month | 10.16 | 5.81
From 97th month till the end of the agreement period | 10.42 | 5.95
Scenario -1 - Electric Energy purchase rates without Delay
Period | Dry Months | Wet Months
 | (NPR. per unit) | (NPR. per unit)
From 1st month to 12th month |  | 
From 13th month to 24th month | 8.4 | 4.8
From 25th month to 36th month | 8.65 | 4.94
From 37th month to 48th month | 8.9 | 5.09
From 49th month to 60th month | 9.16 | 5.23
From 61st month to 72nd month | 9.41 | 5.38
From 73rd month to 84th month | 9.66 | 5.52
From 85th month to 96th month | 9.91 | 5.66
From 97th month till the end of the agreement period | 10.16 | 5.81
Scenario - 2 - Electric Energy purchase rates with Delay in COD by more than six months and less than 18 months
Illustration: Where COD is late by more than six months and less than 18 months when compared to RCOD, then there will be only 7 price escalations
Inline with PPA, analysis has been done considering Average Base energy during Dry Season as 124 GWh and Average Base energy during Wet Season as 277 GWh, to calculate the impact of the total realization in both scenario
Loss of 5% due to delay in achieving RCOD will have a huge impact in the financials of the project.
Scenario-1 | 
Total Realisation during dry season (NPR. Million) | 37,643
Total Realisation during wet season (NPR. Million) | 48,022
Scenario-2 | 
Total Realisation during dry season (NPR. Million) | 35,674
Total Realisation during wet season (NPR. Million) | 45,559
Indicative Total Dry Season loss (NPR. Million) | 1,970
Indicative Total Wet Season loss (NPR. Million) | 2,463
Indicative Loss (NPR. Million) | 4,433
Indicative Loss % | 5%
As per the provisions of the PPA, there will be reduction in project revenue realization in case of delay in RCOD

## Slide 124: Planned, Proposed and Under - Construction Hydropower Projects Portfolio (As per NEA)
With 943 MW under-construction and 3.2 GW planned and proposed hydro projects, Nepal aims for higher power generation in upcoming years
With a vision to meet growing country’s electricity demand and emerge as a key player in cross-border electricity trade market, Nepal has taken necessary initiatives to develop hydropower projects portfolio consisting of several planned, proposed and under-construction projects. Details are outlined below -
Under Construction Hydro Projects (NEA Annual Reports) |  | 
Sl. No | Project Name | Capacity (MW)
1 | Upper Tamakoshi Hydropower Project | 456
2 | Tanahu Hydropower Project | 140
3 | Rahuganga HEP | 40
4 | Upper Sanjen | 14.6
5 | Sanjen | 42.5
6 | Rasuwagadi | 111
7 | Madhya Bhotekoshi | 102
8 | Upper Trishuli 3B | 37
Total |  | 943.1
Planned & Proposed Hydro Projects (NEA Annual Reports) |  | 
Sl. No | Project Name | Capacity (MW)
1 | Upper Arun HEP | 1,061
2 | Upper Modi A HEP | 42
3 | Upper Modi HEP | 18.2
4 | Dudhkoshi Storage HEP | 635
5 | Uttar Ganga Storage HEP | 828
6 | Tamakoshi V HEP | 95
7 | Aadhikhola Storage HEP | 180
8 | Chainpur Seti HEP | 210
9 | Begnas Rupa Pump Storage HEP | 150
Total |  | 3,219.2
Source - NEA Annual Report;

## Slide 125: Royalty Provisions
Royalty provisions are governed by Hydropower Development Policy, 2058 (2001)
Generation License issued by DoED for STPP Project – May 2019
Royalty is levied on the installed capacity Since the installed capacity of the project is 100 M.W., royalty for entire capacity shall be submitted.
For installed Kilowatt: For the first time, within 15 (fifteen) days from the date on which the first turbine generator until comes into commercial operation, thereafter every year at the same time.
For energy: For the first time, within 4 (four) months from the date on which the first turbine generator unit comes into commercial operation, thereafter in every 4/4 months.
Royalty Provisions in Hydropower Development Policy, 2058 (2001)
A hydropower generator shall pay the royalty as follows to Government of Nepal after the commencement of electricity generation.
In the case of the hydropower projects which sell energy for internal consumption and exports the remaining energy, the energy fee equivalent to that chargeable for the export- oriented project shall be charged on the quantum of energy exported abroad.
Energy royalty = (Generated energy-Self consumption) X Average Selling Price X Energy Royalty Rate.
Capacity royalty = Capacity Royalty Rate X ( 1+5/100) year- 2058 X Installed capacity (kW)
Type |  | Up to 15 years |  | After 15 years from the date of Commercial Operation | 
 |  | Annual capacity royalty, per kW | Energy Royalty, per kWh | Annual capacity royalty, per kW | Energy Royalty, per kWh
Export Oriented run of the river | Commercial Basis | Rs. 400 / - | 7.5% | Rs. 1800 / - | 12%
 | Non-Commercial Basis | Rs. 400 / - | 15% | Rs. 400 / - | 15%
Royalty Mechanism

## Slide 126: Modes of Trading for hydropower projects in Nepal
India and Nepal are collaboratively advancing regional energy integration through strategic cross-border transmission initiatives
Power Exchange
PEC Mechanism
Power Exchange Committee (PEC) is one of the mechanisms for power trading between Nepal and India. Power imports from India are conducted through Bilateral trade.
The meeting for this mechanism is held once a year. The amount of power trade and its tariff is mainly discussed.
This mechanism is applied to power trading in areas remote from the 400kV interconnection point with India.
Other Bilateral transactions
Export to the Indian state of Haryana during Nepal’s rainy season from June 1 to October 31 for five years from FY 2023-24.
Nepal entered the Indian power market in April 2021 through the Indian Energy Exchange (IEX), marking the start of Cross-Border Electricity Trade (CBET) via the power exchange platform.
Currently, Nepal is allowed to trade in Day Ahead Market (DAM) and Real Time Market (RTM)
For the power plants to be traded on the IEX, NEA submits an application every year, which is approved by CEA.
NVVN acts as nodal agency who facilitates the trading in power exchange
NVVN holds both trader and Nodal Agency roles, enabling it to manage trade settlements and defaults.
Few of the Power plants which follows this transaction are : Kaligandaki ‘A’ Hydropower Project (140 MW), Solu Khola (83 MW), Middle Marsyangdi Hydropower Project (68 MW).
A government-to-government trade between Nepal and Bangladesh to export 40 MW of electricity to Bangladesh over a 5-year period has been approved between Nepal, India, and Bangladesh on . November 15, 2024
The CEA permit was granted and exports from Nepal to Bangladesh were implemented, only for one day as for 2024.
For this tripartite G to G trade, electricity will be exported from Nepal to Bangladesh over a five-month period from June to November, which is Nepal's rainy season.
The unit price for trade between Bangladesh and Nepal will be 6.4 cents/kWh, and metering will be done in Muzaffarpur in India. In addition, Bangladesh will pay to India a transmission charge and cost equivalent to transmission losses occurring within India.
Nepal - India Power Exchange Committee (PEC) constituted for consultation of power trade in 1992.
Source: NEA Annual Report 2023/24, NVVN Directors Report 2023-24, JICA Report
Tripartite Framework
Bilateral Trade

## Slide 127: Assessing Nepal’s Power Sector actual growth against historic studies-based Projections (1/2)
Comparison of actual electricity demand trends against several scenario-based projections under various studies indicate significant deviations
Source - NEA Annual Report; Electricity Demand Forecast (2015-40) WECS; NEA Load Forecast
Chart: 
 | 3866 | 7601 | 12999
 | 3866 | 8111 | 14864
 | 3866 | 8523 | 16546
 | 3866 | 14871 | 22432
 | 3866 | 15304 | 24265
 | 4866 | 6704 | 8270 | 8957 | 10454 | 11301 | 12197
 | 5023 | 6929 | 8863 | 9790 | 11199 | 12365 | 13638
 | 13296 | 14600 | 16690
 | 3744 | 5560 | 6525 | 7313 | 10693 | 12165
2015
2018
2020
2021
2023
2024
2025 (P)
3,866
5,023
6,704
7,601
9,790
10,454
11,301
12,999
WECS ED (2015-40) BAU (4.5% GDP)
WECS ED (2015-40) Ref (7.2% GDP)
WECS ED (2015-40) High (9.2% GDP)
WECS ED (2015-40) Ref + Policy
WECS ED (2015-40) High + Policy
NEA Load Forecast (Base)
NEA Load Forecast (Optimistic)
JICA Master Plan (Optimum)
Actuals
Comparison of Actuals vs Historically Forecasted National Electricity Demand (GWh)
Chart: 
 | 4 | 0.4 | 9 | 7.6 | 6.7 | -2.4 | 4.8 | 5.6 | 2
2015
0.4
2016
2017
2018
2019
-2.4
2020
2021
2022
2.0
2023
Ø 4
Actual demand covers internal and export sales, Source – NEA Annual Report 2023/24
Nepal’s Annual GDP Growth (%), World Bank
Comparison of actual electricity demand trends against several scenario-based projections under various studies (such as NEA Load Forecast, WECS led Electricity Demand Forecast (2015-40) and JICA Master Plan 2024 indicate significant deviations. In alignment to 4% average GDP growth over the years, projection scenarios with ~4% GDP growth resembled closely with the actual demand. Hence, it is imperative to consider this resemblance in the future projections for realistic results

## Slide 128: Assessing Nepal’s Power Sector actual growth against historic studies-based Projections (2/2)
Similar to demand, actual installed capacity addition also varies from the optimistic projections under several studies
Chart: 
 | 1721 | 3384 | 5787
 | 1721 | 3611 | 6617
 | 1721 | 3794 | 7366
 | 1721 | 6621 | 9987
 | 1721 | 6814 | 10803
 | 862 | 1988 | 2225 | 2507 | 3194 | 3194 | 3294
 | 3380 | 4100 | 6289
 | 787 | 1074 | 1262.5 | 1451 | 2304 | 3157
2015
2018
2020
2021
2023
2024
2025 (P)
WECS ED (2015-40) BAU (4.5% GDP)
WECS ED (2015-40) Ref (7.2% GDP)
WECS ED (2015-40) High (9.2% GDP)
WECS ED (2015-40) Ref + Policy
WECS ED (2015-40) High + Policy
JICA Master Plan (Optimum)
Actuals
Nationwide Master Plan Study on Storage-type Hydro
Comparison of Actuals vs Historically Forecasted Installed Capacity Mix (MW)
Source - NEA Annual Report; IBN Energy Demand – MAED; Electricity Demand Forecast (2015-40) WECS; NEA Load Forecast
In alignment to the demand side, the projected capacity additions from several reports have also varied significantly from the actual development. It is imperative for the sector to consider these, inherit key landscape factors and envisage a 10% - 25% reduction in the projected capacity additions for upcoming years.

## Slide 129: Key Targets and Interventions driving electricity consumption in Nepal
Key initiatives across drivers like EVs, ECooking, Smart Street Lights, Railways and Industrialization is envisaged to boost electricity consumption
Policy | Source | Target
Electric vehicles (EV) | Assessment of Electric Mobility Targets for Nepal’s 2020 Nationally Determined Contributions (NDC) Nepal SDGs Status and Roadmap 2016-2030 | By 2025, 25% of private vehicle, 20% of public vehicle sales is EV By 2030, 90% of private vehicle, 60% of public vehicle sales is EV Electric vehicles in public transport systems (%) 2015:1%, 2019:5%, 2022:20%, 2025:35%, 2030:50%
Electric cooking | Nepal SDGs Status and Roadmap 2016-2030: | 30% of cooking heat sources is wood, 39% is LPG, and the remaining 31% is electricity in 2030
Smart Street Light | NEA Annual Report 2020/2021 | Smart streetlight (solar LED streetlights) is introduced to the same extent as 2018 onward
Electric railway | The Fifteenth Plan (Fiscal Year 2019/20 – 2023/24) By National Planning Commission | 900 km electric railway will start operation in 2030.
Steelwork | Several references such as Federation of Nepalese Chamber of Commerce and Industry | Assumed after 2022, a new steelwork will start operation every two years.
Industrial zone and Special economic zone | Follow Up Data Collection Survey for Transmission and Distribution Network Development Special Economic Zone Authority (SEZA) | Development of 10 industrial districts and 14 special economic zones
Improvement of energy efficiency | National Energy Efficiency Strategy, 2075 | 0.84%(2022)→1.68%(2030)→1.68%(2040)
Policy Interventions to drive electricity demand in Nepal
Source - JICA Integrated Power System Development Plan 2024
Nepal has been proactively setting targets and devising policy interventions across sectors to promote enhanced electricity consumption. These initiatives are envisaged to increase internal consumption and curb total emissions aiding Nepal’s zero emissions targets

## Slide 130: Historical sale of electricity by NEA in IEX
Country | Trader | Mode of transaction | IEX segment/ Buyer | Project Name | Quantum (MW) | Start date | End date
Nepal | NVVN | Power Exchange | DAM and RTM | Upper Dordi | 24.25 | 1 Sep 2024 | 31 Aug 2025
Nepal | NVVN | Power Exchange | DAM and RTM | Lower Modi | 19.4 | 1 Oct 2024 | 30 Sep 2025
Nepal | NVVN | Power Exchange | DAM and RTM | Kabeli B1 | 24.25 | 1 Oct 2024 | 30 Sep 2025
Nepal | NVVN | Power Exchange | DAM and RTM | Dordi Khola | 26.19 | 19 Nov 2024 | 31 May 2025
Nepal | NVVN | Power Exchange | DAM and RTM | Solu Khola | 83.42 | 19 Nov 2024 | 31 May 2025
Nepal | NVVN | Power Exchange | DAM and RTM | Upper Balephi ‘A’ | 34.92 | 19 Nov 2024 | 31 May 2025
Nepal | NVVN | Power Exchange | DAM | Devighat Hydropower Project | 14.55 | 19 May 2023 | 30 Apr 2024
Nepal | NVVN | Power Exchange | DAM | Trishuli Hydropower Project | 23.28 | 19 May 2023 | 30 Apr 2024
Nepal | NVVN | Power Exchange | DAM | Marsyangdi Hydropower Project | 67 | 01 Jun 2023 | 31 May 2025
Nepal | NVVN | Power Exchange | DAM | Chilime Hydropower Project | 21.44 | 19 May 2023 | 30 Apr 2024
Nepal | NVVN | Power Exchange | DAM | Middle Marsyangdi Hydropower Project | 68 | 01 June 2023 | 31 May 2025
Nepal | NVVN | Power Exchange | DAM | Kaligandaki ‘A’ Hydropower Project | 140 | 01 June 2023 | 31 May 2025
Nepal | NVVN | Power Exchange | DAM | Likhu IV Hydropower Project | 51 | 01 June 2023 | 31 May 2025
Nepal | NVVN | Power Exchange | DAM | Solu Hydropower Project | 22.8 | 01 June 2023 | 30 Apr 2024
Nepal | NVVN | Power Exchange | DAM | Kabeli B-1 Hydro Power Project (25 10MW) | 24.25 | 26 Dec 2022 | 30 Sep 2023
Nepal | NVVN | Power Exchange | DAM | Lower Modi Hydro Power Project (20 MW) | 19.4 | 26 Dec 2022 | 30 Sep 2023
Nepal | NVVN | Power Exchange | DAM | Upper Kalangagad Hydro Power Project | 32.7 | 5 Sep 2023 | 31 May 2024
Nepal | NVVN | Power Exchange | DAM | Upper Chameliya | 37.3 | 5 Sep 2023 | 30 Jun 2024
Nepal | NVVN | Power Exchange | DAM and RTM | Kabeli B-1 Hydro Power Project | 24.25 | 1 Oct 2023 | 30 Sep 2024
Nepal | NVVN | Power Exchange | DAM and RTM | Lower Modi Hydro Power Project | 19.4 | 1 Oct 2023 | 30 Sep 2024
Nepal | NVVN | Power Exchange | DAM and RTM | Upper Dordi A | 24.25 | 10 Nov 2023 | 31 Aug 2024
Nepal | NVVN | Power Exchange | DAM and RTM | Solu Khola | 83.42 | 8 Dec 2023 | 31 May 2024
Nepal | NVVN | Power Exchange | DAM and RTM | Dordi Khola | 26.19 | 8 Dec 2023 | 31 May 2024
Nepal | NVVN | Power Exchange | DAM and RTM | Devighat Hydro Power Project | 14.55 | 01 May 2024 | 30 Apr 2025
Nepal | NVVN | Power Exchange | DAM and RTM | Trishuli Hydro Power Project | 23.28 | 01 May 2024 | 30 Apr 2025
Nepal | NVVN | Power Exchange | DAM and RTM | Marsyangdi Hydropower Project | 67 | 01 Jun 2024 | 30 Apr 2025
Nepal | NVVN | Power Exchange | DAM and RTM | Middle Marsyangdi Hydropower Project | 68 | 01 Jun 2024 | 30 Apr 2025
Nepal | NVVN | Power Exchange | DAM and RTM | Chilime Hydropower Project | 21.44 | 01 May 2024 | 30 Apr 2025
Nepal | NVVN | Power Exchange | DAM and RTM | Kaligandaki ‘A’ Hydropower Project | 140 | 01 Jun 2024 | 30 Apr 2025
Nepal | NVVN | Power Exchange | DAM and RTM | Likhu IV Hydropower Project | 51 | 01 Jun 2024 | 30 Apr 20255
Nepal | NVVN | Power Exchange | DAM and RTM | Solu hydropower Project | 22.8 | 01 May 2024 | 30 Apr 2025
Nepal | NVVN | Power Exchange | DAM and RTM | Upper Balephi A | 34.92 | 16 Feb 2024 | 31 Oct 2024
Nepal | NVVN | Power Exchange | DAM and RTM | Upper Kalangagad Hydro Power Project | 37.3 | 01 Jun 2024 | 30 Apr 2025
Nepal | NVVN | Power Exchange | DAM and RTM | Upper Chameliya Hydro Power Project | 38.8 | 01 Jul 2024 | 30 Apr 2025
NVVN: NTPV Vidyut Vyapar Nigam; DAM: Day Ahead Market; RTM: Real Time Market

## Slide 131: Estimated impact of sale of electricity from the project in IEX on NEA revenue (1/3)
YEAR 1 |  |  |  |  |  |  |  |  |  |  |  | 
Month type | Month as per English calendar | Nepali months | No. of days | Additional energy (Mn kWh) | PPA tariff (NPR/kWh) | PPA tariff (INR/kWh) | Avg price on exchange (based on FY22-25 IEX DAM prices) (INR/kWh) | Difference (INR/kWh) | Trader (NVVN/PTC) margin (INR/kWh) | Transmission line losses (%) | Net revenue for NEA (INR Mn) | Net revenue (NPR Mn)
Wet | Jun | 16th Jeshta onw. | 16 | 12 | 4.8 | 3.02 | 5.81 | 2.79 | 0.07 | 3% | 29 | 47
Wet | Jun/Jul | Asadh | 32 | 22 | 4.8 | 3.02 | 5.42 | 2.40 | 0.07 | 3% | 49 | 77
Wet | Jul/Aug | Shrawan | 31 | 21 | 4.8 | 3.02 | 5.26 | 2.23 | 0.07 | 3% | 44 | 70
Wet | Aug/Sep | Bhadra | 31 | 21 | 4.8 | 3.02 | 5.45 | 2.43 | 0.07 | 3% | 48 | 76
Wet | Sep/Oct | Ashwin | 31 | 21 | 4.8 | 3.02 | 5.07 | 2.05 | 0.07 | 3% | 40 | 64
YEAR 2 |  |  |  |  |  |  |  |  |  |  |  | 
Month type | Month as per English calendar | Nepali months | No. of days | Additional energy (Mn kWh) | PPA tariff (NPR/kWh) | PPA tariff (INR/kWh) | Avg price on exchange (based on FY22-25 IEX DAM prices) (INR/kWh) | Difference (INR/kWh) | Trader (NVVN/PTC) margin (INR/kWh) | Transmission line losses (%) | Net revenue for NEA (INR Mn) | Net revenue (NPR Mn)
Wet | Jun | 16th Jeshta onw. | 16 | 12 | 4.9 | 3.11 | 5.81 | 2.70 | 0.07 | 3% | 28 | 45
Wet | Jun/Jul | Asadh | 32 | 22 | 4.9 | 3.11 | 5.42 | 2.31 | 0.07 | 3% | 47 | 74
Wet | Jul/Aug | Shrawan | 31 | 21 | 4.9 | 3.11 | 5.26 | 2.14 | 0.07 | 3% | 42 | 67
Wet | Aug/Sep | Bhadra | 31 | 21 | 4.9 | 3.11 | 5.45 | 2.34 | 0.07 | 3% | 46 | 73
Wet | Sep/Oct | Ashwin | 31 | 21 | 4.9 | 3.11 | 5.07 | 1.96 | 0.07 | 3% | 38 | 61
YEAR 3 |  |  |  |  |  |  |  |  |  |  |  | 
Month type | Month as per English calendar | Nepali months | No. of days | Additional energy (Mn kWh) | PPA tariff (NPR/kWh) | PPA tariff (INR/kWh) | Avg price on exchange (based on FY22-25 IEX DAM prices) (INR/kWh) | Difference (INR/kWh) | Trader (NVVN/PTC) margin (INR/kWh) | Transmission line losses (%) | Net revenue for NEA (INR Mn) | Net revenue (NPR Mn)
Wet | Jun | 16th Jeshta onw. | 16 | 12 | 5.1 | 3.21 | 5.81 | 2.61 | 0.07 | 3% | 27 | 44
Wet | Jun/Jul | Asadh | 32 | 22 | 5.1 | 3.21 | 5.42 | 2.21 | 0.07 | 3% | 45 | 71
Wet | Jul/Aug | Shrawan | 31 | 21 | 5.1 | 3.21 | 5.26 | 2.05 | 0.07 | 3% | 40 | 64
Wet | Aug/Sep | Bhadra | 31 | 21 | 5.1 | 3.21 | 5.45 | 2.24 | 0.07 | 3% | 44 | 70
Wet | Sep/Oct | Ashwin | 31 | 21 | 5.1 | 3.21 | 5.07 | 1.86 | 0.07 | 3% | 36 | 58

## Slide 132: Estimated impact of sale of electricity from the project in IEX on NEA revenue (2/3)
YEAR 4 |  |  |  |  |  |  |  |  |  |  |  | 
Month type | Month as per English calendar | Nepali months | No. of days | Additional energy (Mn kWh) | PPA tariff (NPR/kWh) | PPA tariff (INR/kWh) | Avg price on exchange (based on FY22-25 IEX DAM prices) (INR/kWh) | Difference (INR/kWh) | Trader (NVVN/PTC) margin (INR/kWh) | Transmission line losses (%) | Net revenue for NEA (INR Mn) | Net revenue (NPR Mn)
Wet | Jun | 16th Jeshta onw. | 16 | 12 | 5.2 | 3.30 | 5.81 | 2.51 | 0.07 | 3% | 26 | 42
Wet | Jun/Jul | Asadh | 32 | 22 | 5.2 | 3.30 | 5.42 | 2.12 | 0.07 | 3% | 43 | 68
Wet | Jul/Aug | Shrawan | 31 | 21 | 5.2 | 3.30 | 5.26 | 1.95 | 0.07 | 3% | 38 | 61
Wet | Aug/Sep | Bhadra | 31 | 21 | 5.2 | 3.30 | 5.45 | 2.15 | 0.07 | 3% | 42 | 67
Wet | Sep/Oct | Ashwin | 31 | 21 | 5.2 | 3.30 | 5.07 | 1.77 | 0.07 | 3% | 34 | 55
YEAR 5 |  |  |  |  |  |  |  |  |  |  |  | 
Month type | Month as per English calendar | Nepali months | No. of days | Additional energy (Mn kWh) | PPA tariff (NPR/kWh) | PPA tariff (INR/kWh) | Avg price on exchange (based on FY22-25 IEX DAM prices) (INR/kWh) | Difference (INR/kWh) | Trader (NVVN/PTC) margin (INR/kWh) | Transmission line losses (%) | Net revenue for NEA (INR Mn) | Net revenue (NPR Mn)
Wet | Jun | 16th Jeshta onw. | 16 | 12 | 5.4 | 3.40 | 5.81 | 2.41 | 0.07 | 3% | 25 | 40
Wet | Jun/Jul | Asadh | 32 | 22 | 5.4 | 3.40 | 5.42 | 2.02 | 0.07 | 3% | 41 | 65
Wet | Jul/Aug | Shrawan | 31 | 21 | 5.4 | 3.40 | 5.26 | 1.85 | 0.07 | 3% | 36 | 57
Wet | Aug/Sep | Bhadra | 31 | 21 | 5.4 | 3.40 | 5.45 | 2.05 | 0.07 | 3% | 40 | 64
Wet | Sep/Oct | Ashwin | 31 | 21 | 5.4 | 3.40 | 5.07 | 1.67 | 0.07 | 3% | 32 | 51
YEAR 6 |  |  |  |  |  |  |  |  |  |  |  | 
Month type | Month as per English calendar | Nepali months | No. of days | Additional energy (Mn kWh) | PPA tariff (NPR/kWh) | PPA tariff (INR/kWh) | Avg price on exchange (based on FY22-25 IEX DAM prices) (INR/kWh) | Difference (INR/kWh) | Trader (NVVN/PTC) margin (INR/kWh) | Transmission line losses (%) | Net revenue for NEA (INR Mn) | Net revenue (NPR Mn)
Wet | Jun | 16th Jeshta onw. | 16 | 12 | 5.6 | 3.51 | 5.81 | 2.31 | 0.07 | 3% | 27 | 43
Wet | Jun/Jul | Asadh | 32 | 22 | 5.6 | 3.51 | 5.42 | 1.91 | 0.07 | 3% | 42 | 67
Wet | Jul/Aug | Shrawan | 31 | 21 | 5.6 | 3.51 | 5.26 | 1.75 | 0.07 | 3% | 37 | 59
Wet | Aug/Sep | Bhadra | 31 | 21 | 5.6 | 3.51 | 5.45 | 1.94 | 0.07 | 3% | 41 | 65
Wet | Sep/Oct | Ashwin | 31 | 21 | 5.6 | 3.51 | 5.07 | 1.57 | 0.07 | 3% | 33 | 53

## Slide 133: Estimated impact of sale of electricity from the project in IEX on NEA revenue (3/3)
YEAR 7 |  |  |  |  |  |  |  |  |  |  |  | 
Month type | Month as per English calendar | Nepali months | No. of days | Additional energy (Mn kWh) | PPA tariff (NPR/kWh) | PPA tariff (INR/kWh) | Avg price on exchange (based on FY22-25 IEX DAM prices) (INR/kWh) | Difference (INR/kWh) | Trader (NVVN/PTC) margin (INR/kWh) | Transmission line losses (%) | Net revenue for NEA (INR Mn) | Net revenue (NPR Mn)
Wet | Jun | 16th Jeshta onw. | 16 | 12 | 5.7 | 3.61 | 5.81 | 2.20 | 0.07 | 3% | 26 | 41
Wet | Jun/Jul | Asadh | 32 | 22 | 5.7 | 3.61 | 5.42 | 1.81 | 0.07 | 3% | 40 | 63
Wet | Jul/Aug | Shrawan | 31 | 21 | 5.7 | 3.61 | 5.26 | 1.65 | 0.07 | 3% | 35 | 55
Wet | Aug/Sep | Bhadra | 31 | 21 | 5.7 | 3.61 | 5.45 | 1.84 | 0.07 | 3% | 39 | 62
Wet | Sep/Oct | Ashwin | 31 | 21 | 5.7 | 3.61 | 5.07 | 1.46 | 0.07 | 3% | 31 | 49
YEAR 8 onwards |  |  |  |  |  |  |  |  |  |  |  | 
Month type | Month as per English calendar | Nepali months | No. of days | Additional energy (Mn kWh) | PPA tariff (NPR/kWh) | PPA tariff (INR/kWh) | Avg price on exchange (based on FY22-25 IEX DAM prices) (INR/kWh) | Difference (INR/kWh) | Trader (NVVN/PTC) margin (INR/kWh) | Transmission line losses (%) | Net revenue for NEA (INR Mn) | Net revenue (NPR Mn)
Wet | Jun | 16th Jeshta onw. | 16 | 12 | 5.9 | 3.72 | 5.81 | 2.09 | 0.07 | 3% | 25 | 39
Wet | Jun/Jul | Asadh | 32 | 22 | 5.9 | 3.72 | 5.42 | 1.70 | 0.07 | 3% | 37 | 59
Wet | Jul/Aug | Shrawan | 31 | 21 | 5.9 | 3.72 | 5.26 | 1.54 | 0.07 | 3% | 33 | 52
Wet | Aug/Sep | Bhadra | 31 | 21 | 5.9 | 3.72 | 5.45 | 1.73 | 0.07 | 3% | 37 | 58
Wet | Sep/Oct | Ashwin | 31 | 21 | 5.9 | 3.72 | 5.07 | 1.35 | 0.07 | 3% | 29 | 46

## Slide 134: Summary
1. Nepal's Domestic Market and Cross Border Potential
Nepal's power sector has undergone a transformative shift from infrastructure expansion to green growth and market efficiency. With an installed capacity of 3,157 MW as of 2024, dominated by hydropower, the country has transitioned from being a net importer to a net exporter of electricity, exporting ~1,946 GWh to India in FY 2023/24. Domestic demand continues to grow, driven by electrification initiatives in industrial, commercial and transport sectors. The transmission network has expanded significantly, with over 11 cross-border links and strategic projects such as Dhalkebar–Muzaffarpur and New Butwal–Gorakhpur supporting export ambitions. Policy reforms, including the Draft Electricity Bill 2080 and ERC Roadmap (2024–2029), aim to enable open access, trading licenses, and direct market participation for IPPs.
2. India Power Market and Outlook
India's electricity market presents a robust opportunity for Nepalese exports, especially during peak demand periods and renewable energy transitions. India’s installed capacity of 475 GW in FY25, includes ~50% from renewables. The short-term electricity market has grown at a CAGR of 15%, with exchange-based transactions accounting for over 56% of the market. Price discovery mechanisms such as DAM, RTM, and TAM facilitate efficient trading, while payment security structures and buyer profiles (e.g., Telangana, Gujarat, Punjab) enhance market reliability. Seasonal price variations, especially during solar hours, offer competitive pricing for Nepal’s hydro exports. Anticipated reforms and growing demand (projected to grow at 5.5% till FY30) further strengthen the outlook for cross-border electricity trade.
3. Commercial Risk Assessment and implication on the Project
The PJ_ST Hydropower Project in Nepal, with a 100 MW installed capacity, is contracted for 70 MW under a Take-or-Pay arrangement with NEA, and includes 30 MW under Take-and-Pay. The official RCOD is set for February 2026, with tariffs escalating annually by 3% for up to eight years. Commercial risks include reserve margin limitations, transmission infrastructure readiness, and pricing constraints for excess energy. Operational risks such as hydrological variability, monthly delivery compliance, and dry season obligations are assessed, along with regulatory risks tied to ownership changes and third-party sales restrictions. Execution risks from RCOD delays may impact tariff escalation and returns. Market access is contingent on NEA and GoI approvals, with future reforms potentially enabling direct market participation. The project is strategically positioned to leverage Nepal’s increasing domestic demand and export opportunities, subject to successful mitigation of identified risks and policy/regulatory developments.