## Slide 1
Project Nimbus – Revised Final Report
Commercial Due Diligence – Bangladesh
Actis GP LLP, October 2020
Deloitte Touche Tohmatsu India LLP

## Slide 2: Disclaimer
This Report has been prepared by Deloitte Touche Tohmatsu India LLP (“DTTI LLP”) in accordance with the Engagement Letter dated 8th June 2020 executed between DTTI LLP and Actis GP LLP (“Client”) and is subject to the scope of work, approach, assumptions and other conditions mentioned in the Engagement Letter and the conditions mentioned in this Report.
This Report and the information contained herein has been prepared by DTTI LLP solely for the benefit of the Client and is intended for use by the Client solely for the purpose of Project Nimbus - Commercial Due Diligence of NBBL’s 220 MW Gas / 212 HSD based power plant in Bangladesh. The Client shall not use this Report for any other purpose and in particular shall not use this Report in connection with the business decisions of any third party and for advisement purposes.
This Report contains analyses that are intended to provide high-level information on the subject and are not an exhaustive treatment of the subject. The analyses in the Report are limited by the scope of work, the time allocated, information made available to DTTI LLP or collected by DTTI LLP and are heavily dependent upon the assumptions specified in the Engagement Letter and this Report. It should be noted that a different set of assumptions will lead to a different analyses. This Report is not intended to be relied upon as a sole basis for any decision and the Client should take decisions only after seeking professional advice and after carrying out their own due diligence procedures, detailed analysis to ensure that they are making an informed decision. This Report is not and should not be construed in any way as giving any investment advice or any recommendations by DTTI LLP to the Client or any other party. The Client shall be solely responsible for any and all decisions (including the implications thereof) made by the Client on the basis of this Report. The Client shall hold us harmless from any claims for damages arising from the use of our deliverables.
This Report has been prepared on the basis of information made available, obtained and collected by DTTI LLP from Client and various secondary sources till 18th July 2020. The sources of any material information used in the Report has been mentioned or cited herein. The information obtained and collected from the Client and various secondary sources has been used on an “as-is” basis without any independent verification by DTTI LLP. DTTI LLP shall not be responsible for any error or omissions, or for the results obtained from the use of this information and provides no assurance regarding the accuracy, timeliness, adequacy, comprehensiveness and/ or completeness of such information and provides no warranty of any kind, express or implied, including, but not limited to warranties of performance and fitness for a particular purpose. DTTI LLP shall not be liable for any losses and damages arising as a result of any inaccuracy or inadequacy or incomprehensiveness or incompleteness of such information.
This Report is solely for the use of the Client, as per the terms of the Contract. The Report is issued on the basis that this Report or any information derived therefrom, shall not be shared with or provided to any third party without the prior written consent of DTTI LLP.

## Slide 3: Abbreviation List
Abbreviations | Description
2P | Proved + Probable
ADB | Asian Development Bank
AIT | Advanced Income Tax
APSCL | Ashuganj Power Station Company Limited
ATV | Advanced VAT
BAU | Business As Usual
BBL | Barrel
BCF | Billion Cubic Feet
BCM | Billion Cubic Meter
BDT | Bangladesh Taka
BERC | Bangladesh Energy Regulatory Commission
BIFPCL | Bangladesh India Friendship Power Company Limited
BPC | Bangladesh Petroleum Corporation
BPDB | Bangladesh Power Development Board
CAGR | Compounded Annual Growth Rate
CCPP | Combined Cycle Power Plant
CDC | China Development Corporation
CEXIM | Exim Bank of China
CIF | Cost, Insurance and Freight
CNG | Compressed Natural Gas
COD | Commissioning Date
Abbreviations | Description
COVID 19 | Coronavirus Disease
DEG | Deutsche Investitions- und Entwicklungsgesellschaft
DES | Delivered Ex-Ship
DESCO | Dhaka Electricity Supply Company
DPDC | Dhaka Power Distribution Company
EC | Energy Charge
EE | Energy Efficiency
EE&C | Energy Efficiency and Conservation Measures
EGCB | Electricity Generation Company of Bangladesh
EIA | Environmental Impact Assessment
EPC | Engineering, Procurement and Construction
ERD | Economic Relations Division Bangladesh
FC | Fixed Charge
FMO | Entrepreneurial Development Bank
FOB | Free-on-Board
FOREX | Foreign Exchange
FSA | Fuel Supply Agreement
FSRU | Floating Storage Regasification Unit
FY | Financial Year
GCV | Gross Calorific Value
GDP | Gross Domestic Product

## Slide 4: Abbreviation List
Abbreviations | Description
GE | General Electric
GF | Gas Field
GIIGLN | International Group of Liquefied Natural Gas Importers
GNI | Gross National Income
GSA | Gas Supply Agreement
GSMP | Gas Sector Master Plan
GTCL | Gas Transmission Company Limited
GW | Giga Watt
HFO | Heavy Fuel Oil
HSD | High Speed Diesel
HTG | HTG Development Group
HVDC | High Voltage Direct Current
IA | Implementation Agreement
IDA | International Development Association
IDO | International Donor Agencies
IFC | International Finance Corporation
IMF | International Montary Fund
IPFF | Investment Promotion and Financing Facility
IPP | Independent Power Producer
Kcal | Kilo Calorie
Kg | Kilo Gram
Abbreviations | Description
KJ | Kilo Joule
KPCL | Karnaphuli Power Company Limited
KW | Kilo Watt
LD | Liquidated Damages
LNG | Liquified Natural Gas
LOI | Letter of Intent
LPG | Liquified Petroleum Gas
MMBTU | Million British Thermal Units
MMSCFD | Million Standard Cubic Feet
MMSCMD | Million Standard Cubic Meter
MPEMR | Ministry of Power, Energy and Mineral Resources, Bangladesh
MSCF | Million Standard Cubic Feet
MTPA | Million Tonnes Per Annum
MU | Million Units (Million kilo-watt-hour)
MVA | Million Volt Ampere
MW | Mega Watt
NBBL | Nutan Bidyut Bangladesh Limited
NDBIB | NDB Investment Bank
NG | Natural Gas
NTPC | National Thermal Power Corporation India
NWPGCL | North West Power Generation Company Limited

## Slide 5: Abbreviation List
Abbreviations | Description
OFID | OPEC Fund for International Development
PGCB | Power Grid Company of Bangladesh
PLF | Plant Load Factor
PNG | Piped Natural Gas
POL | Petroleum, Oil and Lubricants
PP | Peaking Power
PPA | Power Purchase Agreement
PSMP | Power Sector Master Plan
QRPP | Quick Rental Power Plant
REB | Rural Electricity Board, Bangladesh
RLNG | Regasified Liquified Natural Gas
RMS | Root Mean Square
RPCL | Rural Power Company Limited
RPP | Rental Power Plant
SCM | Standard Cubic Meter
SEPCO | SEPCO Electric Power Construction Corporation
SGCL | Sunderban Gas Companu Limited
SHR | Station Heat Rate
SIPP | Small Independent Power Producer
ST | Steam Turbine
TK | Bangladeshi Taka
Abbreviations | Description
TL | Transmission Line
TV | Taxable Value
UAEL | United Ashuganj Energy Ltd
UAEL | United Ashuganj Energy Ltd
UECL | United Enterprises & Co. Ltd
UK | United Kingdom
UMPL | Unique Meghnaghat Power Limited
USD | United States Dollar
VAT | Value Added Tax
WTI | West Texas Intermediate
WZPDCL | West Zone Power Distribution Company Limited

## Slide 6: Conversion Factors
Particular | Conversion Factor
1 MTPA | 3.6 MMSCMD
1 SCM | 35.3 SCF
1 MVA | 0.85 MW
1 MMBTU | 25.2 SCM
Efficiency of Power Plant | 860 / Station Heat Rate

## Slide 7: Summary

## Slide 8: Power Market | Supply Requirement to Meet Average Demand (Summary)
Bangladesh may require ~11,500 MW of newer capacity addition by FY26 and additional ~7,800 MW between FY27 and FY30 to meet the rising demand
With the current planned capacity in pipeline, there is a potential for ~3,000 MW and ~4,100 MW of incremental capacity addition from non-liquid based plants by FY26 and FY30 respectively
levels of each power plant in Bangladesh 2) For plants not covered under PSMP, an average PPA duration for 22 years has been considered for Non-Rental Plants (and an extension of 5 years for some cases beyond 22 years) and (5+5) years for Rental / Quick Rental Plants. 3) Replacement of Liquid / Rental plants has been considered as their current average tariff ranges from Tk 9 / unit – Tk 28+ / unit whereas Gas / LNG / Nuclear / Imported Coal based plants are expected to have per unit tariff at less than TK 9 / unit based on estimates
Source: BPDB; PSMP 2016, Deloitte Analysis Note: 1) Plant Retirement Based on PSMP 2016 projections as well as estimations based on COD / dispatch
Sr. No | Parameter | Details | Output | Ref Slides
1 | Average Demand Projection & Supply Requirement | The power demand projection has been considered based on PSMP 2016 projections with base correction for GDP Elasticity, demand growth in FY19, estimated EE&C measures in Bangladesh as well as impact of Covid-19 The power supply requirement to meet the demand has been estimated based on average gross dispatch levels of 80% | Average Demand (Base Case) FY 20: 15,673 MW FY 30: 21,561 MW Supply Requirement FY 26: 19,951 MW FY 30: 26,951 MW | 45-55
2 | Current Supply & Requirement of Additional Capacity | The current supply portfolio in Bangladesh consists of 18,961 MW with major contribution of natural gas (~57%) and HFO/HSD based plants (~32%) To meet the average power demand, we have projected the supply capacity requirement considering the following: Expected Retirement: ~6,000 MW by FY30 Replacement of Rental & Liquid Based Plants from economic perspective: ~4,800 MW Replacement of inefficient gas based capacity : ~670 MW | Considering retirements and replacements, the additional capacity required : FY 26: ~11,500 MW FY 30: ~7,828 MW | 
3 | Planned Capacity Addition & Requirement of Incremental Addition to Capacity | As per our estimates, Bangladesh may add the following non-liquid based capacity from the planned projects being tracked in the country : FY 26: ~8,500 MW Between FY27 and FY30 : ~3,720 MW (includes 2,400 MW of Nuclear based power capacity) However, Bangladesh may further require additional incremental capacity of ~3,000 MW by FY26 and ~4,100 MW between FY27 and FY30 to meet the average power demand | The incremental non liquid based capacity (beyond planned) required: FY 26: ~3,000 MW FY 30: ~4,108 MW | 54-67

## Slide 9: Gas Allocation & Tariff Hikes for Power Sector | Summary
Power Sector has historically received the highest allocation for Natural Gas and is expected to continue receiving similar priority in future; The Natural Gas / LNG tariff for power sector may increase at a rapid pace than historical increase due to LNG imports and planned subsidy reductions by GoB
Sr. No | Parameter | Details | Output | Ref Slides
1 | Gas Allocation by BERC & Allocation Guidelines by Petrobangla | In FY20 BERC has proposed the natural gas / LNG allocation (in the ratio of ~75%:25%) to be ~95 mmscmd considering the planned LNG imports in the country with power sector being allocated 42% of the total supply in line with historical allocations to the sector Petrobangla had also come up with Gas Priority Guidelines with Fertilizer and Power Sector receiving highest priorities (1,2) for gas allocation with further recommendations to provide higher gas allocation to new plants with ~50% efficiency running on Combined Cycle operations an reducing allocations to low efficient plants | Allocation in mmscmd in FY20: Total 95 Power – 40 Industry – 16 Captive Power – 16 Domestic – 13 Fertilizer – 5 CNG – 4 Commercial – 1 Tea Garden – 0.1 | 39
2 | Tariff Hikes for Natural Gas | Between FY10 and FY20, the BERC has increased the natural gas tariff for power sector 4 times only at a CAGR of ~4.7% only The tariff in FY10 was BDT ~2.82 / SCM (~$0.8 / MMBTU) which was gradually increased to BDT ~4.45 / SCM (~$1.4 / MMBTU) for FY20 The tariff hike in FY20 by BERC considered the LNG imports in the country leading to a single blended natural gas tariff for all consumer segments in Bangladesh However the power sector is still receiving subsidy of ~65% on the weighted average cost of supply of natural gas / LNG which is ~ BDT 12.6 / SCM (~$ 3.97 / MMBTU) | Natural Gas Tariff projections for Power Sector: FY20 – BDT 4.45 / SCM ($1.4 / MMBTU) | 41-43, 180-182
Source: BERC, Gas Sector Master Plan 2017, Deloitte Analysis;
The power sector has been receiving the highest allocation of natural gas with Petrobangla also supporting the same; The natural gas prices for power sector is based on blending of Natural Gas (Domestic Sources) and LNG Imports with a single blended tariff for each consumer segment

## Slide 10: Plant Dispatch | Summary
Based on the estimated levelized tariff for Nimbus and the current merit order profile, the plant should be able to get full dispatch while running on natural gas
Sr. No | Parameter | Details | Output | Ref Slides
1 | Tentative Merit Order | We have estimated the tentative Merit Order in Bangladesh based on the following: Estimated levelized tariff for upcoming imported LNG based plants, imported Coal Based plants, Power Import from India (Adani’s Godda Plant and Roopur Nuclear Plant) based on industry estimates on capex, fuel costs and efficiency levels Estimated Levelized tariff of Nimbus Plant based on the prevailing operating parameters as per the PPA, GSA, FSA and O&M agreements and the fuel prices as per current prices set by GoB for power players | Expected Total Tariff Range (US Cents / unit) as per Merit Order: Domestic Gas: 1.2 – 5.8 Imported Power from India (Existing): 4.3–9.4 Imported LNG Based plants: 8.1 –9.4 Imported Coal Based Plants: 8.4 – 8.8 Nuclear (Rooppur): 8.8–9.4 Imported Power from India (Godda): 10.1–10.6 HFO : 11–17.5 HSD – 18.8 – 31.3 | 73-79
2 | Nimbus Placement in Merit Order | The levelized Tariff for Gas operation for Nimbus could range between US Cents 3-4 / kWh whereas the operations on HSD could range between US cents 17 – 20 / kWh | Position in Merit Order: Natural Gas : 2nd/3rd Quartile (34%-64% of MOD) HSD : Potential Issue in Dispatch due to high cost | 
The proposed Nimbus plant is expected to receive full dispatch on Natural gas based on economic / merit order perspective in Bangladesh; However the plant may face dispatch challenges in case it is run on HSD due to high cost in the current merit order
Source: Nimbus PPA / FSA / GSA / O&M Agreements Note 1) The normative parameters such as Gas Calorific Value, Oil Heat Value, PLFs, Dependable Capacity, Escalable & Non-escalable pricing components have been considered as per the agreements executed by Nimbus 2) No escalation in fuel prices have been assumed 3) Fuel wise plant parameters considered for estimation levelized tariff. Please refer to Slide 79 for details

## Slide 11: Gas Supply Outlook | Summary
The current reserves at Shahbazpur should be able to supply gas for ~21 years. In case of PPA extension of Aggreko & Venture plant, Shahbazpur reserves would sustain operation for ~16 years
Sr. No | Parameter | Details | Output | Ref Slides
1 | Gas Availability | Remaining reserves (2P) at Shahbazpur field were ~27 MMSCMD (351 BCF) in December 2017 as per Petrobangla Due to newer gas finds, the remaining reserves at Shahbazpur were increased in December 2018 to ~45.5 MMSCMD (586 BCF); Also there was an additional find at Bhola North fields for 32.6 MMSCMD (420 BCF) | Gas Reserves according to two estimates Dec’19 Estimate: Shahbazpur: 549 BCF (~42.6 MMSCMD) Bhola North: 420 BCF (~32.6 MMSCMD) | 37, 86-87
2 | Gas Requirement (No PPA extension for Venture & Aggreko) | Currently 3 power plants operate in the Bhola Island with a cumulative capacity of 353 MW. The retirements as per PSMP and current PPAs for Bhola I, Venture and Aggreko plants are tentatively at FY37, FY22 and FY22 respectively Considering their current efficiency levels and a normative PLF of 80% the existing plants at Bhola Island and the proposed Nimbus Plant together may require ~2.5 MMSCMD (88 MMSCFD) of gas annually till FY22 and ~1.76 MMSCMD (62 MMSCFD) from FY23 onwards considering plant retirements | The expected gas availability for NBBL in accordance with the Gas Estimate and utilization: Dec’19 Estimate : 21 years (only Shahbazpur) and 22+ years (considering Bhola) | 
3 | Gas Requirement (PPA extension for 5 years for Venture & Aggreko) | The Venture & Aggreko plants together require ~ 0.7 MMSCMD (26 MMSCFD) of gas annually. Both these plants are over 10 years of age and hence further PPA extension is not expected However in case these plants do get PPA extensions (5 Years till FY27), then the gas reserves at Bhola Island would have to supply to the plants affecting the overall availability of gas for Nimbus | The expected gas availability for NBBL in accordance with the Gas Estimate and utilization: Dec’19 Estimate : 16 years (only Shahbazpur) and 22+ years (considering Bhola) | 
Source: BPDB, Petrobangla, Deloitte Analysis Note 1) The Efficiency of, Venture 33 MW and Aggreko 95 MW considered as per existing efficiency levels in FY19 2) The Efficiency of Nimbus Plant considered at 46% (in line with PPA condition with 80% PLF 3) All the plants have been considered to be operating at 80% average annual PLF to determine annual gas requirement 4) 2P Reserves estimated for Dec 19 considering plant dispatch levels of ~80% for the Bhola I, Venture and Aggreko plants
As per the revised reserve estimates by Petrobangla for Shahbazpur & Bhola North fields, there seems to be sufficient gas reserves for NBBL; However a technical gas reserve study needs to be conducted for validation of the same

## Slide 12: Gas Transmission Outlook | Summary
Due to delay in construction of dedicated pipeline to Nimbus plant, NBBL has arranged temporary supply of natural gas from Bhola I gas supply pipeline; Plans for pipeline connecting Bhola Island to Barishal do not pose a risk in short to medium term for supply to NBBL
Sr. No | Parameter | Details | Output | Ref Slides
1 | Current Arrangement | The distribution franchise for Bhola island is with SGCL Currently, Bhola 1 Power Plant receives gas from Shahbazpur Gas Field via underground pipeline from Gas Field to SGCL Valve Station at Borhanuddin For NBBL 200 MW CCPP, a pipeline has been proposed from Shahbazpur Gas Field to Plant site However, considering delay in construction, NBBL has constructed a temporary pipeline and RMS for gas supply from Bhola 1 RMS. The current Bhola 1 RMS is capable of supplying ~2.1 MMSCMD (75 mmscfd) gas, which would be sufficient for both plants Post commissioning of the SGCL – Shahbazpur pipeline (expected by FY21) for NBBL, the gas would be supplied directly from the fields | Current Gas transmission arrangement from Bhola 1 RMS is sufficient to meet requirements for both plants at max utilization | 89-90
2 | Future Gas outlook for Bhola island | Construction of the SGCL – Shahbazpur pipeline (7 Kms, 12 inch diameter) is expected to be completed by FY21 leading to direct gas supply from Shahbazpur for NBBL plant With the new discovery of Gas in Shahbazpur East 1 and Bhola North Fields, the Government is considering a Bhola-Barishal gas pipeline to supply gas generated on Bhola island to consumers on mainland Bangladesh. The proposed pipeline is undergoing initial feasibility assessment with route survey and environmental studies being carried. | The Bhola Barishal pipeline is undergoing initial feasibility study with expected commissioning in ~5-7 years (post successful feasibility outcome) | 
Source: Petrobangla, GTCL, SGCL, NBBL, Industry Reports, Deloitte Analysis; Note 1) The gas requirement for both plants have been estimated at dispatch levels of 100% with SHR of Bhola I considered at 52% efficiency (as per actual achieved in FY19) and for Nimbus Plant at ~46% based on design SHR as per EPC contract
The SGCL – Shahbazpur pipeline is expected to be commissioned early next year (FY21) leading to direct gas supply to NBBL plant from Shahbazpur fields; The Bhola – Barishal pipeline is undergoing feasibility study which may take ~5-7 years for construction upon successful feasibility outcome

## Slide 13: Electricity Transmission Outlook | Summary
There is no constraint on the current planned evacuation from NBBL Plant towards Barishal Substation via 230 KV TL connecting Bhola-Barishal
Sr. No | Parameter | Details | Output | Ref Slides
1 | Current Arrangement | Nimbus will evacuate the power generated through Bhola I switchyard, which is connected to the 230 kV TL connecting Bhola Island to Barisal (N) Substation Currently, the 230 kV transmission line is loaded at 320 MW and it has max capacity of 545 MW. This is sufficient for evacuation of 220 MW power from Nimbus | Current Line is sufficient for evacuation of additional power from Nimbus | 97-100
2 | Potential considerations for evacuation of power | Loading constraint at Barisal N S/S due to insufficient existing capacity. The maximum evacuation possible from Barishal N S/S is 510 MW, but the evacuation capacity required with Bhola 1 (225 MW), Aggreko (95 MW) and Nimbus (220 MW) is 540 MW Potential backdown due to delayed commissioning of Gopalganj – Aminbazar 400 kV line. The Power from Payra (1320 MW) Imported Coal Based Power plant is planned to be evacuated by commissioning the Payra-Gopalgonj-Aminbazar 400 kV lines. Due to delay in the commissioning of the Gopalganj-Aminbazar TL, an evacuation constraint at Gopalgonj could have cascading effect on the power plants in the Bhola region Loading Constraint at Barisal (N) substation and Barisal – Gopalgonj 132 kV line in case of Payra power evacuation Due to delay of Payra-Gopalganj TL, there may be an evacuation constraint if power from Payra Coal Plant is evacuated using Payra-Patuakhali-Barisal (N) line at substation level. | While there is no constraint on transmission till Barishal N S/S, few considerations might pose some challenges for the evacuation of power from Barishal (N) Substation. This loading constraint at Barishal N could have a cascading impact on Bhola power plant. However, a detailed load flow study needs to be done to ascertain the same | 
Source: PGCB, NBBL, Deloitte Analysis Note 1) The power factor has been assumed at 0.85 considering industry standards
The current evacuation plan via 230 KV TL connecting Bhola – Barishal has sufficient capacity for NBBL; However the Barishal N substation may face loading constraints in case of full dispatch from Bhola Island Plants or dispatch from Payra Power Plant via Barishal
Detailed Load Flow Study required to ascertain actual risk for NBBL Plant

## Slide 14: DISCOM Credit Risk Assessment | Summary
Historically, BPDB had reliance on Government Subsidy to reduce losses; The same is expected to continue considering the gap in its power purchase and sales; However it has made regular payments to IPPs for power purchase with no payment defaults till date
Sr. No | Parameter | Details | Output | Ref Slides
1 | BDPB Historic Profitability | BPDB (Generation & Bulk Supply) has historically been incurring losses, primarily due to the differential in the overall power purchase cost and the allowed bulk supply tariff for BPDB. However the infusion of Government subsidy in the form of cash subsidy (since FY 18), has led to reduction in overall losses in FY19 making it match its overall revenue requirement from operations | Salient FY 19 parameters: BPDB has ~85% Billing to Cost Ratio Revenue : 332 BDT Bn Profit : -1 BDT Bn | 108-122
2 | BPDB Liquidity Position | Average creditor days range of ~50-70 days since FY15 whereas the average debtor days range of ~170-190 days However BPDB has made regular payments to IPPs historically | Salient FY 19 Parameters: Creditor Days: 66 Debtor Days: 182 | 
3 | BPDB Fixed Charge Payment to private players | As per our estimation, Bangladesh’s total power purchase cost of BDT 390 Bn in FY19, comprised ~BDT 173 Bn of fixed charges only Based on our demand supply outlook, Bangladesh’s average power demand is expected to grow at a CAGR of ~10.4% from ~7,800 MW to ~15,700 MW by FY26 We have projected the fixed charge payment obligations for BPDB considering the planned capacity additions as well as retirement of rental / quick rental plants (which have higher fixed charges due to their PPA tenures) | BPDB’s estimated Fixed Charge Payout: FY19 – BDT 173 Bn FY26 – BDT 281 Bn While the expected FC Payout CAGR growth is ~7.1%, it is lower than average power demand growth of ~10.4% | 
Source: BPDB, Industry Reports, Deloitte Analysis; Note [1]: BPDB’s fixed charge obligations estimated considering variable & fixed cost assumptions for HSD, HFO, Gas, Planned imported fuel based capacity additions among others. Please refer to Slide 113 for details
With subsidy infusion in the form of cash, BPDB’s financial position is expected to improve; Overall power demand growth is expected to grow at CAGR of ~10.4% which is much higher than fixed payment obligations growth of ~7.1%

## Slide 15: Fuel Supplier Credit Risk Assessment (BPC & SGCL)| Summary
BPC and SGCL are both profitable companies and hence are expected to make timely payments to their creditors; No risk is envisaged from a fuel supply perspective for Nimbus
Sr. No | Parameter | Details | Output | Ref Slides
1 | BPC Historical Profitability | BPC has been earning profits for the past 4 years (was loss making till FY14). Average profit of ~ BDT 54 Bn from FY15 – FY 19 The profitability was due to decline in Global Crude prices from ~$100 / barrel (Pre FY15) to ~$40-60 / Barrels (FY15 onwards) | Revenue FY19: BDT 453 Bn (CAGR ~5% FY15-19) Profit FY19: BDT 38 Bn | 123-130
2 | BPC Payable Assessment | BPC’s payables mainly comprises of payments to international crude suppliers and other natural gas companies in Bangladesh Last 4 years, accounts payable for trading activities has been consistent (these would majorly be accountable for imports) However, overall accounts payable has reached BDT ~230 Bn which indicates that BPC may be delaying payments for domestic operations | Average from FY16-FY19 Creditor Days: ~319 days Accounts Payable: Overall: ~ BDT 243 Bn Trading: ~ BDT 40 Bn | 
3 | BPC Receivables Assessment | BPC receives its trading receivable roughly within ~200-230 days signifying cash risk for the company | Average from FY16-FY19 Debtor Days: ~229 days Accounts Receivable: Trading: ~ BDT 254 Bn Others: ~ BDT 1 Bn | 
1 | SGCL Historical Profitability | SGCL has been profitable company with its revenue & net profitability rising at ~83% CAGR in the last 5 years. The revenue has increased primarily due to increased gas sales in its geographic area | Revenue FY 19: BDT 3,522 Mn Profit FY 19: BDT 399 Mn | 
2 | SGCL Liquidity | Overall receivables decreased from an ~2-4 months between FY15 -FY18 to ~1.2 month in FY19 indicating improved liquidity position SGCL’s creditor payable days has increased from ~5 months in FY18 to ~6.5 months in FY19 | D/E reduced from~6 in FY16 to ~4 in FY19 CR improved from ~1.5 in FY16 to ~1.9 in FY 19 | 
Source: BPDB, SGCL, Deloitte Analysis
In case of any future financial constraint faced by BPC and SGCL, the GoB is expected to provide financial support given the strategic importance of the power sector

## Slide 16: Foreign Participation Assessment | Summary
Gas based plants have witnessed major foreign investment from players such as Pendekar Group, GE, Standard Chartered, IDOs like IFC/ADB among others; Upcoming plants have foreign equity investment ~ 4000 MW with major recipients being plants on imported coal & LNG based plants
Sr. No | Parameter | Details | Output | Ref Slides
1 | Foreign Investment in Privately Owned Commissioned Plants | Investment has been mainly attracted by Gas based plants, with ~ 1,400 MW for Equity investment, 890 MW for Foreign Loan and 2,000 MW for Multilateral Agencies (MLA) based funding Overall, ~1,997 MW attracted foreign equity investment, ~ 2,057 attracted foreign loan and ~2,525 MW attracted MLA based funding, with Gas being the majority, followed by HSD | Key players given in table below | 131-139
2 | Foreign Investment in Privately Owned Upcoming Plants | Investment has been mainly attracted by LNG and imported Coal based plants. LNG attracted ~ 1,885 MW for Equity investment, 718 MW for Foreign Loan and 1,301 MW for MLA based funding. Whereas Imported Coal based attracted investment for ~1,531 MW for equity investment and ~1,224 MW for Foreign loan based funding. Overall, ~4,027 MW attracted foreign equity investment, ~ 2,391 attracted foreign loan and ~1,416 MW attracted MLA based funding. | Key players given in table below | 
 | Foreign Equity | Foreign Loan | Multilateral
 | Pendekar Energy (920 MW) | DEG (310 MW) | ADB (1,096 MW)
 | GE (341 MW) | Sumitomo Mitsui (300 MW) | IFC (1,036 MW)
 | APR Energy (300 MW) | Standard Chartered (288 MW) | IsDB (341 MW)
 | Sembcorp Utilities (282 MW) | Clifford Capital (282 MW) | IDA (360 MW)
 | Lakdhanvi Group (104 MW) | SMO (Netherland) (115 MW) | ICD, OFID (149 MW)
1
2
3
4
5
Following table constitutes major foreign players for operational plants
 | Foreign Equity | Foreign Loan | MLA
 | HTG Group & SEPCO -3 (1,224 MW) | CEXIM Bank (1,244 MW) | ADB & IDB (718 MW)
 | GE (1,167 MW) | DFCC & HNB (114 MW) | IFC (583 MW)
 | Reliance Power & JERA (718 MW) |  | 
 | PowerChina (307 MW) |  | 
 | Changzhou Hutang Coal Power Co. Ltd.(China) (162 MW) |  | 
1
2
3
4
5
Following constitutes the list of major foreign players for upcoming plants
Source: BPDB, Industry Reports Deloitte Analysis; Note: 1) The data for foreign equity, loan and multilateral investments do not indicate mutually exclusive investments 2) Some of the upcoming power projects may be delayed beyond FY26

## Slide 17: Foreign Participation Assessment | Summary
~1400 MW of commissioned capacity and ~1200 MW of upcoming (LNG) capacity could be looked at as an investment opportunity in the near future
Sr. No | Parameter | Details | Output | Ref Slides
1 | Investment opportunity in existing plants | There are presently ~3,400 MW operational, privately owned gas based plants, out of which ~ 2,000 MW has been commissioned over 7 years (and hence not considered for opportunity identification from investment point of view) The remnant ~1,400 MW of capacity, commissioned in last 7 years may provide suitable investment opportunity. | Identified plants given in table below | 135-137
2 | Investment opportunity in upcoming plants | 220 MW Gas based capacity is expected by private players (NBBL) For LNG based capacity addition, we expect ~ 1,200 MW of privately owned plants to be commissioned by FY26. These plants are owned by Summit, United Group, with 2 more LNG plants being planned by Anlima Textile / GE and the Unique Groups | Identified plants given in table below | 
Plant Name | Capacity (MW) | COD | PLF FY19 | Efficiency | Owner
Summit Bibiyana II | 341 | 2015 | 76% | 28.88% | Summit
Kushiara Power | 163 | 2017 | 76% | 35.70% | Max
Sembcorp NWPC | 282 | 2018 | 31% | 42.71% | Sembcorp
United Ashuganj | 195 | 2015 | 24% | 42.51% | United
Summit Meghnaghat | 305 | 2015 | 24% | 43.09% | Summit
Regent Power | 108 | 2014 | 37% | 37.26% | Regent
Plant Name | Capacity (MW) | COD (Estimated) | Owner Group
Meghnaghat 600 MW CCPP – Summit | 584 | 2024 | Summit Group
Meghnaghat 600 MW CCPP – UMPL | 583 | 2024 | United Group
Meghnaghat 500 MW - Anlima Textile & GE | 450 | 2027-2030 | Anlima & GE
Meghnaghat UECL | 450 | 2027-2030 | Unique Energy
Source: BPDB, Industry Reports Deloitte Analysis; Note: 1) Summit 305 MW has been running at duel fuel with HFO due to gas shortage in FY16 and FY17. With increasing gas availability, it is expected to ramp up dispatch Note 2) Sembcorp 282 MW was commissioned in October 2018 and is expected to ramp up dispatch from FY20 onwards
Following table indicates the list of projects for potential investment (commissioned in the last 7 years)
Following table indicates the list of upcoming projects for potential investment opportunity in Bangladesh

## Slide 18: Contract Risk Assessment | Summary
Doc | Sr. No | Parameter | Key Risk | Ref Slides
PPA | 1 | Tariff | Recovery of capacity charge is based on dependable capacity which provides an incentive to achieve a higher dependable capacity. However, there is no such incentive in the O&M contract The Reference Heat Rate is not adjusted for the life of plant (yearly degradation) | 139-149
 | 2 | Start-up Payment | Since energy payment is based on Reference Heat Rate it would most likely be that the fuel consumed during the start-up would be partially recoverable through tariff. Thus for 40 free start-ups Company may have some revenue loss | 
 | 3 | Supplemental Tariff Payment | The applicability of Supplemental Tariff is only if the cost incurred by Company is more than USD 450K There is no provision for Supplemental Tariff recovery in case of Force Majeure Event | 
 | 4 | O&M | O&M costs are not pass through and are paid based on a reference rate quoted in the PPA. On the other hand, O&M contracts specifies a flat rate of O&M cost plus escalation. Thus in case the plant is not dispatched it could lead to under recovery of the O&M costs | 
 | 5 | Taxes | Taxes are not a pass through except for taxes on fuel/gas | 
 | 6 | Usage of Alternate Fuels | Right to switch to alternate fuel is provided only to BPDB, NBBL cannot do it suo-moto In case Gas is not supplied and NVVN raises it as an PE event and BPDB does not give permission to switch even then Capacity Payments would continue to happen, which reduces any financial risk on the project | 
 | 7 | Late Payment Fee | The PPA does not have any provision for late payment fee whereas the GSA/FSA/O&M agreements have the same. This could lead to working capital issues. However, the PPA allows encashing of LC or right to suspend in case of payment delays | 
 | 8 | FM/PE situation | No restoration cost can be recovered in the case of an FM event Also in case FM/PE Event is declared by the Company then the FM/PE Ratio would be dependent on the dependable capacity or 0 in case of non working condition. This would have an impact on the payment of Capaity charges. Also since Grid system failure is part of FM event any such failures could lead to under recovery depending on the applicable FM Ratio | 
Source: PPA, GSA, FSA

## Slide 19: Contract Risk Assessment | Summary
Doc | Sr. No | Parameter | Key Risk | Ref Slides
PPA | 9 | Termination | There is not provision of mutual termination or any exit clause in the PPA Payment in case of Company Event of Default is only for any outstanding loans, debts and winding up costs. No compensation for equity investments would be provided | 150-156
 | 10 | Offtake Guarantee | No offtake guarantee is a risk However since capacity payments are guaranteed this could be acceptable | 
 | 11 | LD due to Forced Outage | O&M has a back to back LD clause with a Cap of 10% of Base Fee. There is no such cap mentioned in the PPA | 
 | 12 | LD due to Declaration & Delivery of Available Capacity | O&M has a back to back LD clause with a Cap of 10% of Base Fee. There is no such cap mentioned in the PPA After beginning of day: No back to back clause in the O&M agreement Failure for dispatch: No back to back clause | 
 | 13 | Operating Norms | For Gas Operation, the reference heat rate is higher in the PPA only for 100% plant factor For Fuel Operation, the reference heat rate is the same for 100% Plant factor, but is lower for PPA reference rate at all other plant factors | 
Source: PPA, GSA, FSA

## Slide 20: Contract Risk Assessment | Summary
Doc | Sr. No | Parameter | Key Risk | Ref Slides
GSA | 1 | Billing & Payment | There is no performance guarantee from the supplier Late payment fee applicable which is not there in case of the PPA | 157-160
 | 2 | Gas Supplier Event of Default | Only supply below 50% is Gas Supplier Event of Default | 
FSA | 2 | Billing & Payment | Payment for Fuel is to be made before delivery while corresponding recovery through sale of power is made 30 days after invoicing power sold | 161-164
 | 3 | Fuel Supplier Event of Default | There is no penalty if the aggregate supply in a year is greater than 50% | 
O&M | 1 | Penalty Mechanism | Liquidated Damages are capped for O&M Agreement | 165-168
 | 2 | Base Fees | No provision for incentive payments for higher dependable capacity | 
 | 3 | Billing & Payment | NBBL is liable to pay late payment charges in case of delay in payment. However there is no back to back clause for the same in the PPA | 
IA | 1 | Equity Lock in | The condition of Equity lock-in restricts the transfer of NBBL’s ownership for a period of 6 years. For a transaction to take place, approval from Government of Bangladesh would be required. | 169-170
 | 2 | Termination | In case of termination due to Company event of default, GOB has only an option but not an obligation to take possession of the facility and pay a compensation amount to NBBL equivalent to the principal outstanding and the interest thereon with no provision to recover equity investments In case facility cannot be restored after an FM event no compensation would be paid by GOB with only termination rights provided to the Company | 
Source: PPA, GSA, FSA

## Slide 21: Policy & Regulatory Overview | Summary
Source: MPEMR, BERC, Petrobangla, ERD, Government Act, Rules and Notifications
Sr. No | Regulation | Description | Ref Slides
1 | Bangladesh Electricity Act, 2018 | The law provides for establishment of an Independent System Operator in Bangladesh, thus making power dispatch according to merit order | 172
2 | Bangladesh Energy Regulatory Commission License Regulations, 2006 and its amendment in 2016 | The existing gas based generation company has to comply with the license terms and conditions and exercise its responsibilities as per the regulations, failing which the Commission may suspend or revoke the license | 
3 | Bangladesh Energy Regulatory Commission (Natural Gas Distribution Tariff) Regulations, 2010 | Regulated gas distribution tariff means higher certainty for gas price compared to a market-based gas pricing arrangement | 
4 | Bangladesh Electricity Regulatory Commission Electricity Grid Code Regulations 2018 | The gas based plant has to abide by the standards, procedures and compliance requirements as stipulated in the grid code | 173
5 | Bangladesh Electricity Regulatory Commission Electricity Distribution (Retail) Tariff Regulations 2016 | Provides for determination of retail tariff on cost-plus basis for electricity distribution companies of Bangladesh; Regulated revenue for distribution companies has impact on Single Buyer receivables, which in turn may impact generation company receivables | 
6 | Quick Enhancement of Electricity and Energy Supply (Special Provisions) Act, 2010 and its amendments in 2015 and 2018 | This Act encourages and facilitates implementation of new generation projects and hence creates competition for the existing generation project | 174
7 | Bangladesh Gas Act 2010 | The regulation provides for restrictions or suspension in supply of gas to customers or disconnection in the gas line in cases of Gas crisis at national level, Need to prioritize gas distribution among users, Gas is used at less than the efficiency prescribed by the Government/Commission/Company | 
8 | Bangladesh Energy Regulatory Commission Dispute Settlement Regulations, 2014 | Provides for the procedures and institutional responsibilities for the purpose of resolution of disputes | 
9 | Vision and Policy Statement on Power Sector Reform, 2000 and National Energy Policy (NEP), 2004 | The pricing policy (NEP) further states that the present subsidy on gas price for power and fertilizer is to be removed gradually. Subsidy, if required, is to be given at the end-user level and the related liabilities cannot be passed on to the utilities The Policy (NEP) also calls for maintenance of adequate reserve margin by installing capacities in excess of peak demand (say 25%) so that the system can reliably accommodate planned maintenance and forced outage | 175

## Slide 22: Policy & Regulatory Overview | Summary
Sr. No | Regulation | Description | Ref Slides
10 | Private Sector Power Generation Policy of Bangladesh, 2004 and Policy Guideline for Small Power Plant (SPP) in Private Sector | The policies offer clarity on power offtake and tariff-related matters for existing IPP projects such as minimum equity requirement of 20%, GoB guarantee on PPA for utility performance, Tax exemptions etc | 176
11 | Policy Guidelines for Enhancement of Private Participation in the Power Sector, 2008 | This policy aims at facilitating selling of power from private power plants shedding light on matters such as choice of fuel, fuel supply responsibility and requisite experience of developers | 177
12 | Renewable Energy Policy of Bangladesh, 2008 | Aims at development of renewable energy resources in Bangladesh and targets to meet 10% of the country’s power demand from RE sources by 2020 | 178
Source: MPEMR, BERC, Petrobangla, ERD, Government Act, Rules and Notifications

## Slide 23: Table of Contents
Bangladesh – Country Overview | 
Power Market Demand Supply Outlook | 
Gas Transmission & Supply Outlook | 
Electricity Transmission Outlook | 
Gas & Fuel Pricing Assessment | 
Discom Credit Risk Assessment | 
Fuel supplier Credit Risk Assessment | 
Assessment of Foreign Participation in Power Sector | 
Contracts Risk Assessment | 
Policy & Regulatory Assessment | 
01
02
03
04
05
06
07
08
09
10

## Slide 24
Bangladesh – Country Overview
Overview of the Bangladesh economy, growth drivers, trade balance and foreign reserves
01
02
03
04
05
06
07
08
09
10

## Slide 25: Bangladesh – Country Overview & Power Sector Value Chain

## Slide 26: Country Overview | Bangladesh
Following figure shows the sectoral and overall GDP growth (%) of Bangladesh for past 5 years: Following figure shows Share of Each Segment in the Overall GDP (%) of Bangladesh in FY15 and FY19.
Bangladesh has grown at an average of 7%-7.5% over the last 5 years backed by strong industrial growth and is expected to continue growth at a higher rate as the Government targets to become an Upper Middle-Income country by 2031
Bangladesh Country Overview: The overall Bangladesh GDP grew at an average of ~7-7.5% in the last 5 years from BDT 15,158 Bn in FY15 to BDT 25,425 in FY19. Bangladesh has targeted to become an “Upper Middle-Income Country” by FY2031 i.e. having GNI per capita between $3,996 - $12,375 According to World Bank, Bangladesh has achieved GNI per capita of ~$1,258 in FY18. The Bangladesh economy needs to grow at a CAGR of ~9%-10% during FY2020 to FY2031 to achieve its per capita income target. Historically, Industrial and services segment has been major growth drivers for the Bangladesh economy with the manufacturing of leather, food products, wearing apparels, transport equipment and construction sectors witnessing stronger growth over the years. The graph to the right (below) shows the Share of Each Segment of GDP in Bangladesh in FY15 and FY19. As can be seen from the graph, Industrial Segment has grown from 30.4% to 35% between FY15 and FY19 and is expected to expand further as the Government pushes for higher growth in the coming years.
Chart: 
 | 3.3 | 2.8 | 3 | 4.19 | 3.92
 | 9.7 | 11.1 | 12.1 | 12.06 | 12.67
 | 5.8 | 6.3 | 6.7 | 6.39 | 6.78
 | 6.2 | 7.1 | 7.3 | 7.86 | 8.15
  6.7%
  6.2%
  3.3%
  9.7%
  FY15
  7.1%
  2.8%
  12.1%
  11.1%
  6.3%
  FY16
  3.0%
  8.2%
  7.3%
  FY17
  12.1%
  6.4%
  7.9%
  FY18
  3.9%
  12.7%
  6.8%
  FY19
  Agriculture
  GDP (at FY06 Constant Prices)
  Industry
  Services
Chart: 
 | 16 | 30.4 | 53.6
Chart: 
 | 13.6 | 35 | 51.4
  Industry
  Agriculture
  Services
  FY15
  FY19
IMF has projected Bangladesh to grow at ~7.3-7.4% p.a. between FY20 and FY24
However the Covid-19 pandemic may restrict higher growth levels in FY20
Source: Bangladesh Bank, Bangladesh Vision 2020, IMG World Economic Outlook 2019, Industry Report;

## Slide 27: Country Overview | Bangladesh Trade Balance & Foreign Reserves
The country’s high trade deficit has been mitigated by the support from overseas Worker’s Remittance and other project aids and global grants
Major import and export items Bangladesh is a net importer of goods and services in the global market The country is dependent on international trade for major petroleum products and capital machinery which constitute ~20% of the total imports The country’s major export revenue comes from its readymade garments and Jute & leather products for which it also imports the raw materials In FY19, the country had a net trade deficit of ~USD 20 Bn Trade Balance Although facing a deficit in its global trade account, Bangladesh has been able to manage its foreign reserves position Its overall foreign reserve position has been supported by Remittances & Multilateral / Bilateral Aids & Grants The overall Worker’s Remittance is expected to USD ~16 Bn in the FY19 assisting the country to bridge the trade gap As can be seen on the graph on the right, the overall Foreign Reserve position of Bangladesh has remained at ~USD 30-33 Bn in the last 4 years A natural hedge exists in the country as majority readymade garment factories are export oriented and get paid in dollars. Consistent foreign reserve account and a natural hedge due to readymade garments showcase positive health for the country from a FOREX perspective
Following chart shows the share of major import and export items for FY 2018-19 in USD Billion Following chart shows the Current & Capital Account Balance of Bangladesh (USD Bn) and the Foreign Reserves (USD Bn):
Chart: 
 | 30.558 | 8.693
 | 2.383 | 1.378
 | 2.932 | 25.27
 | 4.325
 | 4.985
 | 5.147
 | 5.731
  10%
  9%
  Import(FY19)
  4%
  5%
  9%
  8%
  55%
  72%
  4%
  25%
  Export(FY19)
  56
  35
  POL
  Capital Machinery
  Textile & Articles
  Iron, Steel, etc.
  Raw Cotton
  Plastics / Rubber
  Others
  Readymade Garment
  Jute / Leather Products
  Others
Chart: 
 | 3.492 | 4.262 | -1.48 | -9.78 | -5.254
 | 1.763 | 1.408 | 4.493 | 9.368 | 5.861
  FY16
  FY15
  FY17
  FY18
  FY19
  Current Account Balance
  Capital & Financial Account
25.0
30.1
Foreign Reserves (USD Billion
33.5
32.9
32.6
Source: Bangladesh Bank, ERD – Govt. of Bangladesh, Deloitte Analysis; Note 1) For Power Import, the exchange rate computation considered at 1 USD = 80 BDT in FY19

## Slide 28
Power Market Demand Supply Outlook
Historical demand & supply, future demand & supply and possible dispatchibility of plant considering merit order
01
02
03
04
05
06
07
08
09
10

## Slide 29: Historical Power Demand, Supply & Merit Order Assessment

## Slide 30: Power Market | Bangladesh Industry Value Chain
Bangladesh follows a Single Buyer Model wherein all generators need to sell power directly to BPDB which in turn sells to discoms. This makes BPDB the largest entity in the power sector.
Generation
Installed Capacity – 18,961 MW
Ashuganj Power Station Company Limited (7.6%)
RPCL / BPDB-RPCL
(1.7%)
Bangladesh Power Development Board (29%)
Rural Electrification Board
(1.3%)
North West Power Generation Company Limited (7.4%)
Electricity Generation Company of Bangladesh (4.4%)
Government Companies
(51.4% Share in IC)
Private, Imports
(48.6% Share in IC)
Independent Power Producers & Small Independent Power Producers (34.3%)
Rental Plants / Quick Rental Plants
(8.1%)
Imports from India
(6.1%)
Single Buyer
Purchase – 68,600 MUs
Bangladesh Power Development Board
Government Company
Transmission
Ct. Km – 11,650 Km
Power Grid Company of Bangladesh Limited
Government Company
Distribution
Purchase from Single Buyer – 66,547 MUs
Rural Electrification Board (49.2%)
West Zone Power Distribution Company (5.84%)
Bangladesh Power Development Board (17.1%)
Northern Electric Supply Company (5.89%)
Dhaka Power Distribution Company (14.1%)
Dhaka Electric Supply Company (8.4%)
Government Companies
Ministry of Power, Energy and Mineral Resources, Government of Bangladesh
Bangladesh Electricity Regulatory Commission (BERC)
Government / Regulator
Source: BPDB, DESCO, DPDC,PGCB, Industry Reports; All figures are for FY2018-19

## Slide 31: Power Market | Historical Power Demand Met
Following figure shows the peak demand met (MW) or peak generation (MW) in Bangladesh for past 5 years: Following figure shows net electricity generated (MU), retail electricity consumed (MU) and Average Power Demand (MW)
The Peak Power Demand Met and retail electricity consumption in Bangladesh grew at a CAGR of ~13% and ~12% respectively over the last 5 years
Chart: 
 | 7817 | 9036 | 9479 | 10958 | 12893
FY15
FY18
FY16
FY17
FY19
  +13.3% CAGR
  Peak Demand Met (MW)
Historical Power Demand: The country’s high GDP growth has also been complemented by the growth of the power sector which is critical to support the industrial and commercial activity The Government of Bangladesh has also set a target for Power for All with 100% electrification by FY2021 The graph to the right (above) presents the trend for peak power demand met in Bangladesh over the past 5 years, i.e. from FY 2015 to FY 2019. It can be seen that the peak power demand met or peak generation has grown at a CAGR of 13.3%. The key reasons include higher GDP growth fueling power demand, Government of Bangladesh’s ambitious Power for All Program The graph to the right (below) for net electricity generated (MU) retail electricity consumed (MU) and Average Power Demand (MW) in the country also exhibits a similar trend with the latter growing at a CAGR of 11.9% over the past 5 years. The average T&D Loss has been in the range of ~12-13% in Bangladesh in the last 5 years.
Chart: 
 | 4698.2772 | 4956.7597 | 6317.7535 | 6939.7014 | 7832.4975
 | 43738 | 52193 | 57276 | 62678 | 70533
 | 39620 | 45299 | 50260 | 55103 | 62037
  FY15
  FY18
  FY17
  FY16
  FY19
  +11.9% CAGR
  Net Electricity Generated (MU)
  Net Electricity Consumed (MU)
  Average Power Demand (MW)
Source: BPDB

## Slide 32: Power Market | Unmet Power Demand
Following graph shows the Peak Demand Met & Peak Demand in Bangladesh in FY19
Unmet Power Demand Although Bangladesh’s peak generation was 12,893 MW in FY19, PSMP 2016 (revisited study) projected a peak demand of 13,975 MW (base case) in FY19 The demand projection by PSMP 2016 (RS) was based on demand data collected from discoms in Bangladesh which signifies there is unmet demand in Bangladesh The study further projects that in case of higher GDP growth rate the peak demand in FY19 could be ~15,051 MW Thus, in terms of overall unmet demand Bangladesh could have ~1,000 MW to ~2,148 MW in FY19 Many studies and news reports also state that there may be unmet demand in Bangladesh due to frequent load shedding, ageing & inadequate transmission networks leading to demand-supply gap
As per PSMP 2016 (RS) there may be ~1,000-2,100 MW (between 8%-16%) of unmet power demand in Bangladesh
Chart: 
 | 12893 | 13975 | 15041
  Peak Demand Met in FY19
  Peak Demand (Base Case)
  Peak Demand (High Case)
(8%)
(16%)
Unmet Demand
Bangladesh’s robust economic growth has underpinned a surge in demand for electricity, which is still currently underserved by Bangladesh’s existing power infrastructure.
In addition, Gas shortages and the unreliability of some power plants due to plant age or inefficiencies have resulted in actual dependable generation capacity being 2 to 4 GW lower than the estimated 13.7 GW that is registered.
- WoodMac, 2018
Despite increased power generation capacity, Bangladesh faces significant outages during the peak demand hours, especially during the irrigation and summer seasons.
Load shedding and power outage accounts for an output loss of nearly 3 percent of the GDP.
About 65 percent of Bangladeshi firms invest in back-up generation, adding to substantial costs in doing business.
- World Bank, Nov 2019
The country may have increased its capacity to produce electricity but the electricity it is producing is of very low quality.
‘Quality power is uninterrupted supply of power with accurate voltage,’
- Shamsul Alam, Energy Advisor, Consumers Association of Bangladesh
Source: BPDB, PSMP 2016 Revised Study, Industry Reports, Deloitte Analysis

## Slide 33: Power Market | Historical Power Demand
Following figure shows the electrification ratio (%) in Bangladesh for past 5 years: Following figure shows the category wise retail electricity consumption (MU) for past 5 years:
Bangladesh has achieved 96% electrification ratio and is on track to achieve 100% ratio by FY2021; Domestic, Commercial and Industrial segments have shown over 8% YoY Growth
Historical Power Demand: The graph to the right (above) presents the electrification ratio in Bangladesh over the past 5 years, i.e. from FY 2015 to FY 2019. As can be seen from the graph, Bangladesh has achieved 93% electrification ratio in FY19 and is on track to achieve 100% electrification by FY2021 The graph to the right (below) showcases the category wise contribution in the retail electricity consumption in Bangladesh Domestic power consumption has been the driving factor for power consumption in Bangladesh along with Commercial and Industrial segment (excluding captive). The CAGR of the various consumer segments between FY15 and FY19 are as follows: Domestic – 12.7% Agriculture – 1.6% Industrial – 8.3% Commercial – 19.5% Others – 27.4% There is also a captive power base of ~3,000 MW in Bangladesh which is serving the industrial power demand and is not included in the above consumption growth.
Chart: 
 | 523.0368 | 851.6212 | 1005.3 | 1179.2042 | 1377.2214
 | 3685.032 | 4230.9266 | 4659.5655 | 5063.9657 | 7512.6807
 | 13305.7392 | 15528.4972 | 17818.9425 | 18415.4226 | 18331.9335
 | 1636.4712 | 1635.2939 | 1553.1885 | 1432.678 | 1743.2397
 | 20469.7584 | 23052.6611 | 25222.977 | 29011.7295 | 33071.9247
  2%
  52%
  9%
  3%
  4%
  34%
  9%
  1%
  FY15
  4%
  3%
  51%
  34%
  2%
  FY16
  45,299
  FY19
  50%
  9%
  3%
  35%
  9%
  62,037
  2%
  FY17
  53%
  33%
  2%
  FY18
  53%
  30%
  12%
  39,620
  50,260
  55,103
  Domestic
  Industrial
  Agriculture
  Commercial
  Others
Chart: 
 | 73.17 | 75.92 | 88 | 90 | 96
  FY15
  FY16
  FY17
  88%
  FY18
  73%
  FY19
  76%
  90%
  96%
Source: BPDB, Power Cell, World Bank, Industry Reports

## Slide 34: Power Market | Historical Power Supply
Following figure shows the Installed Capacity (MW) and fuel-wise percentage contribution in the installed capacity for past 5 years: Following figure shows average Gross PLF of Gas, HFO and HSD based plants in Bangladesh for the past 5 years:
The Installed Capacity in Bangladesh has grown at a CAGR of ~15% in the last 5 years with Gas and HFO based plants contributing ~80% of the installed capacity
Historical Power Supply: The graph to the right (above) presents the Installed Capacity (MW) and fuel-wise percentage contribution in the installed capacity for past 5 years i.e. from FY 2015 to FY 2019. It can be seen that the installed capacity has grown at a CAGR of 14.7% which is almost inline with the Peak Power Demand Met in Bangladesh. Bangladesh has higher contribution of Gas and HFO based power plants along with HSD based plants About ~2,000 MW of installed capacity has been commissioned as Rental / Quick Rental power plants with average PPA tenure of 3-5 years These plants were commissioned to quickly meet the power deficit in the country. However these plants generally have smaller capacity (<~100 MW) and consume higher fuel due to their operation mode at lower efficiencies (simple cycle for Gas engines) The graph to the right (below) presents the average PLF of Gas, HFO and HSD based power plants in the country for the last 5 years. Gas based plants ran at ~55% PLF in the country, followed by HFO and HSD at ~27% and ~17% respectively in FY19 In it important to note that ~ 55% PLF on average is due to the fact that there is ~ 2,000 MW of aged plants which typically run at low PLF (<30%) due to efficiency issues. Newer gas power plants typically run at PLF of ~ 70-85%
Chart: 
 | 500 | 600 | 600 | 3 | 30
 | 200 | 250 | 250 | 660 | 1160
 | 230 | 230 | 230 | 524 | 524
 | 2301 | 2629 | 2785 | 230 | 230
 | 927 | 1028 | 880 | 3443 | 4770
 | 6781 | 7628 | 8810 | 1380 | 1370
 | 9714 | 10877
  25%
  21%
  62%
  8%
  8%
  21%
  18,961
  15,954
  5%
  62%
  FY15
  13,555
  5%
  10,939
  FY16
  6%
  21%
  4%
  12,365
  6%
  FY17
  61%
  9%
  22%
  4%
  57%
  FY18
  7%
  FY19
  65%
  +14.7%
  Gas
  Coal
  Hydro
  HFO
  HSD
  Import
  Solar
Chart: 
 | 53.1 | 56.6 | 52.3 | 49.8 | 53.7
 | 36.8 | 37.7 | 40.8 | 36 | 27.3
 | 21 | 23 | 34.1 | 37.4 | 16.8
  FY15
  37%
  FY16
  50%
  FY17
  53%
  FY18
  21%
  FY19
  57%
  36%
  38%
  23%
  52%
  34%
  41%
  37%
  54%
  27%
  17%
  Gas
  HFO
  HSD
Source: BPDB, Deloitte Analysis; Note 1) For PLF computation, the auxiliary consumption has been considered at 3% for gas based power plants

## Slide 35: Power Market | Merit Order
The Merit Order showcases that Domestic Gas based power plants have the lowest cost of power in Bangladesh, followed by HFO and HSD
Following Figure shows the Tentative Merit Order in Bangladesh based on the Average Power Purchase Cost / Power Generation Cost by BPDB as a Single Buyer in FY2019: As can be seen above, the total cost of generation in Bangladesh typically ranges from Tk 0.9 – 40 / kWh with a few plants having overall cost of generation beyond Tk 80 / kWh (excluded from the above graph) These high cost plants are run at part load and only for meeting peak generation in a short duration of time As mentioned earlier, Bangladesh also has ~2,000 MW of Rental / Quick Rental plants with PPA tenure of 3-5 years i.e. their fixed cost recovery is done within an extremely short duration which leads to high cost of generation compared to plants with PPA of 20-25 years
  75%
  70%
  10%
  65%
  60%
  25
  90%
  55%
  85%
  50%
  0%
  20
  45%
  0
  40%
  35%
  30%
  5
  20%
  5%
  100%
  25%
  15%
  10
  40
  95%
  35
  80%
  30
  15
  Total MUs sold in Bangladesh in FY19 – 70,533 MUs
  Tk / KWh
  Gas
  HSD
  Hydro
  Coal
  Import
  HFO
  SOLAR
Tk 0.9 – 4.6 / kWh – Gas
Tk 3.5 – 7.5 / kWh – Imported Power
Tk 9 – 14 / kWh – HFO
Tk 15 – 25 / kWh – HSD
 | Fuel | Total MU
 | Gas | 48,306
 | HFO | 11,426
 | HSD | 2,022
Source: BPDB, Deloitte Analysis

## Slide 36: Natural Gas Supply Assessment

## Slide 37: Power Market | Natural Gas Supply
Natural Gas consumption has been almost stagnated since FY16 due to lack of additional discoveries in the country
Following figure shows the sectoral consumption of Natural Gas in Bangladesh (mmscmd) in the last 6 years: Following figure shows the remaining reserves of (2P, BCM) of natural gas in the last 5 years:
Historical Gas Demand & Supply: The graph to the right (above) presents the sectoral and overall consumption of natural gas in Bangladesh over the past 6 years, i.e. from FY 2014 to FY 2019. Power Sector is the largest consumer of natural gas with 35 mmscmd consumed by grid connected power plants and 12.2 mmscmd by captive power plants. The Government of Bangladesh had stopped providing new captive power connections in 2015 and had also stopped new household PNG connections However with planned LNG terminals the Govt. has tentatively resumed newer connections to these consumer categories. As per Petrobangla, about 23 mmscmd of natural gas demand is latent due to natural gas production availability issues The graph to the right (below) presents the remaining reserves of domestic natural gas in Bangladesh At the current production level of ~75-76 mmscmd, the remaining reserves of ~325 BCM (~890 mmscmd) in FY2018 is expected to last for the next 11-12 years considering no new reserves are operationalized. As per various news sources, Bangladesh discovered ~1 TCF (~77 mmscmd / 28 BCM) of natural gas in the Shahbazpur area and 420 BCF (~33 mmscmd / 12 BCM) in Bhola North However for Shahbazpur field Petrobangla had upgraded the total 2P reserves of the field by ~6.9 BCM (19 mmscmd) only in FY2018 whereas for Bhola North it had considered ~12 BCM (33 mmscmd) as 2P reserves
Chart: 
 | 0.06 | 0.06 | 0.07 | 0.08 | 0.07 | 0.08
 | 11.15 | 11.64 | 12.48 | 12.45 | 12.45 | 12.22
 | 4.17 | 4.18 | 4.08 | 3.81 | 3.33 | 4.47
 | 0.69 | 0.71 | 0.7 | 0.67 | 0.63 | 0.62
 | 11.01 | 11.46 | 12.1 | 12.66 | 12.92 | 12.76
 | 3.11 | 3.33 | 3.61 | 3.64 | 3.58 | 3.36
 | 7.88 | 9.17 | 10.97 | 11.98 | 12.25 | 12.33
 | 26.17 | 27.52 | 31 | 31.31 | 30.93 | 34.98
  7.9
  FY14
  FY15
  FY16
  FY17
  FY18
  FY19
  64.2
  80.8
  68.1
  75.0
  76.6
  76.2
  +4.7%
  Power
  Domestic (PNG)
  Tea Estate
  Industry
  Commercial
  CNG
  Fertilizer
  Captive
Chart: 
 | 80.82
 | 22.8
  104
  Unmet Demand
  23
As per Petrobangla, Bangladesh had an unmet demand of 23 mmscmd in FY19 due to low gas production in the country
Chart: 
 | 412.1643 | 385.3771 | 364.8127 | 337.4671 | 324.7875
  FY18
  FY17
  FY16
  FY14
  FY15
  -5.8%
  Remaining Reserve for Natural gas (2P, BCM)
Availability of Domestic Natural Gas at current production level: 11-12 Years
Source: Petrobangla, Deloitte Analysis

## Slide 38: Power Market | Natural Gas Supply
With limited Natural Gas reserves, the Government of Bangladesh has promoted imported LNG as one of the substitutes to meet the energy need of the country
Following figure shows the sector wise natural gas demand in Bangladesh in the next 5 years (Mmscmd): Following figure shows import capacity of LNG and volume of LNG imported in 2018 and 2019 in MMSCMD:
Gas Demand projection: The graph to the right (above) presents the gas demand projection by Petrobangla from FY2019 – FY2023 As per Petrobangla, the gas demand in FY2019 was ~104 mmscmd against the actual consumption / supply of ~81 mmscmd signifying demand shortfall of ~23 mmscmd This shortfall is expected to be met by LNG imports Overall, the gas demand is expected to increase to ~140 mmscmd by FY2023 increasing at a CAGR of 7.9% from FY2019 LNG Imports: Considering the depletion of the existing natural gas fields, Bangladesh has commissioned ~1,000 mmscfd (~7.86 MTPA / 28.3 mmscmd) of FSRU’s for import of LNG These FSRUs are operational as on February 2020 Further ~4,000 mmscfd (~31.44 MTPA / 113 mmscmd) of planned FSRUs / Land based terminal have been announced by various players in Bangladesh which have either been delayed or shelved. The Government of Bangladesh has also announced development of a 7.5 MTPA (~27 mmscmd) of onshore land based terminal in Bangladesh which is the only planned expansion under development at any stage In terms of production of domestic natural gas, BERC expects the gas production to be ~73 mmscmd in FY20 Thus, overall Bangladesh is expected to continue with the existing supply capacity of ~101 mmscmd till FY24 which may increase to ~128 mmscmd by FY30
Figures in mmscmd
Chart: 
 | 0.084986 | 0.084986 | 0.084986 | 0.084986 | 0.084986
 | 16.2323 | 19.745 | 22.068 | 25.4674 | 28.5552
 | 8.9802 | 8.9802 | 8.9802 | 8.9802 | 8.9802
 | 0.82153 | 0.87819 | 0.93484 | 0.96317 | 0.96317
 | 14.7025 | 17.7337 | 19.8017 | 22.7762 | 25.4674
 | 4.6742 | 4.7309 | 4.7592 | 4.7875 | 4.8442
 | 12.6912 | 12.6912 | 12.6912 | 12.6912 | 12.6912
 | 45.4674 | 47.2238 | 49.0368 | 58.8669 | 58.8669
  13
  13
  13
  9
  FY20
  9
  9
  FY19
  5
  5
  13
  9
  FY21
  9
  FY22
  13
  5
  FY23
  104
  112
  118
  135
  140
  +7.9%
  Power
  Industry
  Domestic (PNG)
  Commercial
  CNG
  Fertilizer
  Captive
  Tea Estate
Chart: 
 | 73 | 73 | 101.3 | 101.3 | 128.3
 | 28.3 | 27
  Existing Average Domestic Gas Production
  Imported LNG Capacity Commissioned
  Total Planned Natural Gas Supply Capacity (FY19-FY24)
  Additional Onshore 7.5 MTPA Planned Terminal
  Total Expected Import Capacity (FY30)
Source: Petrobangla, BERC, Industry Reports, Deloitte Analysis
Current Capacity
Expected between FY25-FY30

## Slide 39: Power Market | Natural Gas Supply
Following graph shows the historical consumption for Natural Gas & Proposed allocation (mmscmd) for Natural Gas as per BERC: The following table illustrates the priority level of each sector for Natural Gas as defined by Petrobangla:
With introduction of LNG in power sector, the gas allocation to the sector is expected to increase from ~31 mmscmd in FY18 to ~40 mmscmd in FY20; further allocation may take place in the future by curtailing gas to low efficient power plants and other non important sectors
Natural Gas / LNG Consumption & Future Projection Power has been provided the highest allocation for natural gas in Bangladesh by BERC for FY20 in line with historical dominance of the sector in gas consumption BERC estimated the blended Natural Gas and LNG consumption in the country to increase from ~76 mmscmd in FY18 to ~95 mmscmd in FY20 The increase considers addition of 24 mmscmd to come from the FSRUs while it also estimates about ~3 mmscmd fall in the domestic natural gas production Gas Priority Guidelines by Petrobangla (2013) In 2013, Petrobangla came up with Gas priority guidelines considering the natural gas shortage in the country The defined priority list for sectors has been illustrated on the graph on the right (bottom) The guidelines also recommend a number of efficiency measures: To reduce gas to the fertiliser sector by 10%, and to increase the efficiency of fertilizer factories To limit the total allocation of gas to the power sector to 40% of the daily gas supply, only provide gas supply to new power plants that have more than 50% fuel efficiency, and are based on combined cycle technology and duel-fuelled. Suspend gas supply to low efficiency power plants; To reduce gas supply to filling stations, price increases for CNG, and To reduce gas supply to low-efficiency captive power plants.
Chart: 
 | 0.072959 | 0.085753
 | 0.63381 | 0.72419
 | 3.584 | 4.2879
 | 3.3344 | 5.4314
 | 12.2541 | 13.3403
 | 12.4541 | 15.8654
 | 12.9215 | 16.0083
 | 30.9272 | 39.5444
  0
  FY18 (Pre-LNG)
  0
  4
  95
  FY20 (Proposed by BERC)
  5
  76
  3
  4
  Tea garden
  Power
  Commercial
  Domestic
  Industry
  Captive power
  Fertilizer
  CNG
+8.6
+3.1
+3.4
+1.1
+2.1
Change in Allocation
+0.7
+0.1
+0.01
=+19.1
Total Increase in Supply
Source: BERC, GSMP, 2017, Industry Reports, Deloitte Analysis
1 | 2 | 3 (Joint) | 
Fertilizer | Power | Industry | Tea Garden
Captive Power | Residential | Commercial | CNG
4 | 5 (Joint) |  | 6

## Slide 40: Natural Gas Pricing Assessment

## Slide 41: Power Market | Natural Gas Supply
GoB has opted for a pooled pricing of Domestic Gas and LNG as per BERC tariff order July 2019; currently GoB is subsidizing LNG cost for majority sectors with power having the highest subsidy
Following table provides the details of the LNG Contracts signed by Bangladesh: Following figure shows the gas prices for power producers in Bangladesh in the last 3 years:
LNG Prices: Bangladesh has so far signed LNG contracts with Qatar, Oman and Petramina (LOI signed) with the total LNG volume under these contracts at 4.5 MTPA The long term LNG contracts with Qatar and Oman are crude linked and hence are subject to international movement of crude prices. The long term contracts for 4.5 MTPA (7.86 mmscmd) would only be able to supply ~60% of the FSRU capacities with ~3.4 MTPA (~12 mmscmd) of LNG which may need to be procured from Short Term / Spot market. The Government had shortlisted 17 players for purchasing ~1 MTPA (~3.6 mmscmd) of Spot LNG in September 2019 In March 2020, the GoB planned to import the spot cargoes by July end to take price advantage of the lower LNG prices in the spot market Impact on Gas Prices for Power Sector: Till June 2019, the natural gas prices for consumer segments were based on the production cost of domestic natural gas However with the import of LNG, BERC in July 2019 has revised the gas prices for various consumer segments (Refer Appendix) The graph on the right (below) showcases the movement of gas prices for power producers in Bangladesh The current gas prices are now pooled with the cost of production of domestic natural gas and imported LNG; However it also includes a subsidy component by the Government of Bangladesh (Refer Appendix for detailed calculation on the same)
Supplier | Country | Capacity (MTPA) | Duration (Years) | LNG Pricing
Oman Trading International | Oman | 1.0 | 10 | 11.9% of 3-month average Brent pricing + $0.40 / MMBtu
RasGas | Qatar | 2.5 | 15 | 12.65% of 3-month average Brent pricing + $0.50 / MMBtu
Petramina | Indonesia | 1.0 | 10 | 
Total |  | 4.5 |  | 
Chart: 
 | 2.82 | 2.99 | 3.16 | 4.45
 | 0.8883 | 0.94185 | 0.9954 | 1.4018
  March 2017 to June 2017
  Pre-March 2017
  July 2017 till June 2019
  July 2019 onwards
  Tk / cum
  $ / mmbtu
Source: Petrobangla, GIIGLN, Deloitte Analysis; Note : 1) Tk / cum converted to $ / MMBtu using conversion factor of 1 USD = BDT 80 and 25.2 SCM = 1 MMBTU 2) The subsidy computed based on difference of weighted average cost of supply of NG/LNG in Bangladesh and the tariff announced by BERC for FY20 onwards

## Slide 42: Power Market | Natural Gas Supply
Following graph depicts the average monthly Brent crude oil price (USD / BBL) and Domestic Natural Gas Prices for Power Sector in Bangladesh (BDT / kWh) from June 2007 to January 2020 Following graph shows the percentage increase in Natural Gas Tariff for power sector compared to proposed hike by Gas distribution companies from 2009 to 2019
Natural Gas Pricing Frequency & Intensity In the last 13 years, the GoB has increased the natural gas price for power sector 5 times only During FY07 to FY19, BERC on an average increase in gas price by ~2%-8% Although the Brent Crude Oil prices witnessed a high variation from ~$130 / bbl to ~$30 / bbl the prices of natural gas for the power sector witnessed marginally Thus, the GoB did not follow the international gas pricing trend for setting the natural gas prices in Bangladesh As mentioned earlier, the commencement of LNG from FY19 led to a sharp increase in domestic natural gas price from BDT 3.16 / cum to BDT ~4.45 / cum Considering the increased subsidy due to LNG the tariff hikes can be expected to be a more frequent process as the GoB has plans to reduce the subsidy in a phased manner
In the last 10 years, the GoB had marginally increased natural gas prices for power sector as entire gas supply was based on domestic production; However with LNG supply, it may increase the prices frequently
Chart: 
| 2009 | 42795 | 42887 | 2019
Proposed hik by gas players | 0.27 | 0.63 | 0.54 | 1.42
BERC hike | 0.08 | 0.06 | 0.060762 | 0.41
Chart: 
“We have to adjust gas prices, and we are saying that again and again”
“If we do not adjust the price, we have to provide subsidy for the additional cost. Even after the adjustment, we will have to subsidize it,”
- Power Minister, Nasrul Hamid, Bangladesh, June 2019
Source: Petrobangla, BPDB, EIA, Industry Reports, Deloitte Analysis

## Slide 43: Power Market | Natural Gas Supply
Following figure shows the expected Domestic Gas Production and LNG Import (mmscmd) in FY20 for Bangladesh (as per BERC): Following figure shows Cost of Supply of Domestic NG, Imported LNG, Weighted Average Cost and Tariff for Power Sector ($ / MMBTU):
LNG Blending in Natural Gas Consumption: As per Bangladesh Electricity Regulatory Commission, the country is expected to import ~24 mmscmd of LNG (out of import capacity of ~28 mmscmd) in FY2020 The domestic natural gas production is expected to reduce marginally at ~73 mmscmd compared to FY2019 Thus, the Natural Gas to Blending Ratio is ~25% for FY2020 Considering the import capacity and challenges in evacuation from FSRUs, the blending ratio is expected to remain at 25% - 30% Gas Price Tariff with LNG Imports: As per BERC, the weighted average domestic gas production cost was ~$ 1.43 / MMBtu in Bangladesh The average weighted cost of supply for LNG import was ~ $ 11.63 / MMBtu Thus, the weighted average supply cost of natural gas (incl. LNG) was ~$ 3.97 / MMBtu. However the GoB has set the blended natural gas supply cost for the Power Sector at ~$1.40 / MMBtu Currently the Government is subsidizing the gas price for power sector by ~65% from the weighted average cost of natural gas supply as whole in Bangladesh
Chart: 
 | 72.5 | 24.06 | 96.56
  Domestic NG
  LNG
  Total
  MMSCMD
Imported LNG to Domestic Gas Blending Ratio - ~25%
Chart: 
 | 1.43 | 11.63 | 3.97 | 1.4
  Gas Tariff for Power Sector
  Domestic NG
  LNG
  Weighted Average Cost of Supply
  Production / Import Supply Cost ($ / MMBTU)
Tariff for Power Sector is still lower than cost of supply of Domestic NG with ~65% subsidy
Even after the recent natural gas tariff hike, the power sector is receiving natural gas (incl. blended LNG) at level below the cost of production of domestic natural gas with overall ~65% subsidy
Source: BERC, Deloitte Analysis

## Slide 44: Power Market | Natural Gas Supply
Following figure shows the sensitivity analysis of Blending Ratio (LNG to NG) on the weighted average gas price in Bangladesh:
Sensitivity Analysis – Blending Ratio of LNG and NG: Currently Bangladesh is expected to produce ~2,560 mmscfd (~73 mmscmd) of Natural Gas and import ~850 mmscfd (~24 mmscmd) of LNG We conducted a sensitivity analysis to assess the impact of blended average cost of natural gas with LNG in case the blending ratio changes from current 25% (LNG : Natural Gas) We also considered the impact on cost of gas in case LNG price moves upward or downwards to $13 / MMBtu and $8 / MMBtu As can be seen on the graph on the right, the pooled prices can vary between $4 / MMBtu (current) to $~7-11 / MMBtu based on the level of LNG price and blending ratio Competitiveness of Natural Gas / LNG with HFO and HSD In FY19, the natural gas price for power sector players in Bangladesh was BDT 3.16 / cum or $1 / MMBtu At the above levels, the average energy charge for BPDB’s gas based power plant was BDT 1.05 / kWh (US Cents 1.3 / kWh) in FY19 During FY19, the average energy charge for BPDB’s HFO and HSD based power plants were BDT ~11.44 / kWh (US cents 14.3 / kWh) and BDT ~19.37 / kWh (US Cents 24 / kWh) Considering the same efficiency for gas power plants in Bangladesh as that of BPDB, the average energy charge for gas based power plants would be under BDT 10 / kWh (US Cents 12.5 / kWh) till about 70% blending ratio of Natural Gas and LNG
Considering a scenario of zero subsidy, the gas / LNG based power plants may be competitive with HFO and HSD plants till 70% blending of Natural Gas and LNG in Bangladesh
Chart: 
 | 3.97 | 4.49 | 5.51 | 6.53 | 7.55 | 8.57 | 9.59
 | 3.06 | 3.4 | 4.06 | 4.71 | 5.37 | 6.03 | 6.69
 | 4.31 | 4.9 | 6.06 | 7.21 | 8.37 | 9.53 | 10.69
  9.5
  30%
  Blending Ratio
  4.5
  25% (Current Level)
  40%
  50%
  80%
  60%
  70%
  10.7
  Weighted Average Cost of Natural Gas with $11.63 / MMBTU LNG (Current Price)
  Weighted Average Cost of Natural Gas with $8 / MMBTU LNG
  Weighted Average Cost of Natural Gas with $13 / MMBTU LNG
Impact of Blending Ratio on Weighted Average Cost of Natural Gas in Bangladesh ($ / MMBTU)
Till 70% Blending Ratio, Natural Gas should be competitive with HFO and HSD
Source: BERC, Deloitte Analysis; Note 1) Sensitivity Analysis based on landed cost of LNG (as per BERC tariff order) of $11.63 / MMBtu and cost of domestic gas production at $1.43 / MMBtu (as per BERC tariff order) which with the current blending ratio of 25% leads to weighted average price of ~$ 3.98 / MMBtu 2) The sensitivity analysis has been done on estimates of LNG price while considering the domestic cost of production of Natural gas constant at FY20 levels

## Slide 45: Demand Projection - Scenario – Business As Usual (PSMP Revised)

## Slide 46: Power Market | Demand Projection (as per PSMP – Revised)
Following figure shows the Peak Demand (MW) Projection in MW till FY26 and FY30: Following figure shows Net Energy Consumption Ex-Bus (MU) and Average Demand (MW) till FY26 and FY30:
Based on revision in the GDP elasticity and consideration of the slow uptake of EE&C measures, the peak demand in Bangladesh may increase to 27,728 MW by FY26 and ~36,350 MY by FY30
Peak Demand Forecasting – PSMP (revised with GDP Elasticity & EE&C impact) PSMP 2016 & its Revision have considered GDP elasticity of Bangladesh at 1.27 with electricity generation The elasticity was computed from the period 2005 to 2014 (10 years) We re-computed the GDP elasticity from 2010 to 2019 (10 years) at 1.62 based on the latest data till FY24 after which we have considered the GDP elasticity at 1.5 considering that Bangladesh would have achieved 100% electrification by then PSMP had also considered the impact of EE&C measures on the overall power demand in Bangladesh. However considering the slow pace of uptake of EE&C measures we have considered the EE&C growth rate considered by PSMP to halve till FY24 and then increase incrementally to reach a similar value by FY30 as considered in the PSMP. Net Energy Consumption (ex-bus) and Average Demand – PSMP: Based on the Peak Demand projected above, we considered the system load factor (ranging between ~60.6% to 64.6%) YoY considered by PSMP 2016 – Revised projections to determine the average power demand during the year The average power demand was used to derive the expected net electricity consumption (ex-bus) for Bangladesh during the period between FY20 to FY26 and FY30 using system load factor considered as above
Chart: 
 | 15230.0449 | 27728 | 36353.6156
  FY20
  FY26
  FY30
  27,728
  15,230
  36,354
  +9.1%
Chart: 
 | 9233.9762 | 17088.5232 | 23491.7064
 | 80889.6315 | 149695.463 | 205787.3478
  FY20
  FY30
  FY26
  Net Electricity Consumption Ex-Bus (MU)
  Average Power Demand (MW)
Due to the impact of Covid-19, Bangladesh may witness a muted growth and hence the energy demand may reduce accordingly for FY20 and beyond
Source: PSMP 2016; PSMP 2016 (Revised Study), BPDB, Bangladesh Bank, Deloitte Analysis; Note 1) Data for EE&C, GDP Growth as per PSMP 2016

## Slide 47: Demand Projection & Scenario – Covid – 19 Impact & Scenarios

## Slide 48: Power Market | Demand Projection (COVID 19)
Following figure shows the GDP Growth Rate Projections considered under COVID 19 Impact Scenarios till FY26 and FY30: Following table shows Peak Demand (MW) Projections till FY26 and FY30:
Considering the impact of COVID 19 on the GDP growth of Bangladesh, the Peak Power Demand may reach ~25,400 MW by FY26 and ~33,400 MW by FY30
Peak Demand Forecasting – (COVID 19 Impact) We have considered the scenario of lower growth due to Covid-19 in Bangladesh for projecting the peak demand We have projected demand under 3 scenarios namely: COVID 19 Base Case – We assumed GDP growth rate in FY20 and FY21 to be 2% (as per IMF Outlook for Bangladesh –April 2020) and 7.8% respectively COVID 19 Pessimistic Scenario – We assumed a Zero Growth outlook for FY20 and 5% growth outlook in FY21 for Bangladesh COVID 19 Optimistic Scenario – We considered a 5% growth outlook in FY20 and an accelerated growth outlook of 9.5% in FY21 for Bangladesh The GDP growth rates post FY21 have been considered in line with PSMP 2016 projections The graph on the right (above) showcases the various GDP growth rates considered under each scenario Peak Demand – PSMP: In line with the above GDP projections we have projected the Peak Power Demand in Bangladesh till FY26 and by FY30 As can be seen from the table on the right, Peak Power Demand is expected to be in the range of ~23,700 – 27,200 MW by FY26 and ~31,100 – 35,700 MW by FY30
Chart: GDP Growth – Scenario Projections
| FY20 | FY21 | FY22 | FY26 | FY30
Covid 19 Base Case | 0.02 | 0.078
Covid 19 Pessimistic Case | 0 | 0.05
Covid 19 Optimistic Case | 0.05 | 0.095
Common Case | 0.05 | 0.095 | 0.076 | 0.067 | 0.059
Column1 | 0.05 | 0.076 | 0.067 | 0.059
Column2 | 0.078 | 0.076 | 0.067 | 0.059
Source: PSMP 2016; PSMP 2016 (Revised Study), BPDB, IFC, Bangladesh Bank, Deloitte Analysis
Chart: 
 | 13932.3487 | 25431.186 | 33366.0566
 | 13499.7833 | 23714.2744 | 31132.4162
 | 14581.1968 | 27203.8452 | 35672.2224
  FY20
  FY26
  FY30
  23,714
  31,132
  Peak Demand (Covid 19 Base Case)
  Peak Demand (Optimistic Case)
  Peak Demand (Pessimistic Case)

## Slide 49: Power Market | Demand Projection (COVID 19)
  Average Demand (Pessimistic Case)
  Average Demand (Optimistic Case)
  Average Demand (Covid 19 Base Case)
Following figure shows the Average Demand (MW) projections under each case till FY24 and by FY30: Following table shows Net Energy Consumption Ex-Bus (MU) for till FY24 and by FY30:
The average demand for power in Bangladesh may reach 15,700 MW by FY26 and ~21,560 MW by FY30 in the COVID 19 Base Case
Chart: 
 | 8447.183 | 15673.24 | 21561
 | 8184.9186 | 14615.1073 | 20118
 | 8840.5796 | 16765.7298 | 23051
  FY26
  FY20
  FY30
Average Demand Based on the Peak Demand projected earlier, we considered the system load factor (ranging between ~60.6% to 64.6%) YoY considered by PSMP 2016 – Revised projections to determine the average power demand during the year The average power demand is expected to be ~15,700 MW by FY26 and 21,600 MW by FY30 in the COVID 19 Base Case It may reach 20,000 MW and 23,050 MW in the pessimistic and optimistic scenario by FY30 respectively Net Electricity Consumption (Ex-Bus): The net electricity consumption (ex-bus) was computed based on average demand for each year As can be seen from the graph on the right (below), the net energy consumption (Ex-bus) may reach 1,38,000 MUs by FY26 and 1,88,900 MUs by FY30 in the base case It may reach 1,76,200 MU and 2,02,000 MUs in the pessimistic and optimistic scenario by FY30 respectively
Chart: 
 | 73997.3233 | 137297.582 | 188875.6368
 | 71699.8872 | 128028.3399 | 176231.6419
 | 77443.4774 | 146867.7931 | 201930.1776
  FY30
  FY20
  FY26
  176,232
  Net Energy Consumption (Covid 19 Base Case)
  Net Energy Consumption (Pessimistic Case)
  Net Energy Consumption (Optimistic Case)
Source: PSMP 2016; PSMP 2016 (Revised Study), BPDB, IFC, Bangladesh Bank, Deloitte Analysis

## Slide 50: Power Market | Demand Projection (Summary)
We have considered the COVID 19 Base Case as our primary demand scenario where the peak demand is expected to reach ~25,400 MW by FY26 and 33,400 MW by FY30
Peak Demand: The following graph shows the Peak Demand (MW) projections in each scenario (PSMP Revised – BAU), COVID 19 (Base, pessimistic and Optimistic Scenario): Average Demand: The following graph shows the Average Demand (MW) projections in each scenario (PSMP Revised – BAU), COVID 19 (Base, pessimistic and Optimistic Scenario):
Chart: 
 | 15230.0449 | 27728 | 36353.6156
 | 13932 | 25431.186 | 33366
 | 13500 | 23714.2744 | 31132
 | 14581 | 27203.8452 | 35672
  FY30
  FY20
  FY26
  Covid 19 - Optimistic Case
  BAU Scenario
  Covid 19 - Base Case
  Covid 19 - Pessimistic Case
Chart: 
 | 9233.9762 | 17809 | 23491.7064
 | 8447.183 | 15673.24 | 21561
 | 8184.9186 | 14615.1073 | 20118
 | 8840.5796 | 16765.7298 | 23051
  FY26
  FY20
  FY30
  BAU Scenario
  Covid 19 - Pessimistic Case
  Covid 19 - Optimistic Case
  Covid 19 - Base Case
Source: Deloitte Analysis
Selected Base Case for Demand – Supply Analysis

## Slide 51: Assessment of Supply Capacity Requirement to meet Power Demand in COVID 19 Base Case

## Slide 52: Power Market | Supply Requirement to Meet Average Demand (FY26)
Total Additional Supply Capacity Requirement to meet Average Demand (FY20-FY26) We have considered an average PLF of 80% of plants to meet 15,673 MW average demand requirement which may require an overall supply capacity of ~19,600 MW by FY26 Currently, the Bangladesh installed capacity base is ~18,960 MW of which ~5,500 MW is planned / estimated to be retired by FY26. Further, given the high economic cost of running liquid fuel / Rental / Quick Rental plants the Govt. has planned alternate cheaper fuel based generation from LNG, imported coal and nuclear and thus the expensive liquid / rental based plants may witness lower dispatch rates as these alternate fuel based plants are commissioned in Bangladesh Thus ~8,700 MW of dispatch able capacity may be present in Bangladesh by FY26 requiring an additional ~11,000 MW of newer capacity to meet the average demand
With planned retirements and projected replacement of liquid fuel & low efficiency plants from economic perspective, Bangladesh may need an additional capacity of ~10,870 MW by FY26
Chart: 
 | 8447 | 15673 | 19591.25
  Average Demand (FY20)
  Average Demand (FY26)
  Total Supply Required to Meet Average Demand (FY26)
  Average Demand
Chart: 
 | 30 | 13487.5 | 8721.5
 | 1160 | 0 | 3741
 | 524 | 1029 | 1025
 | 230 | 345
 | 4770 | 4099.5
 | 1370
 | 10877
  1,370
  1,025
  1,160
  Replacement of Remaining Liquid and Rental Plants (from Economic Perspective)
  Installed Capacity (FY19)
  Planned Retirement (till FY26)
  1,029
  18,961
  -5,474
  -4,766
  Gas
  Coal
  HSD
  Hydro
  HFO
  Import
  Solar
Chart: 
 | 30 | 8721.5 | 19591
 | 1160 | 10869.5
 | 524
 | 230
 | 0
 | 0
 | 6777.5
  Additional Capacity Required to meet Average Demand in FY26
  8,722
  Total Supply Requirement (FY26)
  1,160
  Total Dispatchable Capacity (FY26)
Source: BPDB; PSMP 2016, Deloitte Analysis Note: 1) Plant Retirement Based on PSMP 2016 projections as well as estimations based on COD / dispatch
levels of each power plant in Bangladesh 2) For plants not covered under PSMP, an average PPA duration for 22 years has been considered for Non-Rental Plants (and an extension of 5 years for some cases beyond 22 years) and (5+5) years for Rental / Quick Rental Plants. 3) Replacement of Liquid / Rental plants has been considered as their current average tariff ranges from Tk 9 / unit – Tk 28+ / unit whereas Gas / LNG / Nuclear / Imported Coal based plants are expected to have per unit tariff at less than TK 9 / unit based on estimates

## Slide 53: Power Market | Supply Requirement to Meet Average Demand (FY26)
Considering the presence of inefficient gas based power plants till FY26 in the overall supply portfolio, there may be an additional requirement of ~700 MW to meet average demand taking total additional capacity required to ~11,500 MW by FY26
Source: BPDB; PSMP 2016, Deloitte Analysis Note: 1) For plants with low efficiency & dispatch, we have considered those plants which are expected to be operational beyond FY26; The installed capacity, efficiencies and dispatch levels have been considered as per FY19 levels 2) For the purpose of the analysis, the dispatch levels of these inefficient plants have been considered to run at maximum 40% PLF annually 3) Total Disapatchable Capacity is as per expected retirement / replacement of liquid & rental plants as mentioned in preceding slides
Following figure shows the additional requirement of supply capacity (MW) by FY26 considering presence of inefficient power plants in the system: Following figure shows the Total Additional Capacity required to meet average demand (MW) till FY26:
Low Dispatchability of Inefficient Gas Plants requiring additional capacity to meet Average Demand As projected earlier, ~6,778 MW of dispatchable gas based capacity is expected to be present in the Bangladesh Supply Portfolio However out of them, ~1,120 MW of Power Plants would continue to be part of the system with lower efficiency (<=35%) and also low dispatch (<-40%) These plants may need additional support to meet the average demand required by FY26 Thus, we have considered an additional requirement of ~672 MW of plants to be able to meet the demand shortfall due to these lower & inefficient plants Total Additional Capacity Required by FY26 to meet Average demand As projected earlier, Bangladesh requires ~10,870 MW of additional low cost fuel based supply (Gas / LNG / Imported Coal / Nuclear among others) However considering the presence of inefficient plants an additional ~700 MW may be required Thus the total additional capacity required to meet support the average demand by FY26 may increase to ~11,500 MW from 10,870 MW projected earlier
Chart: 
 | 8722 | 8050 | 8050 | 19591
 | 672 | 11541
  Total Dispatchable Capacity (FY26)
  Additional Capacity Required to meet Average Demand in FY26
  Total Supply Capacity Required to Meet Average Demand in FY26
  Fall in Dispatchable Capacity due to inefficient plants
  672
Chart: 
 | 1120
  Gas Plants with efficiency <=35% and PLF <=40%
Gas Plants Operational till FY26 = 6,778 MW
Chart: 
 | 448 | 448 | 1120
 | 672
  Estimated dispatch capacity (at 40% PLF)
  Requirement of additional capacity to compensate low dispatch
  Total Capacity of Plants with Low efficiency & dispatch

## Slide 54: Power Market | Supply Requirement to Meet Average Demand (FY30)
Total Additional Supply Capacity Requirement to meet Average Demand (FY27-30) We have considered an average PLF of 80% of plants to meet 21,500 MW average demand requirement by FY30 which may require an overall supply capacity of ~27,000 MW by FY26 We have considered the total dispatchable capacity in the Bangladesh system to be ~19,600 MW based on the average demand of ~15,700 MW by FY26 The overall supply capacity of Bangladesh is expected to retire ~470 MW of additional gas based power capacity during FY27-FY30 Thus ~19,100 MW of dispatchable capacity may be present in Bangladesh by FY30 requiring an additional ~7,800 MW of newer capacity to meet the average demand between FY27 and FY30
As average demand rises to ~21,500 MW by FY30, Bangladesh may need an additional supply capacity of ~7,800 MW between FY27-FY30 taking total supply capacity of the system to ~27,000 MW
Chart: 
 | 21561 | 26951.25
  Average Demand (FY30)
  Total Supply Required to Meet Average Demand (FY30)
  Average Demand
Chart: 
 | 19591 | 19123 | 19123 | 19123 | 26951
 | 468 | 7828
  Total Dispatchable Capacity by FY30
  Planned Retirement between FY27-FY30 (Gas Plants)
  Total Dispatchable Capacity Required to Meet Average Demand (by FY26)
  468
  Additional Capacity Required to Meet Average Demand by FY30
  Total Supply Requirement by FY30
Source: BPDB; PSMP 2016, Deloitte Analysis Note: 1) Total Supply needed to meet average demand based on normative Plant Load Factor of 80% 2) Plant Retirement Based on PSMP 2016 projections as well as estimations based on COD of each power plant in Bangladesh 3) 2) For plants not covered under PSMP, an average PPA duration for 22 years has been considered for Non-Rental Plants (and an extension of 5 years for some cases beyond 22 years) and (5+5) years for Rental / Quick Rental Plants

## Slide 55: Power Market | Supply Requirement to Meet Average Demand (Summary)
Total Additional Supply Capacity Requirement to meet Average Demand (till FY30) As the average power demand increases to ~15,700 MW and ~21,500 MW by FY26 and FY30 respectively, the supply capacity will also require to increase to ~19,600 MW and ~27,000 MW respectively Based on the current installed capacity in FY19, Bangladesh is expected to witness retirement of ~5,500 MW by FY26 and ~470 MW between FY27-FY30 Further, we expect that the Government may replace the liquid fuel / rental based power plants as newer & efficient power plants are set up in the country replacing ~4,800 MW by FY26 There may be an additional requirement of ~670 MW in the system as some gas based inefficient plants may still continue operations in the system with a lower dispatchability of ~40% Thus, Bangladesh may require ~11,500 MW of newer capacity addition by FY26 and ~7,800 MW between FY27 and FY30 to meet the rising demand
Bangladesh may require ~11,500 MW of newer capacity addition by FY26 and incremental ~7,800 MW between FY27 and FY30 to meet the rising demand
Chart: 
 | 15673 | 19591 | 21561 | 26951.25
  Total Supply Required to Meet Average Demand (FY26)
  Average Demand (FY30)
  Average Demand (FY20)
  Total Supply Required to Meet Average Demand (FY30)
Chart: 
 | 18961 | 8048.6 | 8048.6 | 8048.6 | 19590.6 | 19122.6 | 19122.6 | 26950.6
 | 672 | 11542 | -0.4 | 468 | 7828 | -0.4
 | 4766
 | 5474.4
  Additional Supply Capacity required to Meet Average Demand till FY26
  Planned Retirement / Replacement Capacity
  Installed Capacity (FY19)
  672
  Planned Retirement by FY30
  Total Dispatchable Capacity by FY26
  Total Supply Capacity by FY26
  468
  Additional Supply Capacity required to Meet Average Demand till FY30
  Total Supply Capacity by FY30
  -10,912
  19,591
  26,951
  Planned Retirement
  Replacement of Liquid / Rental Plants
  Lower Dispatch due to inefficient gas plants
levels of each power plant in Bangladesh 2) For plants not covered under PSMP, an average PPA duration for 22 years has been considered for Non-Rental Plants (and an extension of 5 years for some cases beyond 22 years) and (5+5) years for Rental / Quick Rental Plants. 3) Replacement of Liquid / Rental plants has been considered as their current average tariff ranges from Tk 9 / unit – Tk 28+ / unit whereas Gas / LNG / Nuclear / Imported Coal based plants are expected to have per unit tariff at less than TK 9 / unit based on estimates
Source: BPDB; PSMP 2016, Deloitte Analysis Note: 1) Plant Retirement Based on PSMP 2016 projections as well as estimations based on COD / dispatch

## Slide 56: Power Market Supply Projection

## Slide 57: Power Market | Supply Projection
Following figure shows the Additional Fuel Wise Capacity (MW) being added in the Bangladesh Power System by FY26: Following figure shows Total Expected Retirement for Power Plants in Bangladesh by FY26:
The GoB is tracking projects with ~17,640 MW of incremental capacity by FY26 with ~11,000 MW based on imported fuels such as coal, LNG & Nuclear by FY26; However not all of these plants are expected to be commissioned by FY26
Installed Capacity Projection Considering the challenges of reducing domestic natural gas reserves, the Government of Bangladesh along with various private players has planned ~17,640 MW of additional power capacity in Bangladesh As energy security measures GoB is promoting imported LNG, imported Coal & nuclear based power as a substitute to the cheaper domestic natural gas based power in Bangladesh and has planned ~12,900 MW from these imported fuels The imported power includes ~1,800 MW of power procurement from India HFO & HSD based power is also being planned in the period to support the peak power requirement till newer & efficient plants aren’t commissioned Retirement Projections For retirement of power plants, we have considered the PSMP 2016 projections for retirement We have also considered a maximum tenure for 22 years for most power plants (non-rental / public and BPDB) and 10 years for rental and quick rental power plants not covered under PSMP 2016 Further, we have also considered the existing dispatch of power plant and their historical dispatch rates to assess and estimate tentative retirements Thus, about ~5,474 MW of installed capacity is expected to be retired by FY26
Chart: 
 | 3020 | 3020 | 6055 | 12866 | 14702 | 16271 | 16432 | 16440 | 17640
 | 3035 | 6811 | 1836 | 1569 | 161 | 8 | 1200
  1,836
  Imported Coal
  LNG
  8
  Gas
  3,035
  Power Import
  6,811
  1,569
  HFO
  161
  HSD
  Solar
  Nuclear
  Total
Source: BPDB; PSMP 2016, Deloitte Analysis Note: 1) Capacity Addition data is as per tracking by BPDB 2) Planned Commissioning of Roopur Nuclear Plant as per secondary research 3) Plant Retirement Based on PSMP 2016 projections as well as estimations based on COD / dispatch levels of each power plant in Bangladesh 4) For plants not covered under PSMP, an average PPA duration for 22 years has been considered for Non-Rental Plants (and an extension of 5 years for some cases beyond 22 years) and (5+5) years for Rental / Quick Rental Plants
Chart: 
 | 4099.5 | 4099.5 | 5128.5 | 5473.5
 | 1029 | 345
  Imported Coal
  Gas
  HFO
  LNG
  Power Import
  345
  HSD
  Solar
  Total
  1,029

## Slide 58: Power Market | Supply Projection (Gas Based Plants)
Following table shows the status of the gas based power plants & their current status till FY26:
Out of planned ~3,000 MW of domestic gas based capacity, ~2,870 MW may be commissioned by FY2026
Domestic Gas Based Plants As per BPDB, about ~3,020 MW of Gas based power plants are currently under various stages of development in the country These plants are expected to be commissioned between FY20 and FY26 We studied the current project progress of each of the proposed power plants under consideration by BPDB to assess their commissioning scenario till FY26 About ~605 MW of the planned projects have achieved COD status during the current financial year i.e. FY20 Of the rest ~2,265 MW of gas based plants are expected to be commissioned during FY20-FY26 Thus ~2,870 MW of gas based plants may get commissioned post FY19 Following graph shows the planned & expected domestic Gas based capacity addition in Bangladesh by FY26
Source: Industry Reports, Deloitte Analysis
Chart: 
 | 3020 | 2870
  Planned Domestic Gas Based Capacity (MW)
  Probable Serviceable Capacity till FY2026 (MW)
Plant | Capacity (MW) | Current Status
Bibiyana #3 CCPP | 400 | COD Achieved in FY20
Shahjibazar 100 MW PP | 100 | -EPC Contract awarded to GE in Nov 2017
Siddhirganj 335 MW CCPP ST Unit | 118 | COD Achieved in FY20
Ghorashal 4th Unit Repowering | 200 | Under EPC by GE; World Bank Funded
Ghorashal 3rd Unit Repowering | 206 | 
Sylhet 150 MW PP Conversion | 87 | COD Achieved in FY20
Bhola 220 MW CCPP (D/F) | 220 | Proposed Nimbus Plant – Expected COD in FY21
Bibiyana South 383 MW CCPP | 383 | EPC Awarded
Ashuganj 400 MW CCPP (East) | 400 | EPC Awarded to Chinese Consortium; ADB Funded
Khulna 330 MW CCPP (D/F) | 336 | EPC Awarded to Chinese Consortium
Mymenshingh 360 MW CCPP | 420 | State Guarantee Provided by GoB; Expected COD by FY26
Mirsorai, Chattogram | 150 | Not likely to go through by FY26 due to low on-ground progress
Total | 3,020 | 

## Slide 59: Power Market | Supply Projection (HFO)
Following table shows the status of the HFO based power plants & their current status till FY26:
Out of planned ~1,569 MW of HFO based capacity, 1,169 MW may be commissioned by FY2026; However due to their high cost of generation, they may be utilized mostly for peaking power support once cheaper alternate sources of power get commissioned
HFO Based Plants As Bangladesh is currently facing supply constraints due to limited domestic gas and LNG availability the private players along with GoB continue to invest in liquid fuel based power plants to meet the increasing power demand These power plants would be providing base load till the time alternate sources of energy are not commissioned. Post commissioning of cheaper alternate sources these plants are from an economic perspective are expected to provide mostly peaking support as their energy costs will be more than Tk 9 / kWh We envisage that these plants may get lower dispatch as cheaper fuel based power plants are commissioned in Bangladesh Out of the planned ~1,569 MW of HFO based plants, ~1,169 MW capacity are under various stages of development and are expected to be commissioned by FY26 Following graph shows the planned & expected HFO based capacity addition in Bangladesh by FY26
Plant | Capacity (MW) | Current Status
Bogura 100 MW Power Plant | 113 | COD Achieved in FY20
Rangpur 113 MW Power Plant | 113 | 
Shikalbaha 110 MW PP | 110 | 
Shikalbaha, Chattogram 54 MW PP | 54 | 
Manikganj 162 MW PP | 162 | EPC underway; Expected COD FY21
Chandpur 115 MW Power Plant | 115 | PPA Signed
Choumohoni, Noakhali 113 MW | 113 | EPC Underway
Julda, Chattogram 100 MW PP | 100 | COD extension provided by BPDB in May 2019
Tangail 22 MW PP (Polli Power) | 22 | EPC Underway
Kanchan, Narayangonj 55 MW PP | 55 | EPC Awarded
Thakurgaon 100 MW Power Plant | 115 | EPC Awarded
Feni 114 MW Power Plant | 114 | COD Achieved in FY20
Potiya, Chattogram 100 MW PP | 116 | Not likely to go through by FY26 due to planned delay
Meghnaghat 104 MW Power Plant | 104 | Not likely to go through by FY26 due to low on-ground progress
Shreepur 150 MW Power Plant | 163 | 
Total | 1,569 | 
Source: Industry Reports, Deloitte Analysis; Note 1) Summit Group has also planned a 300 MW of HFO based power plant in Bangladesh which is currently not being tracked by BPDB; However the status of the project is currently unknown and hence not considered for the purpose of this analysis
Chart: 
 | 1569 | 1169
  Planned HFO Based Capacity (MW)
  Probable Serviceable Capacity till FY2026 (MW)

## Slide 60: Power Market | Supply Projection (Imported Coal based Plants)
Following table shows the status of the planned imported coal based power projects in Bangladesh for the next 5 Years: Following graph shows the planned imported coal based Capacity and the probable Serviceable Capacity (MW) in Bangladesh by FY2026 given the fuel supply scenario:
Out of planned 6,811 MW of imported coal based capacity, only ~2,640 MW may be commissioned by FY2026
Imported Coal Bangladesh is progressing towards commissioning 2 imported coal power plants in Payra and Rampal area respectively However both these projects are facing challenges in terms of transmission evacuation and environmental challenges respectively Considering the delay in the Payra (1st Phase) project, we envisage that the 2nd phase may get delayed beyond FY2026 Further, most of the other planned projects for imported coal are expected to be delayed beyond FY26 due to issues of financial closure and logistical challenges (refer table on the right) The status of the Barisal 307 MW power plant in terms of physical progress is unknown and hence expected to get delayed beyond FY26 Supply Infrastructure The coal for the Payra 1st phase has been planned to be imported from Indonesia, China, and Australia (Currently Payra has signed contract with Indonesia for coal supply) The coal supply infrastructure also presents a challenge for Bangladesh with the current draft levels at Payra port able to support only ~30,000 tonnes of coal capacity per ship At the current coal supply level of 30,000 Tonnes, ~2,500-3,000 MW of imported coal capacity may be serviceable Since long haul ships have a capacity of ~70,000 tonnes, the overall transportation cost per tonne is expected to increase for Payra The GoB has initiated process for dredging the Payra Port’s main channel in January 2019 with work commencement by June 2019
Chart: 
 | 6811 | 2640
  Planned Imported Coal Based Capacity (MW)
  Probable Serviceable Capacity till FY2026 (MW)
Plant | Capacity (MW) | Current Status
NWPGCL’s (GoB owned) Payra (1st Phase) | 1320 MW | Currently Test Run of 1 Unit underway; Transmission Evacuation Constraint till FY21
NWPGCL’s (GoB owned) Payra (2nd Phase) | 1320 MW | Not likely to go through by FY26 due to delay of operationalization of 1st phase
BIFPCL (JV between BPDB and NTPC, India), Rampal | 1320 MW | EPC Ongoing; Environmental Challenges
S Alam Group’s - 2x612 MW Chattogram | 1224 MW | Not likely to go through by FY26 due to Issues in Financial Closure
RPCL’s (GoB Owned) Patuakhali | 1320 MW | Project Scrapped in FY2020
BPDB’s Barishal CFPP | 307 MW | Not likely to go through by FY26 due to low on-ground progress
Source: Industry Reports, Deloitte Analysis; Note 1) There are other multiple imported coal based fuel projects under planning stages in areas such as Mongla, Moheshkali among others with fund support from Chinese firms. According to secondary sources, there has been no major active development initiative in these projects due to delay in financial support from the firms 2) Power Plant support estimation by current coal supply levels estimated at 80% Gross PLF with efficiency of ~35%, coal GCV of 5000 kcal / kg and coal unloading times between 1-1.3 days

## Slide 61: Power Market | Supply Projection (LNG Infrastructure)
Following table shows the planned LNG Capacity additions in Bangladesh and their current status Following figure shows import capacity of LNG and volume of LNG imported in 2018 and 2019 in MMSCMD:
Although ~3,000 MW of LNG based installed capacity has been planned, the current availability of imported LNG may restrict these plants operations; A ~27 MMSCMD onshore LNG Terminal at Moheshkali is under planning stage and may get commissioned post FY26
LNG Infrastructure Currently only 2 FSRUs with a combined capacity of ~7.86 MTPA (28.3 MMSCMD / 1,000 MMSCFD) has been commissioned in Bangladesh The current FSRU Capacity of ~7.86 MTPA (28.3 MMSCMD) can support ~6,000 MW-6,500 MW of gas based plants However, the entire capacity is still not being utilized due to challenges of weather, ocean currents and pipeline connectivity The Government has put on hold plans to develop more FSRU based LNG import facilities and is instead planning to setup onshore LNG Terminals which would atleast take 4-5 years for construction post award of EPC contract The GoB is current under planning stage of an onshore 7.5 MTPA (27 MMSCMD) LNG Terminal at Moheshkali Considering the COVID 19 pandemic and the time taken for construction of the terminal, the onshore terminal is expected to be commissioned between FY26-FY30
Type | Operator | Location | Capacity in MTPA (mmscmd) | Status
FSRU | Reliance | Kutubdia | 3.95 (14.2 MMSCMD) | May get delayed due to financial challenges at Reliance
Land | Petronet | Kutubdia | 7.86 (28.3 MMSCMD) | MoU Signed; Delayed
FSRU | HSMPL | Kutubdia | 3.95 (14.2 MMSCMD) | Cancelled in Nov 2018
Land | HQC | Moheshkhali | 7.86 (28.3 MMSCMD) | Shortlisted for RfP
Land | Semcorp | Moheshkhali | 3.95 (14.2 MMSCMD) | Proposal Submitted, Status Unknown
Source: Petrobangla, RGPPL, Industry Reports, Deloitte Analysis; Note 1) Power Plant Support from current FSRU capacity considered at ~45% efficiency, GCV of 8500 kcal / scm and 80% Gross PLF levels
Figures in mmscmd
Chart: 
 | 73 | 73 | 101.3 | 101.3 | 128.3
 | 28.3 | 27
  Total Planned Natural Gas Supply Capacity (FY19-FY24)
  Existing Average Domestic Gas Production
  Imported LNG Capacity Commissioned
  Additional Onshore 7.5 MTPA Planned Terminal
  Total Expected Import Capacity (FY30)
Current Capacity
Expected between FY26-FY30

## Slide 62: Power Market | Supply Projection (LNG based Power Plants)
Considering current status & Govt. push for LNG based plants we expect ~1,200 MW of the proposed LNG power plants may get commissioned by FY2026
Following table shows the status of the planned imported LNG based power projects in Bangladesh for the next 5 Years and their status:
Plant | Capacity (MW) | Current Status
750 MW CCPP – Reliance Power | 718 MW | The estimated investment for the project is ~USD 1 Billion including ~500 MMSCFD of FSRU based LNG Terminal by FY23. Currently as per Industry Sources, the Plant is being taken over by JERA with the FSRU not being part of the deal Considering financial challenges being faced by RPower, the project may get delayed beyond FY26
Roazan 400 MW+-10% CCPP - BPDB | 450 MW | Tender Document issued in December 2019 Considering Covid-19 related delay of 6 months and construction period of 3-4 years after EPC Contractor Selection the project may get delayed beyond FY26
Meghnaghat 600 MW CCPP - Summit | 583 MW | PPA Agreement signed with BPDB in March 2019 Expected completion in FY24
Haripur 250 MW CCPP - BPDB | 250 MW | Not likely to go through by FY26 due to low on-ground progress
Meghnaghat 600 MW CCPP – UMPL | 584 MW | PPA Agreement signed with BPDB in July 2019 Expected Completion in FY24
Meghnaghat 500 MW - Anlima Textile & GE | 450 MW | Proposal under evaluation by MPEMR as on May 2019
Meghnaghat UECL (Not present in BPDB Projection) | 450 MW | Under Consideration by Cabinet Committee as on May 2019 Currently not part of the BPDB projections
Installed Capacity Projection (Serviceable) LNG We also assessed the current status of the projects to evaluate the status of commissioning of each of the proposed LNG based power plant in Bangladesh As can be seen from the table on the right, only 2 projects (Meghnaghat 583 MW – Summit and Meghnaghat 584 MW – UMPL) projects have signed PPAs and are under active development Further both these projects are expected to be LNG/NG based as their PPAs have tariff structures based on LNG and NG fuels and hence even in case of non-supply of LNG these plants may get Natural Gas fuel allocation (Estimated Tariff of Tk 2.95 / kWh or US Cents 3.7 / kWh on Domestic Gas; Tk 5.44 / kWh or US Cents 6.7 / kWh on RLNG and Tk 12.6 / kWh or US Cents 15.8 / kWh on HSD1,2) We expect these plants to be commissioned by FY26 Following graph shows the planned LNG Installed Capacity as per BPDB and our estimated commissionable capacity (MW) by FY2026
Chart: 
 | 3035 | 1167
  Probable Serviceable Capacity till FY26 (MW)
  Planned LNG Installed Capacity till FY2026 (MW)
Source: Industry Reports, Deloitte Analysis; Note 1) The estimated tariff is based on tariff data available in secondary domain and converted to Taka from USD at exchange rate of 1 USD = BDT 80 2) The levelized tariff for both plants is same as per Industry Sources. However for Summit’s plant, the tariff also considers operation based on HSD fuel and hence a tariff for HSD has also been provided.

## Slide 63: Power Market | Supply Projection (Power Trade & Import)
Power Trade between Nepal & Bangladesh Apart from India, Bangladesh has planned to import ~2,000 MW using dedicated transmission line infrastructures. It has also been exploring the possibility of short term power trading with Nepal wherein Bangladesh would be supplying power to Nepal during winter months and drawing power from Nepal during summers In June 2019, Government of Nepal and Bangladesh signed a MoU to use India’s existing transmission lines to Nepal and Bangladesh for bilateral power trade and to explore possibilities of setting up dedicated transmission lines The Government of India has also discussed plan to sign a tri-partite agreement between the nations to enable short term power trade Impact on Overall Power Import in Bangladesh The current HVDC Corridor of 1,000 MW (Bheramara – Behrampur) and 160 MW Tripura-Commilla line is already running at high capacity utilization factor of ~75-80% A 340 MW transmission line from Tripura is currently under development and is expected to be commissioned by FY26 Similarly a planned imported coal based project ~1,496 MW is being setup by Adani Power in Jharkhand, India which would be dedicated for exporting power to Bangladesh The power plant is expected to be commissioned by FY26 and may have a tariff ranging from ~Tk 8-8.5 / kWh Thus, the power trade between Nepal and Bangladesh is unlikely to have a major impact on supply for Bangladesh due to lack of transmission capacity between the two countries in the near future
Following table shows the proposed power import plans by PSMP Bangladesh by FY2041 Following table shows the proposed power import plans by BPDB by FY26 and expected power import (MW)
The planned power trade between Bangladesh & Nepal may be delayed due to transmission constraints; ~1,800 MW of power trade between Bangladesh and India has been planned using dedicated transmission infrastructure by FY26
Source: PSMP, Industry Reports, Deloitte Analysis
Line | MW | Remarks
Bheramara - Baharampur | 1000 | Existing
Tripura - Comilla | 160 | Existing
Bheramara - Baharampur | 500 500 | Additional extension of Bheramara HVDC; Power import from Nepal
Tripura - Comilla | 300 | Construction of HVDC (500MW) in Comilla
Rangia/Rowta - Barapukuria | 1,000 | Power import by using Case 2 T/L (±800kV DC)
Rangia/Rowta - Barapukuria | 500 500 | Power import by using Case 2 T/L (±800kV DC)
From Nepal (Purnea - Barapukuria) | 500 500 | Power import by using Case 3 T/L (initially 400kV AC)
Bongaigaon/Rangia - Jamarpur | 500 500 | Power import from Bhutan
Bibiyana - Meghalaya (PSPP) | 1,000 | PSPP in Meghalaya State
From Nepal | 500 500 | Power import by using Case 3 T/L (upgrade to 765kV AC)
Cox's Bazar – Myanmar | 500 | Power import from Myanmar
Total | ~9,000 | 
Chart: 
 | 1836 | 1836
  Planned Imported Power by BPDB (FY26) (MW)
  Probable Serviceable Capacity till FY2026 (MW)

## Slide 64: Power Market | Supply Projection for average demand (FY26)
With 11,542 MW of incremental capacity required to meet average demand, Bangladesh has planned capacity addition of ~9,900 MW; With ~1,350 MW being planned with liquid based fuels, the supply portfolio still requires ~3,000 MW for economical & cheaper dispatch by FY26
Installed Capacity Projection (Serviceable) Based on our assessment of planned Gas based power plants, ~about 2,900 MW of planned capacity addition may be commissioned based on existing progress on the projects We expect ~1,200 MW of LNG based power plants with signed PPA & provision to run on Natural Gas may get operationalized by FY26 BPDB has planned the Sayedpur 161 MW HSD based plant which is expected to be commissioned by FY23 The power import from India includes planned commissioning of Adani’s ~1,500 MW Godda Power project which requires construction of a dedicated transmission line which is expected to be commissioned along with the plant by FY26 The planned HFO / HSD capacity may be commissioned considering the peaking power requirements and is expected to be phased over time as newer & efficient power plants are commissioned Thus, with projected capacity requirement of 11,540 MW by FY26 to meet average demand Bangladesh may add ~9,900 MW of capacity However the above capacity addition also includes ~1,350 MW of liquid fuel plants which may still be replaceable from economic perspective
Following figure shows the Serviceable Additional Fuel Wise Capacity (MW) Projection being added in the Bangladesh Power System till FY26: Following figure shows the probable and required capacity addition (MW) by FY26 in Bangladesh
Chart: 
 | 2870 | 2870 | 4037 | 6677 | 8513 | 9699 | 9860 | 9868
 | 1167 | 2640 | 1836 | 1186 | 161 | 8
  8
  HSD
  Gas
  Solar
  LNG
  Imported Coal
  Power Import
  HFO
  Total
Source: Industry Reports, Deloitte Analysis Note 1) Additional Plant Capacity Additions based on BPDB plans and Industry Reports on the current project progress and estimations for COD 2) Apart from the capacity addition, ~5,400 MW of power plants are expected to be retired between FY20-FY26 which has been discussed earlier – The same has been considered while projecting the Total Serviceable Capacity
Chart: 
 | 8521 | 8521 | 11542
 | 3021
  Total Capacity Required to Meet Average Demand by FY26
  Addition of Non-Liquid fuel based capacity by FY26
  Additional Capacity required to meet Average Demand by FY26
Additional Capacity of ~3,000 MW needed to meet the Average Demand by FY26
Liquid Based

## Slide 65: Power Market | Supply Projection for average demand (FY30)
Following figure shows the Additional Fuel Wise Capacity (MW) being added in the Bangladesh Power System by FY30: Following figure shows the probable and required capacity addition (MW) between FY27 and FY30 in Bangladesh
Bangladesh is expected to add ~3,700 MW of incremental capacity between FY27 and FY30 with ~diversified fuels such as, imported coal and nuclear;
Installed Capacity Projection Based on the installed capacity projections provided by BPDB and PSMP 2016, we envisage that currently the following capacities may get commissioned by FY30 Bangladesh is expected to add a ~7.5 MTPA onshore Land Based LNG Terminal between FY25 and FY30 which may lead to a revision in the Planning for Gas/LNG based power plants based on the dispatchability status of power plants by FY26 Imported Coal – The 2nd Phase of NWPGCL’s Payra project (1,320 MW) may be commissioned by FY30 as the 1st phase is expected to be completely operationalized by FY21 Nuclear – Bangladesh is currently constructing the Roopur Nuclear Power Plant. Both units of the power plant (2x1200 MW) may be commissioned by FY30 Retirement Projections Considering the retirement projections by PSMP and our estimations for retirement based on ageing profile, we expect ~470 MW of capacity to get retired between FY27 and FY30
Chart: 
 | 1320 | 1320 | 3720
 | 2400
  Imported Coal
  HSD
  Power Import
  HFO
  Solar
  Nuclear
  Total
Source: BPDB, PSMP 2016, Industry Reports, Deloitte Analysis Note: 1) Capacity Addition data is as per tracking by BPDB and secondary sources 2) Plant Retirement Based on PSMP 2016 projections as well as estimations based on COD / dispatch levels of each power plant in Bangladesh 3) Considering that most of the liquid fuels based plants would be replaced with better and efficient plants with cheaper fuels, we have not considered the planned retirement of 455 MW of HFO based plants in the above analysis. These plants may be present in the system but are expected to have marginal dispatch or support peaking requirements.
Chart: 
 | 3720 | 3720 | 7828
 | 4108
  Addition of Non-Liquid fuel based capacity between FY27-FY30
  Additional Capacity required to meet Average Demand by FY30
  Total Capacity Required to Meet Average Demand by FY30
Additional capacity of ~4,100 MW needed between FY 26 & FY30 to meet Average Demand; In case of delay in commissioning of Roopur Power Plant, the supply requirement could increase by 2,400 MW

## Slide 66: Power Market | Demand – Supply Projection for average demand (Summary)
With ~12,200 MW of non-liquid based planned capacity addition in Bangladesh by FY30, the country may still require an incremental capacity addition of ~7,100 MW of economical and cleaner fuel based power projects by FY30 to meet the average demand
Following table shows the total planned installed capacity (MW) by FY26 and FY30
Considering the replacement potential of liquid / rental / inefficient plant dispatch in Bangladesh, there may be requirement of incremental capacity addition of ~3,000 MW by FY26 and ~4,100 MW between FY27 and FY30 to meet the projected average demand
Source: BPDB; PSMP 2016, Deloitte Analysis Note: 1) For plants with low efficiency & dispatch, we have considered those plants which are expected to be operational beyond FY26; The installed capacity, efficiencies and dispatch levels have been considered as per FY19 levels 2) For the purpose of the analysis, the dispatch levels of these inefficient plants have been considered to run at maximum 40% PLF annually 3) Total Disapatchable Capacity is as per expected retirement / replacement of liquid & rental plants as mentioned in preceding slides 4) The total capacity thus derived is to meet the Average Demand only
Chart: 
 | 8521 | 8521 | 11542
 | 3021
  Total Additional Dispatchable Capacity Required to Meet Average Demand by FY26
  Addition based on planned projects of Non-Liquid fuel power plants between FY20-FY26
  Incremental Capacity (post current projected capacity addition) required to meet Average Demand by FY26
Chart: 
 | 3720 | 3720 | 7828
 | 4108
  AAddition based on planned projects of Non-Liquid fuel power plants between FY27-FY30
  Total Additional Dispatchable Capacity Required to Meet Average Demand by FY30
  Incremental Capacity (post current projected capacity addition) required to meet Average Demand by FY30

## Slide 67: Power Market | Supply Projection for Peak Demand
Bangladesh is expected to have additional capacity requirement of ~6,400 MW by FY30 to meet its peaking power demand
Following figure shows the total peak power demand (MW) and potential of replacement / addition of liquid based capacity (MW) to meet peak demand in FY26 As per our supply projections, Bangladesh requires ~19,600 MW of economical & cleaner fuel based capacity to meet the average demand by FY26 and ~27,000 MW by FY30 To meet the peaking power demand in FY30, there may be further incremental capacity addition requirement of ~6,400 MW This incremental supply capacity requirement may be met by addition of new cleaner & economical power plants or may be met by running the liquid fuel power plants which may continue to remain operational by virtue of their PPAs
Source: Industry Reports, Deloitte Analysis Note 1) Additional Plant in Capacity Additions based on BPDB and Projects tracked by PSMP and secondary sources. 2) Plant Retirement Based on PSMP 2016 projections as well as estimations based on COD / dispatch levels of each power plant Bangladesh 3) For plants not covered under PSMP, an average PPA duration for 22 years has been considered for Non-Rental Plants and 10 years for Rental / Quick Rental Plants.
Chart: 
 | 25431 | 19591 | 19591 | 19591
 | 5840 | 6113
  Estimated Liquid Based Power Projects in system by FY26
  Estimated Non-Liquid based Power Plants in System to meet Average Power Demand (FY26)
  Projected Peak Demand in FY26
  Incremental Capacity Required to meet Peak Demand by FY26
Chart: 
 | 33366 | 26951 | 26951 | 26951
 | 6415 | 5698
  Projected Peak Demand in FY30
  Estimated Non-Liquid based Power Plants in System to meet Average Power Demand (FY30)
  Incremental Capacity Required to meet Peak Demand by FY30
  Estimated Non-Liquid fuel based power plants in system by FY30

## Slide 68: Plant Dispatchability

## Slide 69: Power Market | Plant Dispatchability
Following graph shows the historical weighted average PLF (%) of gas based plants belonging to Private Producers, BPDB and Public Utilities from FY17 to FY19 Following graph shows the weighted average efficiency of gas based plants belonging to Private Producers, BPDB and Public utilities in FY19
In terms of the overall gas based plants in Bangladesh, Private Producers have had the highest average dispatch in the last 4 years due to their higher efficient plants
Net PLF & Efficiency for Gas Based Power Plants (Historical) As can be seen on the graph on the right (above), between FY16 to FY19, the average PLF of gas based power plants in Bangladesh has been ranging between ~50% to 57% The IPP / SIPPs have had the highest PLF in terms of the overall gas based portfolio with an average of ~65-70%% in the last 4 years BPDB’s gas based plants have had the lowest average PLF in the last 4 years (~35% to 45%) Although the Rental/Quick Rental Plants also have one of the lowest efficiencies (~34%) , they have been running at dispatch levels of ~45-70% as in interim solution to meet the power requirements Though Public Plants belonging to govt. entities such as APSCL, NWPGCL, EGCB among others have higher efficiency at ~42, the plants have been running at lower dispatch due to gas availability and maintenance challenges. However, in FY 19 these plants have seen a much higher dispatchability as compared to previous years
Source: BPDB, Deloitte Analysis Note: 1) The graphs above contain only plants operational in FY19 as per BPDB Annual Report 2) Auxiliary Consumption of ~3% has been considered while determining PLFs 4) Plants running on dual fuels & plants running on lower dispatch levels due to recent commissioning have not been included for that particular year
Chart: 
 | 65.2857 | 66.6208 | 70.7142 | 66.7285
 | 69.1178 | 53.2055 | 46.0331 | 58.8092
 | 51.3512 | 57.2729 | 45.6748 | 52.0509
 | 46.3538 | 40.9841 | 36.5409 | 44.0165
 | 56.6087 | 52.3057 | 49.7764 | 53.6977
  57%
  FY17
  FY16
  52%
  50%
  FY18
  FY19
  54%
  65%
  41%
  69%
  51%
  46%
  67%
  53%
  57%
  71%
  46%
  46%
  37%
  67%
  59%
  52%
  44%
  IPP/SIPP
  BPDB
  Rental /Quick Rentals
  Public Plants
  Average (Bangladesh)
Chart: 
 | 40 | 33.5 | 41.7626 | 32.7678
  Rental / Quick Rental
  IPP / SIPP
  Public Plants
  33%
  34%
  40%
  BPDB
  42%

## Slide 70: Power Market | Plant Dispatchability
Following graph shows the gas-plant wise Efficiency (%) & their respective PLF (%) in FY19
Chart: 
| 38.26 | 35.510000000000005 | 38.26 | 38.26 | 37.26 | 28.88 | 35.839999999999996 | 35.699999999999996 | 43.09 | 42.71
 | 87.7598 | 52.5183 | 82.7744 | 76.6276 | 40.4883 | 79.1853 | 60.1388 | 78.5404 | 26.8342 | 34.3049
 | 31.5232 | 30.721 | 39.9767 | 58.3703 | 94.254 | 5.2554 | 50.7362 | 63.7162 | 77.4895 | 79.4575 | 27.0422 | 27.6755 | 56.9034 | 85.2985 | 64.5905 | 59.7845 | 18.5616 | 27.9538 | 77.9812 | 53.0987 | 42.1631
 | 18.1103 | 70.6021 | 36.5993 | 56.5649 | 6.4065 | 78.7574 | 67.0858 | 66.4613 | 65.9333 | 71.0277 | 69.1955 | 45.6508 | 79.1763 | 67.9163 | 73.8421 | 67.907 | 26.8087 | 40.0717 | 19.5909 | 52.7986 | 86.5401
 | 53.2892 | 57.7585 | 66.8783 | 87.0507
  Efficiency (%)
  PLF (%)
With about ~3,300 MW of capacity having lower than 33% efficiency and lower dispatch at less than 40%, there may be gas –reallocation from these plants to higher efficient plants for optimum utilization of gas
EGCB 412 MW
APSCL (South) 450 MW
APSCL (North) 450 MW
Bhola 225 MW
Haripur 360 MW
S.Baha 225 MW
APCL 225 MW
RPCL 210 MW
Summit 305 MW
Meghnaghat 450 MW
Sembcorp 282 MW
UAEL 195 MW
  BPDB
  Rental
  IPP
  Public
Bheramara 360 MW
S.Ganj U1/U2 210/220 MW
Ghorashal 365 MW
High Efficiency (>40%) / High PLF (>60%) : Total 3,360 MW
Low Efficiency (<33%) / Low PLF (<40%): Total 3,320 MW
The above quadrant depicts the plants having Efficiency less than 33% and also with PLFs less than 40%
The total cumulative capacity of these plants are 3,320 MW (30% capacity) and generated 6,343 MUs in FY19 (13% of total gas based generation)
These plants consumed an estimated ~6 mmscmd of gas in FY19 (17% of the total gas allocation)
Summit 305 MW has been running at duel fuel with HFO due to gas shortage in FY16 and FY17. With increasing gas availability, it is expected to ramp up dispatch
Sembcorp 282 MW was commissioned in October 2018 and is expected to ramp up dispatch from FY20 onwards
Potential for Gas Allocation
Source: BPDB, Deloitte Analysis Note: 1) The graphs above contain only plants operational in FY19 as per BPDB Annual Report 2) Size of the Bubbles on the graph depict the Installed Capacity of the Plant

## Slide 71: Power Market | Plant Dispatchability
Following graph shows the gas-plant wise efficiency (%) and PLF (%) in Bangladesh in FY19 for Private Producers Following table shows the Installed Capacity (MW) and COD (as per PSMP) for Rental Plants which continue to operate beyond FY19
Re-allocation of gas from in-efficient rental plants in Bangladesh could allow IPP/SIPPs to achieve ~75-77% annual dispatch levels ensuring optimum utilization of Gas
PLF & Efficiency for Gas Based Power Plants of Private Producers The overall gas consumption by IPPs/SIPPs in FY19 was tentatively ~10 mmscmd which led to net generation of ~13,000 MUs On the other the rental plants consumed ~3 mmscmd and generated ~3,200 MUs in FY19 Most of the rental plants are smaller in size (~50 MW) and run under single cycle mode and thus lead to lower efficient utilization of gas These rental plants were commissioned to meet the rising energy deficit in Bangladesh during the early 2010s and were contracted to be operated for an initial period of ~5 years However most of the rental power plants are yet to be retired as the GoB has allowed these plants to operate to meet the power demand We expect these plants to continue to operate for the next 2-3 years with retirements / replacements occurring from FY23 due to their old age and inefficiency In case of retirement and re-allocation of gas from these rental plants to IPP/SIPPs based efficient units, the average PLF of IPP / SIPPs can move from ~67% in FY19 to ~75%-77% by FY26
Chart: 
| 38.26 | 35.510000000000005 | 38.26 | 38.26 | 37.26 | 28.88 | 35.839999999999996 | 35.699999999999996 | 43.09 | 42.71
 | 84.7598 | 49.5183 | 79.7744 | 73.6276 | 37.4883 | 76.1853 | 57.1388 | 75.5404 | 23.8342 | 31.3049
 | 74.4895 | 76.4575 | 54.7585 | 24.0422 | 62.9333 | 68.0277 | 66.1955 | 42.6508 | 76.1763 | 64.9163 | 70.8421 | 64.907 | 23.8087 | 37.0717 | 16.5909 | 49.7986 | 83.5401
 | 63.8783 | 84.0507
  Efficiency (%)
  PLF (%)
  RPP/QRPP
  IPP / SIPP
Source: BPDB, PSMP 2016 Deloitte Analysis Note 1) The PLF estimation based on re-allocation of gas from rental and quick rental plants to IPP / SIPP plants having efficiency higher than ~40% in FY19 2) Size of the Bubbles on the graph depict the Installed Capacity of the Plant
Sl. No. | Particulars | Installed Capacity | COD
1 | Aggreko. (85MW) | 85 MW | 2011
2 | Aggreko (95MW) | 95 MW | 2011
3 | Energyprima Kumargaon | 50 MW | 
4 | Energyprima Shahjibazar | 50 MW | 2008
5 | Venture | 33 MW | 2009
6 | Precision Energy Ltd. | 55 MW | 2010
7 | Max Power Ltd | 78.5 MW | 2011
8 | United Ashugonj Power | 53 MW | 2011
9 | Energyprima Fenchugonj | 44 MW | 2012
Total |  | 543 MW | 

## Slide 72: Power Market | Plant Dispatchability
Following graph shows the overall expected Gas/LNG availability for Gas / LNG for Private Producers based power plants in Bangladesh by FY26 Following graph shows the expected dispatchability for Gas / LNG based plants in Bangladesh by FY26
The increase in gas allocation to power sector could increase the average PLF of IPP / SIPP portfolio from 67% in FY19 to ~80% by FY26
Supply of NG / LNG to Gas based power plants As per the current BERC proposed gas allocation framework for FY20, ~40 mmscmd of natural gas is expected to be allocated to power sector in FY20 However, considering the importance of the power sector on the economy of Bangladesh we expect the Government to allocate incremental ~10 mmscmd to the sector by FY26 from the existing domestic & LNG supply considering highest priority of the sector This could be achieved by curtailing supply to sectors like households and transportation which can be substituted with LPG The GoB is also planning to promote the Captive Based Power Plants owners to shift to grid based electricity supply to reduce wastage of gas in the smaller engines used by captive owners. Average PLF of Gas Based Plants Thus, with higher gas allocation, the overall dispatch potential of the plants could lead to an overall PLF of 75% for the entire portfolio by FY26 with the plants belonging to IPPs / SIPPs running at even higher dispatch of ~75%-80% due to their better efficiency
Source: BPDB, BERC, Deloitte Analysis Note: 1) The PLF estimation has been based on the tentative capacity additions & retirements considered as part of Market Demand and Supply module 2) All newer gas based plants have been assumed to have efficiency factor of 45% (in line with market trends) 3) The GoB has been exploring LPG as an alternate fuel for household and transportation sectors 4) The GoB has also been promoting electricity from grid supply as a viable alternative to captive power plants which consumer natural gas currently and this may lead to additional availability of Natural gas to the grid connected power plants
Chart: 
 | 34.9 | 39.5444 | 50
  FY20 (Proposed by BERC)
  FY19
  FY26 (Estimated)
  Gas Allocation to Power Sector
Chart: 
 | 53 | 58.5339 | 75
 | 67 | 72 | 80
  FY19
  FY20
  FY26
  53%
  67%
  59%
  72%
  ~80%
  75%
  Average PLF of Gas Based Plants (overall)
  Average PLF of Gas Based Plants (IPP / SIPPs)
Basis Gas Allocation

## Slide 73: Commercial Dispatchability for Nimbus

## Slide 74: Power Market | Plant Dispatchability (Based on merit Order)
Following table shows the assumptions for determining tariff for Nimbus Plant: Following table shows the estimated levelized tariff for Nimbus Plant based on fuel & dispatchability:
Considering the prevailing tariff schedule (as per PPA) & fuel prices in Bangladesh, the levelized tariff for Nimbus on Gas Fuel could range between Tk ~2.5 – 3.6 / unit (at dispatch levels of 100% to 60%)
Tariff Assumption for Nimbus To assess the economic dispatch of the Nimbus plant we have estimated the levelized tariff of the Nimbus power plant We have considered the fixed & variable O&M costs as per the Tariff Schedule provided in the PPA Further we have projected the energy charge (fuel cost) based on the plant dispatchability levels, heat rates and fuel consumption estimations The levelized tariffs have been subsequently compared with the present merit order of Bangladesh The broad assumptions for the estimation has been shown in the table on the right (above) Estimated Levelized Tariff As can be seen from the table on the right (below), in case of the plant running on gas, the levelized tariff could range between Tk 2.5 / kWh to Tk 3.6 / unit Similarly in case the plant is run on HSD the levelized tariff could increase to Tk ~14.1 – 16.9 / kWh
Source: PPA; Deloitte Analysis Note: 1) The above tariff projections has been based on data solely available in the PPA and the prevailing fuel prices in Bangladesh at 30th May 2020. 2) The per unit tariff have been projected considering annual inflation rate – foreign assumed at 2%, annual inflation rate – local assumed at 6% and Discount factor of 10%; No escalation in fuel prices has been assumed 3) 1 USD to BDT considered at 85 BDT
Particulars | Unit | Value (on Gas) | Value (on HSD)
Fuel Price | BDT/SCM (Gas) BDT / Lit (Oil) | 4.45 | 65
Heat Value | KJ / kWh | As per PPA based on PLF | 
Energy Charge | Taka / kWh | Variable O&M - As per tariff Schedule Fuel Cost as per prevailing fuel prices & heat value | 
Fixed Charges | USD / Taka /KW-month | As per PPA Tariff Schedule | 
USD/BDT exchange rate |  | 85 | 
PLFs | Levelized tariff (Tk / kWh) |  | Levelized tariff (USD cents/ kWh) | 
 | Gas | HSD | Gas | HSD
100% | 2.53 | 14.14 | 2.98 | 16.63
80% | 2.91 | 15.10 | 3.43 | 17.76
60% | 3.61 | 16.90 | 4.25 | 19.88

## Slide 75: Power Market | Plant Dispatchability – Gas Operations (BDT / unit)
The following graphs projects the YoY Tariff projections with Gas as Primary Fuel with average dispatch levels of 100%, 80% and 60%
Chart: YoY Tariff Projections with Gas as Primary Fuel (BDT / kWh)
| Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7 | Y8 | Y9 | Y10 | Y11 | Y12 | Y13 | Y14 | Y15 | Y16 | Y17 | Y18 | Y19 | Y20 | Y21 | Y22
Total Tariff (Gas at 100% PLF) | 2.621 | 2.6278 | 2.635 | 2.6423 | 2.65 | 2.658 | 2.6662 | 2.6748 | 2.6837 | 2.693 | 2.2115 | 2.2216 | 2.232 | 2.2429 | 2.2542 | 2.266 | 2.2783 | 2.2911 | 2.3045 | 2.3185 | 2.333 | 2.3482
Total Tariff (Gas at 80% PLF) | 3.0241 | 3.0325 | 3.0412 | 3.0503 | 3.0597 | 3.0694 | 3.0795 | 3.0901 | 3.101 | 3.1124 | 2.5103 | 2.5226 | 2.5354 | 2.5487 | 2.5626 | 2.5771 | 2.5921 | 2.6079 | 2.6243 | 2.6414 | 2.6593 | 2.678
Total Tariff (Gas at 60% PLF) | 3.7594 | 3.7703 | 3.7817 | 3.7935 | 3.8058 | 3.8185 | 3.8318 | 3.8455 | 3.8598 | 3.8747 | 3.0716 | 3.0876 | 3.1044 | 3.1218 | 3.14 | 3.1589 | 3.1786 | 3.1992 | 3.2207 | 3.2431 | 3.2665 | 3.2909
PLFs | Levelized tariff (Tk / kWh)
100% | 2.53
80% | 2.91
60% | 3.61
The first year tariff for Nimbus on Gas as primary fuel could range at Taka 2.62 – Taka 3.76 / unit depending on dispatch levels (60% to 100%)
Source: PPA; Deloitte Analysis Note: 1) The above tariff projections has been based on data solely available in the PPA and the prevailing fuel prices in Bangladesh at 30th May 2020. 2) The per unit tariff have been projected considering annual inflation rate – foreign assumed at 2%, annual inflation rate – local assumed at 6% and Discount factor of 10%; No escalation in fuel prices has been assumed

## Slide 76: Power Market | Plant Dispatchability – Gas Operations (US Cents/ unit)
The following graphs projects the YoY Tariff projections with Gas as Primary Fuel with average dispatch levels of 100%, 80% and 60%
Chart: YoY Tariff Projections with Gas as Primary Fuel (US Cents / kWh)
| Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7 | Y8 | Y9 | Y10 | Y11 | Y12 | Y13 | Y14 | Y15 | Y16 | Y17 | Y18 | Y19 | Y20 | Y21 | Y22
Total Tariff (Gas at 100% PLF) | 3.0835 | 3.0916 | 3.0999 | 3.1086 | 3.1177 | 3.127 | 3.1367 | 3.1468 | 3.1573 | 3.1683 | 2.6018 | 2.6136 | 2.6259 | 2.6387 | 2.652 | 2.6659 | 2.6804 | 2.6954 | 2.7112 | 2.7276 | 2.7447 | 2.7626
Total Tariff (Gas at 80% PLF) | 3.5577 | 3.5676 | 3.5779 | 3.5885 | 3.5996 | 3.6111 | 3.623 | 3.6354 | 3.6482 | 3.6616 | 2.9532 | 2.9677 | 2.9828 | 2.9985 | 3.0148 | 3.0318 | 3.0496 | 3.0681 | 3.0874 | 3.1075 | 3.1286 | 3.1505
Total Tariff (Gas at 60% PLF) | 4.4228 | 4.4357 | 4.4491 | 4.463 | 4.4774 | 4.4924 | 4.508 | 4.5241 | 4.5409 | 4.5584 | 3.6136 | 3.6325 | 3.6522 | 3.6727 | 3.6941 | 3.7164 | 3.7396 | 3.7638 | 3.789 | 3.8154 | 3.8429 | 3.8717
PLFs | Levelized tariff (US cents / kWh)
100% | 2.98
80% | 3.43
60% | 4.25
The first year tariff for Nimbus on Gas as primary fuel could range at US cents 2.98 – 4.25 / kWh depending on dispatch levels (60% to 100%)
Source: PPA; Deloitte Analysis Note: 1) The above tariff projections has been based on data solely available in the PPA and the prevailing fuel prices in Bangladesh at 30th May 2020. 2) The per unit tariff have been projected considering annual inflation rate – foreign assumed at 2%, annual inflation rate – local assumed at 6% and Discount factor of 10%; No escalation in fuel prices has been assumed

## Slide 77: Power Market | Plant Dispatchability – HSD Operations (BDT/ unit)
The following graphs projects the YoY Tariff projections with as Primary Fuel with average dispatch levels of 100%, 80% and 60%
Chart: YoY Tariff Projections with HSD as Primary Fuel (BDT / kWh)
| Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7 | Y8 | Y9 | Y10 | Y11 | Y12 | Y13 | Y14 | Y15 | Y16 | Y17 | Y18 | Y19 | Y20 | Y21 | Y22
Total Tariff (HSD at 100% PLF) | 14.1497 | 14.1587 | 14.1681 | 14.1777 | 14.1878 | 14.1982 | 14.2089 | 14.2201 | 14.2317 | 14.2438 | 13.9593 | 13.9723 | 13.9858 | 13.9999 | 14.0145 | 14.0296 | 14.0454 | 14.0619 | 14.079 | 14.0969 | 14.1155 | 14.1349
Total Tariff (HSD at 80% PLF) | 15.113 | 15.1241 | 15.1356 | 15.1475 | 15.1598 | 15.1726 | 15.1859 | 15.1996 | 15.2139 | 15.2287 | 14.873 | 14.889 | 14.9056 | 14.9229 | 14.9408 | 14.9595 | 14.979 | 14.9992 | 15.0204 | 15.0423 | 15.0653 | 15.0892
Total Tariff (HSD at 60% PLF) | 16.9241 | 16.9386 | 16.9537 | 16.9693 | 16.9855 | 17.0023 | 17.0197 | 17.0377 | 17.0565 | 17.0759 | 16.6012 | 16.6222 | 16.6441 | 16.6667 | 16.6903 | 16.7149 | 16.7404 | 16.767 | 16.7948 | 16.8237 | 16.8538 | 16.8852
PLFs | Levelized tariff (Tk / kWh)
100% | 14.14
80% | 15.10
60% | 16.90
The first year tariff for Nimbus on HSD as primary fuel could range at Taka 14.15 – Taka 16.92 / unit depending on dispatch levels (60% to 100%)
Source: PPA; Deloitte Analysis Note: 1) The above tariff projections has been based on data solely available in the PPA and the prevailing fuel prices in Bangladesh at 30th May 2020. 2) The per unit tariff have been projected considering annual inflation rate – foreign assumed at 2%, annual inflation rate – local assumed at 6% and Discount factor of 10%; No escalation in fuel prices has been assumed

## Slide 78: Power Market | Plant Dispatchability – HSD Operations (US Cents/ unit)
The following graphs projects the YoY Tariff projections with as Primary Fuel with average dispatch levels of 100%, 80% and 60%
Chart: YoY Tariff Projections with HSD as Primary Fuel (US Cents / kWh)
| Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7 | Y8 | Y9 | Y10 | Y11 | Y12 | Y13 | Y14 | Y15 | Y16 | Y17 | Y18 | Y19 | Y20 | Y21 | Y22
Total Tariff (HSD at 100% PLF) | 16.6467 | 16.6573 | 16.6683 | 16.6797 | 16.6915 | 16.7037 | 16.7164 | 16.7295 | 16.7432 | 16.7574 | 16.4228 | 16.438 | 16.4539 | 16.4704 | 16.4876 | 16.5055 | 16.5241 | 16.5434 | 16.5636 | 16.5846 | 16.6065 | 16.6293
Total Tariff (HSD at 80% PLF) | 17.78 | 17.7931 | 17.8066 | 17.8206 | 17.8351 | 17.8501 | 17.8657 | 17.8819 | 17.8987 | 17.9162 | 17.4976 | 17.5164 | 17.536 | 17.5563 | 17.5774 | 17.5994 | 17.6223 | 17.6462 | 17.671 | 17.6969 | 17.7238 | 17.752
Total Tariff (HSD at 60% PLF) | 19.9107 | 19.9278 | 19.9455 | 19.9639 | 19.9829 | 20.0027 | 20.0231 | 20.0444 | 20.0664 | 20.0893 | 19.5309 | 19.5556 | 19.5812 | 19.6079 | 19.6357 | 19.6646 | 19.6946 | 19.7259 | 19.7586 | 19.7925 | 19.828 | 19.8649
PLFs | Levelized tariff (US Cents / kWh)
100% | 16.63
80% | 17.76
60% | 19.88
The first year tariff for Nimbus on HSD as primary fuel could range at US Cents 16.63 –19.88 / unit depending on dispatch levels (60% to 100%)
Source: PPA; Deloitte Analysis Note: 1) The above tariff projections has been based on data solely available in the PPA and the prevailing fuel prices in Bangladesh at 30th May 2020. 2) The per unit tariff have been projected considering annual inflation rate – foreign assumed at 2%, annual inflation rate – local assumed at 6% and Discount factor of 10%; No escalation in fuel prices has been assumed

## Slide 79: Power Market | Plant Dispatchability (Based on merit Order)
Based on the estimated levelized tariff for Nimbus and the current merit order profile, the plant should be able to get dispatch on gas fuel while even running at 60% PLF
Following Figure shows the Tentative Merit Order in Bangladesh based on the Average Power Purchase Cost / Power Generation Cost by BPDB as a Single Buyer in FY2019 and the estimated levelized tariff of Nimbus Plant: We have estimated the levelized tariff for Nimbus plant based on the prevailing operating parameters as per the PPA, GSA, FSA and O&M agreements and the fuel prices as per current prices set by GoB for power players As per the current Merit Order profile, the Nimbus plant should be able to get dispatch while running with Gas as it would still displace liquid fuels However in case the plant is forced to run with HSD, then there may be dispatch challenges as the plant would be displacing only the last 10% of the plants in merit order
  75%
  70%
  10%
  65%
  60%
  25
  90%
  55%
  85%
  50%
  0%
  20
  45%
  0
  40%
  35%
  30%
  5
  20%
  5%
  100%
  25%
  15%
  10
  40
  95%
  35
  80%
  30
  15
  Total MUs sold in Bangladesh in FY19 – 70,533 MUs
  Tk / KWh
  Gas
  HSD
  Hydro
  Coal
  Import
  HFO
  SOLAR
Current Position in Merit Order (on Gas Fuel) – 34%-64% - 2nd/3rd Quartile
Current Position in Merit Order (on HSD) – 91% - 97% 4th Quartile
Source: Nimbus PPA / FSA / GSA / O&M Agreements Note 1) The normative parameters such as Gas Calorific Value, Oil Heat Value, PLFs, Dependable Capacity, Escalable & Non-escalable pricing components have been considered as per the agreements executed by Nimbus 2) No escalation in fuel prices have been assumed 3) Power Import from India based on estimated cost at Tk 8.1 -8.5 / kWh based on secondary sources
The proposed Nimbus plant is expected to receive plant full dispatch on Natural gas fuel based on economic / merit order perspective in Bangladesh; However the plant may face challenge in case it is forced to run with HSD due to high cost in the current merit order
Upcoming RLNG Plants (Summit, UMPL) at TK ~5.44 / kWh
Fuel (Nimbus) | PLFs | Levelized tariff (Tk / kWh)
Gas | 100% | 2.53
 | 80% | 2.91
 | 60% | 3.61
Fuel (Nimbus) | PLFs | Levelized tariff (Tk / kWh)
HSD | 100% | 14.14
 | 80% | 15.10
 | 60% | 16.90
Estimated Levelized Tariff (Bangladesh) | BDT / kWh | Cut off for Merit Order Coverage
Imported LNG Based Plants | ~6.5-~6.7 | ~75%
Imported Coal based plants | ~6.7 – 7.0 | ~75%-77%
Power Import from India | ~8.1 – 8.5 | ~80%
Nuclear | ~7- 7.5 | ~80%
for Adani’s Godda power plant 3) For Imported LNG based plants, levelized tariff range considered at capex of BDT 6.5 Cr / MW, PLF of 80%, Efficiency at 45% and
Fuel Price at $8 / mmbtu; For Imported Coal based power plants, levelized tariff range considered at capex of BDT 9.8 Cr / MW, PLF of 80%, Efficiency of 34%, Coal GCV of 5000 kcal / kg and landed coal cost of $95 / tonne; For Nuclear Power Plant, Capital cost considered at BDT 50 Cr / MW (incl. IDC) based on $12.65 Bn project cost (secondary sources) at 90%:10% Debt Equity Funding by Russia at Libor +1.75% Interest Rate (Considered at ~3%) and PLF of 80%.

## Slide 80
Gas Supply & Transmission Outlook
Bangladesh gas transmission network overview, existing & upcoming LNG evacuation infrastructure assessment and gas supply assessment for Nimbus
01
02
03
04
05
06
07
08
09
10

## Slide 81: Gas Transmission | Overview (Bangladesh)
Bangladesh has been expanding its natural gas pipeline infrastructure to provide natural gas / LNG to the household & industrial users in a bid to reduce dependence on expensive alternate fuels such as LPG, HSD and HFO
Gas Transmission (Overview) Currently, Gas Transmission Company Ltd. (GTCL) is solely responsible to own, operate, maintain and construct all high pressure gas transmission pipelines in Bangladesh. Currently, the total operational pipeline infrastructure spanned around 1,559 km in cumulative length has grown at a CAGR of ~10% between FY12 and FY19 The primary push for expansion of Gas Pipelines has been the Government’s agenda to bring natural gas connectivity to the entire country and provide a cheaper and alternate fuel to households using LPG and to provide gas supply to industrial users who have to use expensive liquid fuels Following graph shows the growth in transmission lines (Kms) in Bangladesh between FY12 to FY19 (Detailed pipeline wise list provided in Appendix)
Jessore
Khulna
Shahjibazar
Sangu
Chittagong
Begumganj
Noakhali
Feni
Semutung
Chandpur
Comilla
Salda Nadi
Meghna
Bakrabad
Titas
Belabo
Kamta
Hatikumrul
Habibganj
Rashidpur
Bibiyana
Maulvibazar
Febchuganj
Beanibazar
Kailashtila
Sylhet
Jalalabad
Chhatak
Jamalpur
Sherpur
Mymensingh
Bogra
Dhaka
Gas Fields
Natural Gas Pipeline Connectivity Points
Jhendah
Kushtia
Bheramara
Bonpara
Summit FSRU
EEEL FSRU
FSRU
Gas Pipeline
Chart: 
 | 814.87 | 816.37 | 920.37 | 1230.07 | 1314.07 | 1378.37 | 1529.37 | 1559.37
  FY18
  FY15
  FY12
  FY17
  FY16
  FY14
  FY13
  FY19
  +9.7%
Source: Petrobangla, GTCL, Industry Reports, Deloitte Analysis

## Slide 82: Gas Transmission | Pipeline & Power Plant (Overview)
The gas based power plants dominate the eastern region due to pipeline connectivity; However the proximity to gas fields play no role in gas transmission charges as Bangladesh has set a fixed tariff for Natural Gas / LNG for all power plants
Gas Pipeline & Power Plant (Overview) The development of gas pipelines on the eastern region has also led to development of the power plants in the eastern region in Bangladesh The power plants are served by the distribution companies which operate in each region in Bangladesh As can be seen from the graph, the major gas cluster areas are in the Dhaka, Sylhet and the adjoining areas where majority of the gas fields are present However, the proximity to gas fields plays no role in gas transmission cost for the power plants Each power plant pays the fixed tariff defined by BERC for purchasing natural gas / LNG as that rate is inclusive of the overall cost for transmission & distribution of natural gas / LNG in Bangladesh
BPDB
IPP
Public
Upcoming BPDB & public
Upcoming private
Gas Pipeline
Jessore
Khulna
Shahjibazar
Sangu
Chittagong
Begumganj
Noakhali
Feni
Semutung
Chandpur
Comilla
Salda Nadi
Meghna
Bakrabad
Titas
Belabo
Kamta
Hatikumrul
Habibganj
Rashidpur
Bibiyana
Maulvibazar
Febchuganj
Beanibazar
Kailashtila
Sylhet
Jalalabad
Chhatak
Jamalpur
Sherpur
Mymensingh
Bogra
Dhaka
Jhendah
Kushtia
Bheramara
Bonpara
Summit FSRU
EEEL FSRU
Source: Petrobangla, GTCL, Industry Reports, Deloitte Analysis

## Slide 83: Gas Transmission | LNG Infrastructure (Till March 2020)
LNG import infrastructure Bangladesh has commissioned two FSRUs near Moheshkali off the coast of Cox Bazar: Excelerate Energy Bangladesh, 500 mmscfd FSRU Summit Corporation, 500 mmscfd FSRU Initially the FSRU’s faced evacuation constraint due to lack of pipeline capacity to evacuate LNG from the FSRUs with the overall transmission from both the FSRUs limited to ~600 mmscfd only Till June 2019, the LNG supply was being using the Moheshkali – Anowara Pipeline (30 inch x 91 Kms) with further evacuation restricted due to non completion of Anwara-Fouzdarhat (42 inch x 30 Kms) over Karnaphuli river Even post commissioning of the Anwara-Fouzdarhat pipeline the LNG was being consumed mostly in the Chattogram division due to constraint of the transmission pipeline from Barakhunda towards Bakhrabhad (24 inch)
The LNG import capacity has been facing evacuation constraints due to inadequate transmission capacity
Source: Petrobangla, GTCL, Industry Reports, Deloitte Analysis
Maheshkali- Anwara (30 inch x 91 Kms)
Anwara-Fouzdarhat (42 inch x 30 Kms)
The decision to increase tariffs was based on the assumption that around 850 MMcf/d of regasified LNG would be supplied to the national gas grid in 2019-20.
At present, two floating storage and regasification units with a combined capacity of 1 Bcf/d of regasified gas -- are supplying around 600,000 Mcf/d of gas to the grid, as the connecting pipelines have yet to be completed.
- BERC Chairman, Monowar Islam, July 2019

## Slide 84: Gas Transmission | LNG Infrastructure (April 2020 onwards)
LNG import infrastructure The GoB planned 3 major pipelines for increasing the LNG supply across Bangladesh as follows: The above pipelines will allow the utilization level of the current FSRU’s to increase to 1 BCF/Day from current 0.6 BCF/day Further the GoB is undertaking the Bogura-Rangpur-Saidpur Gas Transmission Pipeline project to connect the northern region of Bangladesh which is also expected to be commissioned by FY21
Bangladesh is developing the LNG supply infrastructure which will make possible for the two commissioned FSRU’s full evacuation of LNG in the national grid
Maheshkali- Anwara (Parallel Line)
Chittagong-Feni-Bakhrabad Pipeline
Dhanua-Nalka & Bangabandhu Bridge-Nalka Gas (Expansion)
Pipeline | Status | Details
Maheshkali- Anwara (Parallel Transmission Line) | Expected COD (FY21) | This pipeline (42 inch x 79 kms) is expected to be completed by Sep 2020 and will allow additional evacuation of LNG from Moheshkali towards Chattogram
Chittagong-Feni-Bakhrabad Pipeline | Commissioned (April FY20) | The pipeline (36 inch x 181 Kms) will allow the LNG to flow towards Dhaka circle and allow full evacuation of the LNG in the national grid
Dhanua-Nalka & Bangabandhu Bridge-Nalka Gas | Expected COD (FY21) | The pipeline (30 inch x 52 kms) is being constructed for strengthening gas supply to western regions in Bangladesh from eastern regions
Source: Petrobangla, GTCL, Industry Reports, Deloitte Analysis
Since the northern region is gradually improving with industrial upgradation, there is a crying need for natural gas supply. It will help boost the economic activities there
- Petrobangla Official, Dec 2018 on the proposed 150 Km Bogura – Saidpur Pipeline Expansion Project
Bogura-Rangpur-Saidpur

## Slide 85: Gas Supply & Transmission Outlook for Nimbus

## Slide 86: Gas Supply Outlook (Bhola Island)
Following table shows current & proposed gas based power plants on Bhola Island their annual gas consumption estimation (mmscfd) under normative dispatch level1,2: Following graph shows the 2P Reserves (BCF) at Shahbazpur and Bhola Fields as per Petrobangla and the expected gas availability for the power plants
The existing plants at Bhola Island & proposed Nimbus power plant may require ~88 MMSCFD of gas annually; The current reserves at Shahbazpur should be able to supply gas for ~21 years
Bhola Island Power Plant - Annual Gas Requirement Currently 3 power plants operate in the Bhola Island with a cumulative capacity of 353 MW These power plants in Bhola ran at average PLF of ~65%-75% in FY19 The retirements as per PSMP and current PPAs for Bhola I, Venture and Aggreko plants are tentatively at FY37, FY22 and FY22 respectively Considering their current efficiency levels and a normative PLF of 80% the existing plants at Bhola Island and the proposed Nimbus Plant together may require ~88 MMSCFD of gas annually till FY22 and ~62 MMSCFD from FY23 onwards considering plant retirements Availability of Gas The remaining reserves (2P) at Shahbazpur field were ~351 BCF (962 MMSCFD) in December 2017 as per Petrobangla Due to newer gas finds, the remaining reserves were increased in December 2018 to 586 BCF (1,605 MMSCFD) with an additional find at Bhola North fields for 420 BCF (1,151 MMSCFD) Based on the gas reserves before additional discovery at Shahbazpur, the reserves may be able to supply gas to power plants for ~10-11 years Considering the additional discovered reserves, the gas supply can last for 22+ years which would provide sufficient supply till the PPA expiry of Nimbus plant The reserves basis the technical study shall be used as an input for the study
Source: BPDB, Petrobangla, Deloitte Analysis Note 1) The Efficiency of Bhola I, Venture 33 MW and Aggreko 95 MW considered as per levels in FY19 2) The Efficiency of Nimbus Plant considered at 46% (in line with PPA condition with 80% PLF) 3) All the plants have been considered to be operating at 80 Gross PLF to determine annual gas requirement 4) 2P Reserves estimated for Dec 19 considering Gross PLF of ~80% for the power plants 4) Conversion factor considered 1 BCF = 2.82 MMSCFD for 365 days 5) Currently the planned EPZ is yet to be setup and hence the gas requirement of the EPZ has not been considered for the analysis.
Chart: 
 | 29.48 | 29.48 | 37.42 | 55.4 | 88.34
 | 7.94 | 17.98 | 32.94
  Venture (33 MW)
  Total
  Bhola (225 MW)
  Aggreko (95 MW)
  8
  Nimbus (220 MW)
Chart: 
 | 351 | 332
 | 420
  Dec-17
  Dec-19 (Estimated)
  Reserves at Shahbazpur
  Reserves at Bhola North
11 Years
21 Years with Shahbazpur Reserves
22+ Years with Additional Bhola Reserves
Expected Years of Gas Availability for Nimbus Plant
FY22
FY22
FY37
Estimated year of retirement
The GoB has also planned an EPZ in Bhola which may further increase the gas requirement of the island. However, it is currently in the initial planning stages

## Slide 87: Gas Supply Outlook (Demand Scenario Analysis)
The Aggreko 95 MW and Venture 35 MW plants are expected to be retired after FY22; In case these plants get extensions, then the gas reserves at Shahbazpur field would be able to supply gas for only ~16 years
Overview Aggreko 95 MW Bhola plant commenced operations in 2011 in Bangladesh and is currently operational from Bhola Island after a tenure extension from GoB with PPA expiry in FY22 Similarly the Venture 33 MW has also received multiple tenure extensions by GoB with the PPA expected to expire during FY22 Both these plants together require ~0.27 BCM (26 MMSCFD) of gas annually Considering that both plants would be over 10 years of age by the time they reach FY22, we do not expect further extension (as per market sources) of the PPAs for the plant with the Nimbus plant being sufficient to replace the dispatch levels from these plants However in case these plants do get PPA extensions (5 Years till FY27), then the gas reserves (BCF) at Bhola Island would have to supply to the plants affecting the overall availability of gas for Nimbus as follows:
Following chart highlights PPA extensions for Aggreko 95 MW plant Following chart highlights major changes for Bhola 33 MW Plant
2011 | Aggreko 95 MW Ashuganj commences operations
2015 | Contract extended for 1 year
2016 | Contract expired; Proposal to shift plant to Bhola
2017 | Proposal sent back by Power Division; capacity payment to be lowered from 14 to 13 USD/unit/month Additionally, tenure to be changed from 3 to 4 years
2018 | Aggreko Bhola 95 MW commences operations
2009 | Venture Power Plant commences operation
2012 | Tenure Extended for 3 more years
2016 | Tenure Extended for 2 years
2018 | Tenure extended by 3 more years
8 Years
16 Years with Shahbazpur Reserves
22+ Years with Additional Bhola Reserves
Expected Years of Gas Availability for Nimbus Plant
Source: BPDB, Petrobangla, Deloitte Analysis Note 1) The Efficiency of, Venture 33 MW and Aggreko 95 MW considered as per existing efficiency levels in FY19 2) The Efficiency of Nimbus Plant considered at 46% (in line with PPA condition with 80% PLF 3) All the plants have been considered to be operating at 80% average annual PLF to determine annual gas requirement 4) 2P Reserves estimated for Dec 19 considering plant dispatch levels of ~80% for the Bhola I, Venture and Aggreko plants
Chart: 
 | 351 | 332
 | 420
  Dec-17
  Dec-19 (Estimated)
  Reserves at Shahbazpur
  Reserves at Bhola North

## Slide 88: Gas Supply Outlook (Bhola Island – Bhola I)
Following graph illustrates the Demand and Supply of gas to Bhola 1 plant from April 2019 to June 2020 (mmscfd) Following graph illustrates the PLF & Efficiency (%) of Bhola 1, from FY16 to FY19
Bhola I overview The daily average demand for Bhola I Power Plant is 35 mmscfd as per Petrobangla However the average supply for gas has been ~28 mmscfd (80% of demand) between April 2019 to April 2020 As can be seen from the graph on the right (above), there has been frequent shutdown / maintenance from December 2019 for Bhola I Most of these shutdown / maintenance have historically lasted for 1-5 days However, since May 2020, the plant has undertaken shutdown GT2 and ST unit due to maintenance leading to further reduction in gas drawal Considering that Bhola I is supplied gas from the Bhola island and since the gas pipeline is not connected to the national grid we don’t envisage any risk of gas diversion from the Bhola island
The Bhola I plant has achieved dispatch levels of ~75%-80% in the last 2 years with sufficient gas supply to operate at the dispatch levels in FY20; Future dispatch outlook remains positive considering no major unplanned shutdown / outage event
Chart: 
Plant Shutdown / Maintenance
Chart: 
 | 57 | 60 | 79 | 76
 | 45.9 | 47.54 | 52.18 | 52.33
  76.0%
  FY18
  FY16
  FY17
  60.0%
  FY19
  57.0%
  52.2%
  45.9%
  47.5%
  79.0%
  52.3%
  PLF (%)
  Efficiency (%)
Source: BPDB, Petrobangla, PGCB, Deloitte Analysis; Note 1) The Petrobangla daily gas supply report only mentions Plant Shut Down / Maintenance as a reason for lower gas supply as marked in the graph above

## Slide 89: Gas Transmission | Gas Supply Outlook (Bhola Island)
Due to delay in construction of dedicated pipeline to Nimbus plant, NBBL has arranged temporary supply of natural gas from Bhola I gas supply pipeline
Proposed Gas Arrangement for Nimbus Plant The distribution franchise for Bhola island is with SGCL. Power plants get supply of gas via the following infrastructure arrangement:
Shahbazpur GF
Bhola North GF
Legend | Infrastructure component
 | GTCL Transmission Line (up to 14 inches)
 | GTCL Proposed Transmission Line ( up to 30 inches)
 | Gas Field (Bhola North & Shahbazpur)
 | Commissioned Power Plant
 | Under Construction Power Plant
Bhola I 225 MW
NBBL 220 MW CCPP
Venture Energy (Sinha) 33 MW
Power Plant | SGCL Infrastructure component
Bhola 1 Power Plant 225 MW | Underground pipeline (2 km, 8 inch) connecting Shahbazpur Gas Field to SGCL Valve Station at Borhanuddin
NBBL 220 MW CCPP (Proposed) | (7 km, 12 inch) pipeline under construction from Shahbazpur Gas Field to Plant site
NBBL 220 MW CCPP (Temporary) | Considering the delay in construction of above pipeline, NBBL has constructed a temporary pipeline and Regulating & Metering Station (RMS) for gas supply from Bhola I RMS The existing Bhola I RMS is capable of supplying 75 mmscfd gas. This would be sufficient to run both the plants at max. utilization
Aggreko 95 MW
Towards barisal
Bhola Town
Source: Petrobangla, GTCL, SGCL, NBBL, Industry Reports, Deloitte Analysis; Note 1) The gas requirement for both plants have been estimated at dispatch levels of 100% with SHR of Bhola I considered at 52% efficiency (as per actual achieved in FY19) and for Nimbus Plant at ~46% based on design SHR as per EPC contract

## Slide 90: Gas Transmission | Gas Supply Outlook (Bhola Island)
Following statements have been made by the Prime Minister & Energy Advisor to the Prime Minister regarding discovery in Bhola Gas Fields and plan to connect Bhola Island to National Grid
The Government of Bangladesh has planned to connect Bhola Island with National Grid which may lead to diverting of gas to other consumers nationally presenting a risk for Nimbus
Government’s inclination to bring gas from Bhola Island to National Grid The GoB has planned the following gas pipeline for connecting Bhola Island with National Grid Currently the Bhola Gas field’s production are entirely consumed in the Bhola Island itself due to lack of connection with the national grid With the new discovery of Gas in Shahbazpur East 1 and Bhola North Fields, the Prime Minister of Bangladesh and the Energy Advisor to the Prime Minister have also expressed interest in connecting the Bhola fields with the national grid to reduce gas supply deficit In case the gas pipeline is build to transport gas from Bhola Island to consumers on mainland Bangladesh, there could be a gas supply risk for Nimbus However the gas pipeline is still in planning stages and may take considerable time to get commissioned considering the approval process and EPC time
The gas can be used in power plants and be added to the national grid through the pipeline, if needed (On new discovery in Bhola Gas Field)
- Prime Minister, Sheikh Hasina, Bangladesh, Jan-2018
The government is trying to bring the gas from Bhola field to the mainland of the country and utilise the energy for power generation and industrial purpose
- Energy Advisor to Prime Minister, Bangladesh, Dr Tawfiq-e-Elahi Chowdhury, Mar-2018
Source: GTCL, Industry Reports, Deloitte Analysis
Pipeline | Status | Details
Bhola-Barishal | Planned | (65 km X 24 inch) pipeline to supply national grid with gas produced in Bhola. Final Stage route survey and environmental studies is in progress.
As per GTCL the estimated commissioning time of the project would be in June 2025 at the earliest. However, considering the current status we expect further delays in case the project is approved. Hence no major risk is envisaged in the short to medium term.

## Slide 91
Electricity Transmission Outlook
Bangladesh electricity transmission network overview, assessment of electricity transmission plan for Nimbus
01
02
03
04
05
06
07
08
09
10

## Slide 92: Electricity Transmission | Overview
Bangladesh currently has over 12,000 kms of transmission lines and over ~25,000 MVA capacity at 132 /33 kV level capable of handling ~21,000 MW of power evacuation
Power Transmission Power Grid Company of Bangladesh (PGCB) is responsible for wheeling of energy from generation stations to distribution companies using the transmission network. It is mandated for the management of national power grid and economic dispatch of electricity throughout the country. The figure (right) highlights the transmission network of PGCB (2019) The following figure (below) highlights the overall transmission capacity as of December, 2019
Chart: 
 | 861 | 3500 | 7706
  400 kV
  230 kV
  132 kV
Chart: 
 | 1000 | 3770 | 1300 | 13385 | 25104
  400/230 kV
  400 kV
  400/132 kV
  230/132 kV
  132/33 kV
  Substation Capacity (MVA)
  Transmission Lines (kms)
Source: PGCB, Deloitte Analysis Note: 1) Map not to scale 2) MVA to MW considered at 0.85 Power Factor

## Slide 93: Electricity Transmission | Historical Growth & Transmission Loss
Bangladesh has expanded its transmission line as it aims to provide 100% electricity access to the population by 2021 and also introduced 400 kV substations for importing power typically requiring transmission of power over large distances
Power Transmission HVDC substation addition is to facilitate import from India, whereas high voltage transmission capacity is to facilitate transfer of electricity over larger distances, bridging the gap between supply and demand In addition to introduction of high voltage, capacity addition CAGR from 2010-2019, at 230 kV and 132 kV is as follows: 230 kV transmission capacity: 2.8% 132 kV transmission capacity : 3.1% 230/132 kV transformation capacity: 6.9% 132/33 kV transformation capacity: 10.9% The highest CAGR growth has been in the 132 / 33 kV level as Bangladesh aimed to connect all households with electricity access by 2021 The 400 kV / 230 kV transmission line have been recently introduced in Bangladesh as the country is planning to introduce power plants in specific clusters such as Moheshkali, Payra, Mongla among others for imported fuel based power plants The transmission loss has also improved in Bangladesh with the loss reducing from 6.3% in FY16 to ~5.7% in FY19
The following figure illustrates the growth of transmission line length of PGCB (MVA) in the past decade, from FY 10 – FY 19
The following figure illustrates the transmission loss in Bangladesh between FY16 to FY19
Chart: 
 | 0 | 0 | 0 | 0 | 500 | 500 | 500 | 500 | 500 | 1000
 | 0 | 0 | 0 | 0 | 0 | 520 | 520 | 1560 | 2600 | 3120
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 650 | 650 | 650
 | 6300 | 6675 | 6675 | 6975 | 8775 | 9075 | 9375 | 9675 | 10275 | 11475
 | 7844 | 8437 | 8727 | 9705 | 10714.3 | 11963.72 | 12655.5 | 14154.5 | 16597.9 | 19907
  FY10
  FY17
  FY11
  FY12
  FY13
  FY14
  FY15
  FY16
  FY18
  FY19
  400/132 kV
  HVDC (MW)
  132/33 kV
  400/230 kV
  230/132 kV
Chart: 
 | 6.3189 | 5.8297 | 5.5154 | 5.6513
  FY16
  5.5%
  5.8%
  FY18
  FY17
  FY19
  6.3%
  5.7%
  Transmission Loss (%)
Source: PGCB, Deloitte Analysis

## Slide 94: Electricity Transmission | Outages
Bangladesh has been facing significant power cuts due to tripping & emergency outages; Delay in undertaking of maintenance and renovation of older lines have been the major cause for power outages
Power Transmission Although the power transmission network of Bangladesh is growing to meet the country’s energy needs, the quality & consistency of power supply is still a challenge Bangladesh has been witnessing increasing power outages due to tripping & emergency outages Between FY17 and FY19, the overall outage (MWh) nearly tripled from 18,712 MWh to ~53,632 MWh with ~40% outages due to tripping and emergency works The major reason for the outages has been attributed to the old installations, delay in maintenance, renovation and modernization.
The following figure illustrates the total outages (MWh) in PGCB’s system (FY17 to April-20)
Chart: 
 | 7606.2 | 10932.58 | 31030.12 | 28015.72
 | 2220.5867 | 3708.25 | 8767.59 | 7663.0033
 | 8884.9767 | 12854.14 | 13834.06 | 11945.4067
  41%
  40%
  13%
  59%
  47%
  FY17
  12%
  47%
  FY18
  26%
  16%
  58%
  FY19
  25%
  16%
  FY20 (till April)
  18,712
  27,495
  53,632
  47,624
  Schedule / Maintenance Work
  Tripping Outage
  Emergency Outage
Three PGCB sub-stations in Mymensingh, Narshingdi, and Brahmanbaria shut off after a transformer tripped at Ashuganj at 7:10 pm.
- PGCB Official after ~4 Mn households left without power on June 10, 2020
Many power transformers and long stretches of power lines are old and have not been replaced in decades though they needed to carry load more than ever before following people’s increasing dependence on electrical appliances.
- Industry Source, March 2020
Overloading rendered 1,023 transformers non-functional in June last year.
As many as 1,535 other transformers got burnt the same month hampering power distribution in many areas.
- Power Cell Official, March 2020

## Slide 95: Electricity Transmission | Major Ongoing Development Projects
Bangladesh is implementing major transmission projects to increase connectivity in the western region and also increasing capacity for power import & cluster based generation projects
Some of the major Transmission Expansion Projects
Construction of Rahanpur to Monakasha Border 400kV Transmission Line to Import Power from India (Jharkhand) to Bangladesh (28 Kms)
Southwest Transmission Grid Expansion Project (For Barisal & Rajshahi) – 132kV to 400 kV lines
Construction of 500 MW HVDC Back to Back Station from Tripura to Comilla
Evacuation for Roopur Nuclear Power Plant at 400 kV towards Dhaka
Construction of Payra – Gopalgonj – Aminbazar 400 kV line & substation
Moheshkali to Bulta (near Dhaka) Transmission Strengthening Projects for Coal / LNG based power plants
Source: PGCB, Deloitte Analysis Note 1) Map not to scale
Note: List of Planned transmission lines is provided in the Appendix

## Slide 96: Electricity Transmission Plan for Nimbus

## Slide 97: Electricity Transmission | Current Plan for Evacuation of Power for Nimbus
Current Transmission evacuation plan for NBBL
Borhanuddin
Payra
Payra
Patuakhali
Gopalganj
Aminbazar
Barishal N
Barishal
Madaripur
Payra LNG
Key | Infrastructure component
 | 220 kV Tx line
 | 220 kV Tx line (UC)
 | 132 kV Tx line
 | 400 kV Tx line
 | 400 kV Tx line (UC)
 | 400 kV Tx line (Plan)
 | Substation
 | Bhola I Switchyard
1
2
3
Substation Capacity of Barisal (N)
Loading at Patuakhali – Barisal TL incase of Payra Evacuation from Patuakhali
Delay in Gopalgonj – Aminbazar TL connectivity
Sl. No. | Stage | Details
1 | Switchyard connection | Nimbus switch yard is to connect with Bhola 1 switchyard for power transmission As per documents provided, we understand the augmentation of Bhola I busbar to allow evacuation of power from Nimbus has been completed
2 | Switchyard to Substation | Bhola 1 switchyard is connected to the 230 kV Transmission Line connecting Bhola Island to Barisal (N) Substation Capacity : 2 X 918 = 1836 Amp ; 621 MW Max Loading – 545 MW Current Loading – 320 MW (225 MW Bhola I and 95 MW Aggreko) Buffer Capacity on Transmission line: 225 MW which should be sufficient to evacuate 220 MW from Nimbus
3 | Barishal (N) S/S and beyond | We have also assessed any potential challenges that may arise for evacuation of power from Barisal (N) Substation The graph on the right shows 3 potential challenges for evacuation of power from Barisal (N) Each of these issues have been discussed in detail in subsequent slides
Source: PGCB, NBBL, Deloitte Analysis Note: 1) Map not to scale 2) UC donates under construction lines
As per Electrical Interconnection & Transmission Plan, Nimbus will evacuate the power generated through Bhola I switchyard via 230 kV transmission line to Barisal (N) substation

## Slide 98: Electricity Transmission | Substation Capacity at Barisal (N)
Potential risks for transmission evacuation Loading constraint at Barisal N S/S due to insufficient existing capacity With overall transformer capacity of Barisal Substation ~510 MW and evacuation of ~540 MW required from Bhola I, Aggreko & NBBL Plants, there may be a requirement of substation capacity augmentation at Barisal (N) In case the augmentation is not conducted, there may be evacuation challenge of NBBL if all plants are running at maximum dispatchable capacity However in case Aggreko 95 MW PPA is not extended beyond FY22, then the evacuation risk would be for short term only
G
NBBL
400 kV
230 kV
132 kV
Generator
G
The transformer capacity at Barisal (N) may need to be augmented to allow all plants from Bhola Island to run at maximum dispatchable capacity
1
Substation Capacity of Barisal (N) = 600 MVA = ~510 MW
Evacuation Capacity Required ~540 MW
Sl. No. | Stage | Details
4 | Barishal (N) S/S | The Transformer Capacity at Barisal (N) Substation at 230kV / 132 kV level is 600 MVA (2x300 MVA) Maximum evacuation possible from Barisal (N) is 510 MW (600 MVA x 0.85 Power Factor) Power Evacuation from Bhola Island Bhola I – 225 MW Aggreko – 95 MW Nimbus – 220 MW Total Evacuation Required – 540 MW
Source: PGCB, NBBL, Deloitte Analysis Note 1) The power factor has been assumed at 0.85 considering industry standards Note: 2) Map not to scale

## Slide 99: Electricity Transmission | Delay in Connectivity to Aminbazar
Potential risks for transmission evacuation Potential backdown due to delayed commissioning of Gopalganj – Aminbazar 400 kV line The Power from Payra (1320 MW) Imported Coal Based Power plant is planned to be evacuated by commissioning the Payra-Gopalgonj-Aminbazar 400 kV transmission lines Although the Payra-Gopalgonj 400 kV line has been commissioned (as on January 2020), the construction work for Gopalgonj – Aminbazar transmission line is ongoing The Gopalgonj-Aminbazar line involves a 7.5 Km underwater stretch over Padma river which may further delay the project In case of delay in the commissioning of the above TL, there may be an evacuation constraint at Gopalgonj which could have cascading effect on the power plants in the Bhola region The Barisal (N) substation is connected to the Gopalgonj Substation using 132 kV TL for further evacuation of power from the substation
G
NBBL
400 kV
230 kV
132 kV
Generator
G
The Gopalgonj-Aminbazar 400 kV TL is yet to be commissioned which may create an evacuation constraint at Gopalgonj in case Payra Imported Coal Based Power Plant is commissioned with full dispatch capacity
Source: PGCB, NBBL, Industry Reports, Deloitte Analysis ; Note: 1) Map not to scale
Aminbazar Substation
Payra Imported Coal TPP
Gopalganj Substation
Aminbazar Substation
Planned Direct Connectivity from Gopalgonj to Aminbazar
2
The Power Grid Company of Bangladesh still needs to build 84 km double-circuit 400 kv transmission line from Gopalganj to connect the Payra power plant to Aminbazar in Dhaka.
They would not be able to complete the task until June 2021.
- Golam Kibria, MD PGCB, & Payra Plant Officials, Mar-20

## Slide 100: Electricity Transmission | Delay in Connectivity to Aminbazar
Potential risks for transmission evacuation Loading Constraint at Barisal (N) substation and Barisal – Gopalgonj 132 kV line in case of Payra power evacuation from Patuakhali Even though the double circuit Payra-Gopalgonj TL has been commissioned, the power evacuation is still being done via Single Circuit leading to reduced power evacuation from Payra This is due to constraint at Gopalgonj substation to handle double circuit transmission In such a situation, the Govt. may choose to evacuate power from Payra via Patukahli to Barisal (N) and beyond Any additional power supply to Barisal substation could increase the challenge of power evacuation from Bhola Islands As mentioned earlier, the Barisal (N) substation may currently need additional capacity augmentation to enable all Bhola Island power plants to operate at maximum dispatchable capacity
In case of partial evacuation of power from Payra to Gopalgonj via Patuakhali TL the capacity constraint of Barisal (N) substation may further increase which may lead to backdown of power generation from Bhola Island Power Plants
Source: PGCB, NBBL, Industry Reports, Deloitte Analysis; Note: 1) Map not to scale
The Gopalganj substation, meant to distribute a part of the electricity generated by the Payra power plant among some north-western areas such as Gopalganj, Madaripur and Fairdpur, was not yet prepared to handle double circuit line.
The 132 kv distribution lines running from the Gopalganj substation are old lines and highly susceptible to tripping PGCB and BPDB Officials, March 2020
Borhanuddin
Payra
Payra
Patuakhali
Gopalganj
Aminbazar
Barishal N
Barishal
Madaripur
Payra LNG
Key | Infrastructure component
 | 220 kV Tx line
 | 220 kV Tx line (UC)
 | 132 kV Tx line
 | 400 kV Tx line
 | 400 kV Tx line (UC)
 | 400 kV Tx line (Plan)
 | Substation
 | Bhola I Switchyard
1
2
3
Substation Capacity of Barisal (N)
Loading at Patuakhali – Barisal TL incase of Payra Evacuation from Patuakhali
Delay in Gopalgonj – Aminbazar TL connectivity

## Slide 101
Gas & Fuel Pricing Assessment
Assessment of landed cost of LNG, HSD and HFO in Bangladesh, historical movement in prices announced by GoB for power sector and fuel price forecast for LNG and HSD
01
02
03
04
05
06
07
08
09
10

## Slide 102: LNG landed price | Historical
Following table presents an illustration of landed cost of LNG for the month of Jan, 2020 (RasGas Contract)
Bangladesh has 2 long term LNG Contracts which are Brent Crude Linked with ~$0.80 / MMBTU as fixed costs along with a ~12.5% slope
Term | Unit | Value | Details
Brent Crude Price | USD / BBL | 63.68 | Previous 3 Months’ average Brent Crude Price
LNG DES | USD / MMBTU | 8.518 | According to RasGas pricing mechanism
VAT on import | USD / MMBTU | 1.278 | 15% VAT on import
Operational cost (Regasification, T&D margin, LNG operational margin) | USD / MMBTU | 0.788 | As per BERC
Petrobangla margin | USD / MMBTU | 0.017 | As per BERC
System loss (on total cost) | USD / MMBTU | 0.148 | As per BERC (~1.4%)
VAT at selling point | USD / MMBTU | 0.537 | As per BERC (~5%)
Total Landed Cost | USD / MMBTU | 11.286 | 
LNG Pricing mechanism The LNG pricing for long term contracts in Bangladesh is linked to Brent Crude For example, Petrobangla has an agreement with Qatar’s RasGas for the supply of 2.5 MMT/Year of lean LNG for 15 years. The LNG pricing is linked to Brent crude oil index, and the LNG DES price with RasGas utilizes the approximate relation: Brent price considered is the previous three month average Brent Crude oil price Apart from the above pricing formula & VAT rates (~total ~20%) in Bangladesh, an average of $0.80/ MMBtu is the cost of regasification, transmission & margins of SOEs Following figure indicates movement of Brent with LNG landed cost, showing the 3 month lag in price movement
Chart: 
| 43101 | 43132 | 43160 | 43191 | 43221 | 43252 | 43282 | 43313 | 43344 | 43374 | 43405 | 43435 | 43466 | 43497 | 43525 | 43556 | 43586 | 43617 | 43647 | 43678 | 43709 | 43739 | 43770 | 43800 | 43831 | 43862 | 43891 | 43922 | 43952 | 43983
Brent Crude oil price (USD/BBL) | 69.0773 | 65.2774 | 66.0167 | 72.106 | 76.9752 | 74.4048 | 74.2541 | 72.5283 | 78.891 | 81.0322 | 64.7482 | 57.3624 | 59.4095 | 63.9605 | 66.1386 | 71.2333 | 71.3177 | 64.2205 | 63.9191 | 59.0418 | 62.8267 | 59.713 | 63.2119 | 67.2171 | 63.6455 | 55.657 | 32.0114 | 18.3785
LNG Landed cost (USD/MMBTU) | 11.8143 | 11.9706 | 12.5746 | 13.0077 | 13.1186 | 12.889 | 13.1206 | 13.4705 | 13.0689 | 11.9574 | 10.841 | 10.8003 | 11.2534 | 11.8639 | 12.2437 | 12.1447 | 11.7671 | 11.1333 | 11.0613 | 10.8442 | 11.0595 | 11.2861 | 11.4892 | 11.0991 | 9.2815 | 6.9444 | 5.3717
Source: Petrobangla, Industry Reports, Deloitte Analysis; Note 1) The premium, taxes, duties, margins and losses considered for estimation of landed cost of HSD in Bangladesh is based on industry & BERC estimates

## Slide 103: LNG landed price | Forecast
Following graph presents the crude oil price forecast as per various Studies (FY20 to FY30) Following graph presents the estimation of landed LNG price in Bangladesh (long term contracts)
Due to Covid-19, Crude Prices have fallen from ~$60 / bbl in FY19 to average ~$35 / bbl in FY20 with major agencies projecting sub $50/ bbl rates in the short to medium term; LNG prices in Bangladesh being linked to crude are thus expected to be muted in line with Oil Forecasts
Brent Crude Price Forecast As the long term contracts for LNG in Bangladesh are linked to Crude Oil prices, we have considered price forecast as per World Bank (long term) and EIA (short term) for projection of landed LNG prices in Bangladesh As can be seen from the graph on the right (above), the Crude Oil prices have fallen dramatically in FY20 due to impact of Covid-19 with average price reducing to $35 / BBL Both World Bank and EIA project price recovery from FY22 with the former projection prices to reach $70 / bbl by FY30 Long Term LNG Price Forecast Based on the above discussed estimates for crude oil, we have projected the landed LNG cost in Bangladesh For FY21, we have considered the average of the price forecast by World Bank and EIA Considering the RasGas contract, the landed cost of LNG in Bangladesh may reach $~8 / MMBTU in FY21 and is expected to increase gradually to $~12.3 / MMBTU by FY30 Till FY25 prices of LNG are expected to be muted due to slow recovery of crude oil prices as projected by the agencies
Chart: Crude Oil Price Forecast ($/BBL)
| FY19 | FY20 | FY21 (P) | FY22 (P) | FY23 (P) | FY24 (P) | FY25 (P) | FY26 (P) | FY30 (P)
World Bank | 61.4 | 35 | 42 | 44.5 | 47 | 49.8 | 52.7 | 55.7787 | 70
EIA | 57.02 | 35.14 | 43.88
Chart: LNG Price Forecast (Landed at Bangladesh) ($/MMBTU)
| FY21 (P) | FY22 (P) | FY23 (P) | FY24 (P) | FY25 (P) | FY26 (P) | FY30 (P)
Estimation for Landed LNG cost at Bangladesh | 8.1201 | 8.3618 | 8.749 | 9.1827 | 9.6318 | 10.23 | 12.3114
Source: World Bank, EIA, Deloitte Analysis Note 1) World Bank Data considered for WTI Crude Oil as per Commodities price Outlook for 2020 -
http://pubdocs.worldbank.org/en/633541587395091108/CMO-April-2020-Forecasts.pdf 2) EIA Price Forecast Considered for West Taxes Intermediate - https://www.eia.gov/analysis 2) Landed LNG price forecast considered in line with RasGas pricing formula with all other cost components for LNG price (taxes, regasification charges, margins , losses considered at FY19 levels)

## Slide 104: Natural Gas Price for Power Sector| Forecast
Following graph presents the price forecast for Domestic Production of natural gas and Landed Price of LNG import ($/MMBTU) Following graph presents the estimation of landed price of Domestic Natural Gas in Bangladesh ($/MMBtu)
Considering the forecasts for domestic gas production cost and imported LNG prices, the natural gas prices for the power sector may increase from the current $1.4 / MMBTU to $2.6 / MMBTU by FY 26
Domestic Gas Price Forecast Between FY09 and FY19, Bangladesh has increased the natural gas tariff for power sector at a CAGR of ~4.7% whereas the average inflation rate (WPI Index) in Bangladesh has grown at an average rate of ~5.5% between FY15 and FY19 We have projected the growth rate of production of domestic natural gas for power sector in line with the tariff hikes in Bangladesh The production cost for natural cost was $1.43 / MMBTU in FY20 as per BERC which is thus expected to increase to $1.88 / MMBTU by FY26 We have projected the landed cost of LNG in Bangladesh considering the crude oil price movement as projected by World Bank and EIA (as discussed earlier) Considering the current blending ratio of ~25% to continue to lack of additional supply infrastructure of LNG and a gradual subsidy reduction of 5% p.a. we have projected the overall natural gas / LNG cost in Bangladesh for the power sector As can be seen from the graph on the right (below), the tariff for natural gas for power sector is expected to increase to $2.58 / MMBTU by FY26
Chart: $/MMBTU
| FY20 | FY21 (P) | FY22 (P) | FY23 (P) | FY24 (P) | FY25 (P) | FY26 (P)
Cost of Domestic Gas Production | 1.43 | 1.4967 | 1.5666 | 1.6397 | 1.7162 | 1.7964 | 1.8802
Landed LNG import cost | 11.63 | 8.1201 | 8.3618 | 8.749 | 9.1827 | 9.6318 | 10.2324
Chart: $/MMBtu
| FY 20 | FY21 (P) | FY22 (P) | FY23 (P) | FY24 (P) | FY25 (P) | FY26 (P)
Tariff for Power Sector | 1.393 | 1.393 | 1.4694 | 1.7085 | 1.9706 | 2.2531 | 2.5794
Source: World Bank, BERC, EIA, Deloitte Analysis; Note 1) The tariff for FY21 has been considered at $1.39 / MMBTU in line with the tariff for FY20 as proposed by BERC despite the fall in projection for landed LNG cost as we do not expect the Govt. to reduce the tariff for natural gas 2) The current subsidy of ~65% to power sector has been assumed to be gradually reduced in line with Govt. Vision and has been considered at 5% p.a. for the purpose of our analysis

## Slide 105: HSD landed price | Historical
Following table presents an illustration of landed cost of HFO for the month of Jan, 2020
Although Bangladesh sources majority of its HSD requirement from International suppliers, the GoB has kept the HSD prices constant with no linkage to global oil price variation
Term | Price (Tk/Litre) | Description
Tariff/Assessable Value (TV) | 31.89 | Price of Crude converted to Tk/Liter
Premium (USD/bbl.) | 2.27 | Premium added to Platts rate
CIF Cost | 33.03 | Indexed to Platts rate + premium
Corresponding Duty (CD) | 3.19 | 10% on TV
Other Taxes (VAT, ATV, AIT) | 7.71 | 25% on (TV + CD)
Other charges | 1.75 | Port costs, financing, surveying and administrative expense
Selling & Distribution Cost () | 1.30 | Transit Loss & Transportation to depot
BPC's Margin | 4.70 | 10% on total cost till sale to dealer
Dealer costs | 5 | Transportation to dealer and dealer margin
Total End/Customer Level Cost | 56.59 | 
HSD Pricing mechanism HSD pricing is linked to Platts Rate (FOB Gulf). The CIF value of HSD is acquired at a premium per barrel to the Platts rate However, the selling rate is fixed by the GoB and does not seem to linked to actual cost of supply of diesel in Bangladesh Following figure indicates movement of Crude Oil with HSD landed cost, (3 month lag in price movement) and the government fixed price of HSD
Source: BPC, Industry Reports, Deloitte Analysis; Note 1) The premium, taxes, duties, margins and losses considered for estimation of landed cost of HSD in Bangladesh is based on industry estimates
Chart: 
  Jan-12
  Jan-19
  Jan-13
  Jan-15
  Jan-14
  Jan-16
  Jan-17
  Jan-18
  Jan-20
  USD / BBL
  Tk / Litre
  Brent Crude oil price (USD/BBL)
  Actual HSD Selling Rate (Tk/Litre)
  HSD Landed cost estimate (Tk/Litre)

## Slide 106: HSD landed price | Forecast
Following graph presents the estimation of landed HSD price in Bangladesh (long term contracts)
The HSD prices are expected to remain at current BDT 65 / liter levels till FY26 considering the lower crude oil price projections; Any price increase / decrease for end consumers would be dependent on GoB’s fiscal targets and other considerations
Long Term HSD Price Forecast Considering the Crude Oil Price Forecast discussed earlier, we have projected the landed HSD cost in Bangladesh We have considered the average of the price forecasts by all agencies discussed above till FY26 for the purpose of estimating crude oil price As can be seen from the graph on the right, the landed cost of HSD in Bangladesh may reach BDT ~51 / liter by FY26 However historically the Bangladesh Govt. has set the price for HSD in Bangladesh without any linkage to international crude price movement in the past Thus, we expect that the GoB may not increase price of HSD till the actual landed cost of price of HSD touches BDT 65 / liter (the current price set by GoB for consumers). In case of actual landed cost of HSD increasing beyond BDT 65 / liter, the Govt. may increase price in line with actual landed cost subject to the Govt.’s fiscal targets and other considerations
Chart: Landed HSD cost Forecast (BDT / Liter)
| FY21 (P) | FY22 (P) | FY23 (P) | FY24 (P) | FY25 (P) | FY26 (P)
Estimation for Landed HSD cost at Bangladesh | 40.94 | 42.14 | 44.07 | 46.23 | 48.46 | 50.83
Source: World Bank, EIA, Deloitte Analysis Note 1) World Bank Data considered for WTI Crude Oil as per Commodities price Outlook for 2020 -
http://pubdocs.worldbank.org/en/633541587395091108/CMO-April-2020-Forecasts.pdf 2) EIA Price Forecast Considered for West Taxes Intermediate - https://www.eia.gov/analysis/ 3) Landed HSD price forecast considered in line with BPC’s pricing formula estimates with all other cost components for HSD price (taxes, regasification charges, margins , losses considered at FY19 levels)

## Slide 107
Discom Credit Risk Assessment
Historical performance of BPDB, average power purchase cost and selling rate assessment, billing & collection assessment, IPP payment history, foreign payment performance, impact of Covid-19 on financial performance
01
02
03
04
05
06
07
08
09
10

## Slide 108: BPDB Historical Performance| Discom Credit Assessment
Following graph shows the Total Revenue and Net Profitability (after subsidy adjustment) (BDT Bn) of BPDB (Generation & Bulk Supply) from FY15 to FY19: Following graph shows the subsidy support to BPDB in the last 5 years (BDT Bn) from FY15 to FY19
BPDB has been historically earning losses with Government providing major support in the form of loans which has further strained BPDB’s financial performance
BPDB Historical Profitability As can be seen from the graph on the right (above), BPDB (Generation & Bulk Supply) has been incurring losses historically in the Generation & Bulk Supply business. The losses are primarily due to the differential in the overall power purchase cost and the allowed bulk supply tariff for BPDB BPDB is dependent on the Government Subsidy for its operations. Subsidy Support from Government The Government of Bangladesh supports BPDB to cover its power purchase cost and power sales cost in the following forms: Subsidy Support as Loan – The GoB has been providing interest bearing Loan as subsidy support to BPDB Interest on Loan for Subsidy – Although BPDB charges the interest on loan for subsidy in the profit and loss account, they have not paid the same to GoB since FY15. Thus, the interest accruals on the loan is also treated as subsidy Cash Subsidy – Since FY18, GoB has started providing direct cash based subsidy to BPDB The introduction of Cash Subsidy has led to reduction in overall losses for BPDB in FY19 making it match its overall revenue requirement from operations
Chart: 
 | 204.8297 | 242.0064 | 271.0347 | 293.6441 | 332.0332
 | -69.3179 | -36.6848 | -42.4267 | -82.562 | -1.0261
  FY17
  FY16
  FY15
  FY18
  FY19
  Revenue (BDT Bn)
  Net Profit / Loss (BDT Bn)
Chart: 
 | 7.8066 | 9.9465 | 11.2883 | 9.562 | 79.6673
 | 91.8521 | 27.949 | 39.9401 | 11.8831 | 12.948
 | 35.4969 | 0
  57
  10
  8
  FY17
  FY16
  FY15
  10
  11
  FY18
  0
  FY19
  100
  38
  51
  93
  Cash Subsidy
  Subsidy (Loan Form)
  Interest on Subsidy
49%
16%
19%
19%
28%
Overall Subsidy as % of Revenue
Source: BPDB, Deloitte Analysis; Note 1) The Net Profit / Loss depicted in the graph (top) includes the subsidy provided by Government of Bangladesh (bottom graph)

## Slide 109: BPDB Net Worth| Discom Credit Assessment
Following graph shows the breakup of Networth (BDT Bn) of BPDB (Generation & Bulk Supply) from FY15 to FY19: Following graph shows the long term liabilities of BPDB in the last 5 years (BDT Bn) from FY15 to FY19
The continued losses has led to net-worth erosion of BPDB; However with cash subsidy from GoB, the net-worth position may start to improve in future
Net Worth of BPDB The continued losses and subsidy support to BPDB in the form of loans has led to erosion of its networth The Government of Bangladesh has been steadily infusing equity in BPDB. However the same has been inadequate to change the solvency position of BPDB Although the networth position of BPDB has been deteriorating till FY18, the position has improved slightly in FY19 due to infusion of cash subsidy in BPDB However BPDB still has a negative net worth of BDT ~211 Bn in FY19 Long Term Liabilities BPDB’s funds its long term asset by Government & loans from International Bilateral / Multilateral agencies only The largest long term debt component is the Subsidy Support as loan from GoB The long term debt has increased at 12% CAGR and currently stands at BDT 621 Bn in FY19 The Debt Equity Ratio due to eroded networth has been negative for BPDB at an average of ~(-) 3.5-4.0 However with the cash infusion as subsidy, the debt equity ratio is expected to improve in the future
Chart: 
 | 126.4468 | 139.8638 | 155.2187 | 168.3638 | 180.999
 | 129.138 | 133.6358 | 139.1601 | 149.1094 | 154.0384
 | -388.8033 | -420.5826 | -460.2517 | -542.7574 | -546.2444
  -166
  -147
  FY15
  FY16
  FY17
  FY18
  FY19
  -133
  -225
  -211
  Paid Up Equity
  Retained Earnings
  Other Funds & Reserves
Chart: 
 | 15.7078 | 40.7907 | 94.8658 | 127.6932 | 129.8172
 | 328.2152 | 356.1642 | 396.1043 | 431.6012 | 431.6012
 | 53.4718 | 53.88 | 54.5803 | 59.17 | 59.8527
  618
  54
  FY16
  397
  53
  FY18
  55
  41
  FY15
  16
  59
  FY19
  451
  546
  621
  60
  FY17
  +12%
  Government Loan (Projects)
  Subsidy Support (Loan)
  Foreign Loan (Projects)
-3.8
-3.9
-4.1
-3.4
-3.8
Debt / Equity Ratio
Source: BPDB, Deloitte Analysis

## Slide 110: BPDB Power Purchase and Selling Rates| Discom Credit Assessment
Following graph shows the average Power Purchase Cost vs Average Selling Cost (BDT / kWh) of BPDB (Generation & Bulk Supply): : Following graph shows the major fuel wise total power purchase cost including capacity charge (BDT / kWh) BPDB in the last 3 years from FY17 to FY19
The contribution of liquid based power in the energy mix has been driving the overall power purchase cost of BPDB higher than the average bulk selling rate
Purchase vs Selling Cost The average power purchase cost for BPDB has been ranging between TK 5.5-6.3 / unit in the last 5 years whereas the average bulk selling rate has been Tk 4.8-5.1 / unit The higher average power purchase cost has been due to continued contribution of liquid fuel based power in the energy mix of Bangladesh The average cost of generation of HFO and HSD based power was Tk ~11-14 / unit for HFO and Tk 20-28 / unit for HSD in the last 3 years These liquid fuels contribute ~20%-25% of the overall energy requirement of Bangladesh It is due this non recovery of the costs from tariff which has been impacting the health of BPDB over the years
Chart: 
 | 6.3143 | 5.575 | 5.6597 | 6.3324 | 6.0124
 | 4.8091 | 5.026 | 5.0699 | 5.0172 | 4.9692
  FY15
  FY18
  FY16
  FY19
  FY17
  -24%
  -10%
  -10%
  -21%
  -17%
  Average Power Purchase Cost
  Average Bulk Selling Rate
Chart: 
 | 2.5977 | 2.8133 | 2.7289
 | 22.422 | 19.9914 | 28.1673
 | 11.5315 | 11.444 | 13.7741
 | 5.5231 | 5.8744 | 5.4604
  FY19
  FY18
  FY17
  Import
  Gas
  HSD
  HFO
Chart: 
 | 38052 | 39804.2 | 48306
 | 2627 | 4520.31 | 2022
 | 9950 | 10849.71 | 11426
 | 4656 | 4782.72 | 6786
 | 1991 | 2721.06 | 1993
  17%
  68%
  66%
  64%
  17%
  5%
  8%
  FY17
  7%
  8%
  FY18
  3%
  16%
  10%
  FY19
  57,276
  62,678
  70,533
  3%
  4%
  3%
  Gas
  HSD
  Import
  HFO
  Others
Following graph shows the major fuel wise contribution in the Bangladesh energy mix (MU) in the last 3 years from FY17 to FY19
Source: BPDB, Deloitte Analysis

## Slide 111: BPDB - Difference in Billing & Collections| Discom Credit Assessment
Following graph shows the total power purchase cost and total annual billing of BPDB from FY15 to FY19: Following graph shows total annual billing & collections in the last 5 years from FY15 to FY19
The difference in power purchase & bulk sales rate has affected liquidity position with only ~1 month of cash & bank balances with BPDB to pay off power purchase cost
BPDB Payments & Collections The difference in the average power purchase rate and average selling rate has led to a mismatch in BPDB’s overall power purchase cost and annual billing to discoms BPDB has been able to bill only ~80%-95% of its total power purchase cost to the discoms Apart from the power purchase cost, BPDB has to incur expenses pertaining to general & administrative activities, long & short term loans, provisions & maintenance activities among others During FY15 and FY16, BPDB was able to collect less than 95% of its billing from discoms which has now improved to 99%-100% range However the annual cash position of BPDB has deteriorated due to an overall mismatch between its revenues and expenditure. During FY18 and FY19, BPDB’s cash balance was only sufficient to pay ~1 Month’s power purchase cost signifying requirement of resilience on borrowings to pay off dues Following graph shows cash & bank balance of BPDB (BDT Bn) in the last 5 years from FY15 to FY19
Chart: 
 | 255.9975 | 256.0397 | 288.5323 | 362.2583 | 389.5212
 | 204.951 | 245.745 | 273.351 | 297.131 | 330.675
  FY15
  FY16
  FY17
  FY18
  FY19
  Total Power Purchase Cost
  Total Annual Billing
80%
96%
95%
82%
85%
Total Annual Billing as % of Total Power Purchase Cost
Chart: 
 | 204.951 | 245.745 | 273.351 | 297.131 | 330.675
 | 193.013 | 222.383 | 274.354 | 293.725 | 332.295
  FY15
  FY16
  FY17
  FY18
  FY19
  Total Annual Billing
  Total Annual Collection
94%
90%
100%
99%
100%
Billing Collection Ratio
Chart: 
 | 0
 | 56.0728 | 51.6676 | 68.5214 | 36.9642 | 38.9828
  FY15
  FY16
  FY17
  FY19
  FY18
  Cash in Hand & Bank
Source: BPDB, Deloitte Analysis

## Slide 112: BPDB Debtor and Creditor Days| Discom Credit Assessment
Following graph shows the Creditor’s Turnover ratio and Creditor Days in the last 5 years from FY15 to FY19 Following graph shows Debtor’s Turnover ratio and Debtor Days in the last 5 years from FY15 to FY19
There is a mismatch in BPDB’s payables & receivables due to delayed payments by discoms to clear the dues which further impact BPDB’s liquidity position
BPDB Debtor & Creditor Receivable Days There is a significant mismatch in BPDB’s liquidity position in respect to the payment made to creditors and receivables from debtors. BPDB’s average creditor days has been in the range of ~50-70 days since FY15 whereas the average debtor days has been in the range of ~170-190 days A lower creditor turnover ratio / creditor days than debtor turnover ratio / debtor days signifies that BPDB is paying more frequently to clear its debt to IPPs / Import / Fuel Suppliers than it is receiving from the power sales to discoms such as DPDC, DESCO, REB among others Historically the BPDB’s total receivables have been ranging between 2-2.5 times its payables Following graph shows Total Accounts Payable and Receivables for BPDB (BDT Bn) in the last 5 years from FY15 to FY19
Chart: 
| FY15 | FY16 | FY17 | FY18 | FY19
Creditor's Turnover Ratio | 6.4543 | 6.8235 | 7.37 | 6.2845 | 5.5165
Creditor's Days | 58.8203 | 48.1731 | 56.3024 | 71.3153 | 66.0069
Chart: 
| FY15 | FY16 | FY17 | FY18 | FY19
Debtor's Turnover Ratio | 2.1077 | 2.1942 | 2.1603 | 1.997 | 2.0401
Debtor's Days | 189.5488 | 171.7204 | 184.5118 | 195.6553 | 182.1374
Chart: 
 | 41.2544 | 33.7924 | 44.507 | 70.7797 | 70.4413
 | 103.9984 | 110.9415 | 133.4404 | 153.6827 | 159.3296
  FY15
  FY18
  FY16
  FY17
  FY19
  Total Accounts Payable
  Total Receivables
Source: BPDB, Deloitte Analysis

## Slide 113: BPDB – Fixed Charge Assessment| Discom Credit Assessment
Following graph shows the tentative power demand growth estimated in Bangladesh between FY19 and FY26 (MW): Following graph shows total estimated total capacity charge payment impact (BDT Bn) for BPDB till FY26[1]
Although average power demand is expected to grow at a CAGR of ~10.4% till FY26, BPDB’s fixed payment obligations may increase from current estimated BDT ~173 Bn to BDT ~281 Bn during the same period at a CAGR of ~7.1% only
Growth in Power Demand in Bangladesh As per our power demand assessment, Bangladesh has an average power demand of ~7,800 MW in FY19 The average power demand (in our Covid -19 base case) is expected to reach ~15,700 MW by FY26 Thus, the average power demand is expected to grow at a CAGR of ~10.4% till FY26 Impact on Fixed Charges Payout by BPDB As per our estimation, Bangladesh’s total power purchase cost of BDT 390 Bn in FY19, comprised ~BDT 173 Bn of fixed charges only Out of the BDT ~173 Bn, rental/quick rental power plants may have cost BPDB BDT ~27 Bn (~15% of total FC) despite having a share of ~9% in the installed capacity in Bangladesh Based on our supply outlook, Bangladesh’s installed capacity of ~18,961 MW in FY19 is expected to reach ~26,400 MW by FY26 leading to an increase in its fixed payment obligations However considering that the rental / quick rental power plants are expected to retire by FY26, there may be some reduction in Fixed Charge payout The graph on the right (below) shows the estimated fixed charge payout by BPDB in FY26 which may reach BDT ~281 Bn growing at a CAGR of ~7.1% which is lower than estimated average power demand growth
Chart: 
 | 7832 | 15673
  FY19
  FY26 (Estimated)
  10.4%
Chart: 
 | 173 | 281
  FY19 (Estimated)
  FY26 (Estimated)
  7.2%
Source: BPDB, Industry Reports, Deloitte Analysis; Note [1]: 1) We have considered the fixed cost of HFO based plants under RPP/QRPP ownership in FY19 based on sample benchmark data of PPAs for a few RPP/QRPP plants in Bangladesh which may lead to variance (+/- 10%) in the total power purchase cost estimated by us and the total power purchase cost reported by BPDB in FY19 2) We have considered the fixed cost of HSD Based plants under RPP / QRPP ownership at the same level as that of entire HSD portfolio in Bangladesh in FY19 which may lead to variance (+/- 10%) in the total power purchase cost estimated by us
and the total power purchase cost reported by BPDB in FY19 3) We have estimated the total power purchase cost of upcoming LNG and Imported coal based power
plants considering the levelized projections for fixed cost of such plants based on industry estimates and 1st year fuel price for LNG at $8 / MMBTU (landed cost) and Coal at $~90 / Tonne (landed cost) 5) The incremental capacity addition required to meet the average demand (apart from the planned capacity addition) has been assumed to be met by LNG based power plants only 6) We have estimated the projected the BPDB payment obligations for meeting average power demand only and not for meeting peak demand.

## Slide 114: BPDB – Variable Charge Assessment| Discom Credit Assessment
Following graph shows total estimated total variable charge payment impact (BDT Bn) for BPDB till FY26: Following graph shows the Estimated Per unit Cost & Revenue Forecast (BDT / kWh)
The growth in power demand at 10.4% CAGR would also lead to increase in variable payment for BPDB from the current 217 Bn BDT to ~409 Bn BDT by FY26; However the growth in variable payment would be lower at 9.5% CAGR leading to overall power increase cost at 8.5% CAGR only
Impact Variable Charges Payout by BPDB As mentioned earlier, Bangladesh paid ~217 Bn BDT as variable charges for the power produced in the country in FY19 Out of the BDT ~217 Bn, liquid fuel based plants (HSD/HFO) are estimated to have contributed to ~142 Bn (65% of the fuel cost) compared to their installed capacity of 6,140 MW (32% of total installed capacity of ~18,961 MW) Going forward we expect the average power demand in Bangladesh to be met by ~19,600 MW of non-liquid based power supply capacity in Bangladesh The graph on the right (below) shows the estimated variable charge payout by BPDB in FY26 to meet the average power demand which may reach BDT ~409 Bn growing at a CAGR of ~9.5% which is lower than estimated average power demand growth Per Unit Cost & Revenue Impact The average power purchase cost of BPDB which stood at BDT ~5.7 / kWh in FY19 may reduce to BDT ~5.0 / kWh primarily driven by replacement of expensive HSD/HFO based generation to economical sources of power such as LNG and Imported Coal We have also considered that in such as supply scenario, the average bulk power selling rate of BPDB may remain constant at BDT 5 / kWh (at FY19 levels) considering the fall in overall power purchase cost for BPDB Thus the gap between BPDB’s revenue and power purchase cost is expected to reduce significantly to marginal levels by FY26
Source: BPDB, Industry Reports, Deloitte Analysis; Note 1) We have considered the average gas price for power sector at BDT 4.45 / SCM as per prevailing tariff with no escalation. 2) We have considered the average Variable Cost per unit (kWh) for Gas, HSD and HFO based plants belonging to Rental / Quick Rental Ownership (RPP/QRPP) in FY19 at same level as that of the entire Gas, HSD and HFO portfolio in Bangladesh in FY19 3) We have considered the fixed cost of HFO based plants under RPP/QRPP ownership in FY19 based on sample benchmark data of PPAs for a few RPP/QRPP plants in Bangladesh which may lead to variance (+/- 10%) in the total power purchase cost estimated by us and the total power purchase cost reported by BPDB in FY19 4) We have considered the fixed cost of HSD Based plants under RPP / QRPP ownership at the same level as that of entire HSD portfolio in Bangladesh in FY19 which may lead to variance (+/- 10%) in the total power purchase cost estimated by us and the total power purchase cost reported by BPDB in FY19 5) We have
estimated the total power purchase cost of upcoming LNG and Imported coal based power plants considering the levelized projections for fixed cost of such plants
based on industry estimates and 1st year fuel price for LNG at $8 / MMBTU (landed cost) and Coal at $~90 / Tonne (landed cost) 6) The incremental capacity addition required to meet the average demand (apart from the planned capacity addition) has been assumed to be met by LNG based power plants only 7) We have estimated the projected the BPDB payment obligations for meeting average power demand only and not for meeting peak demand
  Average Bulk Power Sale Price
Chart: 
 | 0
 | 4.97 | 5.03
  FY19
  FY26 (Estimated)
Chart: 
 | 2.98
 | 2.05
  5.0
Chart: 
 | 3.16
 | 2.52
  5.7
  Average Capacity Charge
  Average Variable Charge
Chart: 
 | 217 | 409
  FY26 (Estimated)
  FY19 (Estimated)
  9.5%

## Slide 115: BPDB – Payment Assessment (Case – Power Demand Growth at 5% CAGR)
Following graph shows total estimated total variable charge payment impact (BDT Bn) for BPDB till FY26: Following graph shows the Estimated Per unit Cost & Revenue Forecast (BDT / kWh)
Considering a lower power demand growth at 5% CAGR till FY26, the total power purchase cost of BPDB is expected to still grow at a lower rate of 3.4% signifying improved financial strength
Impact on Fixed and Variable Charges Payout by BPDB We considered a low power demand scenario of ~5% CAGR to assess the impact of BPDB’s payment obligation Thus, the average power demand would increase from the current ~7,832 MW to ~11,020 MW by FY26 In such a case, we expect the fixed charges to remain constant at BDT ~280 Bn in line with our projections in base case However the variable charge is expected to reduce to BDT ~212 Bn compared to BDT ~410 Bn in the base case in line with lower generation Thus, the overall power purchase cost would increase at a CAGR of only 3.4% which would be lower than the power demand growth rate of 5% Per Unit Cost & Revenue Impact The average power purchase cost of BPDB which stood at BDT ~5.7 / kWh in FY19 may reduce to BDT ~5.1 / kWh considering the fuel substitution with cheaper fuels (LNG and Imported Coal) We have assumed the bulk power sale rate to remain at 5 BDT / unit as in the base case Thus the gap between BPDB’s revenue and power purchase cost is still expected to reduce significantly to marginal levels by FY26
Source: BPDB, Industry Reports, Deloitte Analysis; Note 1) We have considered the average gas price for power sector at BDT 4.45 / SCM as per prevailing tariff with no escalation. 2) We have considered the average Variable Cost per unit (kWh) for Gas, HSD and HFO based plants belonging to Rental / Quick Rental Ownership (RPP/QRPP) in FY19 at same level as that of the entire Gas, HSD and HFO portfolio in Bangladesh in FY19 3) We have considered the fixed cost of HFO based plants under RPP/QRPP ownership in FY19 based on sample benchmark data of PPAs for a few RPP/QRPP plants in Bangladesh which may lead to variance (+/- 10%) in the total power purchase cost estimated by us and the total power purchase cost reported by BPDB in FY19 4) We have considered the fixed cost of HSD Based plants under RPP / QRPP ownership at the same level as that of entire HSD portfolio in Bangladesh in FY19 which may lead to variance (+/- 10%) in the total power purchase cost estimated by us and the total power purchase cost reported by BPDB in FY19 5) We have
estimated the total power purchase cost of upcoming LNG and Imported coal based power plants considering the levelized projections for fixed cost of such plants
based on industry estimates and 1st year fuel price for LNG at $8 / MMBTU (landed cost) and Coal at $~90 / Tonne (landed cost) 6) The incremental capacity addition required to meet the average demand (apart from the planned capacity addition) has been assumed to be met by LNG based power plants only 7) We have estimated the projected the BPDB payment obligations for meeting average power demand only and not for meeting peak demand
  Average Bulk Power Sale Price
Chart: 
 | 0
 | 4.97 | 5.03
  FY19
  FY26 (Estimated)
Chart: 
 | 2.2
 | 2.9
  5.1
Chart: 
 | 3.16
 | 2.52
  5.7
  Average Capacity Charge
  Average Variable Charge
Chart: 
 | 217 | 212
 | 173 | 281
  FY26 (Estimated)
  FY19 (Estimated)
  390
  493
  3.4%
  Capacity Payments
  Variable Charge Payments

## Slide 116: BPDB Liquidity Assessment – Public Sources| Discom Credit Assessment
Impact of Foreign Currency Reserves on payment by BPDB to Foreign Sponsors Idle liquid Fuel Plants one of the major causes of Capacity Payments
BPDB is facing difficulties in making the payments for electricity imports and foreign loans due to a crisis of US dollar in state-owned commercial banks.
Though BPDB has paid the necessary fund in the local currency, the state-run banks are yet to make the payment due to foreign currency crisis. NTPC of India has already imposed a surcharge against Agrani Bank Ltd for the delay.
- Industry Source, Dec 2019
We have presented a few snippets from primary/secondary sources on the liquidity position of BPDB and the overall market perception on over capacity in Bangladesh
Delay in Payment to IPPs Impact of Fixed Charge on GoB’s Finances
During the last fiscal year, the Bangladesh Power Development Board (BPDB) had to pay almost Tk9,000 crore to 74 private companies as capacity payment. In turn, as compensation, the government had to provide subsidy to the power board.
Subsequently, the power board had to suspend payments to private power producers for more than five months
"After getting budgetary support from the government, the dues have been cleared," Selim Abed, member (finance) of the BPDB
- Selim Abed, Member (Finance),BPDB, May 2020
We are worried that private investments across the country have not grown in line with power generation," said an official of a private power company.
"This is already affecting the power board and if things go on like this, the government will find itself in a big financial mess”
- Official of Private Power Company, May 2020
Idle state’ of the costly diesel-based power plants was causing the hemorrhage of the government’s funds because of the capacity payments that the BPDB needs to pay to those power plants
- Dr. Ahmed Kaikaus, Power Division Secretary, Oct 2019
Source: Industry Reports

## Slide 117: BPDB – IPP Relations Assessment | Discom Credit Assessment
Historically the Government has not defaulted on payment to IPPs and provides payment guarantees to all IPPs in Bangladesh; Bangladesh also has not terminated any PPA for operational plants in the last 5 years
Govt. Guarantee for Power Plants As per Industry sources, the Government provides payment guarantees for payment defaults by BPDB, PGCB and other GOB owned Power utilities for all existing IPPs in Bangladesh Although there has not been any payment default to IPPs in the last 5 years, there has been delay in payments to IPPs on a few occasions Outlook for PPA extensions / terminations Based on our assessment of the PPA extensions / terminations, most Rental Power Plants, Public plants and BPDB plants are operating in extension to their operational life in Bangladesh The table on the right illustrates a few plants which have received extensions in Bangladesh As per Industry sources, BPDB has not terminated any PPA in the least 5 years for operational plants In April 2019, BPDB had terminated two PPA for 2 power plants (108MW Basila, Keraniganj power plant and 108MW Gabtali power plant) for failure to commission the plants even after 8 years (PPA signed in October 2011) However even these plants had received another 1 year extension for commissioning with the GoB backtracking on the PPA
Following chart highlights a few tenure extensions for Power Plants in Bangladesh:
Sr. No | Plant name | Capacity (MW) | COD | Extension
1 | Venture Energy | 38.50 | 2009 | 2 years (2015) 3 years (2018)
2 | Kumargaon (Energyprima) | 50 | 2008 | 3 years (2012) 3 years (2015)
3 | NEPC Consortium (IPP/SIPP) | 110 | 1999 | 3 Year (2014) 2 Years (2019)
3 | Bogra (Energyprima) | 20 | 2008 | 3 years (2012) 3 years (2015)
4 | Shahjibazar (Energyprima) | 50 | 2008 | 3 years (2012) 3 years (2015)
3 | Powerpac Motiyara | 100 | 2012 | 5 years (2017)
4 | Precision Energy (Ashuganj) | 55 | 2010 | 5 years (2017)
5 | Kathakali-Rajshahi | 50 | 2010 | 5 years (2017)
6 | Sinha power -Chapainawabganj | 50 | 2010 | 5 years (2017)
7 | UEL-Ashuganj | 53 | 2011 | 5 years (2013)
8 | KPCL –II | 115 | 2010 | 5 years (2016)
9 | Khanjahan Ali – Summit | 40 | 2010 | 5 years (2016)
10 | Acorn Infra | 100 | 2012 | 5 years (2017)
11 | Dutch Bangla | 100 | 2011 | 5 years (2016)
Source: BPDB, Industry Reports, Deloitte Analysis; Note 1) Over the last 10 years, a few power plants have retired in Bangladesh and hence their PPAs have expired on completion of their tenure.

## Slide 118: BPDB Liquidity Assessment – Covid 19 | Discom Credit Assessment
Following graph shows the change in change in monthly generation power portfolio in Bangladesh (MU) Pre & Post Covid Following graph shows the tentative change in Power Purchase Cost for BPDB (monthly) in BDT / kWh due to Covid -19 Pandemic
The fall in energy demand due to Covid-19 epidemic has led to a decrease in liquid based generation which is expected to reduce the overall power purchase cost for BPDB
Fall in Power Generation due to Covid 19 pandemic Bangladesh imposed national holiday from 26th March 2020 due to the Covid-19 pandemic which has led to an average monthly power generation fall by ~16% in April 2020 compared to April 2019 The fall has been due to shutdown of industries and commercial establishments which forms ~42% of the total electricity demand segment in Bangladesh The curtailment of power demand has also led to a shift in the power generation mix in Bangladesh with BPDB backing down costly HFO based generation plants and shutting down HSD based generation completely. The liquid based power generation share in the fuel mix has fallen from 20% in April 2019 to 8% in April 2020. In absolute terms the generation fell from ~1,230 MUs to ~419 MUs representing an absolute fall by 66% Gas based power plants have increased their share in the fuel mix due to their cheaper cost whereas coal based power witnessed the increase due to test runs of NWPGCL Payra Unit 1 (660 MW). Impact on overall power purchase cost of BPDB We have projected the overall impact of the shift in generation mix as well as reduced generation on the average power purchase cost of BPDB We considered the average variable charge to remain at similar levels of FY2019 with BPDB continuing to pay fixed charges to all power plants Considering an average Fixed Charge of ~BDT 2.4 / kWh in FY2019 we have projected power purchase cost of BPDB in April 2020 At the current levels, the overall power purchase cost for BPDB may fall from BDT 5.7 / unit in FY2019 to BDT 5.0 in April 2020
Chart: 
 | 619.2283 | 404.728
 | 52.4725 | 24.9044
 | 1234.6929 | 419.3722
 | 3.9545 | 5.7581
 | 168.5314 | 417.162
 | 4075.9124 | 3894.8255
  75%
  1%
  0%
  66%
  3%
  20%
  10%
  April 2019 (Pre Covid)
  8%
  8%
  0%
  8%
  April 2020 (Post Covid)
  6,155
  5,167
  Hydro
  Gas
  Coal
  Oil
  Solar
  Import
+9.2%
+5.3%
0%
-11.9%
-0.4%
-2.2%
Change in Fuel Mix
Monthly Generation (MU)
-2.2%
-16%
Overall Fall in Generation
Chart: 
 | 2.4 | 2.66
 | 3.28 | 2.32
  FY-2019 (Pre Covid)
  April-2020 (Post Covid)
  5.7
  5.0
  Fixed Charge
  Energy Charge
The per unit FC is expected to increase due to lower generation whereas shift from Oil to Gas based generation is expected to reduce energy charge
Source: BPDB, Deloitte Analysis

## Slide 119: BPDB Liquidity Assessment – Covid 19 | Discom Credit Assessment
Following graph shows the change in total power purchase cost (BDT Bn) in Bangladesh in Pre & Post Covid Scenario Following graph shows the tentative impact on power sales to discoms by BPDB (BDT Bn) due to Covid -19 Pandemic
Apart from the reduction in power purchase cost, BPDB’s revenue is also expected to be impacted; However as BPDB sells power on a fixed bulk supply tariff, the overall difference in power purchase cost & revenue from sales could reduce substantially
Fall in Overall Power Generation Cost The reduction in power generation by 16% and shift from liquid to gas based generation is expected to reduce monthly power generation cost of BPDB by ~28% The average liquid based generation cost for BPDB at BDT ~16 / kWh is being replaced by cheaper gas based power generation at BDT ~2.7 / kWh The per month saving in power purchase cost could come down by ~BDT 10 Bn Fall in Overall Power Sales We have considered the average billing rate of FY2019 to assess the tentative fall in revenue for BPDB for post covid-19 scenario In FY2019, the average billing rate for BPDB was ~BDT 5.00 / Unit to the discoms which has been kept at same level for FY20 In such a scenario, BPDB’s average revenue from power sales could fall from BDT 31 Bn in April 2019 (tentative) to BDT 26 Bn in April 2020 Despite the revenue fall, the overall profitability position for BPDB should ideally improve as the difference in Power Purchase & Sales would reduce substantially to become at par. The GoB has waived for Late Payment Charges for domestic consumers till May 2019 which is expected to lead to a delay in overall collections for discoms The Discoms in turn are expected to delay their payments to BPDB which may need short term support from the Government of Bangladesh to pay its dues to various IPPs as well as fuel suppliers and vendors for its own power plants
Chart: 
 | 3.3812 | 2.6196
 | 0.08562 | 0.088897
 | 19.668 | 9.8344
 | 0.048664 | 0.038304
 | 1.3904 | 2.5636
 | 11.1226 | 10.5762
  31%
  41%
  4%
  0%
  38%
  55%
  0%
  9%
  April 2019 (Pre Covid)
  10%
  26
  0%
  0%
  10%
  April 2020 (Post Covid)
  36
  -28%
  Oil
  Gas
  Hydro
  Solar
  Coal
  Import
Chart: 
 | 30.58 | 25.675
  April 2019 (Pre Covid)
  April 2020 (Post Covid)
Source: BPDB, Deloitte Analysis

## Slide 120: BPDB Liquidity Assessment – Covid 19 | Discom Credit Assessment
Fall in Oil Imports due to lower industrial use and Oil based generation BPDB instruction to stop liquid fired plants
The demand for fuel oil in Bangladesh has dropped from 18,000 tonnes per day to 6,000 tonnes due to the nationwide shutdown since March 26.
- Bangladesh Petroleum Corporation, April 2020
We have presented a few snippets basis primary/secondary available sources on the liquidity impact of coronavirus on BPDB as well as the impact on liquid fired plants
Delay in payments to IPP due to Covid-19 Delay in collection from End-Consumers by Discoms to Impact overall payments to BPDB
However, the private power plants have not been paid since January
- Power Division, May 2020
"A financial shortage was anticipated in the current situation. Knowing that, as our longtime partners, we have urged them to cooperate with us in such a crisis period,“
-Engineer Md Belayet Hossain, BPDB (Chairman), May 2020
"We have a record of hundred percent bill collection. But we have received only 10 percent of the total bills for the month of March,"
- Md Kausar Ameer Ali, managing director of DESCO, May 2020
All diesel-fired power plants, having the total generation capacity of 1,140 megawatts (MW), are now shut along with a good number of furnace oil-fired ones.
BPDB has asked the plant owners to keep majority of the oil-fired power plants shut to save the entity from counting huge payment for electricity purchase.
- BPDB, April 2020
Source: BPDB, Deloitte Analysis

## Slide 121: Bulk Level & Retail Tariff Hike History | Discom Credit Assessment
Following graph shows the historical average bulk supply tariff in Bangladesh (BDT / kWh) Following graph shows the historical average bulk supply tariff in Bangladesh (BDT / kWh)
Bulk Supply Tariff (BST) The Average Bulk Supply Tariff in Bangladesh has only been increased twice between March 2014 and March 2020 The tariffs for Bulk Supply are set for each distribution utility in Bangladesh by BERC and BPDB supplies power at that particular rate The average bulk supply rate for the utilities has been shown on the graph on the right (above) and currently stands at BDT 5.17 / kWh Retail Supply Tariff (RST) The average retail supply tariffs have been hiked at a higher frequency and quantum compared to Bulk Supply tariffs in the last years The cost of supply increase for The increase in tariffs has also led to an improvement in the financial performance of the discoms Considering the increase of imported fuel based power generation (LNG, Coal) as well as Power Import from India, the Bulk Supply Cost of BPDB is expected to increase substantially (refer Slide) This increase in the payment obligations of BPDB may require an increasing trend in tariff hikes at both BST and RST levels in Bangladesh
Historically the annual average tariff hikes in Bangladesh has been kept at ~1.7 to ~2.5%; The increasing reliance of imported fuel based generation in Bangladesh is expected to lead to an increasing trend in the frequency & quantum of tariff hikes
Chart: 
 | 4.67 | 4.77 | 4.77 | 5.17
  Mar-14
  Sep-15
  Dec-17
  Mar-20
  1.7%
  Average Bulk Supply Tariff
Chart: 
 | 6.15 | 6.33 | 6.77 | 7.13
  Mar-20
  Mar-14
  Sep-15
  Dec-17
  2.5%
  Average Retail Supply Tariff
Source: BPDB, Deloitte Analysis

## Slide 122: Assessment of Distribution Utility Profitability | Discom Credit Assessment
Most of the discoms in Bangladesh are profitable due to the Government increasing retail tariffs periodically while bulk supply tariffs were kept same between FY15 to FY19
Following graph shows the historical profitability of some of the discoms in Bangladesh in BDT Bn Following graph shows the historical profitability of some of the discoms in Bangladesh in BDT Mn
Improving Profitability & Net worth Most of the the power distribution utilities in Bangladesh excluding BPDB’s distribution business and WZPDCL have been posting Net Profits in the last 3 years The major reason for the increasing profits is the continued increase in Annual Retail Tariffs by BERC while the Bulk Supply Tariff were not increased between September 2015 till November 2020 Although BPDB’s own distribution business is under net losses, it earned operating profit in FY2018 and FY2019 to the tune of ~BDT 372 Mn and BDT 483 Mn respectively The net worth of the distribution utilities also has been increasing due to improving financial performance with DPDC having the highest net worth among the utilities in comparison The Government of Bangladesh has been injecting regular equity in BPDB’s distribution business to offset its losses However the distribution utilities are not directly subsidized by the Government with their tariff structure revised regularly to ensure profitability by cross-subsidization
Chart: 
 | -1.9223 | -0.1296 | 0.32695 | 0.17581
 | -0.97748 | 0.23352 | 0.70196 | 0.47189
 | -0.72 | 0.75945 | 1.9642 | 1.1026
  BPDB (Distribution)
  WZPDCL
  DPDC
  DESCO
  -0.98
  0.47
  FY2018
  FY2019
  FY2017
Chart: 
 | 38.5118 | 9.627 | 13.8037 | 15.0216
 | 42.9315 | 11.727 | 17.504 | 15.9546
 | 53.3446 | 13.6103 | 74.6722 | 18.406
  DESCO
  BPDB (Distribution)
  WZPDCL
  DPDC
  FY2017
  FY2018
  FY2019
Source: BPDB, WZPDCL, DPDC, DESCO, Deloitte Analysis

## Slide 123
Fuel Supplier Credit Risk Assessment
Historical performance of BPC and SGCL, receivables and payment assessment, current liquidity position for immediate payment obligations
01
02
03
04
05
06
07
08
09
10

## Slide 124: Bangladesh Petroleum Corporation | Supplier Credit Assessment
Following graph shows the Total Revenue from sales and Net Profitability (BDT Bn) of BPC from FY10 to FY11 and FY15 to FY19:
BPC has been earning profits since FY15 due to a downward trend in the global crude market which has helped it to improve its solvency
BPC Profitability Bangladesh Petroleum Corporation is the GoB owned entity responsible overall import, production & supply of petroleum products Apart from import of petroleum products, it operates Eastern Refinery Limited and Chittagong LPG Bottling Plant As can be seen from the graph on the right (above), BPC has been earning profits in the last 4 years. However BPC has been known to earn losses till FY14 From FY15 onwards BPC has been able to earn profits as the Global Crude prices declined from ~$100 / barrel to ~$40-60 / Barrels BPC does not follow a market linked pricing and typically follows a fixed pricing model. It is due to this that in the high crude price era BPC was making losses however in a low crude price regime the company has turned profitable BPC Net Worth & Long Term Liabilities Due to the historical losses, BPC’s current net-worth is negative. However it has been improving since FY15 and has shown ~65% improvement since FY15 On the other hand, the long term liabilities of BPC comprises of Loans / Bonds from the Government which has historically been given to BPC to pay the difference in its fuel import bill and sales to consumers About 99% of the long term liabilities are BPC’s dues to the Government of Bangladesh
Following graph shows the Net Worth of BPC (BDT Bn) from FY10 to FY11 and FY15 to FY19
Chart: 
 | 174.036 | 230.759 | 377.8481 | 337.1987 | 329.9041 | 473.8284 | 453.2148
 | -25.712 | -97.9 | 43.0421 | 77.533 | 45.5102 | 65.3338 | 38.4609
  FY10
  FY18
  FY11
  FY19
  FY16
  FY17
  FY15
  Total Revenue
  Total Profit
Chart: 
 | -222.2051 | -320.2041 | -468.87 | -401.3373 | -367.8272 | -291.9576 | -165.1761
 | 170.91 | 210.91 | 462.749 | 462.7098 | 462.7098 | 462.6578 | 443.534
  FY11
  FY10
  FY18
  FY16
  FY17
  FY19
  FY15
  Networth
  Long Term Liabilities
Source: BPC, Deloitte Analysis

## Slide 125: Bangladesh Petroleum Corporation | Supplier Credit Assessment
Following graph shows the Major Import & Domestic production & Processing Cost of BPC (BDT Bn) from FY16 to FY19: Following graph shows the Revenue Earned from Sale of Goods by BPC (BDT Bn) from FY16 to FY19
BPC’s import costs are benchmarked to international crude prices; However its revenue growth is constrained by the GoB pricing mechanism which has kept the major fuel prices unchanged since 2016
BPC Import & Domestic Production / Processing Cost BPC is majorly dependent on importing petroleum products to meet the country’s liquid fuel demand About ~60-70% of the BPC’s cost of goods comprises of import costs with refined fuel comprising ~75% of the overall imports BPC operates just one refinery (Eastern Refinery Limited) with capacity of refining 1.5 Million Tonnes of Crude annually It has planned to increase the capacity to 3.0 Million Tonnes which will assist in increasing the domestic refining capacity to ~50% of the overall imports in Bangladesh (at FY 19 levels) from current 25%. BPC’s Revenue BPC’s annual revenue from sale of goods has increased at ~9.5% in the last 5 years which is in stark contrast to its cost of goods which increased at 25% BPC’s average selling rate is defined by the Government of Bangladesh which governs BPC’s overall revenue The GoB hasn’t revised prices for HSD, SKO, HOBC, Petrol, Furnace Oil since 2016 and for LPG the prices were last set in 2009 The prices for Bunker Fuel and LDO were revised in 2018 and 2019 respectively Thus the constant pricing of fuels has been the primary reason for the reduced growth in BPC’s cost
Chart: 
 | 61.3159 | 84.0451 | 68.9733 | 101.6095
 | 6.6052 | 12.4066 | 20.9152 | 12.8249
 | 111.1031 | 144.3391 | 233.0067 | 233.765
 | 32.2592 | 41.3235 | 46.0381 | 60.8039
  FY16
  282
  211
  369
  FY18
  FY17
  61
  FY19
  409
  7
  12
  13
  32
  21
  41
  46
  61
  25%
  Imported Furnace Oil
  Imported Domestic Production & Processing Cost
  Imported Refined Oil
  Imported Crude Oil
Chart: 
 | 333.6364 | 327.5866 | 462.8014 | 437.7966
  FY17
  FY16
  FY18
  FY19
  9.5%
  BPC’s Revenue from Sale of Goods
Source: BPC, Deloitte Analysis

## Slide 126: Bangladesh Petroleum Corporation | Supplier Credit Assessment
Following graph shows the & Accounts Receivable of BPC (BDT Bn) and average Debtor Days from FY16 to FY19: Following graph shows the & Accounts Payable of BPC (BDT Bn) and average Creditor Days from FY16 to FY19:
There is a mismatch in BPC’s receivable & payable’s frequency; However given the strategic importance of importing Petroleum products, BPC trading payables are expected to be supported by GoB for any payment shortfall to international oil companies
Receivables Assessment BPC receives its revenue from its subsidiaries namely Eastern Refinery Limited, Padma Oil Company, Jamuna Oil Company, Meghna Oil Company, LP Gas Limited, Eastern Lubricants Ltd. The receivables at the end of FY19 were ~60% of BPC’s annual revenue In terms of receivable frequency, BPC receives its trading receivable roughly evert ~200-230 days signifying cash risk for the company Payables Assessment BPC’s payables mainly comprises of payments to international crude suppliers and other natural gas companies in Bangladesh The accounts payable from trading activities has been quite consistent in the last 4 years as these would majorly be accountable for imports However the overall accounts payable has reached BDT ~230 Bn which indicates that BPC may be delaying payments for domestic operations Considering the strategic importance of importing petroleum products & enforcement principles of international oil contracts, the payables for BPC’s Trading activities are expected to be within payment timeline (as per contract) and supported by Government of Bangladesh
Chart: 
| FY16 | FY17 | FY18 | FY19
Accounts Receivable (Trading) | 204.0627 | 257.5179 | 304.707 | 251.2385
Accounts Receivable (Others) | 1.45 | 1.45 | 1.4 | 1.4
Debtor Days (Overall) | 200.2311 | 258.7612 | 222.8308 | 232.9222
Chart: 
| FY16 | FY17 | FY18 | FY19
Accounts Payable (Trading) | 33.6309 | 34.1974 | 46.3024 | 45.6771
Accounts Payable (Others) | 184.1111 | 244.8443 | 315.0577 | 230.8931
Creditor Days (Overall) | 352.267 | 321.5034 | 316.6078 | 284.4856
Source: BPC, Deloitte Analysis

## Slide 127: Bangladesh Petroleum Corporation | Supplier Credit Assessment
  1.2
Following graph shows the Current Assets and Current Liabilities (BDT Bn) of BPC from FY16 to FY19: Following graph shows the Annual Cash & Bank Balance (BDT Bn) of BPC FY16 to FY19:
The overall liquidity position has improved for BPC with the short term liquidity position sufficient to meet any immediate payment obligations
Overall liquidity Position The overall liquidity position of BPC has improved backed by profits from trading and delaying its payables to creditors The current ratio has increased to 1.2 to 1.8 in the last 5 years BPC’s Cash & Bank Balance has also shown a remarkable growth from BDT 58 Bn to BDT 263 Bn in just 4 years Thus, BPC’s short term liquidity position should be sufficient to meet any immediate payments to its creditors
Chart: 
 | 290.7509 | 411.7859 | 565.4089 | 567.1977
 | 241.476 | 329.003 | 409.5181 | 323.1207
 | 1.2041 | 1.2516 | 1.3807 | 1.7554
  FY17
  FY16
  FY18
  FY19
  Current Assets
  Current Liabilities
  Current Ratio
Chart: 
 | 58.2371 | 123.3689 | 207.0713 | 263.1023
  FY16
  FY17
  FY18
  FY19
  Cash & Bank Balance
Source: BPC, Deloitte Analysis

## Slide 128: SGCL Performance
Following graph shows the Total Revenue from sales and Net Profitability (BDT Mn) of SGCL in the last two years
SGCL being a distribution company has been earning profits since the last 5 years with ~99% of its revenue coming from supply of gas to power sector
SGCL Historical Performance & Supply Profile As a gas distribution company, SGCL has been profitable company with its revenue & net profitability rising at ~83% CAGR in the last 5 years The revenue has increased primarily due to increased gas sales in its geographic area About ~99% of SGCL’s revenue comes from supply of natural gas to power sector As SGCL mainly sources the gas from Bhola Gas Field, its distribution is limited to the consumers in the Bhola Island However SGCL provides gas to NWPGCL’s Bheramara Power Plant (410 MW) which is already connected to the national gas grid SGCL is the supplier of NWPGCL’s plant as it falls under its supply area
Following graph shows the YoY Gas purchase of SGCL and its consumer consumption breakup (mmscmd) from FY15 to FY19
Chart: 
 | 314.4 | 875.5 | 1100.9 | 2668.5 | 3521.7
 | 35.9 | 60.8 | 38.9 | 216.6 | 399
  FY15
  FY16
  FY19
  FY17
  FY18
  Total Revenue
  Total Profit After Tax
Chart: 
 | 0.24907 | 0.80696 | 0.95203 | 2.0999 | 2.6621
  FY16
  FY15
  FY17
  FY18
  FY19
  Gas Purchase
Chart: 
 | 0.0198 | 0.041581
 | 2.0856 | 2.643
  98.5%
  FY18
  FY19
  2.1
  2.7
  99.1%
  Power
  Others
83%
83%
CAGR
Consumer Category | Number of Consumers / Details
Power | Aggrego 95 MW Bhola 34.5 PP Rental Plant Bhola I 225 MW NWPGCL Bheramara 410 MW1
Domestic | 2286
Commercial | 3
Industrial | 4
Captive Power | 2
Source: SGCL, Deloitte Analysis; Note 1) The NWPGCL Bheramara 410 MW is not located in Bhola Island and hence not supplied natural gas via Bhola Fields. It falls under SGCL’s command area and is supplied natural gas via the National Gas Grid

## Slide 129: SGCL Performance
Following graph shows the Total Sales from gas and annual collections (BDT Mn) of SGCL in the last two years
SGCL’s Billing-Collection efficiency has improved in FY19 to 1.2 months of average receivables; The profitability has also allowed SGCL to lower its debt equity ratio signifying improvement in overall solvency
SGCL Billing & Collection Efficiency SGCL’s collection efficiency has ranged from ~76% to ~120% in the last 5 years According to its annual reports, its overall receivables has decreased from an average ~2-4 months between FY15 to FY18 to ~1.2 month in FY19 indicating improved liquidity position On the other hand, SGCL’s creditor payable days has increased from ~5 months in FY18 to ~6.5 months in FY19 The major creditors of SGCL are BAPEX and BGFCL (both GoB owned companies) Debt Equity & Current Liquidity Ratio SGCL’s profitability has helped it to reduce its long term loans from Government of Bangladesh & Petrobangla The Debt Equity Ratio has reduced from a high of ~6 in FY16 to ~4 in FY19 The management of SGCL has also indicated that the Debt Equity Ratio is expected to further reduce in the coming years as it intends to pay its long term loans to improve solvency In terms of liquidity, the Current Ratio of SGCL has improved from ~1.5 in FY16 to ~1.9 in FY 19
Following graph shows the debt equity ratio and current ratio of SGCL from FY16 to FY19
Chart: 
 | 262.9 | 844.5 | 1042.7 | 2470.1 | 3179.5
 | 198.9 | 854.1 | 757.4 | 2379.1 | 3796.8
  FY15
  FY17
  FY16
  FY19
  FY18
  Total Sales (Gas)
  Total Collections
3.5
2
2.6
4
1.2
Receivable (Months)
Chart: 
| FY16 | FY17 | FY18 | FY19
Debt Equity Ratio | 5.9784 | 5.7843 | 4.2727 | 4.0633
Current Ratio | 1.51 | 1.28 | 1.4 | 1.86
Payable (Months)
5
6.5
Source: SGCL, Deloitte Analysis

## Slide 130: Financial Performance of Petrobangla
During FY16 to FY18, Petrobangla made a net loss of BDT 18-19 Bn annually; However the financial position of Petrobangla is supported by Energy Security & Gas Development Funds as well as direct subsidy from the GoB in its reserves
Profitability During FY16 to FY18, Petrobangla earned loss at operating and net levels Its operating and net losses have been consistently in the range of range of BDT~18 – 20 Bn annually As per the BERC’s natural gas price tariff orders, there is cross subsidy at consumer segment and also at an aggregate level with the same being at ~22% in the tariff order set in FY2019 The subsidy at the aggregate level is one of the major reasons for the net losses of Petrobangla Net Worth Despite the losses, Petrobangla has a positive networth at BDT 191 Bn. The net worth is supported by the Gas Development and Energy Security Funds setup by the Government where consumers pay a part of the tariff for supporting exploration activities in Bangladesh This fund is collected by the distribution companies from the consumers and transferred to BAPEX for exploration activities In addition the subsidy provided by the Government seem to be appropriated at the Revenue Reserve level A part of the fund is also being used for renewable energy by the Government as part of Energy Security initiatives
Source: Petrobangla, Industry Reports, Deloitte Analysis
Following graph shows the historical profitability of Petrobangla (BDT Bn) Following graph shows the historical net-worth of Petrobangla (BDT Bn)
Chart: 
 | -20.089 | -20.093 | -20.312
 | -17.8831 | -18.7426 | -18.2569
  FY2016
  FY2018
  FY2017
  Operating Profit / (Loss)
  Net Profit / (Loss)
Chart: 
 | 34.5114 | 50.2687 | 117.7851
 | 51.3171 | 18.9929 | 54.6028
 | 17.6371 | 18.3869 | 18.9995
 | 0.0015 | 0.0015 | 0.0015
  FY2017
  103
  FY2016
  FY2018
  88
  191
  18
  19
  18
  19
  Gas Development & Energy Security Funds
  Paid Up Capital
  Capital Reserve
  Revenue Reserve

## Slide 131
Assessment of Foreign Participation in Power Sector
Investment overview by private players, major portfolio of foreign equity investors, lenders and multilaterals in power projects, identification of opportunities for Actis
01
02
03
04
05
06
07
08
09
10

## Slide 132: Foreign Equity Participation in Power Sector | Investments in Power Plants
The following figure highlights the major historical power sector investments with regards to foreign equity investment in genration projects over the years:
360 MW Haripur Power (AES) (USA)
110 MW NEPC Consortium
50 MW DPA Power Gen (Aggratech AG) (Germany)
52 MW Lakdhanvi (Lakdhanvi) (Sri Lanka)
341 MW Summit (GE) (USA)
300 MW APR Energy (APR Energy) (USA)
52 MW Raj Lanka (Lakdhanvi) (Sri Lanka)
149 MW Ace Alliance (Initially won by Atkin Alliance (Sri Lanka); bought by Summit)
2000
2002
2011
2015
2016
2019
The Bangladesh power sector has been witnessing an increasing trend of foreign participation in the generation segment led by private IPPs and equity investment firms
Source: BPDB, Industry Reports, Deloitte Analysis
450 MW Meghnaghat (AES) (USA)
2003
450 MW Meghnaghat (AES sells to CDC Globeleq) (UK)
2005
360 MW Haripur Power (AES sells to CDC Globeleq) (UK)
2007
360 MW Haripur Power (CDC Globeleq sells to Pendekar) (Malaysia)
450 MW Meghnaghat (CDC Globeleq sells to Pendekar) (Malaysia)
110 MW NEPC Consortium (bought by CDC Globeleq) (UK)
110 MW NEPC Consortium (CDC Globeleq sells to Pendekar) (Malaysia)

## Slide 133: Foreign Debt Participation in Power Sector | Investments in Power Plants
The following figure highlights the major historical power sector investments with regards to foreign debt investment in generation projects over the years
KPCL 110 MW Commissioned (IFC)
360 MW Haripur Power (IDA)
100 MW Dutch Bangla Power (Mashreq Bank)
100 MW IEL Consortium (Mashreq Bank)
115 MW KPCL Unit 2(DEG & FMO)
40 MW Khanjahan Ali (Standard Chartered)
53 MW United Ashuganj (Standard Chartered)
108 MW Regent Power (IFC)
52 MW Raj Lanka (Lakdhanvi, NDBIB)
52 MW Lakdhanvi
341 MW Summit (ADB, IFC, IsDB)
195 MW UAEL (Standard Chartered Bank, WB IPFF, DEG, IFC)
Dhaka Northern & Southern Power (WB IPFF)
105 MW Orion Rupsha (Mercantile & Mashreq Bank)
282 MW Sembcorp (Clifford, IFC, CDC )
300 MW Kodda (Clifford, Sumitomo)
149 MW Ace Alliance (OFID)
1999
2002
2011
2012
2015
2016
2019
The foreign investments have also witnessed debt participation by Bilateral / Multilateral Donor Organizations, Investment & Commercial Banking Institutions
Source: BPDB, Industry Reports, Deloitte Analysis
450 MW Meghnaghat (ADB)

## Slide 134: Foreign Participation in Power Sector | Upcoming Investments
The following figure highlights the major planned / upcoming power sector investments with regards to foreign debt & equity investment based in generation projects
Siddhirganj 335 MW CCPP ST (World Bank)
Manikganj 162 MW (Changzou Hutang Coal Power) (China)
Feni 114 MW (Lakdhanvi (Sri Lanka); DFCC Bank & HNB Bank)
Payra Pataukhali 1320 MW Phase 1 (CMC (China); CEXIM Bank)
Thakurgaon 100 MW (EMA Power Investment (UAE), Daelim Energy (South Korea);MLAs)
Bhola 220 MW (Shapoorji Pallonji (India); AIIB & IsDB)
Ashuganj 400 MW CCPP (IDB, ADB, KfW & OPEC)
LNG based 750 MW CCPP (Reliance Power(India), JERA (Japan);ADB & IDB)
Chattogram 2 X 612 MW (SEPCO-3 & HTG (China);CEXIM Bank)
Meghanghat 600 MW CCPP (Summit) (GE (USA); IFC)
Barishal 307 MW (PowerChina (China))
Meghanghat 600 MW CCPP (Unique) (GE (USA))
Meghanghat 500 MW (Anlima) CCPP (GE (USA))
Payra Pataukhali 1320 MW Phase 2 (CMC (China); CEXIM Bank)
2020
2021
2022
2023
2024
2027
Identified as upcoming in supply outlook
Planned Projects (may be delayed beyond FY26)
The upcoming generation project pipeline also showcases strong foreign equity & debt participation
Source: BPDB, Industry Reports, Deloitte Analysis
Note: A few international players such as Sojits, Mitsubishi, Petronet LNG etc. have invested / planned investments in the Bangladesh economy (LNG Terminals, Ports, Renewable Energy Industrial Zones among others) which may directly / indirectly support the energy sector

## Slide 135: Foreign Participation in Power Sector | Investment Overview
Asset portfolio for FY19 The installed capacity for FY 19 was 18,961 MW, out of which the private sector comprised of 8,043 MW Company wise portfolio is as provided in the Appendix As mentioned earlier, Bangladesh has witnessed significant foreign investment in the power sector A large part of the foreign investment has been geared towards the private player power plants with ~4,000 MW of capacity receiving foreign equity & loan support The Multilateral agencies have also provided investment support to the public and private players in the power sector with ~2,500 MW witnessing investment from Multilateral agencies (equity / loan) Apart from the private players, the foreign and multilateral agencies have also invested in public sector plants with ~1,200 MW and ~2,800 MW of public portfolio receiving investment from them respectively The BPDB plants are generally funded via loans from Multilateral agencies and Government of Bangladesh only Thus considering the foreign investment concentration towards privately owned power projects, Actis can look for potential opportunities in this segment
With over ~2,000 MW of Private Player backed power projects in Bangladesh receiving foreign investment, there may be a potential for Actis to evaluate prospective opportunity for investment
Following figure shows the distribution of installed capacity (MW) for FY19
Chart: 
 | 5498 | 5498 | 9758 | 16261 | 17801 | 18961
 | 4260 | 6503 | 1540 | 1160
  1,160
  BPDB
  Public
  Total
  IPP / SIPPs
  Rentals
  Import
Total Private - ~8,000 MW
Chart: 
 | 1997 | 2057 | 2525
  Foreign Equity Investment
  Multilateral Investment
  Foreign Loan
  Private Plants (MW)
Source: BPDB, Industry Reports Deloitte Analysis; Note: 1) The data for foreign equity, loan and multilateral investments do not indicate mutually exclusive investments

## Slide 136: Foreign Participation in Power Sector | IPP Portfolio
Foreign investment in Privately Owned Plants In terms of foreign investment, major foreign players & multilateral agencies have preferred Gas based power plants for investment in Bangladesh These investments have been in line with global preference for cleaner fuels for investments In terms of equity investment by foreign players, ~1500 MW of gas based capacity have witnessed investment in the form of foreign equity and ~2,000 MW have had multilateral investments While plants operating on HFO also managed to acquire foreign funding from all three avenues, they were majorly funded via foreign loan mode The table on the right (below), highlights the major players who have invested in the IPP space as foreign equity and loans as well as Multilateral players with significant exposure in Bangladesh The gas based portfolio has attracted players such as Pendekar Energy, Sembcorp and GE and multilateral agencies such as IFC and ADB HSD operated plants secured equity investment from APR Energy and Aggratech AG and loans from Eastern Bank ltd and Saudi-Bangladesh Industrial and Agricultural Investment Company.
Gas based plants have witnessed majority investment by foreign players with Pendekar Energy being the largest foreign players and ADB / IFC being the largest multilateral players
Following figure shows the distribution of foreign investment (MW) according to operating fuel of plant for commissioned plants
Following table constitutes the list of major foreign players and multilateral funders for operational plants
 | Foreign Equity | Foreign Loan | Multilateral
 | Pendekar Energy (920 MW) | DEG (310 MW) | ADB (1,096 MW)
 | GE (341 MW) | Sumitomo Mitsui (300 MW) | IFC (1,036 MW)
 | APR Energy (300 MW) | Standard Chartered (288 MW) | IsDB (341 MW)
 | Sembcorp Utilities (282 MW) | Clifford Capital (282 MW) | IDA (360 MW)
 | Lakdhanvi Group (104 MW) | SMO (Netherland) (115 MW) | ICD, OFID (149 MW)
1
2
3
4
5
Chart: 
 | 1432.991 | 889.991 | 2040.991
 | 350 | 100 | 0
 | 214 | 1066.972 | 484
  1,997
  Foreign Equity
  2,057
  2,525
  Foreign Loan
  Multilateral
  100
  Gas
  HFO
  HSD
Source: BPDB, Industry Reports Deloitte Analysis; Note: 1) The data for foreign equity, loan and multilateral investments do not indicate mutually exclusive investments

## Slide 137: Foreign Participation in Power Sector | Asset Identification (Commissioned)
Potential investment area for Actis (Commissioned Plants) ~3,400 MW of privately owned gas power plants are currently operational in Bangladesh In terms of the overall ~3,400 MW of gas based capacity, ~2,000 MW of capacity have been commissioned over 7 years ago These power plants would be of older technology and may not provide a suitable opportunity for new investments Thus, ~1,400 MW of capacity remains in the system which have been commissioned in the last 7 years and may provide for a suitable investment opportunity The table on the right (below) lists out the projects which have been commissioned in the last 7 years in Bangladesh (privately owned gas based power plants) All the plants are IPP / SIPP owned and are not rental in nature Actis may evaluate these plants in terms of potential investment opportunity
Following chart indicates the capacity & age of gas based plants of private players in Bangladesh in FY19 Following table indicates the list of projects for potential investment (commissioned in the last 7 years)
Plant Name | Capacity (MW) | COD | PLF FY19 | Efficiency | Owner
Summit Bibiyana II | 341 | 2015 | 76% | 28.88% | Summit
Kushiara Power | 163 | 2017 | 76% | 35.70% | Max
Sembcorp NWPC | 282 | 2018 | 31% | 42.71% | Sembcorp
United Ashuganj | 195 | 2015 | 24% | 42.51% | United
Summit Meghnaghat | 305 | 2015 | 24% | 43.09% | Summit
Regent Power | 108 | 2014 | 37% | 37.26% | Regent
Chart: 
 | 3407.4 | 1906.4 | 1393.9 | 1393.9
 | 1501 | 512.5
  Gas Based PP Portfolio of Private Players
  Age X<7
  Age >= 10 Years
  Age 7>=X<10
Source: BPDB, Industry Reports Deloitte Analysis; Note: 1) Summit 305 MW has been running at duel fuel with HFO due to gas shortage in FY16 and FY17. With increasing gas availability, it is expected to ramp up dispatch Note 2) Sembcorp 282 MW was commissioned in October 2018 and is expected to ramp up dispatch from FY20 onwards
~1,400 MW of gas based plants have been commissioned by the private players in the last 7 years which may provide a potential investment opportunity given their age and technology

## Slide 138: Foreign Participation in Power Sector | Planned Investments in Power Sector
Foreign investment according to fuel (Upcoming) As projected in our supply scenario, ~17,000 MW of capacity expansion has been planned in Bangladesh till FY26 out of which ~5,500 MW has been planned by private players Of these, ~4,000 MW of capacity has been planned with foreign equity investment and ~2,300 MW of capacity also receiving foreign loan support In terms of fuel wise investment, LNG is the preferred choice for Multilateral investments with ~1,300 MW having some form of multilateral investment The major players in terms of foreign investors for private power plants are HTG Group & SEPCO 3 which have planned investments in Imported Coal Based power, followed by GE which is investing in LNG based power plants Although the private players have planned significant capacity expansions, the disbursements / financial closure of many of these plants are yet to be completed and hence their commissioning may be delayed as projected in our supply scenario
The foreign players have planned equity investments in ~4,000 MW privately owned power plants with LNG and Imported coal based power plants having highest investments
Following figure shows the distribution of foreign investment for upcoming Private Player owned Plants in Bangladesh (MW) Following constitutes the list of major foreign players and multilateral funders for upcoming privately owned plants
 | Foreign Equity | Foreign Loan | MLA
 | HTG Group & SEPCO -3 (1,224 MW) | CEXIM Bank (1,244 MW) | ADB & IDB (718 MW)
 | GE (1,167 MW) | DFCC & HNB (114 MW) | IFC (583 MW)
 | Reliance Power & JERA (718 MW) |  | 
 | PowerChina (307 MW) |  | 
 | Changzhou Hutang Coal Power Co. Ltd.(China) (162 MW) |  | 
1
2
3
4
5
Chart: 
 | 220 | 220 | 1301
 | 1885 | 718 | 0
 | 1531 | 1224 | 115
 | 391 | 229 | 0
  Foreign Equity
  4,027
  229
  Foreign Loan
  Multilateral
  220
  2,391
  220
  1,416
  115
  Gas
  HFO
  LNG
  Imported Coal
Source: BPDB, Industry Reports Deloitte Analysis; Note: 1) The data for foreign equity, loan and multilateral investments do not indicate mutually exclusive investments

## Slide 139: Foreign Participation in Power Sector | Asset Identification (Upcoming)
Potential investment opportunity for Upcoming Plants Although, ~3,000 MW of Gas based capacity addition has been planned in Bangladesh, only ~220 MW of the capacity is expected to be commissioned by private players The sole planned 220 MW of gas based capacity addition by private players is the Nimbus plant In terms of LNG based power plant capacity addition, we expect ~1,200 MW of privately owned plants to be commissioned by FY26 These plants are owned by Summit, United Group, with 2 more LNG plants being planned by Anlima Textile / GE and the Unique Groups
Following chart shows the distribution of upcoming gas based capacity, with identification of private capacity as potential investment play
Plant Name | Capacity (MW) | COD (Estimated) | Owner Group
Meghnaghat 600 MW CCPP – Summit | 584 | 2024 | Summit Group
Meghnaghat 600 MW CCPP – UMPL | 583 | 2024 | United Group
Meghnaghat 500 MW - Anlima Textile & GE | 450 | 2027-2030 | Anlima & GE
Meghnaghat UECL | 450 | 2027-2030 | Unique Energy
Following table indicates the list of upcoming projects for potential investment opportunity in Bangladesh
Chart: 
 | 3035 | 1167
  Planned LNG Installed Capacity till FY2026 (MW)
  Probable Serviceable Capacity till FY26 (MW)
Following graph shows the planned LNG Installed Capacity as per BPDB and our estimated commissionable capacity (MW) by FY2026
Chart: 
 | 2870 | 220 | 220
 | 2650
  Capacity Planned by Private Plants
  Probable Serviceable Capacity Addition for Gas Based Plants till FY26
  Capacity Planned by BPDB / Public Entities
~1,200 MW of LNG based plants are expected to be commissioned by the private players which may provide potential investment opportunity
Source: BPDB, Industry Reports Deloitte Analysis

## Slide 140
Contracts Risk Assessment
Analyze the key terms & provisions of the PPA, GSA, FSA, O&M, IA and identify risks and their mitigation measures
01
02
03
04
05
06
07
08
09
10

## Slide 141: Power Purchase Agreement | Salient Features
Entire Capacity of 220 MW capacity is contracted with BPDB for 22 years
Salient features: Term: 22 years, extendable upon mutual agreement Dispatch: Based on merit order; No minimum offtake guarantee Sale to third parties: Not allowed Fuel: The preferred fuel of operation is gas. In case of gas unavailability, BPDB can decide to switch from gas to fuel or to cease operations Commissioning: The plant is required to be commissioned within 28 months after execution of project agreements Delivery Point: High voltage side of the 230 kV step up transformer in its switchyard Normative Availability: 90% for first 10 years, 85% thereafter. Force Majeure/ Political Event: Either parties can claim relief from obligations. Proportionate payment will be made in case facility is partly operational Event of default: Default due to other counterparties will not constitute event of default Termination: Expiry or Event of Default Dispute Resolution: Through expert or Arbitration; Governed by laws of England and Wales Performance Security: By NBBL – Proposal Security, Performance Security, Operations Security Deposit By BPDB – Letter of Credit from BPDB and Guaranteed by Government of Bangladesh
Key Risks
According to the terms of the Power Purchase Agreement, the facility should have been commissioned by 28th December 2019 (i.e. 28 months from execution of project agreements). However, presently, the facility is still under construction and the expected COD is June 2020.
Vide letter dated 22nd August 2019 to BPDB, NBBL had requested for an extension of the Required COD on account of delay in construction of gas transmission facility and in obtaining two Government Authorizations, both of which are grounds for extension in commissioning timelines as per the project agreements.
In case the timeline extension is not authorized by BPDB, NBBL will have to pay liquidated damages (@USD 100 per day per MW of delay beyond 28 months from execution of agreements). Moreover, delay of more than 12 months will constitute a Company (NBBL) Event of Default and thereby allow termination of the PPA
Considering high cost of fuel in Bangladesh, there is a possibility that the plant will not find a place in the merit order and will thus not be scheduled if it has to be scheduled using HSD
Source: PPA, Deloitte Analysis

## Slide 142: Power Purchase Agreement | Salient Features
Separate Reference tariff quoted for gas and fuel based operations
Salient features: Tariff is based on reference capacity charge and energy charge rates quoted as part of bid separately for gas and fuel based operations. Capacity charges payable on dependable capacity; Energy charge payable on net energy output Fuel charges will be based on price paid for gas/ fuel. All taxes and transportation costs paid for gas/ fuel are pass through Penalty/ incentive for availability: Proportionate recovery based on availability Transmission Charges: Not included in tariff since delivery is at plant periphery BPDB will continue to pay Capacity charges in case of failure to delivery gas due to failure of transmission facility BPDB will pay capacity charge if station is not scheduled Reference station heat rate is quoted in the bid based on plant load factor Cost of any restoration/ additions on account of a Political Event can be recovered through a revision in Reference Fixed and Variable Charge Rates Payment Security by BPDB: Aggregate of two months of capacity payment and variable O&M adjusted for inflation assuming 85% of contracted/dependable capacity
Key Risks
Recovery of Operations and Maintenance Costs are based on Net Energy Output. Any reduction in the power scheduled from the plant by BPDB may lead to under-recovery of O&M costs.
Recovery of capacity charges is based on dependable capacity. Therefore, any increase in dependable capacity beyond the threshold level will lead to a greater capacity charge recovery to NBBL. However, the corresponding incentive is not incorporated in the Operation and Maintenance Agreement signed with the O&M Contractor.
Tariff
Fixed
Variable
Tariff Structure
Non Escalable
Foreign Escalable
Foreign Variable O&M
Local Variable O&M
Local Escalable
Fuel Cost
Source: PPA, Deloitte Analysis

## Slide 143: Power Purchase Agreement | Salient Features
Reference Tariff Schedule – Gas Operations
Contract Year | Non Escalable Capacity Price (USD/kW-Month) | Foreign Escalable Capacity Price (USD/kW-Month) | Local Escalable Capacity Price (Taka/kW-Month) | Foreign Variable O&M Price (USD/kWh) | Local Variable O&M Price (Taka/kWh)
1 | 11.920 | 1.4839 | 33.0000 | 0.0003 | 0.0032
2 | 11.920 | 1.4839 | 33.0000 | 0.0003 | 0.0032
3 | 11.920 | 1.4839 | 33.0000 | 0.0003 | 0.0032
4 | 11.920 | 1.4839 | 33.0000 | 0.0003 | 0.0032
5 | 11.920 | 1.4839 | 33.0000 | 0.0003 | 0.0032
6 | 11.920 | 1.4839 | 33.0000 | 0.0003 | 0.0032
7 | 11.920 | 1.4839 | 33.0000 | 0.0003 | 0.0032
8 | 11.920 | 1.4839 | 33.0000 | 0.0003 | 0.0032
9 | 11.920 | 1.4839 | 33.0000 | 0.0003 | 0.0032
10 | 11.920 | 1.4839 | 33.0000 | 0.0003 | 0.0032
11 | 7.7020 | 1.4839 | 33.0000 | 0.0003 | 0.0032
12 | 7.7020 | 1.4839 | 33.0000 | 0.0003 | 0.0032
13 | 7.7020 | 1.4839 | 33.0000 | 0.0003 | 0.0032
14 | 7.7020 | 1.4839 | 33.0000 | 0.0003 | 0.0032
15 | 7.7020 | 1.4839 | 33.0000 | 0.0003 | 0.0032
16 | 7.7020 | 1.4839 | 33.0000 | 0.0003 | 0.0032
17 | 7.7020 | 1.4839 | 33.0000 | 0.0003 | 0.0032
18 | 7.7020 | 1.4839 | 33.0000 | 0.0003 | 0.0032
19 | 7.7020 | 1.4839 | 33.0000 | 0.0003 | 0.0032
20 | 7.7020 | 1.4839 | 33.0000 | 0.0003 | 0.0032
21 | 7.7020 | 1.4839 | 33.0000 | 0.0003 | 0.0032
22 | 7.7020 | 1.4839 | 33.0000 | 0.0003 | 0.0032
Source: PPA, Deloitte Analysis

## Slide 144: Power Purchase Agreement | Salient Features
Reference Tariff Schedule – Fuel Operations
Contract Year | Non Escalable Capacity Price (USD/kW-Month) | Foreign Escalable Capacity Price (USD/kW-Month) | Local Escalable Capacity Price (Taka/kW-Month) | Foreign Variable O&M Price (USD/kWh) | Local Variable O&M Price (Taka/kWh)
1 | 13.2200 | 2.1568 | 39.9440 | 0.0003 | 0.0034
2 | 13.2200 | 2.1568 | 39.9440 | 0.0003 | 0.0034
3 | 13.2200 | 2.1568 | 39.9440 | 0.0003 | 0.0034
4 | 13.2200 | 2.1568 | 39.9440 | 0.0003 | 0.0034
5 | 13.2200 | 2.1568 | 39.9440 | 0.0003 | 0.0034
6 | 13.2200 | 2.1568 | 39.9440 | 0.0003 | 0.0034
7 | 13.2200 | 2.1568 | 39.9440 | 0.0003 | 0.0034
8 | 13.2200 | 2.1568 | 39.9440 | 0.0003 | 0.0034
9 | 13.2200 | 2.1568 | 39.9440 | 0.0003 | 0.0034
10 | 13.2200 | 2.1568 | 39.9440 | 0.0003 | 0.0034
11 | 10.6700 | 2.1568 | 39.9440 | 0.0003 | 0.0034
12 | 10.6700 | 2.1568 | 39.9440 | 0.0003 | 0.0034
13 | 10.6700 | 2.1568 | 39.9440 | 0.0003 | 0.0034
14 | 10.6700 | 2.1568 | 39.9440 | 0.0003 | 0.0034
15 | 10.6700 | 2.1568 | 39.9440 | 0.0003 | 0.0034
16 | 10.6700 | 2.1568 | 39.9440 | 0.0003 | 0.0034
17 | 10.6700 | 2.1568 | 39.9440 | 0.0003 | 0.0034
18 | 10.6700 | 2.1568 | 39.9440 | 0.0003 | 0.0034
19 | 10.6700 | 2.1568 | 39.9440 | 0.0003 | 0.0034
20 | 10.6700 | 2.1568 | 39.9440 | 0.0003 | 0.0034
21 | 10.6700 | 2.1568 | 39.9440 | 0.0003 | 0.0034
22 | 10.6700 | 2.1568 | 39.9440 | 0.0003 | 0.0034
Source: PPA, Deloitte Analysis

## Slide 145: Power Purchase Agreement | Key Terms
Tariff
Sr. No | Parameter | Conditions | Key risks
Comment on the key variables in tariff – fixed and escalable components of capacity and energy charges for gas and diesel |  |  | 
1 | Tariff | Tariff = Capacity Payment + Energy Payment (in BDT, payable on monthly basis) Capacity Payment and Energy Payment are payable based on Dependable Capacity (MW) and Net Energy Output (KWh) respectively for the month Capacity Payment = Non-Escalable Capacity Payment + Escalable Capacity Payment Non-Escalable Capacity Payment = Reference Non-Escalable Capacity Price (USD/KW, as per Sch. 6 of PPA) x USD to BDT Exchange Rate x Wtd. Avg. Dependable Capacity for the month (MW) Escalable Capacity Payment = Foreign Escalable Capacity Payment + Local Escalable Capacity Payment Foreign Escalable Capacity Payment = Reference Foreign Escalable Capacity Price (USD/KW, as per Sch. 6 of PPA) x USD to BDT Exchange Rate x Foreign Inflation Indexation Factor x Wtd. Avg. Dependable Capacity for the month (MW) Local Escalable Capacity Payment = Reference Local Escalable Capacity Price (BDT/KW, as per Sch. 6 of PPA) x Local Inflation Indexation Factor x Wtd. Avg. Dependable Capacity for the month (MW) Energy Payment = Variable O&M Payment + Fuel Payment Variable O&M Payment = Foreign Variable O&M Payment + Local Variable O&M Payment Foreign Variable O&M Payment = Reference Foreign Variable O&M Price (USD/KWh, as per Sch. 6 of PPA) x USD to BDT Exchange Rate x Foreign Inflation Indexation Factor x Net Energy Output for the month (KWh) x min (0.85 / avg. PF for the month, 1) Local Variable O&M Payment = Reference Local Variable O&M Price (BDT/KWh, as per Sch. 6 of PPA) x Local Inflation Indexation Factor x Net Energy Output for the month (KWh) x min (0.85 / avg. PF for the month, 1) | Recovery of capacity charge is based on dependable capacity which provides an incentive to achieve a higher dependable capacity. However, there is no such incentive in the O&M contract The Reference Heat Rate is not adjusted for the life of plant (yearly degradation)
Source: PPA, Deloitte Analysis

## Slide 146: Power Purchase Agreement | Key Terms
Tariff
Sr. No | Parameter | Conditions | Key risks
 | Tariff | Fuel Payment for operation on Fuel Oil = Quantity (kg) x Price (BDT/kg) for the leftover Fuel Oil at the end of the previous month + Sum of {Quantity of Fuel Oil (kg) received in each consignment during the month x Fuel Oil Price (BDT/kg) for the consignment} – Quantity (kg) x Price (BDT/kg) for the leftover Fuel Oil at the end of this month, Where, Quantity (kg) of the leftover Fuel Oil at the end of any month = (Total Heat of Fuel Oil received during the month and left over in previous month based on the actual Fuel Oil Heat Value – Heat consumed from Fuel Oil based on Reference Heat Rate as per Sch. 6 of PPA) / Wtd. Avg. Actual Fuel Oil Heat Value Fuel Oil Price allowed to be recovered through Energy Payment = Price paid to the fuel supplier + Duties, taxes, fees, surcharges, etc. paid to Govt. authority + Freight, ocean loss, insurance, bank charges, letter of credit charges, lighterage, handling commission, port dues, survey fee, storage and handling charges, etc. incurred at actuals Fuel Payment for operation on Gas = Gas price (BDT/MSCF) as defined in GSA / (0.95 x 1.055) x Heat consumed from Gas based on Reference Heat Rate as per Sch. 6 of PPA (Where, there is no adjustment for the actual Btu content of the Gas above or below the assumed 950 Btu of HHV per SCF of Gas) | 
2 | Energy payment during commissioning | Payable by BPDB for the Net Energy Output delivered to the Delivery Point during testing and commissioning | 
3 | Start-up Payment | Payable by BPDB for each start-up of a Gas Turbine following the dispatch instruction in excess of 40 free start-ups for each Gas Turbine for a Contract year. Such start-ups will exclude start-ups following Forced Outage, Maintenance Outage, Scheduled Outage or Force Majeure Event declared by the Company. Consists of a fixed component (for maintenance) and fuel component (for Gas or Fuel Oil) SC (main) = 5,000*CE*FIIF; SC (Gas) = 500*GP/(0.95*1.055) | Since energy payment is based of Reference Heat Rate it would most likely be that the fuel consumed during the startup would be partially recoverable through tariff. Thus for 40 free startups Company may have revenue loss
Source: PPA, Deloitte Analysis

## Slide 147: Power Purchase Agreement | Key Terms
Delivery Point
Sr. No | Parameter | Conditions | Key risks
3 | Supplemental Tariff Payment | Supplemental Tariff for Political Events other than Change in Law In case the Political Event results in damage / adverse effects on the facility, which is repaired / remedied by the Company. Difference between the restoration costs approved in accordance with Sec. 11B.3 of the Implementation Agreement and any insurance proceeds. Supplemental Tariff for Change in Law : In case the Change in Law requires material modification or capital addition by the Company (as per Sec. 11B of the Implementation Agreement), or any increase in operating costs as approved by GOB in the manner provided by the Imp. Agreement To be calculated in the same manner and basis as the Capacity Payment and Energy Payment, and will be payable on monthly basis | The applicability of this is only if the cost is more than USD 450K No Supplemental Tariff recovery would be there in case of any damage due to an FM event
5 | True-up for Exchange Rate | In case of variation of the Exchange Rate from the Indexation Date (used for invoicing) and the payment date, the differential amount of foreign components of Tariff due to such changes in Exchange Rate will be paid by BPDB / refunded by the Company, as the case may be on the 5th Business Day after receiving such Payments from the Company | 
Delivery Point for the offtake of power and the applicable transmission and wheeling charges, rebates, incentives and penalties |  |  | 
1 | Point of Delivery - Power | Point of delivery will be high voltage side of the 230 kV step-up transformer. The Company will construct a 230 kV switchyard at its own cost There are no Transmission and Wheeling Charges, Rebates, incentives or penalties in the tariff (The point of delivery is at the plant periphery and therefore, no there is no transmission charge component in tariff) | No risk of evacuation envisaged. The Tx capacity has a max. loading of 545 MW Buffer Capacity on Transmission line: 225 MW which should be sufficient to evacuate 220 MW from Nimbus
Source: PPA, Deloitte Analysis

## Slide 148: Power Purchase Agreement | Key Terms
Pass Through Costs
Sr. No | Parameter | Conditions |  | Key risks
Ability to pass through costs (fuel costs, fuel quality, major maintenance, O&M, taxes etc.) to BPDB |  |  |  | 
1 | Fuel Costs | Fuel Costs are pass through: Gas – Gas price (BDT/MSCF) as prescribed by the regulatory commission including all transportation charges and taxes payable Fuel Oil – Price paid to the fuel supplier, Duties, taxes, fees, surcharges, etc. paid to Govt. authority, Freight, ocean loss, insurance, bank charges, letter of credit charges, lighterage, handling commission, port dues, survey fee, storage and handling charges, etc. incurred at actuals |  | 
2 | Fuel Quality | Fuel Oil – the actual Heat Value of Fuel Oil are considered for Energy Payment Gas – a HHV of 950 Btu/SCF is considered for Gas. There is no adjustment for the actual Btu content of the Gas as per PPA. However, GSA provides a provision for the revision of the HHV. Thus there is no risk due to fuel quality. |  | 
3 | Major Maintenance | Costs of major maintenance are built-in in the Tariff. However, the hours of schedule outages and maintenance outages are taken into consideration for the purpose of scheduling and dispatch Also for LD computation, there are allowable thresholds for the outage hours, up to which LD will not be applicable (876/1376 hours for gas and 1190/1580 hours for Fuel oil for Major maintenance/standard maintenance) | There is no provision for separately allowing such costs. Thus in case the plant is on 0 PLF then all the maintenance cost would be recovered | 
4 | O&M | O&M expenses are allowed in the Tariff under the Variable O&M Payment that is payable based on the Reference Rates and the Net Energy Output | O&M costs are not pass through and are paid based on a reference rate quoted in the PPA. On the other hand, O&M contracts specifies a flat rate of O&M cost plus escalation. Thus in case the plant is not dispatched it could lead to under recovery of the O&M costs | 
Source: PPA, Deloitte Analysis

## Slide 149: Power Purchase Agreement | Key Terms
Additional Tariff
Sr. No | Parameter | Conditions | Key risks
5 | Taxes | Custom Duties and VAT paid under protest but should have been exempted and which are not refunded by the Customs Authority within 270 days after Company files refund claims will be passed through. There are few tax-exemptions to the Company as per Sec. 13.1(e)(ii) to 13.1(e)(xv) of the PPA Other than the exemptions as per the PPA and IA, the Company will have to pay all taxes, contributions, rates, charges and fees payable to any Govt. authority, arising in connection to construction, ownership, operation or maintenance of the facility. These are built-in in the Tariff and there is no separate provision for pass-through of these items. | Taxes are not a pass through except for taxes on fuel/gas Rest exemptions as mentioned still hold true
6 | Insurance | In case due to Political Event the cost of insurance increases then the additional cost of insurance due to such Political Event shall be treated as a Pass Through Item | 
7 | Protective Devices for EIF | In case PGCB requires the Company to modify or expand the requirements for protective devices after Project Effective date then PGCB shall reimburse the Company for these costs as per the IA | 
Source: PPA, Deloitte Analysis

## Slide 150: Power Purchase Agreement | Key Terms
Additional Tariff
Sr. No | Parameter | Conditions | Key risks
Comment on PPA terms (if any) regarding additional tariff (over and above the existing PPA tariff) |  |  | 
1 | Use of alternate fuels | The preferred fuel for operation will be Gas. In case of a Gas Supplier Force Majeure Event or a Political Event, the Company should promptly inform BPDB and the Other Fuel Notice Parties of such an Event. Within 5 days of receipt of notice, BPDB shall decide to: a) Switch from Gas to Other Fuel b) Cease operations and specify whether the Company should use any remaining fuel oil at the facility In case of such an event, the Company will first procure fuel oil for 15 days supply for continuous operation of the facility at 80% dependable capacity (three days supply in case the event occurs before COD) Once the Force Majeure Event/ Political event has passed, the Gas Supplier will serve a Cessation Notice following which the Company shall cancel any outstanding fuel orders within 2 days of receipt of such notice. The canceled outstanding Fuel Oil will be required to be supplied by the Fuel Supplier to BPDB who shall indemnify the Company for loss due to such diverted fuel oil. Any excess store of fuel oil of more than 3 days requirement will be utilized to generation till the stock reduces to 3 days worth of requirement. | Switch from Gas to other fuel only covers FM and PE events Right to switch to alternate fuel is provided only to BPDB, NVVN cannot do it suo-moto In case Gas is not supplied and NVVN raises it as an PE event and BPDB does not give permission to switch even then Capacity Payments would continue to happen, which reduces any financial risk on the project
2 | Change in law | There is a provision for Supplemental Tariff for Change in Law, in case the Change in Law requires material modification or capital addition by the Company (as per Sec. 11B of the Imp. Agreement), or any increase in operating costs as approved by GOB in the manner provided by the IA The Supplemental tariff is to be calculated in the same manner and basis as the Capacity Payment and Energy Payment, and will be payable on monthly basis | 
Source: PPA, Deloitte Analysis

## Slide 151: Power Purchase Agreement | Key Terms
Rebates/Incentives
Sr. No | Parameter | Conditions | Key risks
3 | Late payment fee | There is no provision for late payment fee or surcharge However, in case of non payment of invoices beyond 10 days following the due date (30 days after invoice submission) the Company can suspend delivery of power however BPDB would still need to continue to pay Full Capacity charges | The PPA does not have any provision for late payment fee whereas the GSA/FSA/O&M agreements have the same. This could lead to working capital issues. However, the PPA allows right to suspend in case of payment delays
4 | Force majeure (FM) and Political Events (PE) situations | There is no provision for any additional tariff In case of partial operation during FM event, BPDB will pay the Company Energy Payment for Net Energy Output and Capacity Payments based on the ratio of dependable capacity (FM Ratio/PE ratio). In case declared by the Company and partial working is possible then ration of Declared Capacity after FM/Declared Capacity before FM FM/PE Ratio shall be 0 in case no working possible and declared by the company FM/PE Ratio shall be 1 in case declared by BPDB, or event of Gas/Fuel Supplier Failure Notification to be given within 3 days of FM event | No restoration cost can be recovered in the case of an FM event Also in case FM/PE Event is declared by the Company then the FM/PE Ratio would be dependent on the dependable capacity or 0 in case of non working condition. This would have an impact on the payment of Capacity charges. Also since Grid system failure is part of FM event any such failures could lead to under recovery depending on the applicable FM Ratio
5 | Back-down instructions from system operators | Capacity Charges would be continued to be paid by BPDB | 
Source: PPA, Deloitte Analysis

## Slide 152: Power Purchase Agreement | Key Terms
Termination Clauses
Sr. No |  | Parameter | Conditions | Key risks
Termination clauses in PPA |  |  |  | 
1 |  | Termination Clause | Termination of the PPA is only possible in case of Company Event of Default or BPDB Event of Default The remuneration for the different cases is as mentioned in the IA. | There is not provision of mutual termination or any exit clause in the PPA. The PPA shall be terminated on event of default or expired Payment in case of Company Event of Default is only for any outstanding loans, debts and winding up costs. No compensation for equity investments would be provided
Comment on the applicable rebates/incentives to be applied to tariff |  |  |  | 
1 |  | Applicable rebates / incentives | There are no applicable rebates/incentives in the PPA | 
Options of non-offtake or expiry of PPA |  |  |  | 
1 |  | Non Offtake | In case of non-offtake, only Capacity Charges will be payable. Sale to third party will not be possible without prior written consent of BPDB | This is risk however since open Access Provisions do not exist in Bangladesh the relevance of this is limited.
2 |  | Expiry of PPA | There is no provision for PPA extension except for Sec 4.1(a), where it states that PPA term will be 22 years following the COD, unless extended or earlier terminated. PPA is silent about the alternative options post termination of PPA | No clear provision for extension mentioned in the PPA
Source: PPA, Deloitte Analysis

## Slide 153: Power Purchase Agreement | Key Terms
Offtake Guarantee
Sr. No | Parameter | Conditions | Key risks
Performance guarantee, offtake guarantee |  |  | 
1 | Offtake guarantee | No provision for offtake guarantee in the PPA There is no minimum offtake guarantee. Similarly, there is no minimum offtake guarantee (take or pay) in FSA/GSA. However, schedule has to be consistent with Technical Limits | No offtake guarantee is a risk however since capacity payments are guaranteed this could be acceptable.
2 | Performance guarantee | Proposal Security (In form of BG): Amount = USD 2,200,000 To secure the obligations of the Project Sponsor to maintain its proposal until execution of the Project Agreements. Performance Security Deposit (In form of BG): Amount = USD 36,000 x Contracted Facility Capacity. As a security for Company’s obligations including obligation to deliver the Operations Security Deposit, pay LD, and achieved Financial Closing by no later than Required Financial Closing Date. Operations Security Deposit (In form of BG): Amount = Two months of Capacity Payments. For payment of LD, other damages, interest or other amounts payable to BPDB. | 
Source: PPA, Deloitte Analysis

## Slide 154: Power Purchase Agreement | Liquidated Damages (1/2)
Comparison of Operational Norms
Sr. No | Parameter | Conditions | Key risks
3 | Liquidated Damages | Delay in Commercial Operation - LD = USD 100 x Contracted Capacity x no of days (beyond 28 months from Project Effective Date i.e. Required COD); subject to a cap of 365 days of damages Failure to meet Contracted Capacity - If the Initial Dependable Capacity < Contracted Capacity, LD = USD 1000 x KW difference in capacity; subject to a cap of 10% of Contracted Capacity | Delay in Commercial Operations: If the project effective date is date of execution of this agreement i.e. August 2017, then Required COD occurred in December 2019 (28 months from effective date). Therefore, there is a delay in commissioning which will attract LD (NBBL has requested for extension of COD upto 30th June 2020 vide its letter dated 22nd August 2019 for delay on account of delay in obtaining Government Authorizations and delay in construction of gas transportation facilities). Contract provisions allow for such day to day extension Max LD applicable is ~USD 8 Mn EPC contract has a back to back clause in which case for every day of delay in CoD due to the EPC contractor a penalty of 0.025% per day with a cap of 10% of the total Contract Value shall be charged Max LD applicable is ~ USD 22 Mn Thus for any delay due to EPC contractor is covered back to back Failure to Meet Contracted Capacity: Max LD applicable is ~ 22 Mn EPC has a back to back clause with a 15% cap to contract value. This comes to ~ 33Mn. So not a risk. EPC contract has an overall LD limit of 20% of Contract Value which is sufficient to cover both the above LD amounts
Source: PPA, Deloitte Analysis

## Slide 155: Power Purchase Agreement | Liquidated Damages (2/2)
Comparison of Operational Norms
Sr. No | Parameter | Conditions | Key risks
3 | Liquidated Damages | Forced Outages – If Equivalent Forced Outage Energy (a) + Maintenance Outage Energy (b)+ Scheduled Outages Energy (c)> Average Dependable Capacity x 1376 hours for gas operation (or 1580 hours for Fuel Oil Operation) in every third contract year or 876 hours for gas operation (or 1190 hours for Fuel Oil Operation) in every other contract year (d) , LD = Capacity Factor (i.e. Average Capacity Price x 1.522) x (a + b + c - d) For first contract year an adjustment of 0.75 has been provided Declaration and Delivery of Available Capacity If the company notifies a Revised Declared Capacity which does not result due to Force Majeure Event or BPDB/PGCB/Gas Supplier/Fuel Supplier/GOB, LD is applied in case of downward revisions in Declared Capacity as follows: 12 hours before start of Day – 5%*Difference in Capacity* Capacity Price After beginning of the Day and upto 3 hours prior to the beginning of the relevant hour – 15%* Difference* Capacity Price If the Company fails to comply with the dispatch instruction which is not due to Force Majeure Event or BPDB/PGCB/Gas Supplier/Fuel, LD = 100% x difference between declared capacity and available capacity x Applicable Relevant Capacity Price | Forced Outage: O&M has a back to back LD clause with a Cap of 10% of Base Fee. There is no such cap mentioned in the PPA Declaration and Delivery of Available Capacity For 12 hours before start of day: O&M has a back to back LD clause with a Cap of 10% of Base Fee. There is no such cap mentioned in the PPA After beginning of day: No back to back clause in the O&M agreement Failure for dispatch: No back to back clause
Source: PPA, Deloitte Analysis

## Slide 156: Power Purchase Agreement | Key Terms
Comparison of Operational Norms
Sr. No | Parameter | Conditions | Key risks
Comparison of operational norms of PPA & EPC Contract |  |  | 
1 | Operating Norms | Operating Norms mentioned in PPA Norms for Start-ups, Facility Loading, and Frequency, PF and Voltage limits Expected Maintenance Intervals Reference Heat Rates (Gas operation) Reference Heat Rates (Fuel Oil operation) Operating Norms mentioned in EPC Contract Net plant output (MW) and Heat Rate for combined-cycle operation on gas and fuel oil Emission, noise and effluent discharge guarantees | For Gas Operation, the reference heat rate is higher in the PPA only for 100% plant factor For Fuel Operation, the reference heat rate is the same for 100% Plant factor, but is lower for PPA reference rate at all other plant factors
Reference Heat Rate as per PPA (Gas Operation) |  | Heat Rate Guarantee as per EPC Contract (Gas Operation) | 
Plant Factor (% of Dependable Capacity) | Ref. Heat Rate (KJ/KWh | % Load (% of Plant Capacity) | Guarantee Heat Rate (KJ/KWh)
100% | 7845 | 100% (221 MW) | 7590
80% | 7858 | 80% (176 MW) | 7861
60% | 8384 | 60% (132 MW) | 8521
40% | 8140 | 40% (88 MW) | 8194
Reference Heat Rate as per PPA (Fuel Oil Operation) |  | Heat Rate Guarantee as per EPC Contract (Fuel Oil Operation) | 
Plant Factor (% of Dependable Capacity) | Ref. Heat Rate (KJ/KWh | % Load (% of Plant Capacity) | Guarantee Heat Rate (KJ/KWh)
100% | 7067 | 100% (212 MW) | 7067
80% | 7356 | 80% (169.6 MW) | 7390
60% | 7956 | 60% (127.2 MW) | 8024
40% | 7462 | 40% (84.8 MW) | 7599
Source: PPA, Deloitte Analysis

## Slide 157: Power Purchase Agreement | Benchmarking SHR with other Gas plants
Following graph shows the gas-plant wise Efficiency (kcal / kWh) & their respective PLF (%) in FY19 (Gas Operations)
Chart: 
| 2247.7783585990592 | 2421.8529991551673 | 2247.7783585990592 | 2247.7783585990592 | 2977.8393351800555 | 2399.5535714285716 | 2408.9635854341736 | 1995.8226966813645 | 2013.5799578553033
 | 87.7598 | 52.5183 | 82.7744 | 76.6276 | 79.1853 | 60.1388 | 78.5404 | 26.8342 | 34.3049
 | 31.5232 | 30.721 | 39.9767 | 58.3703 | 94.254 | 6.4065 | 50.7362 | 63.7162 | 77.4895 | 79.4575 | 27.0422 | 27.6755 | 56.9034 | 85.2985 | 64.5905 | 59.7845 | 18.5616 | 27.9538 | 77.9812 | 53.0987 | 42.1631
 | 18.1103 | 70.6021 | 36.5993 | 56.5649 | 78.7574 | 40.4883 | 66.4613 | 65.9333 | 69.1955 | 45.6508 | 79.1763 | 67.9163 | 73.8421 | 67.907 | 26.8087 | 40.0717 | 19.5909 | 52.7986 | 86.5401
 | 53.2892 | 57.7585 | 66.8783 | 67.0858 | 87.0507 | 71.0277 | 80
  Efficiency – SHR (kcal /kWh)
  PLF (%)
The Nimbus plant’s design SHR is lower than most gas based power plants in Bangladesh; Actual SHR to be dependent on the dispatch levels achieved
Source: BPDB, Deloitte Analysis Note: 1) The graphs above contain only plants operational in FY19 as per BPDB Annual Report 2) Size of the Bubbles on the graph depict the Installed Capacity of the Plant 2) For Nimbus, the SHR has been considered at 80% PLF with design SHR of ~1,878 kcal / kWH
  BPDB
  IPP
  Rental
  Public
  Nimbus

## Slide 158: Power Purchase Agreement | Other risks
Comparison of Operational Norms
Sr. No | Parameter | Conditions | Key risks
2 | Pre-operational Period | Both BPDB and the Company shall try to obtain all permits/licenses/approvals to enable it to performs its obligations The Company shall provide the following documents to BPDB - EPC Contract, permits and licenses, O&M Agreement, Testing procedures and protocols, Start up and test schedules, Insurance documents, Test Results, Plans and drawings and Quality Control Programs The Company will obtain power for construction either by itself or from a relevant electrical utility in Bangladesh as facilitated by BPDB Operating Procedures - The company has to provide BPDB with draft operating procedures at least 180 days before the Scheduled COD, dealing with all operational interfaces between BPDB and the Company Within 90 days BPDB shall notify the company of any changes or amendments. The company shall provide revised draft operating procedures at least 45 days prior to the Scheduled COD Disagreement over the revised draft procedures shall be referred for resolution to the Joint Coordinating Committee within 7 days after submission of draft operating procedures. Either party may, from time to time, request revisions to the Operating procedures on mutual consent Upto COD, the Company shall submit progress reports to BPDB and the Engineer every month. After the financial closing date the Company shall also provide a monthly notice the Scheduled COD and any change therein Upto COD, the Company shall submit quarterly progress reports to BPDB on progress of Gas Transportation Facilities | The Timelines mentioned in operating procedures don’t add up to ensure that the decision is made 30 days prior to the COD
Source: PPA, Deloitte Analysis

## Slide 159: Gas Supply Agreement | Salient Features
NBBL has a 22 year arrangement with Sundarban Gas Company Limited for supply of gas
Salient features: Term: 22 years, extendable upon mutual agreement before 15 years Procurement from third parties: not allowed unless gas is unavailable at by gas supplier Transmission Facility: Pipeline constructed and operated by SGCL; Cost borne by NBBL. Failure of transmission facility will attract liquidated damages to be paid by Gas Supplier Quantity: Subject to Maximum Hourly Quantity (1,604 MSCF); doesn’t exceed Daily Contract Quantity (35,000 + 10% MSCF) assuming an HHV of 950 Btu/ SCF Point of Delivery: Outlet flange of RMS at the boundary of the site Price: As per Published Gas Price by GOB adjusted for Higher Heating Value; inclusive of taxes and transportation charges Force Majeure/ Political Event: Either parties can claim relief from obligations. Gas suppliers failure to deliver gas other than due to transportation issue constitutes a Political Event. BPDB will decide whether to switch from gas to fuel or to cease operations Minimum Supply Guarantee: 50% of Hourly Contract Quantity (1458 +/-0% MSCF) for 7884 hours reduced by Gas ordered not delivered or non confirming gas Interruption due to transmission facility failure Gas not delivered or accepted due to force majeure/political event Major Scheduled Outage Termination: Event of default; Force Majeure/Political Event not remedied within 12 months
Key Risks
A Gas supplier Event of Default is only in case when the supply is less than 50% of the total aggregate gas demand for the entire year
SGCL does not give any performance guarantee
The term of the GSA is valid only subject to availability of gas
Source: GSA, Deloitte Analysis

## Slide 160: Gas Supply Agreement| Key Terms
Sr. No | Parameter | Conditions | Key risks
1 | Term | Agreement commences from the Project Effective Date i.e. when all project agreements have been executed till the expiry of the PPA Before 15 years, the parties may mutually decide to extend the term of the agreement. Else it shall expire at the end of the Contract period. | The term is subject to availability of gas; which is a risk as in case if gas in not available the term of the agreement would not hold
2 | Pricing | Price - as per the Published Gas Price. In case Published Gas Price is not available, parties may mutually decide on an alternate index within 15 days of discontinuance to the Published Gas Price, otherwise the matter will be referred to an Expert Price Adjustment - Invoice amount will be adjusted to accommodate the deviations from 950 Btu per cubic foot The price will be paid including all delivery, transportation charges and taxes payable Amount paid during any month will be equal to the prevailing gas price multiplied by the number of MSCF of gas delivered | In case the quality is less than 900 Btu the gas would not be acceptable, however as mentioned in the PPA Capacity charges would be paid in case of Gas supply Failure. So this is not a risk.
3 | Billing and Payment | The Supplier shall raise invoices monthly, on or after 7 days after end of month with a due date of 32 days for the Company to make the payment. No dispute can be raised by the Company for a meter inaccuracy of less than 2% Late Payment - Interest payable at Bangladesh Bank Rate plus 2% per annum Payment Dispute: Invoices should be disputed within 180 days and after dispute resolution through an Expert or arbitration, the disputed amount shall be paid within 3 business days The supplier may suspend delivery if the undisputed amount remains unpaid for 3 days unless the company provides a Letter of Credit for an amount equal to 1.5 times the invoice amount with a validity of 60 days. The supplier may suspend delivery and encash LC if amount remains unpaid for 45 days after invoice date | There is no performance guarantee from the supplier Late payment fee applicable which is not there in case of the PPA
Key risks in GSA
Source: GSA, Deloitte Analysis

## Slide 161: Gas Supply Agreement| Key Terms
Sr. No` | Parameter | Conditions | Key risks
4 | Liquidated Damages | Payable by Gas Supplier: For outage and interruptions in transportation facilities beyond the permitted maintenance (876/1376 hours) 1. Applicable in case failure of supplier to deliver gas due to transportation facilities failure other than due to Force Majeure or a Political Event, LD = Capacity Charges + any liquidated damages payable by the Company under the PPA Payable by the Company: 1. If A. Scheduled outages + B. maintenance outages + C. forced outages + D. Delay lost energy > Threshold level (876 hours or 1376 hours for major maintenance years) LD = Avg Gas Price * Hourly Supply Quantity *0.05*((A+B+C+D) -TL)) In case aggregate supply is more is greater than Annual Threshold Quantity then no LD shall be paid. Also LD is capped at (Annual Threshold Quantity- Actual Delivered)*Gas price Annual Threshold Capacity: 50% of the hourly contract quantity (1458 MSCF of gas/hour) x 7884 hours | 
5 | FM/PE Events | In case of FM/PE event BPDB can provide an option for switching to liquid fuel or cessation of plant. In case of later BPDB shall continue to pay Capacity charges. | 
Key risks in GSA
Source: GSA, Deloitte Analysis

## Slide 162: Gas Supply Agreement| Key Terms
Sr. No` | Parameter | Conditions | Key risks
6 | Gas Supplier event of default | Company shall give a notice of default in case of following events except when such default is caused due to breach of any of the project agreements by the Company or due to Force Majeure or a Political Event: Assignment of Agreement by the supplier in contravention with the provisions of assignment under the agreement Dissolution of the supplier except for privatization or amalgamation/restructuring/reorganization/corporatization provided a reasonable guarantee to the performance of the succeeding entity and all supplier's obligations have been assigned to the new entity Any event of default by GOB, Fuel Supplier or BPDB under their respective agreements Failure of the supplier to commission the transport facility within 30 days after the Required COD Any material breach by BPDB that is not remedied in 30 days after notice from the Company Failure of the Gas Supplier to deliver an aggregate amount of Gas greater than 50% of the aggregate amount of gas shown in the gas order in any 12 month period Incorrect statements, representations, warranties Change in Law making execution unlawful/unenforceable | Only supply below 50% is Gas Supplier Event of Default
Key risks in GSA
Source: GSA, Deloitte Analysis

## Slide 163: Fuel Supply Agreement | Salient Features
NBBL has a 22 year arrangement with Bangladesh Petroleum Corporation for supply of fuel as a back up fuel
Salient features: Term: 22 years, extendable upon mutual agreement Point of Delivery: Discharge flange of loading jetty at Barisal/ Jhalakati Depot Price: As per price of reference fuel by GOB; inclusive of refinery price, inland freight margin, gross margin, other statutory charges Transmission: NBBL responsible for all transportation beyond Receiving Point; Transportation cost recovered from BPDB Quantity: Amount of fuel oil equal to 15 days supply for continuous operation of the facility at 80% at the prevailing Dependable Capacity Minimum Supply Guarantee: 50% of fuel ordered in any 12 month period Termination: Event of default; Force Majeure/Political Event not remedied within 12 months
Key Risks
Payment for fuel oil needs to be made 3 days before receipt of oil. On the contrary, payment against power supplied to BPDB is made on a monthly basis will a lag of 30 days. Incongruence in payment terms would mean larger working capital lock in.
NBBL is responsible for transportation of fuel oil from the Receiving Point, unloading at jetty and storage of oil thereafter. Any disruption in the water transportation facility will cause delay in receipt of oil.
Oil Field
NBBL Site Unloading Facility
BPC (Jamuna/Meghna) Depot Tank Terminal
Through Ocean Going Vessel
Fuel Supply Logistics
Source: FSA, Fuel Transportation Agreement, Deloitte Analysis

## Slide 164: Fuel Supply Agreement| Key Terms
Sr. No | Parameter | Conditions | Key risks
1 | Obligation | The company agrees to purchase & the supplier agrees to supply fuel to meet the requirement The facility shall operate on Gas and to the extent gas is not available, it shall operate on fuel oil The supplier shall deliver fuel at the Receiving Point Failure to supply fuel shall not constitute a breach if damages are paid to the Company under the FSA and the PPA (paid by company) | 
2 | Transportation Facility | The receiving point for the fuel transported by water vessel shall be the discharge flange of loading jetty located at Barisal/Jhalakati Depot of the fuel supplier The fuel supplier shall be responsible for all facilities upstream of the Receiving Point and for transportation and delivery of fuel oil to the Receiving Point The Company shall be responsible for all facilities downstream of the Receiving Point and for transportation and delivery of fuel oil from the Receiving Point to the facility The company will install and maintain the Company receipt and storage facilities for storing and utilizing the fuel oil The fuel supplier will ensure that it has all equipments and facilities ready for first delivery of fuel at the Initial Delivery Date (i.e. 18 months or more from the Project Effective Date). The Initial Delivery Date may be delayed on account of Force Majeure or a Political Event but shall not be later than 120 days before the Scheduled COD as per the PPA | Downstream transportation already completed. Jetty at plant site ready and transportation agreement through barges signed with Kingfisher Limited
3 | Quantity | On receipt of Fuel Supplier Switch Order in case of Gas Supplier Force Majeure/Political Event/ Supply Failure, the supplier will have upto 90 days to commence deliveries of Fuel Oil and an additional 15 days to deliver fuel oil in an amount equal to the applicable fuel oil storage quantity Failure to complete delivery within the stipulated time will attract liquidated damages The Company may amend its fuel order 15 days prior to start of the relevant month Any upwards adjustments less than 15 days prior to the relevant month upto 10% will be complied with by the fuel supplier. Fuel supplier shall use reasonable efforts to supply fuel in excess of 10% where required. At any time, the Company shall maintain atleast 3 days fuel oil storage quantity except in cases of Force Majeure, Political Event, or default by GOB/BPDB/PGCB/Gas supplier or fuel supplier | The upward adjustment of fuel is limited to 10% if the adjustment is made with 15 days or less. The same limit is not applicable in case of revision of schedule by BPDB
Key risks in FSA
Source: FSA, Deloitte Analysis

## Slide 165: Fuel Supply Agreement| Key Terms
Sr. No | Parameter | Conditions | Key risks
4 | Pricing | Price will be based on Reference Fuel establish by GOB which may include fixed selling price, Gross Margin, refinery price, inland freight margin, statutory development surcharge and duties, and any change therein | 
5 | Billing and Payment | The supplier shall submit an invoice atleast 10 days prior to delivery at Receiving Point based on liter quantity. The Company is required to make payment against the invoice no later than 3 days prior to delivery Any dispute regarding the quantity of fuel oil delivered will be resolved as per the methodology for dispute resolution | Payment for fuel is to be made before delivery while corresponding recovery through sale of power is made 30 days after invoicing power sold
6 | Fuel Supplier Event of Default | Company shall give a notice of default in case of following events except when such default is caused due to breach of any of the project agreements by the Company or due to Force Majeure or a Political Event: Assignment of Agreement by the supplier in contravention with the provisions of assignment under the agreement Dissolution of the supplier except for privatization or amalgamation/restructuring/reorganization/corporatization provided a reasonable guarantee to the performance of the succeeding entity and all supplier's obligations have been assigned to the new entity Any event of default by GOB, Gas Supplier or BPDB under their respective agreements Any material breach by BPDB that is not remedied in 30 days after notice from the Company Failure of the Fuel Supplier to deliver an aggregate amount of Fuel greater than 50% of the aggregate amount of gas shown in the gas order in any 12 month period Incorrect statements, representations, warranties Change in Law making execution unlawful/unenforceable | In case of shortfall in delivery of fuel, there is no penalty if the aggregate supply in a year is greater than 50%.
Key risks in FSA
Source: FSA, Deloitte Analysis

## Slide 166: Fuel Storage| Key Provisions
Sufficiency of Fuel Storage Arrangement At 100% PLF, at the minimum density of FO permissible, the storage capacity of Fuel Oil Tank is sufficient for 15 days storage. At lower PLFs & higher densities, the number of equivalent operational days of FO stored increases, thus the FO storage capacity is sufficient. Following chart shows the key terms utilized for calculation of storage capacity
Fuel Storage Requirements and Transportation Arrangements
Transport & Storage Arrangement: HSD is to be transported via tankers/barges from Barishal/Jhalokathi Fuel Oil Depot to Bhola, Borhannudin NBBL Plant Site and an Agreement is in place between Kingfisher Shipping Lines and NBBL At Plant Site, Fuel shall be unloaded at Fuel Oil Jetty and transferred to Fuel Oil Tank via unloading pumps. There are 2 unloading pumps with capacity of 70 m3/hour each Fuel Oil Tank storage capacity comprises 3 X 5400 cum Key Provisions of Fuel Transportation Agreement: Term of Agreement: 5 years from execution Carrier to ensure min 3 Tanker Barges of 300 – 500 MT in operational condition & deputed full time for maintaining stock of Facility After loading at BPC Terminal, each Tanker Barge will reach Facility within 6 hours from leaving BPC Terminal. Max. Unloading time for Discharge of Cargo is 72 hours (after settling time) from the arrival of tanker barge at Facility. Penalty for delay shall be charged at rate of BDT 15,000 per day Total quantity of initial HSD order is 30,20,000 L (~ 3 days FO operation) & Rate of HSD transportation is BDT 0.48/L (incl AIT) Liquidated Damages: If Carrier fails to depute their Tanker Barge to BPC Terminal as per date intimated in 15 days advance notice for cargo delivery, Carrier shall reimburse amount equal to penalty by BPDB as per PPA If Cargo contaminated beyond 0.05% in 3 consecutive shipments, the total cost of cargo (found contaminated beyond 0.05% (incl Fuel carrying cost, taxes/duties, any other cost) will be deducted from Carrier invoice
Term | Unit | Legend | Value | Source
Plant Capacity | MW | Z | 212 | PPA
Plant Energy output (100% PLF) | kWh | Y | 50,88,000 | Z*24*1000
FO Density | Kg/L | A | (0.82-0.87) | FSA
Calorific Value | kJ/Kg | B | 43011.52 | FSA
Heat Rate (100% PLF) | kJ/kWh | C1 | 7067 | PPA
Fuel Requirement per day (100% PLF) | L | D1 | 9,60,900 – 10,19,491 | (Y*C1)/(B*A)
FO Tank Size | L | E | 54,00,000 | P&ID
FO Tank number | # | F | 3 | P&ID
Storage capacity | Days | G | 15-16 | (E*F)/(D1)

## Slide 167: Operations and Maintenance Agreement | Salient Features
5 year operation and maintenance agreement signed with Chennai based Operations Energy Group, a sister concern of Shapoorji Pallonji
Salient features: Term: 5 years, extendable upon mutual agreement Fees: Monthly fee of Tk 11.50 Mn escalated by 5% annually plus any reimbursable expenses Obligations: Maintenance of facility, maintain dependable capacity to achieve dependable capacity as per PPA Subcontracting: Allowed Liquidated Damages: For exceeding Forced + Scheduled + Maintenance outages – LD as per PPA subject to 10% of base fee Downward revision of declared capacity – LD as per PPA subject to 10% of base fee Facility Heat Rate > Guaranteed Test Heat Rate – LD is payment made for excess fuel subject to 20% of base fee Maximum Limit of liability – 30% of base fee Force Majeure/ Political Event: Either parties can claim relief from obligations Termination: Event of default not cured for 45 days, Force Majeure for 6 months or more, mutual consent and Nationalization of the power plant Governing Law: Laws of Bangladesh
Key Risks
The obligation of the O&M contractor towards liquidated damages as prescribed in the contract are capped which may not cover the liability incurred by the owner of the power plant.
The O&M contactor’s performance obligation as per the contract is restricted to maintaining the dependable capacity as per the PPA which specifies a threshold level of dependable capacity. However, the tariff structure under the PPA is such that every increase in dependable capacity beyond the threshold level results in additional recovery of capacity charges. This serves as an incentive for the power plant operator to always maximize his dependable capacity. A corresponding incentive mechanism is absent from the O&M contract resulting in limited merit for the O&M contractor to maximize dependable capacity of the plant beyond the threshold level.
Source: O&M Agreement, Deloitte Analysis

## Slide 168: O&M Agreement | Key Terms
Sr. No | Parameter | Conditions | Key risks
Study the minimum performance guarantees and penalty mechanisms to meet performance standards |  |  | 
1 | Minimum performance guarantee | No such Minimum performance guarantee has been provided for in the O&M Agreement other than the Guaranteed output that will be determined from the Guarantee Tests performed by the EPC Contractors | 
2 | Penalty Mechanisms | If the prescribed Forced Outage + Maintenance Outage + Scheduled Outage MWh is exceeded beyond a threshold limit; LD is capped at 10% of the Base Fee In the event of downward revision of the Declared Capacity prior to the beginning of the relevant day; LD is capped at 10% of the Base Fee In case the Facility Heat Rate exceeds the Guarantee Test Heat Rate; LD is capped at 20% of the Base Fee Total LD is capped at 30% of the Base Fee | Liquidated Damages are capped
3 | Base Fees | Base Fees Period 1 - Only reimbursement of expenses incurred as actual costs approved as per the budget plan Period 2 - Monthly fee of Tk 11.50 Mn escalated by 5% annually plus VAT thereon | No incentive payments for higher dependable capacity
4 | Billing and Payment | The Operator will raise in invoice within 5 days of every month Payments by the Owner should be made within 30 days Late Payment - If an invoice remains unpaid for 60 days, interest @ 5% needs to be paid | No late payment surcharge available as per the PPA. This is not back to back with the PPA
Minimum performance guarantees and other risks
Source: O&M Agreement, Deloitte Analysis

## Slide 169: O&M Agreement | Benchmarking O&M Cost for Nimbus (Gas Operation)
O&M Cost Comparison with Power Plants in Bangladesh (Gas Operation)
  1.2
  0.8
  1.1
  0.9
  1.0
  0.4
  0.3
  0.0
  1.3
  0.1
  0.5
  0.2
  0.6
  0.7
  0.01
  0.02
  0.03
  0.08
  0.08
  0.09
  0.43
  0.11
  0.12
  0.14
  0.16
  0.17
  0.05
  0.19
  0.23
  0.30
  0.31
  0.35
  0.42
  0.21
  0.45
  0.50
  0.77
  1.26
  0.07
  0.18
NBBL’s Reference Rate Tariff for Variable O&M under Gas based operations is lower than most of the actual O&M cost of the BPDB plants and in line with O&M costs for Private Plants
Source: Industry Reports, Deloitte Analysis; Note 1) For Nimbus, the Reference O&M costs has been considered as per PPA and have been converted to local BDT / kWh at 1 USD = 85 BDT 2) Each bar represents one power plant in the above graph
  Nimbus (Tk / kWh)
  BPDB / Public (Tk / kWh)
  Private (Tk / kWh)

## Slide 170: O&M Agreement | Benchmarking O&M Cost for Nimbus (HSD Operation)
O&M Cost Comparison with Power Plants in Bangladesh (HSD Operation)
  5.5
  1.0
  4.5
  2.5
  1.5
  6.0
  2.0
  3.0
  3.5
  4.0
  5.0
  6.5
  0.5
  0.0
  1.78
  6.12
  0.53
  1.23
  0.01
  0.03
  0.16
  0.42
  0.25
  0.31
  0.44
  0.16
  BPDB / Public (Tk / kWh)
  Nimbus (Tk / kWh)
  Private (Tk / kWh)
NBBL’s Reference Rate Tariff for Variable O&M under HSD based operations is lower than most of the actual O&M costs of BPDB & private plants
Source: Industry Reports, Deloitte Analysis; Note 1) For Nimbus, the Reference O&M costs has been considered as per PPA and have been converted to local BDT / kWh at 1 USD = 85 BDT 2) Each bar represents one power plant in the above graph

## Slide 171: Implementation Agreement | Key Provisions
An overarching tripartite agreement signed with Government of Bangladesh (GOB) and Power Grid Company of Bangladesh (PGCB) for setting up of the power plant on Build-Own-Operate basis on 28th August 2017
Salient features: Government Authorizations: To be obtained by NBBL. Any delay by GOB will cause the Required COD to be pushed forward Equity lock-in: 51% of Ordinary share capital for 6 years; except with GOB consent or as public offering Force Majeure/ Political Event: GOB and PGCB can’t claim relief Taxes: NBBL is exempt from tax/withholding tax in Bangladesh Guarantee: GOB will pay any amount due from BPDB, PGCB, Gas Supplier, Fuel Supplier in case of failure to pay Termination: Event of default, Force Majeure/Political Event not remedied within 12 months Repatriation of funds: Governed by Exchange Regulations Act 2016; NBBL permitted to purchase dollars for repatriation Event of Default: Includes default by BPDB, gas/fuel supplier Compensation: In case of termination due to GOB event of default, NBBL can choose to transfer the facility to GOB in exchange for a compensation which includes: Total principle outstanding + interest thereon + winding up costs Equity investment reduced by 5% on straight line basis Net Cash Flow for 5 years discounted at 12% Any additional equity reduced by 3.2% on straight line basis Interconnection facility: NBBL will construct and operate a 230 kV switchyard adjacent to the power plant where it will deliver power to the existing 230 kV switchyard of PGCB at the existing Bhola I power plant
IA
Power Purchase Agreement
Gas Supply Agreement
Fuel Supply Agreement
Land Lease Agreement
Key Risks
The condition of Equity lock-in restricts the transfer of NBBL’s ownership for a period of 6 years. In case approval is not obtained from the Government of Bangladesh, the transaction cannot be affected.
In case of termination due to Company event of default, GOB has only an option but not an obligation to take possession of the facility and pay a compensation amount to NBBL equivalent to the principle outstanding and the interest thereon.
Source: Implementation Agreement, Deloitte Analysis

## Slide 172: Implementation Agreement | Key Terms
Termination Payment
Sr. No | Parameter | Conditions | Key risks
Performance guarantee, offtake guarantee |  |  | 
1 | Termination Payment | Company Event of Default: In case of Company Event of Default, GOB has a right but no obligation to acquire the Company’s rights and pay a compensation amount to NBBL equivalent to the principle outstanding and the interest thereon. In case GOB does not purchase the asset no obligation would exist further on GOB | Right to buy only to BPDB No provision to recover equity investments
2 |  | Force Majeure: In case of FM event there is no restoration cost which would be reimbursed to the Company. In case after the FM Event the Company concludes that the Facility cannot be restored in which case the Company can terminate the agreement however there would be no obligation on GOB for any payment | In case facility cannot be restored after an FM event no compensation would be paid by GOB only termination rights provided to the Company
Source: PPA, Deloitte Analysis

## Slide 173
Policy & Regulatory Overview
Analyze the key clauses affecting Nimbus in Power Sector Governing laws for licensing, tariff determination, private sector participation, grid rules, energy policy & visions, gas supply among others
01
02
03
04
05
06
07
08
09
10

## Slide 174: Policy & Regulatory Overview | Implications for Power Generators
We have reviewed the various policies and regulations in force for gas based power generators in Bangladesh and identified the key implications for the generators
Bangladesh Electricity Act, 2018
Provides for licensing regulations for electricity generation
1
Licensing requirement poses entry barrier to a new entrant in the Bangladesh power generation space, resulting in favorable condition for the existing player as far as market competition is concerned;
The existing gas based generation company has to comply with the license terms and conditions.
The law provides for establishment of an Independent System Operator in Bangladesh, thus making power dispatch according to merit order. This is favorable for generators having low cost of generation
Bangladesh Energy Regulatory Commission License Regulations, 2006 and its amendment in 2016
Provides for the license application and approval processes, responsibilities of a licensee, annual license fees, license renewal process, conditions for license suspension and revocation, and license termination process.
2
The existing gas based generation company has to comply with the license terms and conditions and exercise its responsibilities as per the regulations, failing which the Commission may suspend or revoke the license.
Bangladesh Energy Regulatory Commission (Natural Gas Distribution Tariff) Regulations, 2010:
Provides for determination of gas distribution tariff
3
Regulated gas distribution tariff means higher certainty for gas price compared to a market-based gas pricing arrangement.
Source: BERC, MPEMR, Bangladesh Bank, BPDB, PGCB, Deloitte Analysis

## Slide 175: Policy & Regulatory Overview | Implications for Power Generators
We have reviewed the various policies and regulations in force for gas based power generators in Bangladesh and identified the key implications for the generators
Bangladesh Electricity Regulatory Commission Electricity Grid Code Regulations 2018:
Provides for grid operation and connectivity standards, scheduling and dispatch procedures, standards for protection, metering and performance, and reporting requirements.
4
The gas based plant has to abide by the standards, procedures and compliance requirements as stipulated in the grid code. Violation of the grid code may ultimately lead to grid imbalance and generation outage, thereby causing financial loss.
Apart from the operating guidelines, a few key clauses have been presented below:
  All generators shall provide Licensee, System Operator and Single Buyer with their proposed outage for year ahead by 31st March
  The System Operator shall provide to the Licensee, the Single Buyer and Generators yearly estimates of requirements for net electrical output on a monthly basis for the year ahead
  The System Operator shall provide to the Licensee, the Single Buyer and Generators weekly estimates of requirements for net electrical output on an hourly basis for the week ahead
Bangladesh Electricity Regulatory Commission Electricity Distribution (Retail) Tariff Regulations 2016:
Provides for determination of retail tariff on cost-plus basis for electricity distribution companies of Bangladesh.
5
Regulated revenue for distribution companies has a direct impact on the receivables of the single buyer (that sales electricity to all the distribution companies at a regulated Bulk Supply Tariff), which in turn can potentially impact the receivables of the generation company (that sales electricity to the single buyer).
Source: BERC, MPEMR, Bangladesh Bank, BPDB, PGCB, Deloitte Analysis

## Slide 176: Policy & Regulatory Overview | Implications for Power Generators
We have reviewed the various policies and regulations in force for gas based power generators in Bangladesh and identified the key implications for the generators
Quick Enhancement of Electricity and Energy Supply (Special Provisions) Act, 2010 and its amendments in 2015 and 2018:
Provides for measures for fast-tracking of power projects (including generation, transmission, distribution, and import of electricity) with the aim to mitigate electricity supply shortage and ensure uninterrupted supply.
6
This Act encourages and facilitates implementation of new generation projects and hence creates competition for the existing generation project. However, the entry barrier in form of licensing requirements exists.
Bangladesh Gas Act 2010:
Provides for the rules governing the transmission, distribution, marketing, supply and storage of natural gas, LNG, CNG, LPG, CBM, etc. in Bangladesh and licensing for the same.
7
Regulated and licensed gas supply value-chain favors planned and organized supply of gas.
The regulation provides for restrictions or suspension in supply of gas to customers or disconnection in the gas line in cases of (not limited to):
  Gas crisis at national level
  Need to prioritize gas distribution among users
  Gas is used less than the efficiency prescribed by the government / commission / company
Bangladesh Energy Regulatory Commission Dispute Settlement Regulations, 2014:
Provides for the procedures and institutional responsibilities for the purpose of resolution of disputes.
8
There is procedural clarity for dispute resolution.
Source: BERC, MPEMR, Bangladesh Bank, BPDB, PGCB, Deloitte Analysis

## Slide 177: Policy & Regulatory Overview | Implications for Power Generators
We have reviewed the various policies and regulations in force for gas based power generators in Bangladesh and identified the key implications for the generators
Vision and Policy Statement on Power Sector Reform, 2000 and National Energy Policy (NEP), 2004:
Vision and Policy Statement – Aims at augmentation of gas-based power generation capacity, network expansion with focus on western region, replacement of liquid fuel in existing generation stations; and recognizes gas resource of Bangladesh
National Energy Policy – Development of indigenous natural gas supply, allocation of natural gas to sectors like power, fertilizer, industrial, commercial, domestic, etc., extension of gas pipeline for equitable development of Bangladesh, gas price setting based on economic cost of supply, provision of stand-by wells to meet emergency situation with an emergency reserve margin of 20%
9
Policy push for gas-based power generation implies government’s focus on the sector to ensure a facilitating environment for the gas-based generation plants in the country.
The Pricing Policy (NEP) for Energy calls for the present price of natural gas to be raised in phases to reach its economic cost of supply
The pricing policy (NEP) further states that the present subsidy on gas price for power and fertilizer is to be removed gradually. Subsidy, if required, is to be given at the end-user level and the related liabilities cannot be passed on to the utilities
The policy (NEP) provides for duty exemption for machinery, equipment, spares and other consumables for energy related projects and protects the power sector development projects from foreign exchange fluctuations
The Policy (NEP) also calls for maintenance of adequate reserve margin by installing capacities in excess of peak demand (say 25%) so that the system can reliably accommodate planned maintenance and forced outage
Source: BERC, MPEMR, Bangladesh Bank, BPDB, PGCB, Deloitte Analysis

## Slide 178: Policy & Regulatory Overview | Implications for Power Generators
We have reviewed the various policies and regulations in force for gas based power generators in Bangladesh and identified the key implications for the generators
Private Sector Power Generation Policy of Bangladesh, 2004 and Policy Guideline for Small Power Plant (SPP) in Private Sector
Private Sector Power Generation Policy – Provides guidelines on the modality for implementation of IPP projects, determination of generation tariff for such IPPs, and Fiscal incentives.
Policy Guideline for SPP – Provides guidelines for establishment of SPPs including plant location, fuel supply, power offtake, price regulation, license requirement, GOB support and Fiscal incentives.
10
The policies offer clarity on power offtake and tariff-related matters for existing IPP projects.
Some of the salient provisions of the policy are:
  Minimum requirement for equity will be 20%
  PPA will be guaranteed by GoB for utility performance
  Protection against changes in taxes, duties and force majeure risk
  Tax Holiday for 15 years (Income Tax)
  Repatriation of equity along with dividends to be allowed freely
  Tax exemption on interest on foreign loans
  Tax exemption on capital gains from transfer of shares by the investing company
  Tax exemption on royalties, technical know-how and technical assistance fees, and facilities for their repatriation
Source: BERC, MPEMR, Bangladesh Bank, BPDB, PGCB, Deloitte Analysis

## Slide 179: Policy & Regulatory Overview | Implications for Power Generators
We have reviewed the various policies and regulations in force for gas based power generators in Bangladesh and identified the key implications for the generators
Policy Guidelines for Enhancement of Private Participation in the Power Sector, 2008
Aims at establishment of private power generation plants from which electricity can be supplied to large consumers at mutually-negotiated tariff as well as to discoms at BERC-determined tariff, implementation of non-discriminatory open access of transmission and distribution, establishment of new power plants and rehabilitation of old public sector plants in PPP mode.
11
This policy aims at facilitating selling of power from private power plants.
Some of the key clauses under the Policy are as follows:
  Given the fast depleting condition of domestic natural gas, the new power plants shall preferably rely on coal, imported gas, liquid fuel, or renewable energy sources like solar, wind, hydro, biomass, municipal waste, and others, as fuels, instead of domestic natural gas.
  Any fuel supply or source of energy has to be arranged by developers for Commercial Power Plants.
  Except for the power plants for which GoB has committed guaranteed fuel supply, GoB will not be responsible to supply fuels, or provide guarantee in favor of any fuel supplier to supply fuels to Commercial Power Plants.
  The interested Private Investors should posses proven experience in developing and operating power plant of same or higher capacity as IPP, Rental Power Plant, SPP or CPP and selling power to Large Consumers.
Source: BERC, MPEMR, Bangladesh Bank, BPDB, PGCB, Deloitte Analysis

## Slide 180: Policy & Regulatory Overview | Implications for Power Generators
We have reviewed the various policies and regulations in force for gas based power generators in Bangladesh and identified the key implications for the generators
Renewable Energy Policy of Bangladesh, 2008
Aims at development of renewable energy resources in Bangladesh and targets to meet 10% of the country’s power demand from RE sources by 2020.
12
Gas-based generating plant can act as a quick-ramping facility for the purpose of grid frequency-balancing in the scenario of addition of significant RE generation capacity in the grid.
Source: BERC, MPEMR, Bangladesh Bank, BPDB, PGCB, Deloitte Analysis

## Slide 181
Annexures

## Slide 182: Annexure A | Natural Gas Tariff History in Bangladesh
Effective From | Power | Fertilizer | Industry | Commercial | Tea estate | Cap. Power | Domestic |  | 
 |  |  |  |  |  |  | Metered | Single Burner | Double Burner
01.08.2009 | 2.82 | 2.58 | 5.86 | 9.47 | 5.86 | 4.18 | 5.16 | 400.00 | 450.00
01.09.2015 | 2.82 | 2.58 | 6.74 | 11.36 | 6.45 | 8.36 | 7.00 | 600.00 | 650.00
01.03.2017 | 2.99 | 2.64 | 7.24 | 14.20 | 6.93 | 8.98 | 9.10 | 750.00 | 800.00
01.06.2017 | 3.16 | 2.71 | 7.76 | 17.04 | 7.42 | 9.62 | 11.20 | 900.00 | 950.00
01.08.2017 | 3.16 | 2.71 | 7.76 | 17.04 | 7.42 | 9.62 | 9.10 | 750.00 | 800.00
01.07.2019 | 4.45 | 4.45 | 10.7 | 23 / 17.041 | 10.7 | 13.85 | 12.6 | 925.00 | 975.00
In the last 10 years, BERC has raised the natural gas prices 6 times for various consumer categories
Figures in Taka / SCM
Source: BERC, Petrobangla, Industry Reports, Deloitte Analysis; Note 1) The Commercial Tariff for Hotels & Restaurants is BDT 23 / cum whereas for small cottage industries is BDT 17.04 / cum

## Slide 183: Annexure B | Natural Gas Price Components in Bangladesh
Particulars | Production Charge | LNG Charge | Gas Development Fund | Fuel Security Fund | Transmission Charge | Distribution Charge | VAT | End Consumer Price
Power Sector | 0.69 | 2.15 | 0.20 | 0.19 | 0.42 | 0.25 | 0.56 | 4.45
Captive Power | 2.13 | 8.13 | 0.61 | 0.58 | 0.42 | 0.25 | 1.73 | 13.85
Fertilizer | 0.69 | 2.15 | 0.20 | 0.19 | 0.42 | 0.25 | 0.56 | 4.45
Industry | 1.65 | 6.13 | 0.47 | 0.45 | 0.42 | 0.25 | 1.33 | 10.70
Tea Estate | 1.65 | 6.13 | 0.47 | 0.45 | 0.42 | 0.25 | 1.33 | 10.70
Commercial (Hotels) | 3.54 | 13.94 | 1.01 | 0.97 | 0.42 | 0.25 | 2.87 | 23.00
Commercial (Small Cottage Industries) | 2.62 | 10.06 | 0.75 | 0.72 | 0.42 | 0.25 | 2.22 | 17.04
(Domestic Metering) | 1.94 | 7.33 | 0.55 | 0.53 | 0.42 | 0.25 | 1.57 | 12.60
The Pricing Mechanism (2019) for each consumer category considers different amount of cross subsidies for each component except transmission & distribution charge which is same for all consumers in Bangladesh
Figures in Taka / SCM
Source: BERC, Petrobangla, Industry Reports, Deloitte Analysis; Note 1) The Commercial Tariff for Hotels & Restaurants is BDT 23 / cum whereas for small cottage industries is BDT 17.04 / cum

## Slide 184: Annexure C | Natural Gas Price Subsidy by Government
As per BERC tariff (2019), power & fertilizer sectors receive the highest subsidy at ~65%; CNG Sales and Hotels and Restaurants provide the highest cross subsidy at ~180% and ~80% respectively
Particulars | Proposed Category Wise Sale (mmscmd) | Tariff (BDT / SCM) | Total Expected Revenue (Bn BDT) | Average Cost of Natural Gas (BDT / SCM) | Total Revenue at Cost Price (BDT Bn) | (+) Subsidy / (-) Cross Subsidy
Symbol | A | B | C = A*B*365/1000 | D | E = A*D*365/1000 | F = 1- E/D
Power | 39.54 | 4.45 | 64.23 | 12.6 | 181.81 | 64.67%
Captive power | 15.87 | 13.85 | 80.20 | 12.6 | 72.94 | -9.96%
Fertilizer | 5.43 | 4.45 | 8.82 | 12.6 | 24.97 | 64.67%
Industry | 16.01 | 10.7 | 62.52 | 12.6 | 73.60 | 15.05%
Tea garden | 0.09 | 10.7 | 0.33 | 12.6 | 0.39 | 15.05%
Hotel and restaurant | 0.29 | 23 | 2.40 | 12.6 | 1.31 | -82.60%
Small and Cottage Industries | 0.44 | 17.04 | 2.73 | 12.6 | 2.02 | -35.28%
CNG-feed gas | 4.29 | 35 | 54.78 | 12.6 | 19.71 | -177.87%
Domestic | 13.34 | 12.6 | 61.35 | 12.6 | 61.33 | -0.03%
Total | 95.29 | 9.8 | 340.84 | 12.6 | 438.09 | 22.20%
Source: BERC, Deloitte Analysis; Note 1) The Average Cost of Natural Gas has been considered at BDT 12.6 / scm which corresponds to a cost of USD 3.97 / MMBTU at 1 USD = 80 BDT and 25.2 SCM = 1 MMBTU
2) The average tariff of BDT 9.8 / SCM (corresponding to USD 3.09 / MMBTU) has been considered basis the overall revenue projected by BERC from the sale of Natural gas to the consumer segments at the mandated tariff.

## Slide 185: Annexure – D - BPDB – Variable Charge Assessment
Following graph shows total estimated total variable charge payment impact (BDT Bn) for BPDB till FY26: Following graph shows the Estimated Per unit Cost & Revenue Forecast (BDT / kWh)
The growth in power demand at 10.4% CAGR would also lead to increase in variable payment for BPDB from the current 217 Bn BDT to ~409 Bn BDT by FY26; However the growth in variable payment would be lower at 9.5% CAGR leading to overall power increase cost at 8.5% CAGR only
Impact Variable Charges Payout by BPDB As mentioned earlier, Bangladesh paid ~217 Bn BDT as variable charges for the power produced in the country in FY19 Out of the BDT ~217 Bn, liquid fuel based plants (HSD/HFO) are estimated to have contributed to ~142 Bn (65% of the fuel cost) compared to their installed capacity of 6,140 MW (32% of total installed capacity of ~18,961 MW) Going forward we expect the average power demand in Bangladesh to be met by ~19,600 MW of non-liquid based power supply capacity in Bangladesh The graph on the right (below) shows the estimated variable charge payout by BPDB in FY26 to meet the average power demand which may reach BDT ~409 Bn growing at a CAGR of ~9.5% which is lower than estimated average power demand growth Per Unit Cost & Revenue Impact The average power purchase cost of BPDB which stood at BDT ~5.7 / kWh in FY19 may reduce to BDT ~5.0 / kWh primarily driven by replacement of expensive HSD/HFO based generation to economical sources of power such as LNG and Imported Coal We have also considered that in such as supply scenario, the average bulk power selling rate of BPDB may remain constant at BDT 5 / kWh (at FY19 levels) considering the fall in overall power purchase cost for BPDB Thus the gap between BPDB’s revenue and power purchase cost is expected to reduce significantly to marginal levels by FY26
Source: BPDB, Industry Reports, Deloitte Analysis; Note 1) We have considered the average gas price for power sector at BDT 4.45 / SCM as per prevailing tariff with no escalation. 2) We have considered the average Variable Cost per unit (kWh) for Gas, HSD and HFO based plants belonging to Rental / Quick Rental Ownership (RPP/QRPP) in FY19 at same level as that of the entire Gas, HSD and HFO portfolio in Bangladesh in FY19 3) We have considered the fixed cost of HFO based plants under RPP/QRPP ownership in FY19 based on sample benchmark data of PPAs for a few RPP/QRPP plants in Bangladesh which may lead to variance (+/- 10%) in the total power purchase cost estimated by us and the total power purchase cost reported by BPDB in FY19 4) We have considered the fixed cost of HSD Based plants under RPP / QRPP ownership at the same level as that of entire HSD portfolio in Bangladesh in FY19 which may lead to variance (+/- 10%) in the total power purchase cost estimated by us and the total power purchase cost reported by BPDB in FY19 5) We have
estimated the total power purchase cost of upcoming LNG and Imported coal based power plants considering the levelized projections for fixed cost of such plants
based on industry estimates and 1st year fuel price for LNG at $8 / MMBTU (landed cost) and Coal at $~90 / Tonne (landed cost) 6) The incremental capacity addition required to meet the average demand (apart from the planned capacity addition) has been assumed to be met by LNG based power plants only 7) We have estimated the projected the BPDB payment obligations for meeting average power demand only and not for meeting peak demand
  Average Bulk Power Sale Price
Chart: 
 | 0
 | 4.97 | 5.03
  FY19
  FY26 (Estimated)
Chart: 
 | 2.98
 | 2.05
  5.0
Chart: 
 | 3.16
 | 2.52
  5.7
  Average Capacity Charge
  Average Variable Charge
Chart: 
 | 217 | 409
  FY26 (Estimated)
  FY19 (Estimated)
  9.5%

## Slide 186: Annexure E | Gas Transmission | Existing Pipelines (1/2)
Sr. No | Project | Diameter (inch) | Length (km) | CoD
1 | North-South Gas Transmission Pipeline | 24 | 175 | 1993
2 | Bakhrabad To Demra Transmission Pipeline | 20 | 68.72 | Jul-85
3 | Bakhrabad To Chittagong Transmission Pipeline | 24 | 174.65 | Jul-85
4 | Ashuganj-Bakhrabad Gas Transmission Pipeline (1st Phase) | 30 | 58.5 | Dec-97
5 | Paschimanchal Gas Transmission Project (a)Bangabandhu (B-B) Bridge | 30 | 9 | Jun-00
6 | Paschimanchal Gas Transmission Project (b) Elenga-Nalka | 24 | 28.5 | Jun-00
7 | Paschimanchal Gas Transmission Project © Nalka-Baghabari | 20 | 35.5 | Jun-00
8 | Beanibazar-Kailashtila | 20 | 18 | Sep-01
9 | Rashidpur-Ashuganj Gas Transmission Pipeline (1st Phase): Rashidpur-Habigonj | 30 | 28 | May-05
10 | Rashidpur-Ashuganj Gas Transmission Pipeline (2nd Phase): Habigonj-Ashuganj | 30 | 54 | May-05
11 | Nalka-Bogra Gas Transmission Pipeline (a) Nalka-Hatikumrul | 30 | 6 | Jun-06
12 | Nalka-Bogra Gas Transmission Pipeline (b) Hatikumrul-Bogra | 20 | 54 | Jun-06
13 | Ashuganj-Monohordi Gas Transmission Pipeline | 30 | 37 | Jul-07
14 | Dhaka Clean Fuel Gas Transmission Pipeline | 20 | 60 | Jun-08
15 | Titas Gas Field (Location-G)-AB Pipeline Gas Transmission Pipeline | 24 | 8 | Dec-12
16 | Srikail Gas Field (Location-2)-AB Pipeline 20-inch 1.50-km Gas Transmission Pipeline | 20 | 1.5 | Mar-13
17 | Monohordi-Dhanua & Elenga-Bangabandhu Bridge East Gas Transmission Pipeline | 30 | 51 | Jun-14
GTCL has been tasked with maintaining the high pressure transmission lines and has acquired / transferred the major transmission lines from other transmission & distribution companies in Bangladesh as per GoB directive
Source: Petrobangla, GTCL, Industry Reports, Deloitte Analysis

## Slide 187: Annexure E | Gas Transmission | Existing Pipelines (2/2)
Sr. No | Project | Diameter (inch) | Length (km) | CoD
18 | Bonpara-Rajshahi Gas Transmission Pipeline | 12 | 53 | Dec-14
19 | Bibiyana-Dhanua Gas Transmission Pipeline | 36 | 137 | Jun-15
20 | Titas Gas Field (Location- C, B & A) To Titas A-B Gas Transmission Pipeline | 10 | 7.7 | Jun-15
21 | Bheramara-Khulna Gas Transmission Pipeline | 20 | 165 | Dec-15
22 | Hatikumrul-Bheramara Gas Transmission Pipeline | 30 | 84 | Dec-16
23 | Titas Gas Field Well No. 23, 24 (Sorail) To Khatihata and Well No. 25, 26 (Malihata) To Khatihata Gas Transmission Pipeline | 20 | 3.3 | Jun-17
24 | Gas Transmission Capacity Expansion-Ashuganj to Bakhrabad Gas Transmission pipeline | 30 | 61 | Dec-17
25 | Maheshkali-Anwara Gas Transmission Pipeline | 30 | 91 | Jun-18
26 | Bakhrabad Siddirgonj Transmission Pipelines | 30 | 60 | Dec-18
27 | Anwara-Fouzdarhat Gas Transmission Pipeline | 42 | 30 | Jun-19
GTCL has been tasked with maintaining the high pressure transmission lines and has acquired / transferred the major transmission lines from other transmission & distribution companies in Bangladesh as per GoB directive
Source: Petrobangla, GTCL, Industry Reports, Deloitte Analysis

## Slide 188: Annexure F | Gas Transmission | Planned Pipelines (1/2)
Sr. No | Project | Objective | Status | Diameter (inch) | Length (km) | Period
1 | Bakhrabad- Meghnaghat- Haripur Gas Transmission Pipeline | For gas supply to Meghnaghat Power Hub, existing & planned Power Stations in Gajaria & Haripur, Economic Zone | Route survey & environmental examination complete DPP sent to Petrobangla | 42 | 50 | 2019-2022
2 | Gas Pipeline construction along the 2nd Bangabandhu Bridge (Railway | Additional gas supply to franchise areas of PGDC and SGDC in North, North-west and South Western regions |  | 36 | 12 | 2020-2023
3 | Shatkhira (Bhomra)- Khulna (Arrongghata) Gas Transmission Pipeline | To supply RLNG imported from India to national grid | Route survey completed and environmental examination in progress | 30 | 65 | 2019-2022
4 | Langalband- Maoua & Zajira-Taker Hat Gas Transmission Pipeline | Expansion of gas service to south-western region on interconnecting with UC pipeline over Padma bridge | Route survey completed | 30 | 70 | 2020-2023
5 | Taker Hat- Faridpur & Taker Hat- Barishal Gas Transmission Pipeline | Gas supply to grater Faridpur and Barishal region |  | 30 | 115 | 2025-2028
6 | Khulna- Gopalganj Taker Hat Gas Transmission Pipeline | For supply to Madaripur, Gopalganj & Khulna areas. |  | 30 | 80 | 2020-2023
The planned pipeline outlook has also been developed to connect the gas starved western region with Natural Gas / LNG Supply
Source: Petrobangla, GTCL, Industry Reports, Deloitte Analysis

## Slide 189: Annexure F | Gas Transmission | Planned Pipelines (2/2)
Sr. No | Project | Objective | Status | Diameter (inch) | Length (km) | Period
7 | Bhola-Barisal Gas Transmission Pipeline | Gas infrastructure development for gas supply to Bhola & Barishal region. | Feasibility study under progress | 30 | 60 | 2022-2025
8 | Payra-Barishal Gas Transmission Pipeline | To feed RLNG up to Barishal, which Is to be received at Payra port area |  | 42 | 87 | 2031-2035
9 | Khulna- Bagerhat- Pirojpur- Jhalakathi- Barisal Gas Transmission Pipeline | Gas supply to South Western region under SGDCL |  | 36 | 110 | 2031-2035
10 | Hatikumrul- Bogra Gas Transmission Pipeline | Development of gas transmission in Northern region of country |  | 30 | 55 | 2033-2036
The planned pipeline outlook has also been developed to connect the gas starved western region with Natural Gas / LNG Supply
Source: Petrobangla, GTCL, Industry Reports, Deloitte Analysis

## Slide 190: Annexure G | Electricity Transmission | Ongoing Development Projects
Currently, ~25 major transmission projects are under implementation
Sr. No | Project | Objective | Scope | Period
1 | Construction of Rahanpur to Monakasha Border 400kV Transmission Line in Chapainawabganj District to Import Power from India (Jharkhand) to Bangladesh | To evacuate Imported Power from under construction Adani Power Jharkhand Limited 1496MW power plant in India and supply the power to the national grid. | 400 kV Double Circuit Transmission Line: 28 km | FY20-FY 22
2 | Southwest Transmission Grid Expansion Project | To ensure adequate and reliable power supply for the upcoming Economic Zones in Barisal Area as well as in Rajshahi area | 400 kV Transmission Lines: 104 km. 230 kV Transmission Lines: 137 km 132 kV Transmission Lines: 27 km. 400 kV Substations: 3 nos. 230 kV Substations: 1 nos. 230 kV GIS Bay Extensions: 2 nos 132 kV GIS Bay Extensions: 2 nos. | FY19-FY24
3 | Construction of 500 MW HVDC Back to Back Station at Comilla North (Bangladesh) for Transfer of Power through Surjamaninagar (Tripura, India) - Comilla North (Bangladesh) | To meet the growing electricity demand of the eastern part of the country. To ensure sufficient facilities to import 500 MW power from Tripura & Assam (India). | Construction of 500 MW HVDC Bacl-to-Back Station at Comilla North including 400 kV GIS Switchyard. | FY19-FY21
4 | Infrastructure Development for Power Evacuation Facilities of Rooppur Nuclear Power Plant | To ensure power evacuation from Rooppur Nuclear Power Plant (RNPP) and qualitative upgradation of Bangladesh power system for the integration & safe operation of Rooppur Nuclear Power Station. | 400 kV Transmission Lines: 609 km (20 km river crossing) 230 kV Transmission Lines: 60 km 400 kV Bay Extensions: 8 nos 230 kV Bay Extensions: 4 nos To implement the frequency control and frequency drop protection, protection system, emergency control system and other associated tasks for qualitative upgradation of Bangladesh Power System. | FY18-FY23
Source: PGCB, Deloitte Analysis

## Slide 191: Annexure G | Electricity Transmission | Ongoing Development Projects
Currently, ~25 major transmission projects are under implementation
Sr. No | Project | Objective | Scope | Period
5 | Replacement of Ashuganj Old 132 kV AIS Substation by New 132 kV GIS Substation Project | Modernization of Ashuganj Old Substation to reduce the chance of National Grid Failure | Replacement of Existing Ashuganj old 132 kV AIS Substation by 132 kV GIS Substation. | FY18-FY21
6 | Development of Transmission Infrastructure at Mirsharai Economic Zone for Reliable Power Supply | To supply reliable and uninterrupted electricity to Mirsharai Economic Zone and evacuate generated power from an upcoming power plant in nearby area. | 400kV double circuit transmission line of 17 km 230/33kV (2 x120/180 MVA) GIS Substation Extension of 230kV GIS Substation (2 nos. 400kV bays) | FY18-FY21
7 | Construction of Bheramara (Bangladesh)-Baharampur(India) 2nd 400kV Transmission Line (Bangladesh Portion) | To ensure reliable transmission for 1000MW power import from India | Bheramara(Bangladesh)-Baharampur(India) 2nd 400 kV double circuit transmission line construction: 28 km 400kV Bay Extension: 2 no's at Bheramara HVDC | FY18-FY21
8 | Construction of Bakerganj-Barguna 132kV Transmission Line & Barguna 132/33kV Substation | To ensure reliable and uninterrupted power supply to Barguna and its neighboring areas | Single Circuit Stringing in Bakerganj-Barguna double circuit towers:50 km Construction of Barguna 132/33 kV AIS Substation: 2x50/75 MVA | FY18-FY21
9 | Matarbari Ultra Super Critical Coal-Fired Power Project (II) (PGCB Part: “Matarbari-Madunaghat 400 kV Transmission Line”) | To evacuate power from upcoming Matarbari 1200 MW Power Station and to create power transmission capacity/ facility between Matarbari and Madunaghat | 400kV transmission line. | FY18-FY21
10 | Patuakhali -Payra 230 kV Transmission Line Project | To supply back feed power to upcoming 1st unit (660 MW) of Payra 1320 MW Power Plant through a sufficient amount of power in local area from Payra coal power plant in future. | To construct 47 km 230kV transmission line. To construct 132 kV Switchyard (except transformer). To extend two 132kV Bay at 132/33 kV existing Substation. | FY17-FY21
Source: PGCB, Deloitte Analysis

## Slide 192: Annexure G | Electricity Transmission | Ongoing Development Projects
Currently, ~25 major transmission projects are under implementation
Sr. No | Project | Objective | Scope | Period
11 | Construction of Patuakhali (Payra) - Gopalganj 400 kV Transmission Line & Gopalganj 400 kV Grid Substation | The main objective of the project is to create necessary facilities to evacuate power from upcoming coal based Payra 1320 MW Power Plant. | Constrcution of 400 kV Double circuit transmission line: 160 km Constrcution of line in line out (LILO OF) of Madaripur –Gopalganj(Old) 132 kV double circuit line at Gopalganj (New) substation (8km) Constrcution of line in line out (LILO OF) of Madaripur –Faridpur 132 kV double circuit line at Gopalganj (New) substation (1km) Construction of 400/132 kV, 3x325 MVA AIS Substation. | FY17-FY21
12 | Dhaka and Western Zone Transmission Grid Expansion Project | To meet up the growing demand by ensuring reliable power supply to industrial, commercial and residential areas of Central Zone (DESCO area of Dhaka), Western Zone, Northern Zone and Southern Zone of Bangladesh by enhancing and strengthening existing grid network. | 400 kV Transmission Line: 22km 230 kV Transmission Line: 144 km 132 kV Transmission Line: 242 km 400 kV Substations: 2 nos 230 kV Substations: 3 nos 132 kV Substations: 10 nos 132 kV Bay Extensions: 20 nos | FY19-FY24
13 | Expansion and Strengthening of Power System Network under Chattogram Area | To transmit electricity from upcoming United 583 MW as well as United 300MW Power plants and from other upcoming power plants at Anowara to the major load centers of Chattogram city | 400 kV Transmission Line: 25.185 km 230 kV Transmission Line: 17.24 km 230 kV Substations: 2nos, 2160 MVA 230kV Bay Extension: 2 nos | FY19-FY22
14 | Enhancement and Strengthening of Power Network in Eastern Region | To meet up the growing demand by ensuring reliable power supply to industrial, commercial and residential points of Greater Comilla, Chittagong, Greater Noakhali area by enhancing & strengthening existing grid network of Eastern Region. | 400 kV Transmission Lines: 12.63 km 230 kV Transmission Lines: 175.91 km 132 kV Transmission Lines: 256.3 km including 157 km re-conductoring 400 kV Substations: 2 nos 230 kV Substations: 2 nos. 132 kV Substations: 10 nos. Bay Extensions: 6 nos. | FY18-FY21
Source: PGCB, Deloitte Analysis

## Slide 193: Annexure G | Electricity Transmission | Ongoing Development Projects
Currently, ~25 major transmission projects are under implementation
Sr. No | Project | Objective | Scope | Period
15 | Barapukuria - Bogura - Kaliakoir 400 kV Transmission Line Project | To extend High Voltage transmission infrastructure upto northern part of the country for import power in future from India, Nepal and Bhutan To transmit the power from proposed 2x800 MW power plant to be built at Jharkhand, India by Adani Group | 400 kV Transmission Line: 260 km 400 kV AIS Bay Extension: 2 nos 230 kV AIS Bay Extension: 2 nos | FY19-FY22
16 | Power Grid Network Strengthening Project under PGCB | The main objective of the project is to build up necessary infrastructures for reliable transmission of power. Specific Objectives | 400 kV Transmission Line: 100 km 230 kV Transmission Line: 330.20 km 132 kV Transmission Line: 334.50 km Renovation of existing 132 kV Transmission Lines: 225 km 400/132/33 kV Substations: 1 no. 230/132 kV new Substations (including one 230 kV Switching Station): 12 nos. 132/33 kV new Substations: 28 nos. Extension of existing substations at 400 kV Substation: 1 no 230 kV Substation: 3 nos. 132 kV Substation: 14 nos. Capacity upgradation of existing: 230/132 kV Substation: 7 nos. 132/33 kV Substation: 28 nos. Renovation of existing 132/33 kV Substation: 5 nos. Specialized Engineering Facilities: 7 nos | FY17-FY24
17 | Energy Efficiency in Grid Based Power Supply Project | The object of this project is to increase reliability and efficiency of the electrical power supply in Bangladesh through expanding and improving the 230 kV and 132 kV power transmission systems of PGCB. | New 230 kV transmission line: 82.48 km New 132 kV transmission line: 111.35 km Renovation of existing 132 kV transmission line: 196 km New 230/132 kV substations: 5 nos. New 132/33 kV substations: 8 nos. Renovation of existing 132/33 kV substations: 6 nos. Bay extensions: 15 nos. | FY17-FY21
Source: PGCB, Deloitte Analysis

## Slide 194: Annexure G | Electricity Transmission | Ongoing Development Projects
Currently, ~25 major transmission projects are under implementation
Sr. No | Project | Objective | Scope | Period
18 | Dhaka - Chittagong Main Power Grid Strengthening Project | The main objectives of the project are to create facilities to transmit power from upcoming Matarbari 1200 MW Power Station and to enhance the power transmission capability between Chittagong and Dhaka. | Meghnaghat-Madunaghat 400 kV double circuit line (214 km) 230 kV double circuit transmission line between Existing Madunaghat and New Madunaghat Substation (8 km) Line In Line Out from Hathazari - Shikalbaha 230 kV Transmission Line at New Madunaghat Substation (5.5 km) 230 kV AIS Switching Station at Meghnaghat 230 kV GIS Switching Station at Madunaghat 400 kV AIS Substation at Meghnaghat with 2x750 MVA transformer 400 kV GIS Substation at Madunaghat with 3x750 MVA transformer Upgradation of existing 132 kV Substation to 230 kV voltage level at Madunaghat Installation of GIB and Shunt Reactor at Matarbari. | FY17-FY21
19 | Aminbazar - Maowa - Mongla 400 KV Transmission Line Project | The main objective of the project is to create facilities to evacuate power from the upcoming Rampal Coal Power Plant. | Construction of Aminbazar - Maowa - Mongla 400 kV double circuit line (164.6 km) Construction of river crossing line beside Padma Bridge (9.4 km) Construction of substation (400 kV portion) at Aminbazar with 3x520 MVA transformers. | FY17-FY21
20 | Mongla-Khulna(S) 230 kV Transmission Line Project | To create power evacuation facilities for upcoming power plants at Mongla (1st Unit 660MW). To supply back feed power to Mongla power plant. | 24 km four circuit 230 kV Mongla-Khulna (S) line (Initially two circuit stringing) Two 230 kV bay extension at Khulna (S) | FY15-FY21
Source: PGCB, Deloitte Analysis

## Slide 195: Annexure G | Electricity Transmission | Ongoing Development Projects
Currently, ~25 major transmission projects are under implementation
Sr. No | Project | Objective | Scope | Period
21 | Amnura 132/33 kV Grid Substation with associated 132 kV Transmission Line Project. | To evacuate power from existing 50 MW and upcoming 100 MW power plants at Amnura and to meet the growing demand of Amnura area of Chapainawabganj district. | 132 kV single circuit pole line from Rajshahi-Chapainawabganj 132 kV line to Amunra substation on single circuit pole line : 15 km (Single Grossbeak) 132/33 kV AIS substation, Double Bus Scheme with 132/33 kV, 1 x 35/50 MVA 3-Phase transformer; 132 kV Line Bay: 4 nos; 132 kV Transformer Bay: 1 no; 132 kV Coupler Bay: 1 no.; 33 kV Transformer Bay: 1 no. | FY15-FY21
22 | Western Grid Network Development Project | To establish a 230 kV transmission link between Rajshahi & Ishurdi. To establish a 132 kV transmission link between Gollamari & Gopalganj To establish a 132 kV transmission link between Bangura & Baghabari. To supply reliable power to Bangura, Satkhira & Madaripur area. To create power evacuation facilities for future generating plants at Khulna.To cater the growing demand of Barindra area (Rajshahi). To reduce the loading of the existing 132 kV Rajshahi-Natore line. To meet up the growing demand of Rangpur area. | 230 kV Transmission Line: 82.15 km 132 kV Transmission Line: 236.31 km 230 kV Substations: 2nos, 1200 MVA 132 kV Substations: 3 nos, 450 MVA 132 kV Bay Extensions: 8 nos | FY16-FY21
Source: PGCB, Deloitte Analysis

## Slide 196: Annexure G | Electricity Transmission | Ongoing Development Projects
Currently, ~25 major transmission projects are under implementation
Sr. No | Project | Objective | Scope | Period
23 | National Power Transmission Network Development Project | To evacuate power from the proposed 225MW power plant at Sikalbaha To Provide reliable power to Chittagong city through Rampur & Sikalbaha To Meet the growing load demand of the areas under the proposed new 132/33 kV substations at Agrabad (Chittagong).; Chouddagram, Ramganj, Bhaluka (Mymensingh), Baroirhat (Chittagong), Benapol, Shariatpur, Barisal-(N), Mahastangarh (Bogra), Jaldhaka (Nilfamari) & Rajshahi-2 | 230 kV double circuit Transmission Line : 69 km 230 kV u/g Line : 8 km 132 kV Four Circuit In Out Underground Line : 3 km 132 kV u/g Line : 6 km 132 kV double circuit interconnecting line : 139 km 132 kV LILO line : 14 km 230/132 kV Substation: 2 nos. 132/33 kV Substation: 11 nos. Bay Extension of existing Substations 230 kV: 4 nos 132 kV: 9 nos. | FY13-FY21
24 | 400/230/132 kV Grid Network Development Project | To evacuate power from upcoming power plant at Ghorasal. To minimize the overloading of existing Tongi-Ghorasal 230 kV transmission line To meet up upcoming demand of Ullon and Dhanmondi area. To strengthen the power supply stability, reliability & transmission capability in Ullon, Dhanmondi as well as inner of Dhaka city. To relieve the overloaded adjacent substations in different areas of the country To meet up upcoming demand of potential areas. | 230 kV GIS Switching Substation 230/132 kV Substation (2x300 MVA): 3 nos. 230/132 kV Substation (3x300 MVA): 1 no 132/33 kV Substation (2x120 MVA): 1 no 132/33 kV Substation: 11 nos. Construction of 400 kV double circuit line : 28 km Construction of 132 kV line: 358 Ckt.km. Construction of 230 kV line: 62.6 Ckt.km. Re-conductoring of 230 kV line: 54 ckt.km 132/33 kV SS Renovation: 3 nos. 132 kV bay Extension: 4 nos. 230 kV bay Extension: 6 nos | FY14-FY21
Source: PGCB, Deloitte Analysis

## Slide 197: Annexure G | Electricity Transmission | Ongoing Development Projects
Currently, ~25 major transmission projects are under implementation
Sr. No | Project | Objective | Scope | Period
25 | Enhancement of Capacity of Grid Substations and Transmission Lines for Rural Electrification. | To enhance the capacity of existing 132/33 kV substation; To increase reliability of power supply at Dhaka area and Renovation /Up-gradation of some existing transmission lines. | 132 kV double circuit line : 40 km 132 kV single circuit line on double circuit tower : 60 km 230 kV double circuit In-Out Line at proposed 230/132/33 kV Substation : 1 km Four circuit Interconnecting 132kV line with existing line to connect proposed 230/132/33 kV Substation : 3.5 km 132 kV Double Circuit In-Out Line at proposed 132/33 kV Substation : 2 km Existing 132 kV Four Circuit Line Re-routing at new 230/132 kV Substation : 2 km 230/132/33 kV Substation with 3x300 MVA transformer and 2x75 MVA transformers 132/33 kV substation with 2×75 MVA transformer 132/33 kV substation with 2×41 MVA transformer: 3 nos. 132/33 kV substation with 2×75 MVA transformer 2x75 MVA 3 phase power transformer at 132/33 kV Substation: 5 nos. Re-conductoring of 132 kV double circuit line : 229 km 132 kV single circuit stringing of existing 132 kV line : 51 km Bay Extension : 6 nos. | FY15-FY21
Source: PGCB, Deloitte Analysis

## Slide 198: Annexure H | Electricity Transmission | Planned Projects
~5 major transmission projects are planned by 2024
Sr. No | Project | Objective | Scope | Period
1 | Renovation and Capacity Enhancement of Existing Grid Substations and Transmission Lines | Upgrading the capacity of existing substations, installing capacitor banks, reconductoring and second circuit stringing of existing transmission lines. | Capacity Upgradation of Existing Substations: 18 nos Capacitor Bank at 33 kV Reconductoring of Existing 132 kV Transmission Line: 199 km Second Circuit Stringing of 132 kV Transmission Lines: 40 km 132 kV new Transmission Line: 6 km | FY20-FY23
2 | Construction of Payra - Gopalganj - Aminbazar 400kV Transmission System | To construct transmission infrastructure for evacuating proposed LNG based combined cycle 3600 MW NWPGCL power stations at Payra (Patuakhali). To enhance stability & reliability of transmission network between Central and Southwest Region. | 400kV transmission line: 490 ckt km Installation of 1000 MVA Power transformer 400 kV Bay Extension: 8 nos 230 kV Bay Extension: 2 nos | FY21-FY23
3 | Transmission Infrastructure Development Project for Southern Area of Chattogram Division & Bangabandhu Hi-Tech City at Kaliakoir | To supply power to the Bangabandhu Hi-Tech city. To ensure reliable power source to the Economic Zones of BEZA at Cox’s Bazar and Chittagong areas. To evacuate the power generated from the upcoming power plants | 230 kV GIS Substation: 2 nos 132/33 kV GIS Substation: 2 nos 230 kV line: 119 km 132 kV line: 72 km 230 kV Bay Extension: 2 nos | FY21-FY24
4 | Madunaghat-Bhulta 765 kV Transmission Line Project | To establish high capacity transmission infrastructure for evacuation of power from Chittagong to Dhaka | 765 kV line: 500 ckt. Km 400kV bay extension: 4 nos | FY21-FY24
5 | Energy Efficiency in Grid Based Power Supply (II) | To meet the growing power demand & quality improvement of DESCO & Adjacent area | 230 kV Substations: 3 nos 230 kV Transmission Lines: 9 km | FY21-FY24
Source: PGCB, Deloitte Analysis

## Slide 199: Contracts Risk Assessment

## Slide 200: Annexure I | PPA Terms
Parameter | Conditions
Term | From Project Effective Date till 22 years from COD, extendable
Proposal Security | Unconditional bank guarantee of $2,200,000 provided by Company to BPDB as guarantee to maintain its proposal until execution of project agreements
Performance Security Deposit | Unconditional bank guarantee of $36000 multiplied by contracted capacity provided by Company to BPDB. It shall terminate upon delivery of Operations Security Deposit
Operations Security Deposit | The Company shall provide Operations Security deposit to BPDB within 30 days of COD equal to 2 months of capacity charge payments.
Company Event of Default | Company Event of Default: BPDB shall give a notice of default in case of following events except when such default is caused due to breach of relevant agreements by BPDB, GOB, PGCB, Gas Supplier, Fuel Supplier, due to Force Majeure or a Political Event: Failure of the Company to maintain Performance Security until delivery of Performance Security Deposit or failure to deliver and maintain Performance Security Deposit Failure of the Company to achieve Financial Closure by Required Financial Closure Date i.e. 9 months from the Effective Date Failure of the Company to achieve Construction Start Date within 90 days from the Financial Closure Date Failure of the Company to achieve Commercial Operation Date within 12 months from the Required Commercial Operation Date Abandonment of the facility or failure of Company to complete construction of the facility for 30 consecutive days between Construction Start Date and Commercial Operation Date Failure of the Company to deliver and maintain the Operations Security Deposit within 30 days from the COD Abandonment of operations of the facility by the Company for 25 consecutive days after COD Any material breach by the Company that is not remedied in 30 days after notice from BPDB Transfer of Company's rights, obligations and the facility itself without consent from BPDB Company Event of default under Implementation Agreement, Land lease agreement, Gas Supply Agreement or Fuel Supply Agreement unless waived by third party or cured Failure of the Company to make payments within 30 days from the due date except when security is available Failure of the Company to achieve Dependable Capacity greater than/equal to threshold capacity (Rectification period of 18 months allowed)

## Slide 201: Annexure I | PPA Terms
Parameter | Conditions
BPDB Event of Default | BPDB Event of Default: Company shall give a notice of default in case of following events except when such default is caused due to breach of any of the project agreements by the Company or due to Force Majeure or a Political Event: Dissolution of BPDB except for privatization or amalgamation/restructuring/reorganization/corporatization provided a reasonable guarantee to the performance of the succeeding entity and all BPDB's obligations have been assigned to the new entity Failure of BPDB in making payments within 30 days from the due date Any event of default by GOB, Gas Supplier, Fuel Supplier or BPDB under their respective agreements Any material breach by BPDB that is not remedied in 30 days after notice from the Company Failure of BPDB to permit commissioning or testing of the facility within 30 days from schedule Failure of BPDB to establish and maintain letter of credit Failure of BPDB to return any undrawn Proposal Security or Performance Security Deposit within 3 days after the required date Incorrect statements, representations, warranties Change in Law making execution unlawful/unenforceable
Obligation upon termination | Upon termination, if the facility is transferred to GOB or its assignee, the Company shall have no obligations except those which arose before termination In case of company event of default, the transfer to facility to GOB and payment of amount due shall constitute the liquidated damages to BPDB In case of the agreement is terminated due to the Company's inability to achieve Financial Closure by Required Financial Closure Date, BPDB may draw upon the Proposal Security
Dispute Resolution | Either party can give a written notice to the other for any dispute, along with description. Failing to resolve the dispute amicably within 30 days, the dispute shall be settled through referral to CEO and the designated representative of BPDB. After the expiry of 15 days from such referral, if the dispute is not settled, it will be referred to an Expert. In case the recommendation of the Expert is not acceptable to either party, it can initiate arbitration proceedings
Representation and warranties | It is a valid company existing under the laws of Bangladesh Execution of obligations under this agreement do not require any further approvals from the Board/Shareholders/Partners Execution of obligations under this agreement will not violate or breach any provisions of the company charter/bylaws/agreements/rules/regulations etc. There is no pending or, to the best of the company’s knowledge, threatened action or proceeding against the Company before any court, Government Authority or Arbitrator
Decision Making | 6 Member Joint Coordinating Committee consisting of members from BPDB (2), PGCB (1) and the Company (3). All decisions to be taken by majority and should be accepted by each party.

## Slide 202: Annexure I | PPA Terms
Parameter | Conditions
Point of Delivery - Power | Point of delivery will be high voltage side of the 230 kV step-up transformer. The Company will construct a 230 kV switchyard at its own cost
Rights and remedies in the event of default | Upon event of default, the non-defaulting party can choose to terminate this agreement by delivering a Notice of Intent to Terminate, specifying in reasonable detail the event of default Following the delivery of Intent to Terminate, the parties shall consult in good faith to remedy the default: a) 45 days: in case of default on payments or security b) 90 days: in any other event of default, or even longer duration of consulting in mutual agreement Notwithstanding the consulting, the defaulting party must undertake efforts to cure the default. In case the default is cured before the delivery of termination notice, the non defaulting party shall have no right to terminate At the expiry of the consultation period, if the default is not remedied or the parties have not reached an agreement, the non-defaulting party may deliver a Termination Notice to the other party BPDB shall not seek to terminate this Agreement without first giving a copy of the notices to the Lenders along with a request to cure the default within the cure period. No such termination will be valid till the expiration of: a) Initial Cure Period b) An Evaluation Period subsequent to expiry of the initial cure period - Earlier of delivery of Election notice by the Lenders to BPDB or 30 days from expiration of Initial Cure Period. Upon delivery of Election Notice, Lenders have a period of 180 days to cure any Company Event of Default c) Lenders Cure Period - Period during which the Lenders either attempt to procure the cure of such default or enforce their rights under the Financing Documents The Company shall not seek to terminate this Agreement without first giving a copy of the notices to GOB along with a request to cure the default within the cure period. No such termination will be valid till the expiration of the cure period. If at the expiry of the cure period, if GOB is diligently attempting to remedy the default, other than a payment default, an additional period of 90 days will be provided
Taxes and Claims | The Company shall be responsible for payment of all statutory taxes, levies, duties, royalty, fees and any kind of levies imposed/charges by GoB for construction and operation of the facility except those charges which are exempt/reimbursible by BPDB under the Implementation Agreement
Governing Law | Rights and obligations of the parties shall be interpreted, construed and governed by the laws of England and Wales

## Slide 203: Annexure I | PPA Terms
Parameter | Conditions
Liquidated Damages | Delay in Commercial Operation - LD = USD 100 x Contracted Capacity x no of days (beyond Required COD); subject to a cap of 365 days of damages Failure to meet Contracted Capacity - If Initial Dependable Capacity < Contracted Capacity, LD = USD 1000 x KW difference; capped of 10% of Contracted Capacity Forced Outages - If Equivalent Forced Outage Energy (a) + Maintenance Outage Energy (b)+ Scheduled Outages Energy (c)> Average Dependable Capacity x 1376 hours for gas operation (or 1580 hours for Fuel Oil Operation) in every third contract year or 876 hours for gas operation (or 1190 hours for Fuel Oil Operation) in every other contract year (d) , LD = Capacity Factor (i.e. Average Capacity Price x 1.522) x (a + b + c - d) Declaration and Delivery of Available Capacity If the company notifies a Revised Declared Capacity which does not result due to Force Majeure Event or BPDB/PGCB/Gas Supplier/Fuel Supplier/GOB, LD is applied in case of downward revisions in Declared Capacity if revision is made less than 12 hours prior to the day when such revision is to be implemented. In case of upwards revision in declared capacity, If the Company fails to comply with the despatch instruction which is not due to Force Majeure Event or BPDB/PGCB/Gas Supplier/Fuel, LD = 100% x difference between declared capacity and available capacity x Applicable Relevant Capacity Price Security Deposits Proposal Security - Shall terminate upon submission of Performance Security Deposit Performance Security Deposit (PSD) - a) Shall terminate upon delivery of Operations security deposit to BPDB, any undrawn portion should be returned to the Company no later than 5 days following the delivery of operations security deposit. b) The term should not extend more than 30 days after the supply commencement date c) The Performance Security deposit can be can be encashed by BPDB to satisfy any obligation of the company when in effect. Upon termination of PPA due to company event of default, the Performance Security Deposit can be forfeited without any notice. d) If prior to COD, the PSD will expire in 30 days and is not renewed by the Company for atleast 3 months, BPDB may encash the deposit in full Operations Security Deposit: The Company shall provide Operations Security deposit to BPDB within 30 days equal to 2 months of capacity charge payments. The Operations Security Deposit should be an unconditional irrevocable BG. The Operations Security deposit may be applicable to payment of LD and accrued interest thereon or Payment of other damages, interest or other amounts that the Company shall be required to pay

## Slide 204: Annexure I | PPA Terms
Parameter | Conditions
Liquidated Damages | Termination of the Agreement BPDB shall be entitled to retain or collect any damages due to the Company, unless not otherwise paid, from the Performance Security Deposit or the Operations Security Deposit Remainder of the Performance Security Deposit or the Operations Security Deposit shall be paid to the Company within 10 business days Procedural Provisions of the Performance and Operations Security Deposit: The Deposits shall have a term of not less than 365 days. Not less than 30 days before expiration should the Deposit’s validity be extended for not less than 12 months. If at any time there remains less than 20 days for the validity of the security deposit, BPDB may encash the then existing Security Deposit in full, provided that: a) Any amounts drawn in these circumstances shall be deposited in a separate bank account established with such bank account as is notified by BPDB to the company b) BPDB may make withdrawals from such bank account only in such amounts and circumstances as contemplated by this Agreement c) If the company provides a Deposit of an amount greater than or equal to required, BPDB shall return the encashed amount to the Company Payment - Damages should be paid within 25 days of LD notice
Alternate Fuels | The preferred fuel for operation will be Gas. In case of a Gas Supplier Force Majeure Event or a Political Event, the Company should promptly inform BPDB and the Other Fuel Notice Parties of such an Event. Within 5 days of receipt of notice, BPDB shall decide to: a) Switch from Gas to Other Fuel b) Cease operations and specify whether the Company should use any remaining fuel oil at the facility In case of such an event, the Company will first procure fuel oil for 15 days supply for continuous operation of the facility at 80% dependable capacity (three days supply in case the event occurs before COD) Once the Force Majeure Event/ Political event has passed, the Gas Supplier will serve a Cessation Notice following which the Company shall cancel any outstanding fuel orders within 2 days of receipt of such notice. The canceled outstanding Fuel Oil will be required to be supplied by the Fuel Supplier to BPDB who shall indemnify the Company for loss due to such diverted fuel oil. Any excess store of fuel oil of more than 3 days requirement will be utilized to generation till the stock reduces to 3 days worth of requirement.

## Slide 205: Annexure I | PPA Terms
Parameter | Conditions
Billings and Payment | The Company shall raise invoices monthly, no later than 7 days after end of month with a due date of 30 days for BPDB to make the payment. If the Company fails to receive the payment by due date, it can draw any the expected amount from the BPDB Letter of Credit (LC) Payment Dispute: Invoices should be disputed within 180 days and after dispute resolution the disputed amount shall be paid within 3 business days Letter of Credit (LC): On the Commercial Operation Date, BPDB shall issue revolving LC for period more than 1 year, to be extended 30 days prior to term expiration, and to be reinstated within 15 days after withdrawal from company. LC amount will be recalculated and adjusted by BPDB within 90 days in case of Gas to Fuel Switch Decision. Upon improper drawing, the Developer shall pay the amount plus interest of bank rate plus 2% p.a., compounded semi-annually Termination of Agreement: within 10 days of termination of PPA, the Company shall return any then-outstanding LC
Force Majeure | Every party can claim relief in relation to a force majeure event in regard to its obligations under the PPA except payments to be made under the agreement Force Majeure shall include outages due to the Electrical Transmission facilities and Grid System In case of partial operation during FM event, BPDB will pay the Company Energy Payment for Net Energy Output and Capacity Payments based on the ratio of dependable capacity (FM Ratio) In case of Gas Suppliers Failure, the FM ratio will be considered as 1
Political Event | Every party can claim relief in relation to a force majeure event in regard to its obligations under the PPA except payments to be made under the agreement No payments shall be made by either party affected by a force majeure event for the period of such event on account of its inability to perform its obligations under force majeure event Political event includes gas and fuel suppliers inability to supply gas/fuel but does not include failure of gas transportation facilities In case of partial operation during Political event, BPDB will pay the Company Energy Payment for Net Energy Output and Capacity Payments based on the ratio of dependable capacity (PE Ratio) The Company will be entitled to receive a supplemental tariff for PE other than Change in Law to recover any restoration costs In case of change in law, the Company will be entitled to supplemental tariff to recover costs of material capital additions and operating costs
Sale to third parties | Sale to third parties is not allowed except with prior written consent from BPDB
Operational Norms | The company must operate the plant as per the Technical specifications provided in the PPA and Prudent Utility Practices

## Slide 206: Annexure I | PPA Terms
Parameter | Conditions
Tariff | Reference Tariff = Reference Capacity Price + Reference Energy Price Capacity Payment based on dependable capacity a) Non Escalable Capacity Price - Reference rate x Exchange Rate x (ratio of dependable capacity x hours/total hours) b) Foreign Escalable Capacity Price - Reference rate x Exchange Rate x Foreign Inflation Index Factor x (ratio of dependable capacity x hours/total hours) c) Local Escalable Capacity Price - Reference rate x Local Inflation Index Factor x (ratio of dependable capacity x hours/total hours) Energy Payment based on Net Energy Output a) Foreign Variable O&M Price - Reference rate x Exchange Rate x Foreign Inflation Index Factor x Net Energy Output (kWh) in half hourly interval x number of intervals x power factor adjustment b) Local Variable O&M Price - Reference rate x Local Inflation Index Factor x Net Energy Output (kWh) in half hourly interval x number of intervals x power factor adjustment c) Gas/ Fuel Oil Price based on Reference Heat Rates - Fuel Oil: Price paid to supplier + taxes/duties paid by the company + freight, ocean loss, insurance, port dues, LC, handling loss etc.; Gas: Gas Price as per GSA based on energy sent out and Station Heat Rate + all transportation charges + taxes Only energy charge will be paid for any energy sent out during testing and commissioning

## Slide 207: Annexure J | GSA Terms
Parameter | Conditions
Obligation | The company agrees to purchase and the supplier agrees to supply gas to meet the facility's requirement The company will not use gas other that that supplied by the supplier except and to the extent the gas is not available at the Point of Delivery Gas supplied will be subject to Maximum Hourly Quantity and shall not exceed Daily Contract Quantity In case the Btu is different from 950 Btu (HHV), the Maximum Hourly Quantity and Daily Contract Quantity will be adjusted accordingly. The Btu should not be less than 900 Btu per Standard Cubic Foot
Failure at Point of Delivery | Before/during commissioning period: Failure of gas to flow across point of delivery due to following will not be considered suppliers default a) Malfunction of suppliers equipment including transportation facility b) Breach of agreement by supplier c) Gas Supplier Event of Default
Operations | At least 3 months prior to Commissioning Period Start Date, the parties will mutually prepare operating procedures. The procedures should be available at least 20 days prior to the Scheduled Commissioning Period Start Date Either party may, from time to time, request revisions to the Operating procedures on mutual consent
Transportation Facility | The transportation facility including the RMS will be constructed and operated by the Supplier and all related costs will be borne by the Company including 5% consultancy fee to the supplier (Upstream of Point of Delivery) Land for the pipeline will be acquired by the Supplier with assistance from the Company If construction is not completed before 30 days prior to the Scheduled Commissioning Period Start Date due to Supplier's failure, Supplier FM or PE, the period will be extended on a day to day basis Following commissioning of transport facilities, its ownership shall be conveyed to the Supplier, who shall undertake all O&M and bear costs thereof The Company shall install and operate Company Transmission Facility to connect to the point of delivery (downstream from Point of Delivery)
Dispute Resolution | Either party can give a written notice to the other for any dispute, along with description. Failing to resolve the dispute amicably within 30 days, the dispute shall be settled through referral to CEO and the designated representative of the supplier. After the expiry of 15 days from such referral, if the dispute is not settled, it will be referred to an Expert. In case the recommendation of the Expert is not acceptable to either party, it can initiate arbitration proceedings In case of dispute between parties as to quantity of gas delivered which cannot be solved mutually, may be referred to an Expert

## Slide 208: Annexure J | GSA Terms
Parameter | Conditions
Company event of default | Supplier shall give a notice of termination in case of following events except when such default is caused due to breach of relevant agreements by BPDB, GOB, PGCB, Gas Supplier, Fuel Supplier, due to Force Majeure or a Political Event: Assignment of Agreement by the Company without written consent of the supplier Occurrence of a Company Event of Default under the Implementation Agreement Winding up, liquidation, bankruptcy of the Company Any material breach by the Company that is not remedied in 30 days after notice from supplier Incorrect statements, representations, warranties Failure of the Company to make payments due under the agreement within 35 days of receiving notice
Gas Supplier event of default | Company shall give a notice of default in case of following events except when such default is caused due to breach of any of the project agreements by the Company or due to Force Majeure or a Political Event: Assignment of Agreement by the supplier in contravention with the provisions of assignment under the agreement Dissolution of the supplier except for privatization or amalgamation/restructuring/reorganization/corporatization provided a reasonable guarantee to the performance of the succeeding entity and all supplier's obligations have been assigned to the new entity Any event of default by GOB, Fuel Supplier or BPDB under their respective agreements Failure of the supplier to commission the transport facility within 30 days after the Required COD Any material breach by BPDB that is not remedied in 30 days after notice from the Company Failure of the Gas Supplier to deliver an aggregate amount of Gas greater than 50% of the aggregate amount of gas shown in the gas order in any 12 month period Incorrect statements, representations, warranties Change in Law making execution unlawful/unenforceable
Rights and remedies in the event of default | Upon event of default, the non-defaulting party can choose to terminate this agreement by delivering a Notice of Termination, specifying in reasonable detail the event of default Following the delivery of Intent to Terminate, the parties shall consult in good faith to remedy the default: a) 45 days: in case of default on payments b) 90 days: in any other event of default, or even longer duration of consulting in mutual agreement Notwithstanding the consulting, the defaulting party must undertake efforts to cure the default. In case the default is cured before the delivery of termination notice, the non defaulting party shall have no right to terminate

## Slide 209: Annexure J | GSA Terms
Parameter | Conditions
Rights and remedies in the event of default | At the expiry of the consultation period, if the default is not remedied or the parties have not reached an agreement, the non-defaulting party may terminate the agreement by giving notice to the other party and their lenders In case the agreement is terminated before COD due to Company Event of Default, the Company shall reimburse the gas supplier for all expenses incurred for procurement of easements rights, design and construction of interconnection facilities etc. Supplier shall not seek to terminate this Agreement without first giving a copy of the notices to the Lenders along with a request to cure the default within the cure period. No such termination will be valid till the expiration of: a) Initial Cure Period b) An Evaluation Period subsequent to expiry of the initial cure period - Earlier of delivery of Election notice by the Lenders to the supplier or 30 days from expiration of Initial Cure Period. Upon delivery of Election Notice, Lenders have a period of 270 days to cure any Company Event of Default c) Lenders Cure Period - Period during which the Lenders either attempt to procure the cure of such default or enforce their rights under the Financing Documents
Obligation upon termination | Upon termination by the Gas supplier, if the facility is transferred to GOB or its assignee, the Company shall have no obligations except those which arose before termination In case of company event of default, the transfer to facility to GOB and payment of amount due shall constitute the liquidated damages to the supplier
Termination | Company/supplier event of default not remedied. The Gas Supplier can only terminate the agreement with prior consent from GOB Force Majeure or Political Event of more than 12 months
Force Majeure | Every party can claim relief in relation to a force majeure event in regard to its obligations under the agreement No payments shall be made by either party affected by a force majeure event for the period of such event on account of its inability to perform its obligations under force majeure event. However, the supplier will not be excused from making payments due to the company under the agreement In case a Force Majeure event affects BPDB, GOB, PGCB, fuel supplier or gas supplier under the applicable agreements rendering the Company unable to perform its obligations, the Company will not be liable for such delay In case of a Gas Supplier Force Majeure Event, the gas supplier needs to inform BPDB who will decide whether to cease operations of the plant or switch operations to fuel oil
Political Events | Every party can claim relief in relation to a force majeure event in regard to its obligations under the PPA No payments shall be made by either party affected by a force majeure event for the period of such event on account of its inability to perform its obligations under force majeure event. However, the supplier will not be excused from making payments due to the company under the agreement

## Slide 210: Annexure J | GSA Terms
Parameter | Conditions
Political Events | In case a Political event affects BPDB, GOB, PGCB, fuel supplier or gas supplier under the applicable agreements rendering the Company unable to perform its obligations, the Company will not be liable for such delay Political event includes gas and fuel suppliers inability to supply gas/fuel but does not include failure of transportation facilities In case of a Gas Supplier Political Event, the gas supplier needs to inform BPDB who will decide whether to cease operations of the plant or switch operations to fuel oil
Liquidated Damages | Payable by Gas Supplier: Applicable in case failure of supplier to deliver gas due to transportation facilities failure other than due to Force Majeure or a Political Event, LD = amount that would have been received by the Company from BPDB has the gas supply not been interrupted except energy charges (i.e. Capacity Charges) + any liquidated damages payable by the Company under the PPA Payable by the Company: 1. If Scheduled outages + maintenance outages + forced outages + Delay lost energy > Threshold level (876 hours or 1376 hours for major maintenance years) The parties owing the liquidated damages shall pay the amount within 25 days
Company representation and warranties | It is a valid company existing under the laws of Bangladesh There is no pending or, to the best of the company’s knowledge, threatened action or proceeding against the Company before any court, Government Authority or Arbitrator Procure and maintain all consents and approvals required for performance under the agreement
Quality | The supplier shall deliver gas in accordance with the quality specifications and max/min pressure specified in the agreement The Company can reject delivery of gas in case it doesn’t conform with the gas specifications. Till such time that the gas fully conforms to the specifications, the non-conforming shall be deemed to not have been tendered The Company also has the option to accept non conforming gas, without any subsequent liability of the supplier
Pricing | Price - as per the Published Gas Price. In case Published Gas Price is not available, parties may mutually decide on an alternate index within 15 days of discontinuance to the Published Gas Price, otherwise the matter will be referred to an Expert Price Adjustment - Invoice amount will be adjusted to accommodate the deviations from 950 Btu per cubic foot The price will be paid including all delivery, transportation charges and taxes payable Amount paid during any month will be equal to the prevailing gas price multiplied by the number of MSCF of gas delivered

## Slide 211: Annexure J | GSA Terms
Parameter | Conditions
Billing and Payment | The Supplier shall raise invoices monthly, on or after 7 days after end of month with a due date of 32 days for the Company to make the payment. No dispute can be raised by the Company for a meter inaccuracy of less than 2% Late Payment - Interest payable at Bangladesh Bank Rate plus 2% per annum Payment Dispute: Invoices should be disputed within 180 days and after dispute resolution through an Expert or arbitration, the disputed amount shall be paid within 3 business days The supplier may suspend delivery if the undisputed amount remains unpaid for 3 days unless the company provides a Letter of Credit for an amount equal to 1.5 times the invoice amount with a validity of 60 days. The supplier may suspend delivery and encash LC if amount remains unpaid for 45 days after invoice date

## Slide 212: Annexure K | FSA Terms
Parameter | Conditions
Obligation | The company agrees to purchase and the supplier agrees to supply fuel to meet the facility's requirement The facility shall operate on Gas and to the extent gas is not available, it shall operate on fuel oil The supplier shall deliver fuel at the Receiving Point Failure to supply fuel shall not constitute a breach if damages are paid to the Company under the FSA and PPA (paid by company)
Quality | The supplier shall deliver fuel in accordance with the quality specifications specified in the agreement The quality shall be inspected by the Company The Company can reject delivery of fuel in case it doesn’t conform with the gas specifications. Till such time that the fuel fully conforms to the specifications, the non-conforming fuel shall be deemed to not have been tendered. Company cannot reject delivery if it doesn’t conform to the specification of LHV, unless the deviation is such that the fuel cannot be used in the facility The Company also has the option to accept non conforming fuel, without any subsequent liability of the supplier Testing of fuel oil delivered will be according to the operational procedures The fuel supplier will test the fuel before loading for transport (in case of transportation by water) and send a Sample Certification to the Company within 2 days of receipt of such oil
Transportation Facility | The receiving point for the fuel transported by water vessel shall be the discharge flange of loading jetty located at Barisal/Jhalakati Depot of the fuel supplier The fuel supplier shall be responsible for all facilities upstream of and for transportation of fuel oil to the Receiving Point The Company shall be responsible for all facilities downstream of the Receiving Point and for transportation and delivery of fuel oil from the Receiving Point to the facility The company will install and maintain the Company receipt and storage facilities for storing and utilizing the fuel oil The fuel supplier will ensure that it has all equipment and facilities ready for first delivery of fuel at the Initial Delivery Date (i.e. 18 months or more from the Project Effective Date).
Quantity | On receipt of Fuel Supplier Switch Order in case of Gas Supplier Force Majeure/Political Event/ Supply Failure, the supplier will have up to 90 days to commence deliveries of Fuel Oil and an additional 15 days to deliver fuel oil in an amount equal to the applicable fuel oil storage quantity Failure to complete delivery within the stipulated time will attract liquidated damages The Company may amend its fuel order 15 days prior to start of the relevant month Any updward adjustments less than 15 days prior to the relevant month up to 10% will be complied with by the fuel supplier. Fuel supplier shall use reasonable efforts to supply fuel in excess of 10% where required. At any time, the Company shall maintain at least 3 days fuel oil storage quantity except in cases of Force Majeure, Political Event, or default by GOB/BPDB/PGCB/Gas supplier or fuel supplier

## Slide 213: Annexure K | FSA Terms
Parameter | Conditions
Pricing | Price will be based on Reference Fuel establish by GOB which may include fixed selling price, Gross Margin, refinery price, inland freight margin, statutory development surcharge and duties, and any change therein
Billing and Payment | The supplier shall submit an invoice atleast 10 days prior to delivery at Receiving Point based on liter quantity. The Company is required to make payment against the invoice no later than 3 days prior to delivery Any dispute regarding the quantity of fuel oil delivered will be resolved as per the methodology for dispute resolution
Company representation and warranties | It is a valid company existing under the laws of Bangladesh There is no pending or, to the best of the company’s knowledge, threatened action or proceeding against the Company before any court, Government Authority or Arbitrator Procure and maintain all consents and approvals required for performance under the agreement
Operations | The parties will collectively appoint: a) Operational Coordinators - Responsible for day to day implementation of operating procedures b) Regional Coordinators - Responsible for operational and implementation of agreement at district/regional level c) Principle Coordinators - Responsible for supervision of all aspects of the agreement and dealing with matters related to pricing and policy Atleast 6 months prior to the Initial Delivery Date, Operational Procedures shall be mutually prepared or prepared through an expert atleast 3 months prior to the Initial Delivery Date in case of disagreement between the parties
Dispute Resolution | Either party can give a written notice to the other for any dispute, along with description. Failing to resolve the dispute amicably within 30 days, the dispute shall be settled through referral to CEO and the designated representative of the supplier. After the expiry of 15 days from such referral, if the dispute is not settled, it will be referred to an Expert. In case the recommendation of the Expert is not acceptable to either party, it can initiate arbitration proceedings Seat of all arbitration proceedings will be in Singapore
Company event of default | Supplier shall give a notice of termination in case of following events except when such default is caused due to breach of relevant agreements by BPDB, GOB, PGCB, Gas Supplier, Fuel Supplier, due to Force Majeure or a Political Event: Assignment of Agreement by the Company without written consent of the supplier Occurrence of a Company Event of Default under the Implementation Agreement Winding up, liquidation, bankruptcy of the Company Any material breach by the Company that is not remedied in 30 days after notice from supplier Failure of the Company to make payments due under the agreement within 35 days of receiving notice

## Slide 214: Annexure K | FSA Terms
Parameter | Conditions
Fuel Supplier event of default | Company shall give a notice of default in case of following events except when such default is caused due to breach of any of the project agreements by the Company or due to Force Majeure or a Political Event: Assignment of Agreement by the supplier in contravention with the provisions of assignment under the agreement Dissolution of the supplier except for privatization or amalgamation/restructuring/reorganization/corporatization provided a reasonable guarantee to the performance of the succeeding entity Any event of default by GOB, Gas Supplier or BPDB under their respective agreements Any material breach by BPDB that is not remedied in 30 days after notice from the Company Failure of the Fuel Supplier to deliver an aggregate amount of Fuel greater than 50% of the aggregate amount of gas shown in the gas order in any 12 month period
Rights and remedies in the event of default | Upon event of default, the non-defaulting party can choose to terminate this agreement by delivering a Notice of Termination, specifying in reasonable detail the event of default Following the delivery of Intent to Terminate, the parties shall consult in good faith to remedy the default: a) 45 days: in case of default on payments b) 90 days: in any other event of default, or even longer duration of consulting in mutual agreement Notwithstanding the consulting, the defaulting party must undertake efforts to cure the default. In case the default is cured before the delivery of termination notice, the non defaulting party shall have no right to terminate At the expiry of the consultation period, if the default is not remedied or the parties have not reached an agreement, the non-defaulting party may terminate the agreement by giving notice to the other party and their lenders In case the agreement is terminated before COD due to Company Event of Default, the Company shall reimburse the fuel supplier for all expenses incurred for design and construction of any facilities etc. Supplier shall not seek to terminate this Agreement without first giving a copy of the notices to the Lenders along with a request to cure the default within the cure period. No such termination will be valid till the expiration of: a) Initial Cure Period b) An Evaluation Period subsequent to expiry of the initial cure period - Earlier of delivery of Election notice by the Lenders to the supplier or 30 days from expiration of Initial Cure Period. Upon delivery of Election Notice, Lenders have a period of 180 days to cure any Company Event of Default c) Lenders Cure Period - Period during which the Lenders either attempt to procure the cure of such default or enforce their rights under the Financing Documents
Obligation upon termination | Upon termination by the Fuel supplier, if the facility is transferred to GOB or its assignee, the Company shall have no obligations except those which arose before termination In case of company event of default, transfer of facility to GOB and payment of amount due shall constitute liquidated damages

## Slide 215: Annexure K | FSA Terms
Parameter | Conditions
Liquidated Damages | Payable by Fuel Supplier before COD: Applicable in case failure of supplier to deliver fuel before the COD other than due to Force Majeure or a Political Event which results in a delay in the Scheduled COD or commissioning of the facility, LD = Carrying cost + 100% of escalable capacity based on dependable capacity being assumed equal to the contracted capacity for the period of delay +Total amount of principle repayment to be made by the Company on the next scheduled repayment date/ the number of days in beginning on the previous scheduled principle repayment date (or in case of 1st principle repayment, beginning on Scheduled COD) and ending on the first scheduled principle repayment date (which will be returned by the Company after COD) + Any liquidated damages paid by the Company Payable by the Supplier after COD: In case of Supplier's failure to deliver fuel after COD, LD = amount that would have been received by the Company from BPDB had the fuel supply not been interrupted except energy charges (i.e. Capacity Charges) + any liquidated damages payable by the Company under the PPA Payable by the Company for failure to accept delivery: Unless the failure is due to Force Majeure, Political Event or failure of supplier to to deliver fuel that meets the specifications of the agreement, LD = difference between the amount which would have been paid by the company to the supplier and the price recovered by the supplier by selling the rejected fuel to an alternate buyer
Force Majeure | Every party can claim relief in relation to a force majeure event in regard to its obligations under the agreement No payments shall be made by either party affected by a force majeure event for the period of such event on account of its inability to perform its obligations under force majeure event. However, the supplier will not be excused from making payments due to the company under the agreement In case a Force Majeure event affects BPDB, GOB, PGCB, fuel supplier or gas supplier under the applicable agreements rendering the Company unable to perform its obligations, the Company will not be liable for such delay In case of Fuel Supplier FM event, the supplier will provide a notice to other Fuel Notice Parties
Political Events | Every party can claim relief in relation to a force majeure event in regard to its obligations under the PPA No payments shall be made by either party affected by a force majeure event for the period of such event on account of its inability to perform its obligations under force majeure event. However, the supplier will not be excused from making payments due to the company under the agreement In case a Political event affects BPDB, GOB, PGCB, fuel supplier or gas supplier under the applicable agreements rendering the Company unable to perform its obligations, the Company will not be liable for such delay Political event includes fuel suppliers inability to supply gas/fuel including failure of transportation facilities In case of Fuel Supplier Political event, the supplier will provide a notice to other Fuel Notice Parties

## Slide 216: Annexure K | FSA Terms
Parameter | Conditions
Termination | Company/supplier event of default not remedied. The Fuel Supplier can only terminate the agreement with prior consent from GOB Force Majeure or Political Event of more than 12 months. Fuel supplier shall not terminate this agreement unless the IA is also terminated
Governing Law | Rights and obligations of the parties shall be interpreted, construed and governed by the laws of England and Wales

## Slide 217: Annexure L | O&M Agreement Terms
Parameter | Conditions
Obligations of the Operator | The agreement will take effect in phases Phase 1 a) Mobilization Plan to be prepared within 6 months from the effective date b) Initial Staffing Plan c) Identification of facility manger within 3 months from the effective date d) Deployment of facility personnel atleast 3 months before the COD e) Provide pre COD, preparatory and assistance services f) O&M program atleast 90 days before the Scheduled COD g) Preparation of O&M procedures atleast 30 days prior to phase 2 h) Organize training program of facility personnel i) Obtain necessary permits and insurance j) Provide technical advice to the owner k) Develop accounting policies and procedures l) Develop purchasing policies and procedures Phase 2 a) Attempt to maximum operational life of the units b) Attempt to minimize unscheduled outages c) Maintain the facility d) Attempt to minimize Auxiliary Power Consumption and Heat Rate e) Minimize take or pay obligations under the fuel/gas supply agreements f) Maintain facility in a manner so as to achieve Dependable Capacity as defined in the PPA 3. Development of an Annual Operation Plan including annual budget, Scheduled Outages, 4. Perform Scheduled outages in accordance with the OEM specifications and coordinate with BPDB, fuel/gas supplier 5. Perform Unscheduled outages, approval from Owner required for any work that costs more than USD 25,0000 6. The Operator may subcontract part of the work
Obligations of the Owner | Provide the operator with Plant Equipment Manual, as built designs and other such information Procure adequate quantity and quality of fuel oil Acquire necessary permits/ approvals Pay property tax and VAT Provision of essential utilities

## Slide 218: Annexure L | O&M Agreement Terms
Parameter | Conditions
Obligations of the Owner | Open and maintain a Major maintenance reserve account to fund necessary costs of Major Maintenance Procuring necessary spare parts/consumables Make timely payments to the operator
Fees | Base Fees a) Period 1 - Only reimbursement of expenses incurred b) Period 2 - Monthly fee of Tk 11.50 Mn escalated by 5% annually plus VAT thereon Any reimbursable expenses
Billing and Payment | The Operator will raise in invoice within 5 days of every month Payments by the Owner should be made within 30 days Late Payment - If an invoice remains unpaid for 60 days, interest @ 5% needs to be paid
Liquidated Damages | By the Operator: a) For exceeding Forced outages, Maintenance outages and scheduled outages, LD = As per PPA subject to a limit of 10% of base fee b) Downward revision of base capacity, LD = As per PPA subject to a limit of 10% of base fee c) Facility heat rate > Guaranteed test heat rate, LD = Payment for excess fuel used subject to a limit of 20% of base fee Maximum limit of liability = 30% of base fee
Insurance | Operator shall maintain a Workers compensation Insurance Operator shall ensure that all subcontractors maintain necessary insurances as per the agreement
Force Majeure & Political Event | Every party can claim relief in relation to a force majeure event in regard to its obligations under the agreement No payments shall be made by either party affected by a force majeure event for the period of such event on account of its inability to perform its obligations under force majeure event. However, any party will not be excused from making payments due to the company under the agreement No party can claim any loss suffered due to Force Majeure Affected party shall give notice within 3 days

## Slide 219: Annexure L | O&M Agreement Terms
Parameter | Conditions
Operators Event of Default | Operators Event of Default: The Owner shall send a Notice of Default except when such default is caused due to breach of relevant agreements the owner or Force Majeure or an Emergency: Contracted capacity falls below Threshold capacity Failure of the operator to maintain the facility as per Prudent Utility Practices not remedied within 30 days Failure of the operator to maintain necessary insurance or permits Failure of the operator to meet payment obligations Abandonment of the facility by the operator for 7 days after COD Any material breach not remedied within 30 days Inability to meet operating parameters of the facility for a continuous period of 18 months Winding up, liquidation, bankruptcy of the Company Incorrect statements, representations, warranties
Owners Event of Default | Owners Event of Default: The Operator shall send a Notice of Default, except when such default is caused due to breach of relevant agreements by the Operator: Failure to make payments for a period of 6 months Bankruptcy/insolvency/liquidation of the owner
Rights and remedies in the event of default | If the default is not cured within 45 days of notice of default, the non affected party may terminate the agreement
Termination | Event of default not cured within 45 days If the facility ceased operation (no damages need to be paid by the Owner) Force Majeure for more than 6 months Termination by mutual consent Expropriation/nationalization of the facility
Dispute Resolution | Each party shall nominate an authorized representative for resolution of disputes. If the dispute cannot be resolved, it shall be referred to Senior Representatives of the parties In case of failure to resolve dispute, the parties have the right to arbitration subject to laws of India
Governing Law | Rights and obligations of the parties shall be interpreted, construed and governed by the laws of Bangladesh

## Slide 220: Annexure M | Implementation Agreement Terms
Parameter | Conditions
Government Authorizations | Within 60 days of execution of IA, the company shall make application for all Government Authorizations in Schedule 1 Notice for any deficiency in application will be sent by the relevant authority within 7 days of receiving the application, otherwise the application will be deemed to be complete In case of Lapse of Consent, the GOB will make all reasonable efforts to expedite the considerations of the company's application Remedy for Government Non-performance - If any Government Authorization is not received within the time prescribed in the IA, then the Required Financial Closing Date and the Required Commercial Operation Date shall be extended on a day-to-day basis If the Government Authorizations are not issued/renewed within 6 months following the time prescribed in the IA, then the Company has the right to terminate the agreement. Upon termination of this agreement, GOB will obtain an unconditional agreement from BPDB, Fuel Supplier, Gas Supplier and PGCB for termination of their respective agreements
Interconnection Facilities | The company will be responsible for construction and operation of the switchyard adjacent to the power plant and the interconnecting equipment. The Interconnection facilities (including an existing 230 kV line and a 230 kV switchyard) are already in place owned by PGCB PGCB shall at its own cost construct and commission the ITF one month prior to the Scheduled COD The ITF completion date as above shall be extended on a day for day basis in case completion is delayed due to Force Majeure or failure on part of the Company In case delay in construction of ITF leads to a delay in COD, a) Scheduled COD shall be extended b) After Scheduled COD, PGCB shall pay to the Company LD = Carrying Cost + 100% of Escalable Capacity Payment which would have been paid in case there was no delay based on contracted capacity + Total amount of principle repayment to be made by the Company on the next scheduled repayment date/ the number of days in beginning on the previous scheduled principle repayment date (or in case of 1st principle repayment, beginning on Scheduled COD) and ending on the first scheduled principle repayment date (which will be repaid by the Company after COD)
Acquisition of shares capital | GOB, BPDB, Gas Supplier, Fuel Supplier or any other Government Authority will not own/control more tan 26% of the ordinary share capital of the company The Initial Shareholders (i.e. Shapoorji Pallonji Infrastructure Capital Company Private Limited) will not transfer shares such that they own less than 51% of the Ordinary Share Capital prior to 6 years following COD, except when: a) In National Interest b) With prior approval from GOB c) As part of public offering

## Slide 221: Annexure M | Implementation Agreement Terms
Parameter | Conditions
Force Majeure | Every party, other than GOB and PGCB, can claim relief in relation to a force majeure event in regard to its obligations No payments shall be made by either party affected by a force majeure event for the period of such event on account of its inability to perform its obligations under force majeure event. However, any party will not be excused from making payments due to the company under the agreement In case of Force Majeure Event that damages the facility, the extension of deadline for fulfilling obligations of the affected party will not be for a duration greater then the restoration schedule
Political Event | Every party, other than GOB and PGCB, can claim relief in relation to a PE event in regard to its obligations under the PPA No payments shall be made by either party affected by a force majeure event for the period of such event on account of its inability to perform its obligations under force majeure event. However, the supplier will not be excused from making payments due to the company under the agreement Political event includes fuel suppliers inability to supply gas/fuel excluding failure of transportation facilities In case of Political Event that damages the facility, the extension of deadline for fulfilling obligations of the affected party will not be for a duration greater then the restoration schedule In case of a material modification/ capital expenditure (greater than USD 450,000) required in the facility due to Change in Law or a Political Event, the company is required to provide to GOB: a) A preliminary estimate of the restoration cost subject to a Threshold amount (i.e. 10% of construction contract price through 5th year, 7.5% of construction contract price after 5th year or 5% of construction contract price after 10th year) b) A preliminary schedule of the completion of such Restoration In case of a political event, a) Prior to COD, the GOB/PGCB shall pay to the company within 25 days of demand, Carrying Cost + Escalable Capacity payment based on the type of political event + Total amount of principle repayment to be made by the Company on the next scheduled repayment date/ the number of days in beginning on the previous scheduled principle repayment date (or in case of 1st principle repayment, beginning on Scheduled COD) and ending on the first scheduled principle repayment date b) After COD, the GOB shall pay within 25 days of demand, Full Capacity payment based on last dependable capacity to the extent such capacity payment is not made by BPDB +Total amount of principle repayment to be made by the Company on the next scheduled repayment date/ the number of days in beginning on the previous scheduled principle repayment date (or in case of 1st principle repayment, beginning on Scheduled COD) and ending on the first scheduled principle repayment date In case of a material modification/capital expenditure required in the facility due to a Force Majeure Event

## Slide 222: Annexure M | Implementation Agreement Terms
Parameter | Conditions
Company event of default | Company Event of Default: GOB shall give a notice of default in case of following events except when such default is caused due to breach of relevant agreements by BPDB, GOB, PGCB, Gas Supplier, Fuel Supplier, due to Force Majeure or a Political Event: Failure of the Company to maintain Performance Security until delivery of Performance Security Deposit or failure to deliver and maintain Performance Security Deposit Failure of the Company to achieve Financial Closure by Required Financial Closure Date i.e. 9 months from the Project Effective Date Failure of the Company to achieve Construction Start Date within 90 days from the Financial Closure Date Failure of the Company to achieve Commercial Operation Date within 12 months from the Required Commercial Operation Date Abandonment of the facility or failure of Company to complete construction of the facility for 30 consecutive days between Construction Start Date and Commercial Operation Date Abandonment of operations of the facility by the Company for 25 consecutive days after COD Transfer of Company's rights, obligations and the facility itself without consent from GOB Any material breach by the Company that is not remedied in 30 days after notice from GOB8. Company Event of default under Implementation Agreement, Land lease agreement, Gas Supply Agreement or Fuel Supply Agreement unless waived by third party or cured Failure by company to submit and maintain Performance Security Deposit/ Operations Security Deposit Failure of the Company to make payments within 30 days from the due date except when security is available
GOB event of default | GOB Event of Default: Company shall give a notice of default in case of following events except when such default is caused due to breach of any of the project agreements by the Company or due to Force Majeure or a Political Event: Compulsory acquisition of the Company's Ordinary Share Capital or any material assets or rights or procurement of more then 25% of the Company's ordinary share capital Dissolution of BPDB except for privatization or amalgamation/restructuring/reorganization/corporatization provided a reasonable guarantee to the performance of the succeeding entity and all BPDB's obligations have been assigned to the new entity Dissolution of Gas/Fuel Supplier except for privatization or amalgamation/restructuring/reorganization/corporatization provided a reasonable guarantee to the performance of the succeeding entity and all BPDB's obligations have been assigned to the new entity Failure of GOB in making payments under Guarantee for 5 days Any material breach by GOB/PGCB that is not remedied in 30 days after notice from the Company Occurrence of an event of default by the gas/fuel Supplier or BPDB Change in Law making execution unlawful/unenforceable

## Slide 223: Annexure M | Implementation Agreement Terms
Parameter | Conditions
Rights and remedies in the event of default | Upon event of default, the non-defaulting party can choose to terminate this agreement by delivering a Notice of Intent to Terminate, specifying in reasonable detail the event of default Following the delivery of Intent to Terminate, the parties shall consult in good faith to remedy the default: a) 45 days: in case of default on payments or security b) 90 days: in any other event of default, or even longer duration of consulting in mutual agreement Notwithstanding the consulting, the defaulting party must undertake efforts to cure the default. In case the default is cured before the delivery of termination notice, the non defaulting party shall have no right to terminate At the expiry of the consultation period, if the default is not remedied or the parties have not reached an agreement, the non-defaulting party may deliver a Termination Notice to the other party The Company shall not seek to terminate this Agreement without first giving a copy of the notices to the GOB along with a request to cure the default within the cure period. GOB will have the option but not an obligation to cure default. If at the expiry of the cure period, if GOB is diligently attempting to remedy the default, other than a payment default, an additional period of 90 days will be provided In case of company event of default, GOB is required to give notice to the lenders of the Company with a request to cure the default within the cure period. No such termination will be valid till the expiration of: a) Initial Cure Period b) An Evaluation Period subsequent to expiry of the initial cure period - Earlier of delivery of Election notice by the Lenders to GOB or 30 days from expiration of Initial Cure Period. Upon delivery of Election Notice, Lenders have a period of 180 days to cure any Company Event of Default c) Lenders Cure Period - Period during which the Lenders either attempt to procure the cure of such default or enforce their rights under the Financing Documents
Obligation upon termination | In case of Company event of default, if the agreement is terminated before financial closing is achieved, the GOB may terminate this agreement and encash the Performance Security Deposit Compensation for termination will be payable in the following manner: In case of termination due to default or Force Majeure or Political Event, the GOB has the option to obtain the rights towards the facility in exchange for reasonable compensation as defined in the IA under different circumstances
Taxes | The company will be exempt from taxation or withholding tax in Bangladesh on its income Several other financial and tax incentives are also prescribed in the IA

## Slide 224: Annexure M | Implementation Agreement Terms
Parameter | Conditions
Dispute Resolution | Either party can give a written notice to the other for any dispute, along with description. Failing to resolve the dispute amicably within 30 days (or 10 days in case of dispute related to an invoice), the dispute shall be settled through referral to CEO and the designated representative of BPDB. After the expiry of 15 days from such referral, if the dispute is not settled, it will be referred to an Expert. In case the recommendation of the Expert is not acceptable to either party, it can initiate arbitration proceedings
Guarantee | The GOB shall deliver to the Company a Guarantee to the effect that GOB will pay any amount due to the Company by BPDB, PGCB, Gas Supplier, Fuel Supplier in case of failure to pay by the aforementioned parties
Termination | Company/GOB event of default not remedied Force Majeure or Political Event of BPDB of more than 12 months Force Majeure or Political Event of the company preventing it from achieving COD with 12 months of Scheduled COD or after COD, preventing operation for 9 months Infeasibility to restore facility due to Political/Force Majeure Event or inability to agree on a restoration schedule
Repatriation of funds | Transfer of funds outside Bangladesh will be governed by Exchange Regulations Act, 2016 Company permitted to purchase dollar through normal commercial banking channels for repatriation of funds
Governing Law | Rights and obligations of the parties shall be interpreted, construed and governed by the laws of England and Wales Arbitration shall be conducted at Dhaka except when the Company desires otherwise i.e. in Singapore

## Slide 225: Annexure M | Implementation Agreement - Termination Clause
Definition of key terms used for calculation of compensation upon termination
Term | Component
A | The sum of following terms: Total amount of principal outstanding to the Lenders under Financing documents and interest Total amount outstanding under any loan agreements for capital improvements, as approved by GoB, taking into account all Supplemental Tariff Payments Total amount of any other outstanding debt incurred by the Company that was approved by GoG, less any insurance proceeds received by the Company following a FME or PE, and not spent for Restoration Any winding up costs, prepayment charges or similar charges passed through by Lenders to the Company in accordance with Financing Documents Total amount outstanding equal to unpaid principal, accrued interest, prepayment penalties, fees, commissions, costs and expenses Principal amount shall not exceed the outstanding amount in amortization schedule, unless directly attributable to GoB Event of Default No accrued interest shall be paid by GoB for interest under Financing Document or loan agreement from and after default by Company, unless default results from default of GoB, PGCB, BPDB, Gas Supplier or Fuel Supplier
B | As of date of transfer of Facility to GoB, the equity investment by shareholders (USD), reduced on a straight line basis from CoD through the term of Implementation Agreement to 5% of initial value. The equity amount shall be further reduced by the following: Estimated cost of maintenance during then Scheduled Outages Estimated cost of maintenance during next major maintenance overhaul Both costs of maintenance to be pro rated by ratio of (i) Number of Days in the period from last such maintenance until date of termination to (ii) number of Days in period between last such maintenance and scheduled date for next such maintenance
C | For a period equal to lesser of 5 years and remainder of PPA term (but not less than 2 years), the Net Cash Flow (USD) for such period, discounted to present value by discount rate of 12% to the base case pro forma presented to Lenders at Financial Closing plus Net Cash Flow under any Supplemental Tariff Net Cash Flow implies net cash profits of the Company less all principal repayment amounts and without regard to depreciation
D | The sum of following terms: Any additional equity amounts (USD) contributed by shareholders under section 11B.1 Any other equity contributions (USD) approved by GoB Each case, the amount to be reduced by 3.2% of original amount of equity contribution for each year following date of contribution
E | The Sum of following terms: Any additional equity amounts (USD) contributed by shareholders under Section 11B.1 prior to PE/FME giving rise to restoration which led to termination by GoB, reduced by 3.2% of original amount of equity contributions for each year following date of such contribution Original equity contributions (USD) adjusted according to B Other equity contributions (USD), prior to PE and approved by GoB, reduced by 3.2 of original amount of equity contributions for each year following date of such equity contribution

## Slide 226: Annexure M | Implementation Agreement - Termination Clause
Termination Applicability
Sr. No | Termination Criteria | Compensation
1 | Company Event of Default | In case of Failure to achieve timely financial closing, or Any other default occurring before Financial Closure the sole right (and remedy) of GoB shall be to encash the Performance Security Deposit in full (acting through BPDB)
2 | Company Event of Default after Financial closure | A (If GoB / designee acquired rights, title & interests)
3 | GoB Event of Default | A+B+C+D (If Company elects to transfer facility to GoB / designee)
4 | Change in Law | A+B+C+D (other than when Restoration/modification is not feasible or GoB determines cost of not acceptable and the facility does not operate for 180 days and during such period Change in Law is not rescinded or modified in a way to permit Restoration or modification)
5 | Failure to achieve Restoration Schedule following Force Majeure | A+E (If GoB / designee acquired rights, title & interests) If GoB elects not to purchase Facility on effective date of termination, then no obligation
6 | Following Political Event | A+B+C+D (If Restoration deemed feasible, but GoB elects to terminate agreement)
 |  | A+B+C+D (If Restoration deemed not feasible)
 |  | A+B+D (If Restoration is feasible, but Company unable to obtain financing for Restoration)
 |  | A+E (Termination due to failure to complete Restoration in timely manner, but Company has made demonstrable good faith effort to effect Restoration)
 |  | A + (E/1.25) (Termination due to failure to complete Restoration in timely manner, but Company has not made demonstrable good faith effort to effect Restoration)
 |  | If PE has continued for 180 days (uninterrupted or intermittent) or following Change in Law, Restoration deemed technically infeasible or GoB determined cost of Restoration unacceptable and Change in Law has not been modified or rescinded to make Restoration technically or financially acceptable and facility has not been operated for 180 days, then: A+B+C+D (If GoB Terminates Agreement) A + B + C/2 + D (If Company Terminates Agreement)
 |  | A+B+D (If GoB terminated Agreement post revision of Restoration Cost Estimate or Restoration Schedule resulting from PE or Change in Law)

## Slide 227: Annexure M | Implementation Agreement - Termination Clause
Termination Applicability
Sr. No | Termination Criteria | Compensation
7 | Following FME or PE under IA, PPA, GSA or FSA | If FME or PE affects BPDB such that the it prevents operations of Facility for more than 12 months or Schedule CoD is delayed by more than 12 months A+B+C+D (GoB Termination) A + B + C/2 + D (Company Termination)
 |  | A+B+D (If FME affects the Facility and GoB elects to terminate if it prevents the Company from achieving the CoD within 12 months of the Scheduled CoD or prevents operations for a continuous period of 9 months or more
8 | Company Inability to Obtain Permits | A+B+C+D (If Company is unable to obtain necessary Government Authorization)

## Slide 228: List of Foreign Investment in Bangladesh Power Sector – Privately Owned Plants

## Slide 229: Annexure N | Plant Sponsors - Commissioned
Sr. No | Name | Fuel | Installed Capacity | Owner Group | Foreign Loan | MLA Funding | Foreign Equity | Remarks
1 | Haripur Power Ltd | GAS | 360 | Pendekar Group | ü | ü | ü | -AES Corporation served as senior sponsor facility with USD 37 million. -PRG (USD 60.9 million) by IDA, underwritten by ANZ Investment bank
2 | Sembcorp NWPC Ltd (Sirajganj 281.991 MW ) | GAS | 281.991 | Sembcorp Group | ü | ü | ü | Loan: -IFC: USD 165 million -CDC Group: USD 103 million -Clifford Capital: USD 103 million Equity: -Sembcorp Utilities: 71% (USD 103 million) -NWPGC: 29%
3 | Meghnaghat Power Ltd | GAS | 450 | Pendekar Group | ü | ü | ü | Loan (USD 220 million) by ADB and other facilities Equity (76%): Pendekar Energy
4 | Summit Bibiyana II Power Company Ltd | GAS | 341 | Summit Group | ü | ü | ü | Loan: -ADB, IFC, IsDB: USD 210 million Equity: -Summit Industrial and Mercantile Corporation Pvt Ltd: 80% -General Electric: 20%
5 | United Ashugang Energy Ltd | GAS | 195 | United Group | ü | ü | û | Loan: -ADB, IFC, IsDB: USD 210 million Equity: -APSCL: 7.58% -United Energy Limited: 92.42%
6 | ACE Alliance Power Limited (149 MW ) | HFO | 149 | Summit Group | ü | ü | û | Loan (USD 68.6 million): -OFID: USD 20 million -IDCOL, ICD, AAPL: Co-financers Equity: -Summit Power Limited: 64%
7 | KPCL Unit (2) | HFO | 115 | Summit Group & United Group | ü | ü | û | Loan (USD 50 million) from DEG, Germany and FMO, Netherlands Equity: -KPCL (Associate company of Summit): 99%
8 | Regent Power Limited | GAS | 108 | Habib Group | ü | ü | û | Loan: -IDCOL: USD 34 million -IFC: USD 20.2 million -Bangladesh Infrastructure Finance Fund Limited: USD 5 million Equity: -Owned by Habib Group: 34% equity (USD 28.8 million)
Legend: ü Yes û No N/A: Not Available
Source: Industry Reports, Deloitte Analysis

## Slide 230: Annexure N | Plant Sponsors - Commissioned
Sr. No | Name | Fuel | Installed Capacity | Owner Group | Foreign Loan | MLA Funding | Foreign Equity | Remarks
9 | Summit Meghnaghat Power Ltd. | GAS | 305 | Summit Group | ü | ü | û | Loan (USD 22 million) by ADB Equity (70%) by Summit
10 | Dhaka Northern Power Limited | HFO | 55 | Doreen Group | ü | ü | û | -75% project cost as debt from IPFF, World Bank and local commercial banks
11 | Dhaka Northern Power Limited | HFO | 55 | Doreen Group | ü | ü | û | -75% project cost as debt from IPFF, World Bank and local commercial banks
12 | Khulna Power Company Ltd. | HFO | 110 | Summit Group & United Group | ü | ü | û | Loan by IFC (USD 55.2 million)
13 | Lakdhanavi Bangla Power Ltd | HFO | 52 | Lakdhanavi Ltd Group | N/A | û | ü | Loan (USD 35 million): -IDCOL: USD 15 million -NDBIB and 4 Sri Lankan banks Equity: Subsidary of Lakdhanavi Ltd (largest IPP in Sri Lanka)
14 | Raj Lanka Power Limited | HFO | 52 | Lakdhanavi Ltd Group | N/A | û | ü | Loan : -Syndicated term loan with NDB: USD 12 million -Reddemable convertible Cumulative preference shares (structured by NDBIB): BDT 1.7 billion Equity: Subsidary of Lakdhanavi Ltd (largest IPP in Sri Lanka)
15 | United Ashugonj Power | GAS | 53 | United Group | N/A | û | û | Loan by Standard Chartered Bank, Mauritius
16 | M/S Banco Energy Generation Ltd. 53.972MW | HFO | 53.972 | Doreen Group | N/A | û | û | Loan: -AKA Bank and Commerzbank of Germany provided ECA (Euler Hermes)-backed debt funding ($26 million) through City Bank
17 | Orion Power Rupsha Limited (OPRL).Khulna (105 MW ) | HFO | 105 | Orion Group | N/A | û | û | Loan: -Mercantile Bank (lead lender) with participation of Mashreqbank PSC
Legend: ü Yes û No N/A: Not Available
Source: Industry Reports, Deloitte Analysis

## Slide 231: Annexure N | Plant Sponsors - Commissioned
Sr. No | Name | Fuel | Installed Capacity | Owner Group | Foreign Loan | MLA Funding | Foreign Equity | Remarks
18 | Dutch Bangla Power & Associates Ltd. | HFO | 100 | Orion Group | N/A | û | û | Loan: -Agrani Bank Limited, Janata Bank Limited and Mashreq Bank psc, Dubai signed a tripartite agreement for providing SBLC facility.
19 | IEL Consourtium & Associates | HFO | 100 | Orion Group | N/A | û | û | Loan: -Agrani Bank Limited, Janata Bank Limited and Mashreq Bank psc, Dubai signed a tripartite agreement for providing SBLC facility.
20 | Kodda Gazipur 300 (Summil Unit-) | HFO | 300 | Summit Group | N/A | û | û | Loan (USD 140 million): - Clifford Capital and Sumitomo Mitsui Banking Corporation
21 | Khanjahan Ali Power | HFO | 40 | Summit Group & United Group | N/A | û | û | -Term Loan from Standard Chartered Bank, Mauritius (USD 19.5 million)
22 | Barkatullah Electro Dynamics Ltd. | GAS | 51 | Barakatullah Electro Dynamics Ltd | û | û | û | Loan by DCL, BRAC Bank, AB Bank, Trust Bank, Janata Bank and Industrial and Infrastructure Development Finance Company Limited (IIDFC) (125 Crore Tk)
23 | Doreen Power Ltd, Feni | GAS | 22 | Doreen Group | û | û | û | Loan by NCC Bank: USD 10 million
24 | Doreen Power Tangail | GAS | 22 | Doreen Group | û | û | û | Loan by NCC Bank and Bangladesh Bank: USD 4.7 million
25 | Venture Energy Resources Ltd, | GAS | 33 | Sinha Group | û | û | û | Loan by IDCOL: BDT 200 million
26 | Baraka Shikalbaha Power Ltd. 105 MW | HFO | 105 | Baraka Power Group | û | û | û | Financed by local banks (BDT 5250 million)
27 | Baraka Patenga Power Limited | HFO | 50 | Baraka Power Group | û | û | û | -Syndicated term loan of (BDT 2.2 billion) by United Commercial Bank -Barakatullah Electro Dynamics equity (USD 12.8 million)
28 | ECPV Power Ltd | HFO | 108 | Energypac Powergeneration | û | û | û | Loan: -IDCOL: USD 30 million - IDLC Finance Ltd: BDT 2.28 billion
Legend: ü Yes û No N/A: Not Available
Source: Industry Reports, Deloitte Analysis

## Slide 232: Annexure N | Plant Sponsors - Commissioned
Sr. No | Name | Fuel | Installed Capacity | Owner Group | Foreign Loan | MLA Funding | Foreign Equity | Remarks
29 | Sinha people Energy Ltd | HFO | 51 | Sinha Group | û | û | û | -Syndicated Term loan (BDT 2180 million) by IIDFC, for which Banglaesh Infrastructure Finance Fund gave BDT 100 crore
30 | Amnura (Sinha Power Generation) | HFO | 50 | Sinha Group | û | û | û | - Syndication of 2348.50 million BDT by IIDFC
31 | Midland East Power .Ltd(MEPL) 150MW Ashuganj B baria | HFO | 150 | Youth Group | û | û | û | - Local Eastern Bank (80% total cost) - Viyelletex Group and Shahibazar power(20% cost)
32 | Paramount BTrac Energy Limited. , Bagabari, Sirajganj (200MW) | HSD | 200 | Bangla Trac Group | û | û | û | 
33 | Desh Energy - Shiddhirgonj 100 MW | HSD | 100 | Mohammadi Group | û | û | û | -City Bank: 3280 million BDT Syndicated financing facilities
34 | Bangla Trac Power Unit-ll Limited | HSD | 100 | Bangla Trac Group | N/A | û | N/A | - Eastern Bank Limited raised syndication term loan of 465 Cr Tk. - Other participating lenders: Bangladesh Infrastructure Finance Fund, Saudi Bangladesh Industrical and Agricultural Investment Company, Rupali Bank and Shahjalal Islami Bank
35 | GBB Power Limited | GAS | 22 | GBB Group | û | û | N/A | Loan(BDT 84 Crore): -Bank Asia and 9 other banks (Uttara Bank Ltd, IFIC Bank Ltd, United Commercial Bank Ltd, Dhaka Bank Ltd, NCC Bank Ltd, Premier Bank Ltd, Mutual Trust Bank Ltd and Bangladesh Commerce Bank Ltd) Equity: - Joint Venture Between GBB Group and Caladonian Power Limited
36 | Kushiara Power Company Limited | GAS | 163 | Max Group | û | û |  | Loan (USD 50 Million and BDT 3900 million) by IDCOL, Pubali Bank Ltd and NCC Bank Ltd
37 | NEPC Consortium Power Ltd. | HFO | 110 | Pendekar Group | N/A | N/A | ü | - NEPC Consortium Power Limited is an indirect subsidiary of Pendekar Energy (L) Limited, a 55:45 joint venture company between the Group and Aljomaih Automotive Company Limited.
38 | APR Energy 300 MW | HSD | 300 | APR Energy | N/A | N/A | ü | - 100% owned by APR Energy
Legend: ü Yes û No N/A: Not Available
Source: Industry Reports, Deloitte Analysis

## Slide 233: Annexure N | Plant Sponsors - Commissioned
Sr. No | Name | Fuel | Installed Capacity | Owner Group | Foreign Loan | MLA Funding | Foreign Equity | Remarks
39 | DPA Power Gen. Int. Ltd | HSD | 50 | Bangladesh Army | N/A | N/A | ü | -joint initiative of the Army-run Bangladesh Diesel Plant, Primordial Energy Ltd and Germany-based Aggretech AG
40 | Precision Energy Ltd. | GAS | 55 | Anlima Yarn Dyeing | N/A | N/A | û | 
41 | Regent Energy & Power Ltd. | GAS | 22 | Habib Group | N/A | N/A | û | 
42 | Energyprima Limited, Kumargaon | GAS | 50 | Hosaf Group | N/A | N/A | û | -Energyprima Limited (EPL), a sister concern of Hosaf Group
43 | Energyprima Limited, Shahjibazar | GAS | 50 | Hosaf Group | N/A | N/A | û | -Energyprima Limited (EPL), a sister concern of Hosaf Group
44 | Energyprima Limited, Fenchugonj | GAS | 44 | Hosaf Group | N/A | N/A | û | -Energyprima Limited (EPL), a sister concern of Hosaf Group
45 | Energyprima Limited, Bogra | GAS | 20 | Hosaf Group | N/A | N/A | û | -Energyprima Limited (EPL), a sister concern of Hosaf Group
46 | Max Power Ltd | GAS | 78.5 | Max Group | N/A | N/A | û | 
47 | Desh Cambridge Kumargaon Power Co. Ltd. | GAS | 10 | Mohammadi Group | N/A | N/A | û | 
48 | Summmit Purbanchal Power Ltd. | GAS | 33 | Summit Group | N/A | N/A | û | 
49 | Shahjanullah Power Generation Co Ltd | GAS | 25 | United Group | N/A | N/A | û | 
50 | Shahjibazar Power Co. Ltd. | GAS | 86 | Youth Group | N/A | N/A | û | 
51 | Midland Power Company Ltd. | GAS | 51 | Youth Group | N/A | N/A | û | -Joint venture effort between Viyellatex Group and Shahjibazar Power Company Limited (49%)
Legend: ü Yes û No N/A: Not Available
Source: Industry Reports, Deloitte Analysis

## Slide 234: Annexure N | Plant Sponsors - Commissioned
Sr. No | Name | Fuel | Installed Capacity | Owner Group | Foreign Loan | MLA Funding | Foreign Equity | Remarks
52 | Acorn Infracture Services Unit-3 Ltd | HFO | 100 | Bangla Trac Group | N/A | N/A | û | 
53 | Acron Infrastructure Services Ltd (Julda) | HFO | 100 | Bangla Trac Group | N/A | N/A | û | 
54 | Confidence Power Bogra Unit-2 Limited | HFO | 113 | Confidence Cement Group | N/A | N/A | û | 
55 | CLC Power Company Ltd | HFO | 108 | Maisha Group | N/A | N/A | û | 
56 | Desh Energy Chandpur Power Company Ltd. (DECPCL) | HFO | 200 | Mohammadi Group | N/A | N/A | û | 
57 | Digital Power & Associates Ltd. | HFO | 102 | Orion Group | N/A | N/A | û | 
58 | Energis Power Corporation Ltd. | HFO | 51 | Shaha Denims | N/A | N/A | û | -Energis Power Corporation is a subsidiary of Shasha Denims Limited
59 | Power Pac Mutiara Keranigonj | HFO | 100 | sikder group | N/A | N/A | û | 
60 | PowerPac Muturia-Jamalpur | HFO | 95 | sikder group | N/A | N/A | û | 
61 | Summit Barisal Power Ltd. | HFO | 110 | Summit Group | N/A | N/A | û | 
62 | Summit Narayangonj Power Ltd. | HFO | 103 | Summit Group | N/A | N/A | û | 
63 | Summit Narayanganj Power Unit-II Ltd. | HFO | 33 | Summit Group | N/A | N/A | û | 
Legend: ü Yes û No N/A: Not Available
Source: Industry Reports, Deloitte Analysis

## Slide 235: Annexure N | Plant Sponsors - Commissioned
Sr. No | Name | Fuel | Installed Capacity | Owner Group | Foreign Loan | MLA Funding | Foreign Equity | Remarks
64 | United Anawara 300 MW | HFO | 300 | United Group | N/A | N/A | û | 
65 | Summit Meghnaghat Power Ltd. | HSD | 203 | Summit Group | N/A | N/A | û | Loan (USD 22 million) by ADB under Public Private Infrastructure development
66 | Aggreko International Projects Ltd. (95MW) | GAS | 95 | Aggreko Energy | N/A | N/A | N/A | 
67 | Aggreko International Projects Ltd. (85MW) | GAS | 85 | Aggreko Energy | N/A | N/A | N/A | 
68 | Northern Power Solution Ltd. | HFO | 50 | N/A | N/A | N/A | N/A | 
69 | UMPL 200 MW | HFO | 200 | United Group | N/A | N/A | N/A | 
70 | United Jamalpur 115 MW | HFO | 115 | United Group | N/A | N/A | N/A | 
71 | Bangla Trac Power Unit- l Limited | HSD | 200 | Bangla Trac Group | N/A | N/A | N/A | 
72 | Aggreko Energy Solution Ltd 100 MW, Aorahati | HSD | 100 | Aggreko Energy | N/A | N/A | N/A | 
73 | Aggreko Power Solution Ltd 100 MW, Bhahmangoan | HSD | 100 | Aggreko Energy | N/A | N/A | N/A | 
74 | Aggreko International Projects Ltd. (55MW) | HSD | 55 | Aggreko Energy | N/A | N/A | N/A | 
Legend: ü Yes û No N/A: Not Available
Source: Industry Reports, Deloitte Analysis

## Slide 236: Annexure O | Plant Sponsors – Upcoming / Planned
Sr. No | Name | Fuel | Installed Capacity | Owner Group | Foreign Loan | MLA Funding | Foreign Equity | Remarks
1 | LNG based 750 MW CCPP | LNG | 718 | Reliance Power | ü | ü | ü | Loan: -ADB (USD 330 million) and IDB Equity: - Reliance Power: 51% -JERA (Japanese) : 49%
2 | Meghnaghat 600 MW CCPP | LNG | 583 | Summit Group | ü | ü | ü | Loan: -IFC and Janata Bank Equity: -Summit Group: 80% -GE: 20%
3 | Thakurgaon 100 MW Power Plant | HFO | 115 | Energypac power venture | ü | ü | ü | Loan: - ECA and MLA based finances raised by Daelim Energy Equity: - EMA Power Investment : 49% -EMA Power Investment (UAE) is a JV between Daelim Energy(South Korea) and IDB Fund II (Islamic Development Bank Infrastructure Fund II)
4 | Bhola 220 MW CCPP (D/F) | Gas | 220 | Shapoorji Palloni Infrastructure Capital | N/A | û | ü | Loan: -Asian Investment and Infrastructure Bank: USD 60 million -Islamic Development Bank: USD 60 million
5 | Chandpur 115 MW Power Plant | HFO | 115 | Doreen Group | û | û | û | Loan: -Syndicated loans (BDT 520 Crore): arranged by Dhaka Bank Equity: -Subsidary of Doreen; investment of BDT 160 crore
6 | Tangail 22 MW PP (Polli Power) | HFO | 22 | X Index Companies | û | û | û | -Prime Bank is mandated to raise syndication finance
7 | Kanchan, Narayangonj 55 MW PP | HFO | 55 | X Index Companies | û | û | û | -Prime Bank is mandated to raise syndication finance
8 | Payra, Patuakhali 1320 Coal Fired Power Plant (1st Phase) | Imported Coal | 1320 | BCPCL | N/A | û | ü | Loan: -CEXIM Bank: USD 1.984 billion Equity: - JV between NWPGCL and CMC (China)
Legend: ü Yes û No N/A: Not Available
Source: Industry Reports, Deloitte Analysis

## Slide 237: Annexure O | Plant Sponsors – Upcoming / Planned
Sr. No | Name | Fuel | Installed Capacity | Owner Group | Foreign Loan | MLA Funding | Foreign Equity | Remarks
9 | Julda, Chattogram 100 MW PP (Accorn Inf ) (Unit-2) | HFO | 100 | Bangla Trac Group | û | N/A | û | Term loan (USD 63 million): IDCOL
10 | Manikganj 162 MW PP | HFO | 162 | Chase Power Ltd | N/A | N/A | ü | -Consortium of Changzhou Hutang Coal Power Co. Ltd.(China) and Icon Enterprise Ltd., and Chase Power Ltd. (Bangladesh)
11 | Feni 114 MW Power Plant | HFO | 114 | Lakdhanavi Limited | N/A | N/A | ü | Loan: - DFCC Bank and HNB Bank: INR 750 million Equity: -Subsidiary of Lakdhanavi Ltd -Lanka Ventures Limited Energy Fund PLC : 26% shareholding and USD 8 million investment
12 | Barishal 307 MW Coal Fired Power Plant | Imported Coal | 307 | ISO Tech Electrification | N/A | N/A | ü | JV between PowerChina (China) and ISO Tech Electrification (Bangladesh)
13 | Chattogram 2 x 612 MW Coal Fired Power Project | Imported Coal | 1224 | S Alam Group | N/A | N/A | ü | Loan: - CEXIM bank: USD 1.739 billion Equity: -JV of Bangladesh S Alam Group (70%), China’s SEPCO-3 Electric Power Constitution Corporation(20%) and HTG Group (10%)
14 | Meghnaghat 600 MW CCPP | LNG | 584 | Unique Group | N/A | N/A | ü | Loan: -IFC and Janata Bank Equity: -Summit Group: 80% -GE: 20%
15 | Shikalbaha 110 MW PP (Kornofuly Power) | HFO | 110 | Baraka Power Group | N/A | N/A | û | 
16 | Choumohoni, Noakhali 113 MW Power Plant | HFO | 113 | Hosaf Group | N/A | N/A | û | 
17 | Meghnaghat 500 MW CCPP | LNG | 450 | Anlima Textiles | N/A | N/A | N/A | Equity: - Anlima textiles - GE Capital Global Energy Investments BV
Legend: ü Yes û No N/A: Not Available
Source: Industry Reports, Deloitte Analysis

## Slide 238: Annexure O | Plant Sponsors – Upcoming / Planned
Sr. No | Name | Fuel | Installed Capacity | Owner Group | Foreign Loan | MLA Funding | Foreign Equity | Remarks
18 | Bogura 100 MW Power Plant (Unit-1) | HFO | 113 | Confidence Cement | N/A | N/A | N/A | - USD135 million term loan facility from IDCOL for Bogra, Rangpur and Chittagong Projects
19 | Rangpur 113 MW Power Plant | HFO | 113 | Confidence Cement | N/A | N/A | N/A | - USD135 million term loan facility from IDCOL for Bogra, Rangpur and Chittagong Projects
20 | Potiya, Chattogram 100 MW PP (Precision Energy) | HFO | 116 | Anlima Textiles | N/A | N/A | N/A | 
21 | Bhairab 50 MW PP | HFO | 54 | N/A | N/A | N/A | N/A | 
22 | Shikalbaha, Chattogram 54 MW PP | HFO | 54 | N/A | N/A | N/A | N/A | 
23 | Meghnaghat 104 MW Power Plant | HFO | 104 | Orion Group | N/A | N/A | N/A | 
24 | Payra, Patuakhali 1320 Coal Fired Power Plant (2nd Phase) | Imported Coal | 1320 | BCPCL | N/A | N/A | N/A | 
Legend: ü Yes û No N/A: Not Available
Source: Industry Reports, Deloitte Analysis

## Slide 239: Annexure P | List of Major Private Investors in Bangladesh
Top 20 Private Players in Bangladesh and their Portfolio in FY19
S. No. | Group | GAS (MW) | HFO (MW) | HSD (MW) | Total (MW)
1 | Summit Group | 679 | 695 | 203 | 1,577
2 | Pendekar Group | 810 | 110 | - | 920
3 | United Group | 273 | 615 | - | 888
4 | Bangla Trac Group | - | 200 | 500 | 700
5 | Aggreko Energy | 180 | - | 255 | 435
6 | Orion Group | - | 407 | - | 407
7 | Mohammadi Group | 10 | 200 | 100 | 310
8 | APR Energy | - | - | 300 | 300
9 | Youth Group | 137 | 150 | - | 287
10 | Sembcorp Group | 282 | - | - | 282
11 | Summit & United Group | - | 265 | - | 265
12 | Max Group | 242 | - | - | 242
13 | Doreen Group | 44 | 164 | - | 208
14 | sikder group | - | 195 | - | 195
15 | Hosaf Group | 164 | - | - | 164
16 | Baraka Power Group | - | 155 | - | 155
17 | Sinha Group | 33 | 101 | - | 134
18 | Habib Group | 130 | - | - | 130
19 | Confidence Cement Group | - | 113 | - | 113
20 | Energypac | - | 108 | - | 108
 | Total | 2,984 | 3,478 | 1,358 | 7,820
The Summit, Pendekar, United and Bangla Trac have a ~50% share in the private power portfolio in Bangladesh; The major gas based power plants players are Summit, Pendekar, United and Sembcorp Groups in Bangladesh with a portfolio of ~2,000 MW
Source: BPDB, Industry Reports Deloitte Analysis

## Slide 240: Annexure Q | Retail Tariff Hike Trend
Consumer Category Wise Electricity Consumption (%)
Chart: 
 | 5.85 | 5.99 | 6.38 | 6.77
 | 2.51 | 3.82 | 4 | 4.16
 | 7.42 | 7.66 | 8.1333 | 8.51
 | 9.58 | 9.8 | 9 | 9.48
 | 6.15 | 6.33 | 6.77 | 7.13
  Mar-20
  Mar-14
  Sep-15
  Dec-17
  Wt. Average Retail Supply Tariff
  Commercial & Office
  Residential
  Industrial
  Agriculture
The average retail price covers the overall bulk power selling rate of BPDB (~BDT 5.0 / kWh) along with the discoms operations cost Thus, most of the discoms in Bangladesh are profitable (i.e. WZPDDCL, DPDC, DESCO among others) as of FY19 The agriculture tariff category has witnessed the highest average CAGR in the last 6 years at ~9% followed by residential category at 2.5% CAGR which contributes ~53% of the total power consumption in Bangladesh The Industrial and Commercial Tariff have increased at a lower CAGR of ~2.4% and 1.2% respectively Thus, at an overall level, the the average retail tariff for consumers has grown at a CAGR of 2.5% in the last 6 years which is higher than the average bulk supply tariff hike rate of ~1.7% CAGR
Source: BPDB, Deloitte Analysis; Note 1) The average tariff for residential consumers have been considered as an average of their telescopic tariffs at 11 KV / 132 Volts / 230 Volts levels . The industrial and commercial users have been considered based on the flat rate as per BERC Tariff Orders for BPDB at 11 KV / 132 Volts / 230 Volts level
+2.5%
+8.8%
+2.4%
+1.2%
+2.5%
CAGR (%)
Average Total Retail Tariff for Key Consumer Categories (BDT / kWh)
Chart: 
 | 53.31 | 2.81 | 29.55 | 12.11 | 2.22
  Others
  3%
  2%
  FY19

## Slide 241
This document is confidential and prepared solely for your information. Therefore you should not, without our prior written consent, refer to or use our name or this document for any other purpose, disclose them or refer to them in any prospectus or other document, or make them available or communicate them to any other party. No other party is entitled to rely on our document for any purpose whatsoever and thus we accept no liability to any party who is shown or gains access to this document.
Deloitte refers to one or more of Deloitte Touche Tohmatsu Limited, a UK private company limited by guarantee, and its network of member firms, each of which is a legally separate and independent entity. Please see www.deloitte.com/about for a detailed description of the legal structure of Deloitte Touche Tohmatsu Limited and its member firms.
© 2020 Deloitte Touche Tohmatsu India LLP. All rights reserved.